## Slide 1: Lecture 17 Embedded Systems Research
CE346 – Microprocessor System Design
Branden Ghena – Fall 2022
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
This is the last lecture!! 😭
  No class after Thanksgiving
  I’ll hold office hours, but in my office
  WARNING: CG50 is busy 3:30-5:00 pm Tuesday/Thursday (CE355)
Project Demos – Tuesday of Exam Week
  Tuesday 12/6, Mudd 3514, 1:00-7:00 pm
  I’ll release a schedule next week (everyone can be accommodated)

## Slide 3: Today’s Goals
Explore sensing systems research
  What does it mean to do “research”
  Explore a research project in that context (Powerblade)
  Discuss some example Sensing Research projects
    Most shallowly
    Signpost project deeply

## Slide 4: Outline
What does research look like:
  Research Overview
  Example: Powerblade
Sensing Systems Research
  Various Projects
  Signpost

## Slide 5: What is research anyways?
I think of research as just “figuring stuff out”
This is part of why research feels so vague: there are many ways to figure things out, depending on the question
  Read papers
  Run experiments
  Send out surveys
  Build something

## Slide 6: Academic research
We all do research all the time in our daily lives
Academic research is mostly about the question you’re figuring out
  Is the question important in some way?
  Is the question something that’s not trivial to answer?
  Does the answer provide value?
Finding the “right” questions is hard

## Slide 7: Academic research in engineering
Often intertwines the act of “figuring out” with engineering
  Need to build something to try out and that can answer the question
Hard part is remembering that the question is more important than the engineering
  Building something that only partially works is fine if it answers the question
  We call this a research prototype
Unfortunately, something working in a research paper is definitely not the same as a working product

## Slide 8: Getting a PhD
PhD students “do research”
Getting a PhD requires a thesis (a good question) and a dissertation (describing and proving the answer)
PhDs in engineering in US
  5-6 years average
  Are paid for! (tuition plus $30k-40k)
  Are not a good monetary decision in CS
    There are other reasons for them, just not for money

## Slide 9: Getting involved in research
Research with faculty
  Often take a 300-level course with a faculty and do well
  Then talk to them about joining their lab
NSF Research Experience for Undergrads
  Summer programs held at universities throughout the US
  You apply for these, like internships
Any research counts! Even if it’s not in exactly your field
  You’ll find more similarities than differences
  It all looks similarly good on applications

## Slide 10: Research outputs
Papers (Journal, Conference, Workshops, etc.)
  Provide a mechanism for others to find your work
  Peer-reviewed papers are reviewed by other professors in the field to ensure that the seem valid
Good papers do the following
  Explain what the problem is
  Explain why the problem is important
  Explain how other research relates to this
  Explain an answer to the problem
  Prove that the answer to the problem is real
  Explain the limitations of the answer

## Slide 11: Outline
What does research look like:
  Research Overview
  Example: Powerblade
Sensing Systems Research
  Various Projects
  Signpost

## Slide 12: Powerblade (DeBruin, Ghena, Kuo, Dutta)
1” x 1” x 1/16” plug load power meter
Measures AC voltage and current and reports real-time power draw over Bluetooth Low Energy
Question: can a plug-load power meter be created in a 2D form factor to enable easy deployability while still being accurate?

## Slide 13: What is the problem and why is it important?
Miscellaneous electrical loads (MELs) occupy an increasingly large percentage of overall energy use

## Slide 14: What is the problem and why is it important?
Existing power meters are too cumbersome for ubiquitous deployment
Goal: unobtrusively measure all plug-loads in a home over a long period of time with high fidelity and low cost
  Needs to be real-world sustainable
  Needs to not impede daily life

## Slide 15: How does other work relate to this?
No other devices are as small as Powerblade
Many use more power themselves
Some do not have wireless communication or measure real power
Real Power?

## Slide 16: What is an answer to the problem?
Must re-think design of power meters from basics
Five core steps that a power meter must handle
  Convert AC mains voltage to usable DC voltage
  Measure voltage
  Measure current
  Calculate power and energy
  Communicate measurements
Revisit each and show that it can be changed

## Slide 17: Answer - creating a usable DC voltage
Basic circuit below applies
  But usually Zin is a large capacitor to provide enough power for the device to run
  We can instead use a small resistor if our average current is very low (< 800 μA)
Belkin Insight
Kill-A-Watt

## Slide 18: Answer - measuring voltage
Sockets take up a lot of physical room
Flexible tabs
Instead use flexible PCB tabs
(This was finicky and non-reusable in practice)

## Slide 19: Answer - measure current
Horizontally wound coil translates magnetic field into a voltage
Creates a signal that is the derivative of current

## Slide 20: Answer - calculate power and energy
Perform computation in a modern microcontroller
  Keeps up with calculations that an IC usually does
  MSP430FRxx - MSP430 with FRAM
Can perform work at a very low average power
  Sampling, integration, computation, and output

## Slide 21: Answer - communicate measurements
Transmitting average power over BLE presents results while keeping within energy budget
  Update average measurements once per second
  Send 5 packets per second for reliability

## Slide 22: Prove that the answer to the problem is real
From 2 W to 1200 W, average error is 1.13%
Device | Power Factor | Power | PowerBlade Error | 
150 W Bulb | 1.00 | 162.17 W | -0.99 W | 0.61%
Fridge | 1.00 | 108.22 W | -5.30 W | 4.90%
Drill (Max) | 0.99 | 253.21 W | 2.96 W | 1.26%
Toaster | 0.99 | 827.87 W | -22.11 W | 2.67%
Vacuum | 0.98 | 1246.96 W | 15.24 W | 1.22%
Microwave | 0.92 | 1729.73 W | 16.01 W | 0.93%
Hot Air Gun | 0.83 | 305.54 W | -1.93 W | 0.63%
TV (Normal) | 0.62 | 196.23 W | -9.03 W | 4.60%
TV (Static Image) | 0.61 | 129.51 W | -4.00 W | 3.09%
50 W CFL | 0.61 | 48.57 W | -9.51 W | 19.58%
Xbox One | 0.57 | 50.44 W | -0.83 W | 1.65%
MacBook | 0.51 | 52.68 W | -4.49 W | 8.52%
Blender | 0.49 | 106.63 W | 36.97 W | 34.67%
Router | 0.46 | 9.11 W | -0.62 W | 6.81%
Drill (Low) | 0.30 | 51.10 W | 20.40 W | 39.92%

## Slide 23: Explain the limitations
Power factor measurements are very power at low wattages
  Although the wattage itself remains accurate
Also change to pogo pins for better, repeatable contact

## Slide 24: Break + xkcd
https://xkcd.com/2456/

## Slide 25: Outline
What does research look like:
  Research Overview
  Example: Powerblade
Sensing Systems Research
  Various Projects
  Signpost

## Slide 26: Conferences for sensing systems research
SenSys
  Conference on Embedded Networked Sensor Systems
IPSN
  Conference on Information Processing in Sensor Networks
MobiCom
  Conference on Mobile Computing and Networking
UbiComp
  Conference on Pervasive and Ubiquitous Computing
Various other systems or HCI venues
  Occasionally Electrical or Civil Engineering venues too

## Slide 27: Sensing systems research
Combination of engineering and exploration
Generally divides into two different focuses
  Often projects will mix some of each domain
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 28: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 29: Permamote (Jackson, Adkins, Dutta)
Goal: create a 10-year wireless sensor
Solutions
  Modern sensors and microcontroller
  Energy harvesting combined with rechargeable battery
  Non-rechargeable battery as backup power
https://lab11.eecs.berkeley.edu/content/pubs/jackson19capacity.pdf

## Slide 30: Permamote low energy design
Uses components with extremely low idle power to limit energy needs
Combination of harvesting plus battery enables continuous operation

## Slide 31: Tock (Levy, Campbell, Ghena, Giffin, Pannuto, Dutta, Levis)
Goal: safe and reliable embedded OS
  Demonstrate this is possible on small embedded platforms
Solutions
  Dedicated OS kernel with separate applications
  Protect applications with hardware features
    Memory Protection Unit
  Protect kernel with language features
    Rust programming language
https://lab11.eecs.berkeley.edu/content/pubs/levy17multiprogramming.pdf

## Slide 32: Tock software organization
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
System Calls
6LoWPAN
SI7021
SD Card
Console
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf
Syscall Interface

## Slide 33: Sensing systems research
Platforms
  How to improve the capabilities of sensing systems
  Examples: lower power, better wireless, new sensors
Applications
  How to use sensing systems to meet some desired goal
  Examples: track human interactions, measure household energy use

## Slide 34: Opo (Huang, Kuo, Pannuto, Dutta)
Goal: sense distance of human interactions
  Real-time, high accuracy, deployable
Solutions
  Ultrasonic allows for low-power detection of nearby devices
  Also provides directionality
  Measure difference in arrival time of RF and Ultrasonic to determine distance
https://lab11.eecs.berkeley.edu/content/pubs/huang14opo.pdf

## Slide 35: Opo low-energy ranging
RX of ultrasonic pulse wakes the device
Listens for RF and ultrasonic to measure time difference

## Slide 36: Powerwatch (Klugman, Adkins, et al.)
Goal: measure electric grid reliability in developing regions
“Access alone is insufficient. Reliability matters too.”
Solutions:
  Wall-powered sensor with battery-backup to detect outages and report over cellular
  Infrastructure to collect measurements and cross-correlate
  Create a team to manage the deployment
https://lab11.eecs.berkeley.edu/content/pubs/klugman19scale.pdf

## Slide 37: Powerwatch deployments require continuous upkeep
Handing someone a sensor does not guarantee long deployment
Initially 1000 devices fell to 600, then 300 over three months

## Slide 38: Outline
What does research look like:
  Research Overview
  Example: Powerblade
Sensing Systems Research
  Various Projects
  Signpost

## Slide 39: The Signpost Project
An example of “Platforms” research
Goal: platform that enables low-effort city-scale sensing deployments

## Slide 40: What things might we want to sense at the scale of a city?

## Slide 41: Air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2018.
[1]
[1]
[2]
[2]

## Slide 42: Audio detection, classification, and localization
[1] Girod et al. The Design and Implementation of a Self-Calibrating Distributed Acoustic Sensing Platform. 2006. [2] Lédeczi et al. Multiple Simultaneous Acoustic Source Localization in Urban Terrain. 2005. [3] Sounds of New York City. 2016.
[1]
[1]
[2]
[3]

## Slide 43: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 45
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 46
Air Quality Monitoring
Urban Noise Classification
Traffic Queue Sensing
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Sounds of New Your City. 2016. [3] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[2]
[3]
Lots of interesting applications and interested parties. But let’s look at the process of actually creating and deploying an application.

## Slide 47: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 48: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 49: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 50: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Sustainable Power
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 51: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Sustainable Power
Weatherproof Casing
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 52: Many steps to building traffic queue sensing
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1]
Sustainable Power
Weatherproof Casing
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012

## Slide 53: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1] Sounds of New York City. 2016
[1]
Sustainable Power
Weatherproof Casing
[1]

## Slide 54: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Storage
Storage Driver
Deploy
[1] Purple Air. 2018
[1]
Sustainable Power
Weatherproof Casing
[1]
Networking Driver

## Slide 55: Signpost Enables City-Scale Sensing
Sensing Hypothesis/Hardware
Deploy
[1] Purple Air. 2018.
[1]
[1]
Integrate with Signpost
Joshua Adkins, Branden Ghena, Neal Jackson, Pat Pannuto, Samuel Rohrer, Bradford Campbell, and Prabal Dutta ”The Signpost Platform for City-Scale Sensing." IPSN’18 - https://brandenghena.com/projects/signpost/adkins18signpost.pdf

## Slide 56
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 57: Key functions are repeated
Sensing Hypothesis/Hardware
Networking
Networking Driver
Storage
Storage Driver
Deploy
[1] Purple Air. 2018
[1]
Sustainable Power
Weatherproof Casing
[1]

## Slide 58
Deployment | Services Needed |  |  |  |  |  | 
 | Power | Networking | Processing | Storage | Time | Synch | Location
Caraoke [3] |  |  |  |  |  |  | 
Bouillet et al. [4] |  |  |  |  |  |  | 
Aircloud [5] |  |  |  |  |  |  | 
Girod et al. [6] |  |  |  |  |  |  | 
Ledeczi et al. [7] |  |  |  |  |  |  | 
SenseFlow [8] |  |  |  |  |  |  | 
Argos [9] |  |  |  |  |  |  | 
SONYC [1] |  |  |  |  |  |  | 
Kyun Queue [10] |  |  |  |  |  |  | 
Micronet [11] |  |  |  |  |  |  | 
Higher power/linux class processing
Can be provided with a GPS

## Slide 59: Software abstraction through a single interface
Sensing Hypothesis/Hardware
Networking
Storage
Sustainable Power
Sensor
Platform
GPS
High Performance Processing
Platform Interface
Platform Controller
- Ubiquitous
- Easy to adapt/implement
- Physically pluggable

## Slide 60
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 61: Some applications require granularity
Data can change greatly in low distances
Outlier
Notes: If we want to

## Slide 62: Deployment overhead drives cost
Expensive to work with the city
Time consuming
Not conducive to experimentation!
Do not rely on wired infrastructure
No wired power
  Solar provides more power density than batteries
No wired networking
Should not modify existing infrastructure

## Slide 63: Multi-tenancy is beneficial to testbeds
One deployment can enable many stakeholders simultaneously
Need to ensure that they do not conflict

## Slide 64
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 65: The Signpost Platform

## Slide 66: Core modules provide shared resources
GPS
Processing
Storage
Making the platform modular supports upgradeability
Networking
BLE
LoRa
3G
Control Module
Radio Module

## Slide 67: Measurement and isolation support multi-tenancy
Power Metering
Isolation
& Monitoring

## Slide 68: Standard interface for accessing shared resources
Any software framework can be used for modules

## Slide 69: Array of Things is one platform approach
Include sensors as platform resources
Applications are software that act on sensor data
High-power hardware and expensive to deploy

## Slide 70: Signpost explores the other end of the spectrum
What can we do with less?
Low-power, low-capability, extremely deployable
Limited provided resources, but lots of extensibility
Focus on modularity
Too difficult to start from scratch for every upgrade/change
  Components are more expensive
  Deployments is more difficult
The platform should be viewed as shared infrastructure!
  Amortize cost with multiple sensors and applications

## Slide 71
City-Scale Sensing Introduction
Signpost
  Motivation
  Shared Resources
  Deployability
  Implementation
  Evaluation

## Slide 72: How much power does a Signpost harvest?
Higher daily variations than directional variations
Notes: Bigger text ,fix font
Write takeaways on the slide

## Slide 73: How much power can each module draw?
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 74: How much power can each module draw?
Seattle 95th Percentile = 3 mW
San Diego 95th Percentile = 162 mW
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 75: How much power can each module draw?
Notes: Make sure to say it only gets better with scaling - better look
takeaway

## Slide 76: Resources are charged to modules which use them
Notes: Fix font

## Slide 77: Applications running on Signpost
Environmental monitoring (posting to Weather Underground)
Vehicle counting (and bell tower)
TV whitespace sensing
Notes: Fix font, callout on diurnal power patter/concert

## Slide 78: Outline
What does research look like:
  Research Overview
  Example: Powerblade
Sensing Systems Research
  Various Projects
  Signpost