## Slide 1: Lecture 04 Input and Output
CE346 – Microprocessor System Design
Branden Ghena – Fall 2023
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Lab on Friday!
  Ford room 3210
  See you all there!!
  Show up on-time. We are going to get started right away
    None of this 5-10 minutes late nonsense
Remember that you need to attend the section you registered for in CAESAR
  If you need to switch for a day, ask Branden for permission in advance on Piazza

## Slide 3: Quiz coming soon
First quiz is next week Tuesday! (10/03)
  15-minute quiz, taken in-class on paper
  Last fifteen minutes of class
  Bring a pencil
  No notes, no calculator
Covers material from the last two weeks, including today
Goals:
  Don’t be worried about the quiz. It won’t be that tough
  Do review class material and make sure you actually understand it

## Slide 4: Today’s Goals
How does a microcontroller interact with peripherals to perform input and output operations?
Explore reliable use of Memory-Mapped I/O
Learn about our first peripherals: Temperature and GPIO
Explore General Purpose I/O (GPIO) peripheral use
  Understand how it works
  Understand what kinds of configurations it might have

## Slide 5: Outline
I/O Motivation
Memory-Mapped I/O
Controlling digital signals
  GPIO
  GPIOTE

## Slide 6: Devices are the point of computers
Traditional systems need to receive input from users and output responses
  Keyboard/mouse
  Disk
  Network
  Graphics
  Audio
  Various USB devices
Embedded systems have the same requirement, just more types of IO
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 7: Devices are core to useful general-purpose computing
Computer
Mouse
Keyboard
Ethernet
Bluetooth
Monitor
Headphones
Ethernet
Bluetooth
Input
Output

## Slide 8: Devices are essential to cyber-physical systems too
Computer
Lidar
Inertial Measurement Unit
Camera
CAN
Throttle Control
Brake Control
Wheel Rotation
CAN
Input
Output

## Slide 9: Device access rates vary by many orders of magnitude
Rates in bit/sec
System must be able to handle each of these
  Sometimes needs low overhead
  Sometimes needs to not wait around
Device | Behavior | Partner | Data Rate (Kb/s)
Keyboard | Input | Human | 0.2
Mouse | Input | Human | 0.4
Microphone | Output | Human | 700.0
Bluetooth | Input or Output | Machine | 20,000.0
Hard disk drive | Storage | Machine | 100,000.0
Wireless network | Input or Output | Machine | 300,000.0
Solid state drive | Storage | Machine | 500,000.0
Wired LAN network | Input or Output | Machine | 1,000,000.0
Graphics display | Output | Human | 3,000,000.0

## Slide 10: Outline
I/O Motivation
Memory-Mapped I/O
Controlling digital signals
  GPIO
  GPIOTE

## Slide 11: How does a computer talk with peripherals?
A peripheral is a hardware unit within a microcontroller
  Sort of a “computer-within-the-computer”
  Performs some kind of action given input, generates output
We interact with a peripheral’s interface
  Called registers (actually are from EE perspective, but you can’t use them)
  Read/Write like they’re data
How do we read/write them?
  Options:
    Special assembly instructions
    Treat like normal memory

## Slide 12: Memory-mapped I/O (MMIO): treat devices like normal memory
Certain physical addresses do not actually go to memory
Instead they correspond to peripherals
  And any instruction that accesses memory can access them too!
Every microcontroller I’ve ever seen uses MMIO
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 13: Memory map on nRF52833
Flash 0x00000000
SRAM 0x20000000
APB peripherals 0x40000000
  Everything but GPIO
AHB peripherals 0x50000000
  Just GPIO
UICR – User Information Config
FICR – Factory Information Config

## Slide 14: Example nRF52 peripheral placement
0x1000 is plenty of space for each peripheral
  1024 registers, each 32 bits
  No reason to pack them tighter than that

## Slide 15: TEMP on nRF52833 example
Internal temperature sensor
  0.25° C resolution
  Range equivalent to microcontroller IC (-40° to 105° C)
  Various configurations for the temperature conversion (ignoring)

## Slide 16: MMIO addresses for TEMP
What addresses do we need? (ignore interrupts for now)
  0x4000C000 – TASKS_START
  0x4000C100 – EVENTS_DATARDY
  0x4000C508 - TEMP

## Slide 17: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;

## Slide 18: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;
  0x4000C000 is cast to a uint32_t*
  Then dereferenced
  And we write 1 to it
  “There are 32-bits of memory at 0x4000C000. Write a 1 there.”

## Slide 19: Example code
To the terminal!
Let’s write it from scratch

## Slide 20: Example code (temp_mmio app)

## Slide 21: Using structs to manage MMIO access
Writing simple C code and access peripherals is great!
Problems:
  Need to remember all these long addresses
  Need to make sure compiler doesn’t stop us!
Solution:
  Wrap entire access in a struct!
  Compilers turn it into the same thing in the end anyways

## Slide 22: C structs
Collection of variables placed together in memory
  typedef struct {
  uint32_t variable_one;
  uint32_t variable_two;
  uint32_t array[2];
  } example_struct_t;
Placement rules - Variables are placed adjacent to each other in memory except:
  Variables are always placed at a multiple of their size
  Padding added to the end to make the total size a multiple of the biggest member
  Microcontrollers can usually ignore these: all registers are the same size!

## Slide 23: Temperature peripheral MMIO struct
  typedef struct {
  } temp_regs_t;

## Slide 24: Temperature peripheral MMIO struct
typedef struct {
uint32_t TASKS_START;
uint32_t TASKS_STOP;
uint32_t _unused_A[62];
uint32_t EVENTS_DATARDY;
uint32_t _unused_B[0x204/4 - 1];
uint32_t INTENSET;
uint32_t INTENCLR;
uint32_t _unused_C[(0x508 – 0x308)/4 – 1];
uint32_t TEMP;
} temp_regs_t;
volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);
With increasingly verbose ways to write the size of the “unused” space (any of these will do, but don’t forget the -1)

## Slide 25: Temperature peripheral MMIO struct
typedef struct {
uint32_t TASKS_START;
uint32_t TASKS_STOP;
uint32_t _unused_A[62];
uint32_t EVENTS_DATARDY;
uint32_t _unused_B[0x204/4 - 1];
uint32_t INTENSET;
uint32_t INTENCLR;
uint32_t _unused_C[(0x508 – 0x308)/4 – 1];
uint32_t TEMP;
} temp_regs_t;
volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);
// code to access
TEMP_REGS->TASKS_START = 1;
while (TEMP_REGS->EVENTS_DATARDY == 0);
float temperature = ((float)TEMP_REGS->TEMP)/4.0;

## Slide 26: Break + relevant xkcd
https://xkcd.com/138/

## Slide 27: Outline
I/O Motivation
Memory-Mapped I/O
Controlling digital signals
  GPIO
  GPIOTE

## Slide 28: Digital signals
Simplest form of I/O
Exist in two states:
  High (a.k.a. Set, a.k.a. 1)
  Low (a.k.a. Clear, a.k.a. 0)
Simpler to interact with
  Constrained to two voltages
  With quick transitions between the two
  No math for voltage level
    Either high or low

## Slide 29: Digital signals map to voltage ranges
Upper range is high signal
  ~0.7*VDD
Bottom range is low signal
  ~0.3*VDD
Middle is undefined
  Only exists during transitions
http://www.sharetechnote.com/html/Electronics_CMOS.html

## Slide 30: General Purpose Input/Output (GPIO)
Read/write from/to external pins on the microcontroller
  Two possible values: high (1) or low (0)
Basic unit of operation for microcontrollers
  Allows them to interact with buttons and LEDs
  Every microcontroller has GPIO

## Slide 31: GPIO on nRF52833

## Slide 32: GPIO on nRF52833
Abstract model of the pin.
This isn’t really how the hardware is implemented. But it’s a reasonable model for users.

## Slide 33: GPIO on nRF52833
Inputs and outputs to/from the peripheral.
GPIO could be controlled by other peripherals. Controlling a pin in use by other peripherals is bad.

## Slide 34: GPIO on nRF52833
Registers within the GPIO peripheral. Configure various things about setup.

## Slide 35: GPIO on nRF52833
Peripheral contents are duplicated for each output pin.
Each pin has its own registers (or portions thereof).

## Slide 36: Multiple ports
nRF52833 has up to 42 I/O pins
  But only 32 can fit in a single 32-bit word
  Splits them into two “ports”
Pins are named based on port
  P0.14 – Button A, P0.23 – Button B
  P1.04 – LED column 4

## Slide 37: GPIO on nRF52833
External pin on the microcontroller

## Slide 38: GPIO on nRF52833
Output chain. Signal comes from OUT register, through output buffer, to external pin.

## Slide 39: GPIO Output
Outputs a high or low signal
Output configurations
  High drive output (either for high, low, or both)
    Sources or sinks additional current
      For powering external devices
    Normal drive: ~2 mA
    High drive: ~10 mA
  Disconnect (a.k.a. High Impedance or High-Z)
    Wired-OR or Wired-AND scenarios (we’ll talk about these later in class)

## Slide 40: GPIO on nRF52833
Input chain. Signal goes from pin, through input buffer, to IN register.

## Slide 41: GPIO Input
Reads in a signal as either high or low
Input Configurations
  Input buffer connect/disconnect
    Allows the pin to be disabled if not being read from
  Pull
    Disabled, Pulldown, Pullup (we’ll discuss in a future lecture)
    Connects an internal pull up/down resistor (~13 kΩ)
    Sets default value of input

## Slide 42: Electrical specifications
High voltage range: 0.7*VDD to VDD (~2.3 volts)
Low voltage range: Ground to 0.3*VDD (~1 volt)
GPIO are extremely fast
  Transition time is <25 ns
  Connected directly to memory bus for faster interactions
  This allows complicated signal patterns to be replicated in software
    If they aren’t implemented as a hardware peripheral
    Known as “bit-banging”

## Slide 43: Pin configuration
DIR register controls direction (input or output) for each pin
  Each bit 0-31 corresponds to pin 0-31
  Reset value: 0x00000000 -> all pins are inputs by default

## Slide 44: Controlling output level
OUT register controls whether each pin is high or low
  Only meaningful if the pin is configured as an Output
  Again, each bit is a single pin and reset is 0x00000000 (all pins low)

## Slide 45: Set/Clear registers
OUT works traditionally: write a 1 for high, 0 for low
OUTSET write a 1 to set that pin (high) zero has no effect
OUTCLR write a 1 to clear that pin (low) zero has no effect
  Lets you modify a pin without modifying the others (or reading first)

## Slide 46: Complex configuration
If you want to change other pin configurations, you do so per pin with the PIN_CNF[n] registers
  There are 32 of them, one per pin
Various fields correspond to different groups of bits
  Direction, Input buffer, Pullup/down, Drive strength, Sensing mechanism
Bits not part of a field should be ignored

## Slide 47: Writing to arbitrary bits
Remember that you can’t just write to arbitrary bits
  You’ll have to use bit-operations to do so
  In C: &, |, ~, ^, <<, >>
For a review of “bit masking” operations, see bonus slides

## Slide 48: Outline
I/O Motivation
Memory-Mapped I/O
Controlling digital signals
  GPIO
  GPIOTE

## Slide 49: Handling interrupts from GPIO
Separate peripheral, GPIOTE (GPIO Task/Event)
  Manages up to 8 individual pins
    Can read inputs and trigger interrupts
    Can also connect outputs from events on other peripherals (PPI)
  Can trigger interrupts for a “Port event” as well
    Any pin in the Port can trigger the interrupt
    Software checks which pin(s) caused the event to occur
    Very low power operation (works with system clocks off)
Unclear why this is a separate peripheral
  Presumably too complicated/expensive to have 42 of them

## Slide 50: Configuring individual input interrupts
Pick an available GPIOTE channel (0-7)
Configure it
  Port and Pin number
  Task (output), Event (input), or Disabled
  Polarity for input events
    Low-to-high
    High-to-low
    Toggle (both directions)
Enable interrupts for channel in GPIOTE (and in NVIC!)
Clear event in interrupt handler
  Doesn’t happen automatically

## Slide 51: Sensing port events
Uses the “Detect” signal. Generated from pin Sense configuration

## Slide 52: Configuring port input interrupts
Configure the Sense for each pin
  High or Low
  Allows different pins to have different “active” states
Select detect mode
  Direct connection to pins
  Latched version (saved even if pin later changes back)
Enable interrupts for port in GPIOTE (and in NVIC!)
Clear event in interrupt handler and value in Latch register
  Doesn’t happen automatically

## Slide 53: Outline
I/O Motivation
Memory-Mapped I/O
Controlling digital signals
  GPIO
  GPIOTE

## Slide 54
Bonus: Bit Masking

## Slide 55: Bit Masking
How do you manipulate certain bits within a number?
Combines some of the ideas we’ve already learned
  ~, &, |, <<, >>
Steps
  Create a “bit mask” which is a pattern to choose certain bits
  Use & or | to combine it with your number
  Optional: Use >> to move the bits to the least significant position

## Slide 56: Bit mask values
Selecting bits, use the AND operation
  1 means to select that bit
  0 means to not select that bit
Writing bits
  Writing a one, use the OR operation
    1 means to write a one to that position
    0 is unchanged
  Writing a zero, use the AND operation
    0 means to write a zero to that position
    1 is unchanged
Select bottom four bits:
num & 0x0F
Set 6th bit to one:
num | (1 << 6)
num | (0b01000000)
Clear 6th bit to zero: num & (~(1 << 6))
num & (~(0b01000000))
num & (0b10111111)

## Slide 57: Example: swap nibbles in byte
Nibble - 4 bits (one hexit)
  Input: 0x4F -> Output 0xF4
  Method:
    1. Shift and select upper four bits
    2. Shift and select lower four bits
    3. Combine the two nibbles
    uint8_t lower = input >> 4;
    uint8_t upper = input << 4;
    uint8_t output = upper | lower; // combines two halves
What are the values of the new upper bits?
Unsigned -> Will be zero
Shifting implicitly zero’d out irrelevant bits. Otherwise we would have needed an & operation too.

## Slide 58: Example: selecting bits
Select bits 2 and 3 from a number
Input: 0b01100100
0b01100100
Mask: 0b00001100
0b01100100
& 0b00001100
0b00000100
Finally, shift right by two to get the values in the least significant position:
0b00000001
In C: result = (input & 0x0C) >> 2;