## Slide 1: Lecture 05 Prototyping & Digital Circuits
CE346 – Microprocessor System Design
Branden Ghena – Fall 2023
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Labs
  Debrief: How did that go?
  See schedule of Lab hours available on Canvas for checkoffs
    Due by end-of-day Thursday
    Postlab Questions are also available (normally due before next lab)
Office Hours
  Had to change location of the earlier Thursday Office Hours
  Added Wednesday 4-5pm hour with me
Quiz
  Today at end of class!
  Someone remind me at ~4:30 if I don’t stop

## Slide 3: Project Proposals
It is time to start forming teams and working on Proposals
  Due next week Thursday! (10/12)
  Project details are posted to Piazza
  Specific proposal details are on Canvas
    1-2 pages, with some specific items you MUST include
Project teams are 2-3 students (4 under rare occasions)
  You may NOT work alone
  There is a partnership survey if you want us to match you with someone
    Due by end-of-day Sunday

## Slide 4: Today’s Goals
Explore another peripheral interaction pattern: DMA
Understand the basics of digital circuitry
  Enough to be able to interact with the Microbit
Discuss prototyping methods and basic circuits components

## Slide 5: Outline
DMA
Digital Circuits
Prototyping
Components

## Slide 6: Reminder: Polling I/O
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
This is the “polling” model of I/O.
“Poll” the peripheral in software repeatedly to see if it’s ready yet.

## Slide 7: Reminder: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code
Continue original code

## Slide 8: Direct Memory Access (DMA)
Even with interrupts, providing data to the peripheral is time consuming for transferring lots of data
  Need to be interrupted every byte, to copy the next byte over
DMA is an alternative method that uses hardware to do the memory transfers for the processor
  Software writes address of the data and the size to the peripheral
  Peripheral reads data directly from memory
  Processor can go do other things while read/write is occurring

## Slide 9: General-purpose DMA

## Slide 10: Full peripheral interaction pattern
Configure the peripheral
Enable peripheral interrupts
Set up peripheral DMA transfer
Start peripheral
Continue on to other code
Interrupt occurs, signaling DMA transfer complete
Set up next DMA transfer
Continue on to other code, and repeat

## Slide 11: Special-purpose DMA
nRF52 uses “EasyDMA”, which is built into individual peripherals
  Only capable of transferring data in/out of that peripheral
  Easier to set up and use in practice
  Only available on some peripherals though (no DMA for TEMP)
Warning: addresses for DMA buffer MUST be in RAM!

## Slide 12: Break + Open Question
What kinds of peripherals/devices should you use the DMA for?

## Slide 13: Break + Open Question
What kinds of peripherals/devices should you use the DMA for?
  Anything where there is a lot of data coming in over a period of time
    Either a big buffer of lots of data, like a radio message
    Or a bunch of individual samples, coming in quickly
  Devices
    Messages to/from other devices (radios, wired busses)
    Sensor readings (if read quickly)
    Canonical example from general computing: disks (HDD/SSD)

## Slide 14: Outline
DMA
Digital Circuits
Prototyping
Components

## Slide 15: Digital signals
Exist in two states:
  High (a.k.a. Set, a.k.a. 1)
  Low (a.k.a. Clear, a.k.a. 0)
Simpler to interact with
  Constrained to two voltages
  With quick transitions between the two
  No math for voltage level
    Either high or low

## Slide 16: Digital signals map to voltage ranges
Upper range is high signal
  ~0.7*VDD
Bottom range is low signal
  ~0.3*VDD
Middle is undefined
  Only exists during transitions
http://www.sharetechnote.com/html/Electronics_CMOS.html

## Slide 17: Digital circuits
Connecting components together with digital signals
  Mostly ICs
  Also buttons/switches and LEDs
Way simpler than analog circuits
  Mostly connecting boxes with wires
  Plus a few resistors here and there
An abstraction
  Not sufficient for fully understanding electronics behavior, but close

## Slide 18: Switches
Single Pole, Double Throw switch
  Middle pin (Pole) connects to one of two outer pins (Throws)
For controlling microcontrollers
  Often connect outer pins to VCC and Ground respectively
  Input then goes High or Low depending on switch state
https://learn.sparkfun.com/tutorials/button-and-switch-basics/

## Slide 19: Buttons
Single Pole, Single Throw switch
  Pole pin either connects to Throw pin or is disconnected
  Come in normally-closed (connected) and normally-open (disconnected)

## Slide 20: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?

## Slide 21: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?
  Floating! Could be any voltage
  Solution: need to connect weakly to either high or low voltage

## Slide 22: Current flows through the “path of least resistance”
Simplification
  Works well for the types of circuits we use
Pull-up resistor
  When button is open (disconnected), the only path is through the resistor
  When button is closed (connected) the least resistance path is through the button to Ground

## Slide 23: Pull-up resistors and pull-down resistors
Resistor sets the “default” value of a wire
  Pull-up connects to VCC
  Pull-down connects to Ground
  Usually 10-100 kΩ
When button is open (disconnected)
  Connection through the resistor sets signal
When button is closed (connected)
  Signal is directly connected to a voltage source
  Much lower resistance means that signal dominates

## Slide 24: Buttons on the Microbit
Normally open buttons
  Disconnected by default
Active low signal
  Activating (pushing) button creates a low signal
Pull-up resistors
  Set button signal high by default

## Slide 25: LEDs
Light Emitting Diodes
  Generate light as current passes through them
  Various colors available
Diodes
  Only allow current to go through one way
  Not particularly relevant for LEDs
    Treat as a digital component
Connect anode to high voltage and cathode to ground
  Plus a resistor to limit the total amount of current
https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds

## Slide 26: Active state for LEDs
LEDs can be active high or active low depending on configuration
  Active high is how people assume they work
  Active low is often used instead
    GPIO pins can usually sink more current than they can source

## Slide 27: LEDs on the Microbit
Microphone LED
  Active high
Simple to use, just set the GPIO high to enable it
Ignore this other part for now

## Slide 28: LEDs on the Microbit
Use two GPIO pins to control each LED
  Row high as VDD
  Column low as Ground
Remember, connections only exist where there are dots

## Slide 29: Controlling the LED matrix
Cannot individually control all LEDs simultaneously
  Need to light one row at a time
  Iterate rows quickly to make them appear on all the time
We’ll have a lab on these later
  Combines GPIO and timers

## Slide 30: Break + Question
Should the spot in green have?
  Pull-up Resistor
  Pull-down Resistor
  Either
  Neither

## Slide 31: Break + Question
Should the spot in green have?
  Pull-up Resistor
  Pull-down Resistor (needs to pull input low by default)
  Either
  Neither

## Slide 32: Outline
DMA
Digital Circuits
Prototyping
Components

## Slide 33: Prototyping goals
Does this thing work at all?
  Particular IC
  Circuit layout
  Software design
  etc.
Sometimes before doing something more serious with it
  Design a PCB, Make a product, etc.
  Not uncommon that the prototype is as far as you’ll get

## Slide 34: Isolating tests
The goal when prototyping is to isolate the question at hand
Do consider
  New sensor/IC/component/whatever
Do not consider
  Power
  Interference
  Enclosure
  Stable microcontroller
  Soldering skills

## Slide 35: Buying Parts
Prototyping vendors
  Where you look for cool stuff to buy
  Sparkfun
  Adafruit
Electronics vendors
  Where you buy parts when you know what you need
  Digikey
  Mouser

## Slide 36: Prototyping methods
Breadboarding
  Plug and connect components as needed
  Build up arbitrarily complex designs from nothing
Development kits
  Pre-fabricated systems design for testing components
Small-scale test PCBs
  Design a PCB that demonstrates the thing you’re interested in
    Making a PCB is less hard than some might think (Eagle, Fritzing, etc.)
    $20-30 for small, low-speed PCBs from batch services like OSHPark

## Slide 37: Breadboards for prototyping
Reusable platform for temporary circuits
Plug in jumper wires and through-hold components

## Slide 38: How a breadboard works
Component leads and wires are inserted into holes in the breadboard
Half-rows of five holes are connected
Vertical columns are connected for power/ground
Holes to
insert wires

## Slide 39: Breadboard LED example
Uses button to control LED

## Slide 40: Breadboard guidelines
Long wires in large bird nests makes debugging very difficult
  Shorter, constrained wires are easier to understand
  In this class, we’ll only have large jumper wires though…
Use the minimum jumpers necessary, mostly use breadboard for connections
Better
Bad

## Slide 41: More permanent breadboards
Breadboards are also known as “Solderless Breadboards”
Protoboard allows configurable circuits
  Solder jumper wires between locations
  Solder adjacent pads to form connection
Usually not worth it (just make a PCB)
  Does solve core problem of breadboards: things getting unintentionally unplugged
  Might be useful for some projects!

## Slide 42: When to not use breadboards
Breadboards work great for digital circuits and simple analog!
High voltage/current are bad for breadboards
  Honestly, anything above 12 volts DC shouldn’t be in a breadboard
  Also avoid high-power applications above a few Watts
  Never put AC in a breadboard!
Sensitive analog circuits
  Particularly anything sensitive to capacitance may not work right
  Sets of metal holes with strips connecting them function as capacitors
Anything in long term use

## Slide 43: Outline
DMA
Digital Circuits
Prototyping
Components

## Slide 44: Prototyping with a breadboard
What kinds of things might you use with a breadboard?
Jumper wire
Microbit!
Resistors/Capacitors
LEDs
Buttons/Switches
Analog Sensors
Various other through-hole components
  Transistors, Op-Amps, other ICs
https://www.adafruit.com/product/2975

## Slide 45: Jumper wires
Connect two rows in the breadboard together
Recommendation:
  Peel off sets of 2-4 wires and keep them stuck together
  Often want to run multiple at once

## Slide 46: Microbit
Always connect LED matrix side up
Breaks out various pins from board
  Need to consult table to know which pins
  https://tech.microbit.org/hardware/schematic/
https://www.sparkfun.com/products/13989
https://learn.sparkfun.com/tutorials/microbit-breakout-board-hookup-guide

## Slide 47: Resistors
Surface Mount Resistors
Variable Resistors
(potentiometer)
Carbon Film Resistors
4 Bands

## Slide 48: Resistor color codes
Colored bands on resistors label the resistance value of the part
First and second bands are the digits
Third band is multiplier
Fourth band is tolerance
  Usually gold: +/- 5%

## Slide 49: Example: determine the resistor

## Slide 50: Example: determine the resistor
56 x 10 Ω = 560 Ω (5%)

## Slide 51: Potentiometers
Vary resistance between zero and some maximum
  1 kΩ, 10 kΩ, 100 kΩ common
Connect middle and an edge for just a changeable resistor
Middle terminal is a movable resistor divider
  Knob changes middle output if outer pins are VCC and Ground

## Slide 52: LEDs
Negative ( - ) lead
Schematic Symbol
Directional component: only allows current to flow one way
Shorter side is the negative one
  i.e. where current flows to
Larger metal component
inside of case or case flat spot is cathode or
negative (-) lead
Shorter wire is cathode or
negative (-) lead
Surface-mount LED

## Slide 53: RGB LED
Three different colors of LED in a single large diffuser
Short leads are negative ends
  One for each color
Long lead is common power
  Common anode
Combinations of LEDs give other colors
  Cyan, Yellow, Violet, White
https://cdn-shop.adafruit.com/datasheets/FLR-100WAS-RGB.pdf

## Slide 54: Sensors
Thermistor
Photoresistor
We’ll come back to these in a future lecture

## Slide 55: Outline
DMA
Digital Circuits
Prototyping
Components