## Slide 1: Lecture 02 Microcontrollers
CE346 – Microcontroller System Design
Branden Ghena – Fall 2025
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Class Updates
No “official” lab this Friday
Personal Software Setup will be posted tonight
  At some point
  Gotta finish updating it
Office hours should start sometime next week
  If you need help with the software setup, always feel free to reach out on Piazza!

## Slide 3: Today’s Goals
Explore microcontrollers
  How do they compare to computers?
  Purpose, capabilities, tradeoffs
Explore the microcontroller(s) on the Microbit
Describe history and state-of-the-art for microcontrollers

## Slide 4: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 5: What’s inside a computer?
Macbook Air (circa 2013, 2nd gen)
  Modern computers are mostly similar
  Intel Core i5 processor
  128 GB Flash storage
  4 GB DDR3 RAM
  1440x900 pixel display
Picked because there is a teardown I like of an embedded device from the same year
https://www.ifixit.com/Teardown/MacBook+Air+13-Inch+Mid+2013+Teardown/15042

## Slide 6: Unscrewing the bottom cover
Top half is the motherboard
  Holds and connects all the parts of the computer
Bottom half are battery packs

## Slide 7: Non-volatile long-term storage: SSD
The SSD is a module that connects through PCIe
In modern laptops the SSD is often soldered directly onto the motherboard

## Slide 8: Investigating the motherboard
Red (front, right)
  Intel core i5 processor
Red (bottom, left)
  Elpida LPDDR3 RAM, 4 GB
Other stuff are mostly radios, USB/Thunderbolt controllers, and power supply
Front
Back

## Slide 9: Generalizing computer design
Computers usually need
  Processor
  Memory (RAM)
  Storage (Flash/SSD)
  External communication
    USB, Thunderbolt, SATA, HDMI, WiFi
  Power management
    Maybe batteries and charging
  Something to connect it all: motherboard

## Slide 10: What’s inside a Fitbit?
Fitbit flex (circa 2013)
Features
  Counts your steps
  Reports via Bluetooth Low Energy
  Lights up some LEDs based on your goals
  Vibrates when its battery is low
https://www.ifixit.com/Teardown/Fitbit+Flex+Teardown/16050
Notes: Fitbit, Wearables, microcontrolles

## Slide 11: Fitbit teardown
Notes: Fitbit, Wearables, microcontrolles

## Slide 12: Fitbit circuit board front
Red (top)
  STMicro 32L151C6 Microcontroller
Blue (left)
  TI BQ24040 Battery Charger
Yellow (right)
  STMicro LIS2DH Accelerometer
Orange (bottom)
  Nordic nRF8001 Bluetooth Low Energy Radio
The back is uninteresting

## Slide 13: Fitbit as a computer
Computers usually need
  Processor
  Memory (RAM)
  Storage (Flash/SSD)
  External communication
    USB, Thunderbolt, SATA, HDMI, WiFi
  Power management
    Maybe batteries and charging
  Something to connect it all: motherboard
  Microcontroller
  Bluetooth radio
  Vibratory motor
  Battery and power management
  Circuit board

## Slide 14: Sidebar: you could make a Fitbit yourself
All those parts are commercially available, so you could make your own Fitbit if you wanted to
Make a circuit board
Buy those parts and solder them on
Write some embedded software
Make a plastic case
… build a big software backend for everything
You’ve got a Fitbit!

## Slide 15: Categories of computer chips
Microprocessor (MPU or Processor)
  CPU
  Most memory and peripherals are external
Microcontroller (MCU)
  CPU + Memory + Peripherals
  Peripherals: separate hardware units within chip
    Often I/O interfaces
  Essentially, a microcontroller is almost an entire computer within a single chip

## Slide 16: Break + Question
Why do laptops/desktops use external memory chips instead of building it into the processor (like a microcontroller)?

## Slide 17: Break + Question
Why do laptops/desktops use external memory chips instead of building it into the processor (like a microcontroller)?
  Flexibility
    If it’s built into the processor, you’re limited to whatever they picked
  Fabrication issues
    DRAM and CMOS gates are somewhat different manufacturing processes (affects yield and costs)
    DRAM takes up a lot of space (multiple chips for many GBs of RAM)
  Some systems are doing this
    Apple M4 includes separate RAM silicon dies in the same processor package

## Slide 18: Modern Chips
System on a Chip (SoC)
  Processor with extensive peripherals
  Example: Radios or ML Accelerators
  Essentially multiple chips combined into one
Evolution of increased complexity over time
  Basically everything is an SoC these days
  What we call Microcontrollers are still mostly self-contained and targeted and simpler, cheaper devices
  What we call Microprocessors are more expensive, more performant, and usually require external memory

## Slide 19: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 20: Generic microcontroller block diagram
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 21: Processor
Microcontroller needs to execute software instructions
Probably just one single-core processor
  Newest chips might have multiple (we’ll come back to that)
  Often a fairly basic processor like you’d learn in CE361 (Comp Arch)
  Usually running a 1-100 MHz clock speeds
    Compare to 3000-5000 MHz for modern desktop processors
A point of consideration for microcontroller processors is what architecture they are

## Slide 22: Background: Instruction Set Architecture
ISA defines the actual instructions as well as the model for how the computer interacts with memory
  ISA also includes the native word size (8, 16, 32, or 64-bit)
    Defines size of registers and pointers
    Also defines the limit of memory available to a system
Does the ISA for a microcontroller matter if you’re not programming in assembly? (and I promise we won’t)

## Slide 23: Background: Instruction Set Architecture
ISA defines the actual instructions as well as the model for how the computer interacts with memory
  ISA also includes the native word size (8, 16, 32, or 64-bit)
    Defines size of registers and pointers
    Also defines the limit of memory available to a system
Does the ISA for a microcontroller matter if you’re not programming in assembly? (and I promise we won’t)
  Yes
  Differences in instruction efficiency and amount are important
  Differences in compiler support are VERY important

## Slide 24: ARM and RISC-V are common microcontroller architectures
Common architectures
  ARM (usually 32-bit) – also used in all smartphones, new Apple hardware
  RISC-V (32-bit) – newer, free, open-source architecture
Previously common
  Various custom architectures created by companies
    8-bit or 16-bit on older systems
  Still found in some microcontrollers
    Original ESP32 used a 32-bit Xtensa architecture
    New ESP32s mostly use a 32-bit RISC-V architecture

## Slide 25: Other processor choices
Some operations may or may not be supported depending on the processor
  Multiplication/Division
  Floating-point
  Atomic operations
  Vector / DSP operations

## Slide 26: ARM Cortex M Series
ARM processors commonly used in microcontrollers
A number of options for increasing capabilities
In practice:
  Cortex-M0+ for low-end systems
  Cortex-M7 for high capability systems
  Cortex-M23 and M33 are newer replacements for those
Arm Core | Cortex | Cortex | Cortex | Cortex | Cortex | Cortex | Cortex
 | M0 | M0+ | M3 | M4 | M7 | M23 | M33
ARM architecture | ARMv6-M | ARMv6-M | ARMv7-M | ARMv7E-M | ARMv7E-M | ARMv8-M | ARMv8-M
Computer architecture | Von | Von | Harvard | Harvard | Harvard | Von | Harvard
 | Neumann | Neumann |  |  |  | Neumann | 
Instruction pipeline | 3 stages | 2 stages | 3 stages | 3 stages | 6 stages | 2 stages | 3 stages
Multiply instructions | Yes | Yes | Yes | Yes | Yes | Yes | Yes
32×32 = 32-bit result |  |  |  |  |  |  | 
Multiply instructions | No | No | Yes | Yes | Yes | No | Yes
32×32 = 64-bit result |  |  |  |  |  |  | 
Divide instructions | No | No | Yes | Yes | Yes | Yes | Yes
32/32 = 32-bit quotient |  |  |  |  |  |  | 
Saturated math instructions | No | No | Some | Yes | Yes | No | Yes
DSP instructions | No | No | No | Yes | Yes | No | Optional
Single-Precision (SP) | No | No | No | Optional | Optional | No | Optional
floating-point instructions |  |  |  |  |  |  | 
Double-Precision (DP) | No | No | No | No | Optional | No | No
floating-point instructions |  |  |  |  |  |  | 
https://en.wikipedia.org/wiki/ARM_Cortex-M

## Slide 27: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 28: Generic microcontroller block diagram
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 29: Multiple types of memory are needed
Systems often have two types of memory
  Volatile memory
    Cheap and fast
    Loses values without power
  Non-volatile memory
    Keeps values without power
    Slower to access and modify
On normal computers, these are RAM and Disk
  Usually DRAM and Flash SSDs

## Slide 30: Volatile memory: SRAM
Same design as registers in traditional computer systems
  No need to refresh it -> lower energy costs
Embedded systems use SRAM for all of their memory (no DRAM)
Tradeoffs:
  Way less energy cost
  Faster to access
  More expensive and physically larger
    So we have less of it in total

## Slide 31: Non-Volatile memory: Flash (usually)
Same design as SSDs and Flash drives
Memory is stored with no energy costs
  Reading is lowish energy and quick
  Writing is high energy and very slow
    Writing also has to occur in blocks (e.g. 512 bytes)
Concern: Flash has a limited lifetime ~10,000 writes
  Only writing to Flash when you load code? Essentially forever
  Recording data to Flash every second? 2.8 hours
  Result: most embedded systems don’t modify their own Flash memory

## Slide 32: SRAM (RAM) versus Flash (ROM) memory
Size and time difference between non-volatile and volatile memory is significantly reduced from traditional computing
  Non-volatile store 2-10x larger than volatile
  Single-cycle RAM. Maybe two-cycles to Flash (to read)
Major difference: energy and writability
  SRAM is low-energy to read and write (no refresh needed)
  Flash is lowish-energy to read, but very high energy to write
Use by software
  Stack/Heap/Data sections (variables) in SRAM
  Code goes in Flash (also const variables)

## Slide 33: Memory design choices
How much memory can we fit without making the microcontroller too high cost or too high power?
  The answer has slowly increased over time
  20 years ago: 2 KB RAM – 32 KB Flash
  Today: 256 KB RAM – 1024 KB Flash
That’s enough memory that you usually don’t need to think about it
  But not enough memory to never think about it

## Slide 34: Differences from memory in standard computers
How to provide memory safety?
  Usually no virtual memory (all addresses are real addresses)
  Nothing stops arbitrary memory overwriting
  Modern systems: Memory Protection Unit
    Specify a small number of ranges and permissions
Hierarchical structure is not enforced
  Same address space for RAM and Flash (very different from traditional)
  Run instructions right inside of Flash
  Keep variables in RAM (or const variables in Flash)

## Slide 35: What about caches?
Often no caches
Caches are about improving performance
  But embedded systems are not often performance-constrained
  AND caches can make timing unreliable
They exist in some high-end microcontrollers
  Often instruction caches only
  Often disabled by default

## Slide 36: Break + Open Question
How little memory (RAM and/or ROM) can a computer have and still be useful?

## Slide 37: Break + Open Question
How little memory (RAM and/or ROM) can a computer have and still be useful?
  If we want to run C code, we need a stack and a global data section
  Function calls may require local variables to be placed in the stack
  To use less memory, we’d need to write applications in registers
  Most variables could probably fit in registers?
  So the limit could get very low
    Enough ROM space for some useful code + a tiny bit of RAM

## Slide 38: Fall 2025: least memory
How little memory might a microcontroller have?
PIC10F200
  384 Bytes of ROM,
  16 Bytes of RAM
  Still actively produced and for sale on Digikey
    $0.58 a piece

## Slide 39: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 40: Generic microcontroller block diagram
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 41: Peripherals
Hardware modules that perform some action
  Specifically, modules within the microcontroller chip
  NOT a separate chip, sensor, or inpu
Examples
  Random Number Generator (RNG)
    Processor can request a random number
    The RNG peripheral does some kind of actions to generate one
    The RNG provides the random number to the processor

## Slide 42: What kinds of peripherals exist?
External connections
  Used by processor to interact with outside world
  Examples
    Read from buttons and switches
    Turn on/off LEDs
    Measure a voltage
    Connect to external sensors chips
Internal systems
  Used by processor to speedup or provide some action it’s not capable of
  Examples:
    Request random numbers
    Encrypt or decrypt some information
    Check the current time

## Slide 43: What do microcontrollers usually have?
Common examples
  Digital inputs and outputs
  Analog inputs and outputs
  Messages over various communication protocols: UART, I2C, SPI
  Set and check timers
Less common (but not rare) examples
  Cryptography accelerators
  Complicated wire protocols (USB, CAN)
  Wireless radios (BLE, 802.15.4, WiFi)
We’ll spend most of class learning various peripherals

## Slide 44: Peripheral design choices
More peripherals mean more capabilities
  But also means more cost for the chip
  Peripherals occupy silicon
  Most peripherals will go unused for a given application…
Flexibility tradeoffs within a given peripheral
  One capability is easier to use
  Many capabilities are more useful
Apple A8 SoC

## Slide 45: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other Stuff
Microbit microcontroller
Microcontroller History

## Slide 46: Generic microcontroller block diagram
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 47: Pins
Peripherals need to electrically connect to outside world
  Attach to pins on the exterior of the chip
More pins allow for more connections
  At increased cost and size
Pin layouts can add more pins for cheaper
  But make soldering and debugging difficult

## Slide 48: Internal connections to pins
Peripherals need to be connected to external pins
  Can any peripheral connect to any pin, or are there limited mappings?
  Modern microcontrollers allow any-to-any connections
Older MCUs had mapping tables and pin selection was more challenging

## Slide 49: What haven’t we talked about?
Power
Programming
Others?
  Clocks
  Antennas
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 50: Powering microcontrollers
Usually require a specific voltage
  E.g. 5 volts, 3.3 volts, 1.8 volts
  Must be stable and supply enough current (or MCU “browns out”)
  Noisy power supply can be an issue
Some microcontrollers have wider ranges of acceptable voltages
  Need to pay attention to acceptable range on I/O though

## Slide 51: Programming microcontrollers
JTAG (Joint Test Action Group)
  Hardware built into the microcontroller for testing purposes
  Can arbitrarily read/write memory
  Can single step process too, at runtime!
    GDB can connect to it! (sort of)
Bootloaders
  Software runs on the microcontroller at boot that waits a short time for someone to contact it and upload code
    Via I/O pins
  Convenient, but sometimes unreliable

## Slide 52: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 53: Micro:bit v2
Circuit board
  Entire thing
  a.k.a “Dev Board”
  a.k.a PCB (Printed Circuit Board)
Microcontroller
  The computer on it
  Microbit has two
    One as a programmer for the nRF (USB->JTAG)
    One for applications that we will use
Microcontrollers

## Slide 54: nRF52833 – Microcontroller on the Micro:bit v2
Processor: 32-bit ARM Cortex-M4F
  32-bit registers and pointers, Floating-point support
  64 MHz clock frequency
Memory:
  128 KB SRAM
  512 KB Flash
Peripherals:
  Various peripherals
    ADC, PWM
    I2C, UART, SPI, USB
    RNG, 32-bit Timers, Watchdog, Temperature
    2.4 GHz Radio: Bluetooth Low energy / 802.15.4
Pins:
  73 total pins, up to 42 I/O pins that can connect to peripherals

## Slide 55: Pins on the nRF52833
73 individual pins
  Plus a big ground pad
Some are used for special purposes
  Power (16)
  External Oscillator (2)
  Debugging (2)
  RF Antenna (1)
  USB (2)
  Not connected at all (8)
Remaining 42 pins can be used as General Purpose I/O (GPIO)
  Digital I/O
  Or connected to other peripherals
Pins

## Slide 56: Accessing nRF52833 pins in software
Pins are collected into “Ports”
  Each Port has 32 pins
42 total GPIO pins
  Port 0 – pins 0-31
  Port 1 – pins 0-9
Referred to as P[port].[pin]
  For example: P0.20, P1.08, P0.00

## Slide 57: Pins on the Microbit
The Microbit uses the nRF52833, and then connects individual pins from the Microcontroller to certain parts of the board
  Every board does this
  The only way to know this connections is to look at the documentation
For example:
  BTN_A connects to P0.14
  BTN_B connects to P0.23

## Slide 58: In our software library
Header file gives names to each pin based on how the Microbit uses it
  https://github.com/nu-ce346/nu-microbit-base/blob/main/software/boards/microbit_v2/microbit_v2.h
You can use these names directly in your code where you need the pin number

## Slide 59: To the datasheet!
nRF52833 Product Specification
  Online: https://docs.nordicsemi.com/bundle/ps_nrf52833/page/keyfeatures_html5.html
  PDF: https://docs-be.nordicsemi.com/bundle/ps_nrf52833/attach/nRF52833_PS_v1.7.pdf

## Slide 60: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History

## Slide 61: Older microcontrollers (90s-00s)
Focus: cheap, small computer systems
PIC
  8, 16, and 24-bit MIPs architecture
  PICAXE available with Basic interpreter
AVR
  8-bit custom architecture (AVR architecture)
  Used in Arduinos
  AT Tiny 4: $0.30 per unit
    4 I/O pins, 32 Bytes RAM, 512 Bytes ROM

## Slide 62: More capable microcontrollers (00s-10s)
Focus: diversify into extreme low power and more capable systems
MSP430
  16-bit custom architecture (MSP430 architecture)
  Capable, but also extremely low power
    <1 μA sleep current
STM32, Atmel SAM series (Cortex-M0, M3, M4, M4F)
  32-bit ARM architecture (ARMv7)
    Leverage success of ARM on smartphones
  Every peripheral under the sun. Plus a variety of memory choices

## Slide 63: Modern system-on-chips (10s-20s?)
Focus: increase memory and capability
  Include radios in the same chip
nRF51 and nRF52 series
  32-bit ARM microcontrollers (Cortex M)
  Include 2.4 GHz radio: Bluetooth Low Energy and 802.15.4/Thread
Others have followed this same path
  TI CC26XX
  Apollo3
  STM32WL

## Slide 64: Future microcontrollers (20s and beyond)
Multi-core systems
  Not for performance, but for separation of concerns
    Run radio code on one core
    Application code goes on the other core
  Also allows BIG.little architecture
    Higher performance core when interpreting data
    Lower performance core for sampling sensors
  nRF54 series really emphasizes this
    Multiple BIG ARM processors and little RISC-V processors

## Slide 65: Popular components rarely die
Majority of popular older options still exist
  Designers can trade off cost, capability, and efficiency alongside “modern features”
Upgrading for an existing product is unlikely
  Large cost, little benefit
Example: Arduino still primarily uses AVR
  Works just fine for its needs
  Also releases new boards with nRF52s (Arduino Nano 33 BLE)

## Slide 66: Fall 2025: cheapest microcontroller
PIC16F15213
  16-bit custom architecture running at 32 MHz
  256 KB of RAM
  3.5 KB of Flash
  8 pins (5 for I/O)
  $0.38 per microcontroller
    Still an “active” chip being manufactured
Can get significantly cheaper prices buying at scale

## Slide 67: Outline
Microcontrollers and Computers
Microcontroller Components
  Processor
  Memory
  Peripherals
  Pins & Other stuff
Microbit microcontroller
Microcontroller History