## Slide 1: Lecture 10 Analog Output
CE346 – Microprocessor System Design
Branden Ghena – Fall 2025
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Design presentations all next week!
  Happy to discuss things before then via Piazza
  I am providing groups with feedback as I have time to
    Sent a couple of emails already (most are just thoughts, no major concerns)
  Let me know if there’s a particular day you can’t present on
Drop deadline is Friday next week
  I’m not worried about anyone in CE346
  But if you’re worried, I’m happy to talk about it.

## Slide 3: Today’s Goals
Explore common methods for generating analog signals
Understand the role of Digital-to-Analog converters
Discuss the concepts of Pulse-Width Modulation
  And the nRF52 implementation of it
Work through examples of how to use PWM

## Slide 4: Outline
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM
Using PWM

## Slide 5: Digital-to-Analog Converters
Generates an analog voltage
DACs are conceptually the inverse of ADCs
  Number of bits of resolution choose analog step size
  Frequency determines step duration

## Slide 6: High resolution versus high frequency
What role does each play in a DAC? Which is more important?
High resolution can accurately represent a voltage
High frequency can accurately represent a changing voltage
In practice:
  Need high enough resolution, then as high of frequency as possible

## Slide 7: Infinite resolution is not sufficient
DAC frequency corresponds to representable signal changes
  Rise and fall times
Even an infinite resolution DAC cannot represent a signal if it is not fast enough

## Slide 8: Low-pass filter smooths output
Low-pass filter delays changes in voltage and smoothly transitions between them
  Low-frequency signals stay
  High-frequency are smoothed
Greatly improves quality of output but must be tuned to the desired signal frequency
  Usually not included in microcontroller

## Slide 9: Resistor string DAC
Use series of voltage dividers and switches to set output voltage
  Generates equally spaced voltages that can be selected between
Needs output buffer to provide stable current
Takes a lot of resistors
  And resistors take a lot of silicon

## Slide 10: Resistor string example
Input code is 101
  Selects switches such that 5/8*Vref is connected to output

## Slide 11: Break + DAC applications
What do you use an analog output for?

## Slide 12: Break + DAC applications
What do you use an analog output for?
  Audio output
    But it needs to be high quality (resolution and speed)
  Motors
    But only with a controller that actually drives them with enough current
  LED brightness
  Not Much
    And these last two can be done more easily with PWM

## Slide 13: DACs are not in all microcontrollers
Not rare, but not ubiquitous either
  Every microcontroller has GPIO
  Just about every microcontroller has an ADC
  Some microcontrollers have DACs (the nRF52833 does not!)
Reasons
  Hardware is complicated (but we could fit it if we wanted)
  Use cases are uncommon (and might need very high quality)
    Many devices can be controller digitally
  Pulse-Width Modulation (PWM) can emulate usably analog signals

## Slide 14: Outline
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM
Using PWM

## Slide 15: Pulse-Width Modulation
Much easier to control high or low than an analog output
Idea: modify how long a signal is high within some switching frequency, a.k.a duty cycle
  On 50% of the time for half voltage
  On 10% of the time for tenth voltage
Controls duty cycle, not frequency!

## Slide 16: PWM to Analog Signal example
PWM period should be much faster than the desired analog signal
  PWM duty cycle represents the voltage along the way
  Multiple duty cycles per output point makes it more accurate

## Slide 17: Low-pass approach works here too
Importantly, many devices are inherent low-pass filters
Heaters, Motors
  Low-pass by physical design
  I.e., they can’t start/stop quickly
LEDs are not
  But our eyes are!

## Slide 18: Controlling PWM
Vary duty cycle by selecting transition points
  Time when set
  Time when unset
Repeat every cycle
  Period much faster than signal if possible
  Makes analog approximation more accurate
    The faster you run it, the less likely it matters that it is not actually analog
    Example: LED switching frequency
Duty cycle could vary cycle-by-cycle if it must

## Slide 19: PWM alignment
Can select alignment as well
  Equivalent to a phase delay
Centering produces cleaner analog output
  Less harmonics
Not relevant for most devices

## Slide 20: Every microcontroller can do PWM
Not every microcontroller has a PWM peripheral
But every microcontroller has timers and digital outputs
All that is needed is a GPIO and a Timer (or two)
  Timer determines when to turn GPIO on and off
  Often can be automated in hardware rather than using an interrupt
    Connect timer expiration to GPIO toggling

## Slide 21: PWM is an example of encoding data on a signal
PWM is a pulse-width modulated signal
There are many other ways to “modulate” a signal to transmit data
  Amplitude, Frequency, and Phase are common
  Layers data on top of an existing “carrier signal”
Used especially for high-speed communication
  Wired (cable lines) or Wireless (basically everything)

## Slide 22: PWM applications
Servos
  Duty cycle chooses angle or rotation speed
Motor controllers
  Duty cycle chooses current and therefore speed
LED brightness
  And “breathing” effect
Audio
  Can sound okay if frequency is high enough

## Slide 23: Controlling LED Matrix brightness
Option 1: PWM peripheral
  Use a single PWM output to control the column
    When timer fires, change which column pin is used for PWM
    PWM frequency should be much faster than row change frequency
  Alternatively, use five PWM outputs to control rows for individual control
Option 2: do it manually (instead of PWM peripheral)
  Need to apply duty cycle on top of the existing stepping through rows
  Add 5 new one-shot app timers, one for each column
    Fire some percentage into the time the LED is active (within the 2 ms)
    Use to toggle individual column LED back to off
    Result: the LED is on for some portion of the time it should be active

## Slide 24: Break + Open Question
Imagine you want to represent the following signal with PWM
  What should the PWM period be?
  What kinds of duty cycle values would you use? (3.3v is 100%)

## Slide 25: Break + Open Question
Imagine you want to represent the following signal with PWM
  What should the PWM period be?
    Signal period is ~10 μs
    PWM period should be at least 2x that
      10x faster seems like a good start
      Then if we want multiple PWM outputs per sample, that’s ~20-40x faster
  What kinds of duty cycle values would you use? (3.3v is 100%)
    2/3.3 = 61% duty cycle max
    0/3.3 = 0% duty cycle min

## Slide 26: Outline
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM
Using PWM

## Slide 27: nRF52 PWM – theory of operation
A clock continuously adds to a counter value
  (just like the Timer peripheral does)
When the counter value reaches COMP[n], the GPIO value on channel n changes from high to low (or vice-versa)
When the counter value reaches COUNTERTOP, the GPIO value on channel n changes from low to high (or vice-versa)
  AND the counter value resets to zero

## Slide 28: nRF52 PWM peripheral
Uses internal timer to create PWM output on up to 4 pins
  4 peripheral instances, so up to 16 pins total
Loads compare values via DMA to rapidly vary “analog” signal

## Slide 29: PWM example
Counter increments up to COUNTERTOP, resets and continues
Period/Frequency
  Chosen by COUNTEROP and timer PRESCALER
Time
Counter Value
One PWM period

## Slide 30: PWM example
Counter increments up to COUNTERTOP, resets and continues
Duty Cycle
  COMP0 chooses first toggle point for OUT[0]
  Second toggle point is when the timer resets
Time
Counter Value
(right-aligned)
(left-aligned)
One PWM period

## Slide 31: Center-aligned PWM
Up-and-down mode enables center-aligned PWM
Duty Cycle
  Comp triggers toggle on rise
  Comp triggers toggle again on fall
)

## Slide 32: DMA with PWM
Every N periods it loads a new configuration from RAM
  N combined with PRESCALER and COUNTERTOP chooses “analog signal” period
Configuration sets COMP values for each output channel
  Also sets polarity (starting value: low or high)
Application of memory loads to channels is configurable

## Slide 33: Waveform mode
Also has the option to change COUNTERTOP every N PWM periods
Allows arbitrary waveforms to be created
  Frequency changes every period
  Duty cycle can also change each period
We don’t normally need this, as a constant frequency with changing duty cycle should be fine

## Slide 34: Other configurations
How many times the entire DMA sequence repeats
  0 to large number, infinite with a configuration in SHORTS
How long to delay between repeating sequence cycles
  Repeats last PWM configuration
Two DMA sequence configurations (0 and 1)
  Can modify one while the other is playing - “Double Buffering”
  Allows continuous signal (for example, music)

## Slide 35: Trading speed and accuracy
How do you get the most accurate PWM values?
  Select the largest COUNTERTOP possible
    Most possible COMP values
    Up to 15-bit resolution (32767 max)
How do you get the fastest PWM frequency?
  Select the smallest COUNTERTOP possible
  PRESCALER also affects this
    16 MHz – 128 kHz (8 possible values)
Fastest PRESCALER + largest COUNTERTOP equals 488 Hz
  Likely need to sacrifice resolution for speed
  Compare to audio output at 44.1 kHz

## Slide 36: Break + Question
Fastest PWM clock speed is 16 MHz (16000000 ticks per second)
What COUNTERTOP value gets you 44.1 kHz? (44100 PWM cycles per second)
  Hint: COUNTERTOP unit – Ticks
How many bits in resolution would the corresponding DAC have?
Time
Counter Value

## Slide 37: Break + Question
Fastest PWM clock speed is 16 MHz (16000000 ticks per second)
What COUNTERTOP value gets you 44.1 kHz? (44100 PWM cycles per second)
  Hint: COUNTERTOP unit – Ticks
  16 MHz / 44.1 kHz = 362.8
How many bits in resolution would the corresponding DAC have?
  log2(362) = 8.5
Time
Counter Value

## Slide 38: Outline
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM
Using PWM

## Slide 39: nRF SDK PWM driver
https://infocenter.nordicsemi.com/index.jsp?topic=%2Fsdk_nrf5_v16.0.0%2Fgroup__nrfx__pwm.html
Initialize PWM with base configuration
  Output pins, Clock frequency, COUNTERTOP, DMA grouping mode
  Handler for events from peripheral
nrfx_pwm_simple_playback(instance, sequence, count, flags)
  Instance: pointer to global variable with registers
  Sequence: struct containing sequence to be played (see next slide)
  Count: number of times (1 or more) to repeat sequence
  Flags: stop peripheral when done, loop forever, various events

## Slide 40: Sequence struct
values: pointer to array of uint16_t values (union of types)
length: length of array
repeats: number of times to repeat each individual value
  Sets period for “analog value” changing

## Slide 41: Example, playing a note with a square wave
Pick PWM frequency to match note frequency
  Combination of PRESCALER, COUNTERTOP, and repeats
  440 Hz for the note A
    PRESCALER 1 MHz, COUNTERTOP 2273 -> 440 Hz
Set duty cycle of PWM to control volume
  50% duty cycle -> COMP value of 1137
Set sequence with an array of length 1, content is {1137} (polarity 0)
  Repeats 0, end_delay 0
Set playback_count to 1 and flags to NRFX_PWM_FLAG_LOOP

## Slide 42: Playing sine waves instead of square waves
Sine waves sound different than square waves
  Sine is more smooth
  Square is more harsh and buzzy
For better sound quality, we can play sine waves via PWM

## Slide 43: Steps to playing a note with a sine wave
Determine sampling rate and set PRESCALAR and COUNTERTOP
Calculate sine wave values for some amount of duration
  Reasonable to calculate one second of data at a time
  sin() function might be too slow here
    Instead calculate sine values in advance and interpolate into an array based on frequency
Translate sine wave values into duty cycle values
  Fill an array with these duty cycle values
Play the array of duty cycle values
  That gets one second of audio
  For music, might change schedule a timer for when to stop current playback and play the next note instead

## Slide 44: Example: playing an arbitrary signal
Chart: Time (ms)
Series2 | 1.7364 | 2.6884 | 3.2438 | 3.1904 | 2.5487 | 1.5636 | 0.61162 | 0.056222 | 0.10959 | 0.75135
Goal: recreate this analog signal
Have to pick a “sampling rate” for representing the signal
The purple dots are sampled at 600 Hz (10 samples per wave)
  We’ll use the PWM to play those values

## Slide 45: Step 1: determine PRESCALAR and COUNTERTOP
PRESCALAR
  Let’s just set the PWM to maximum rate: 16 MHz
COUNTERTOP (you determine this)
  16,000,000 ticks per second / 600 cycles per second = 26,667 ticks per cycle
  Set COUNTERTOP to 26667
  If we wanted repeats, we’d further decrease this
    10 repeats -> COUNTERTOP = 2667

## Slide 46: Step 2: calculate signal values
Chart: Time (ms)
Series2 | 1.7364 | 2.6884 | 3.2438 | 3.1904 | 2.5487 | 1.5636 | 0.61162 | 0.056222 | 0.10959 | 0.75135
Voltage values calculated from the signal
  Need to convert to values relative to COUNTERTOP
Sample | Time (ms) | Value (Volts)
1 | 0.139 | 1.736
2 | 1.806 | 2.688
3 | 3.472 | 3.244
4 | 5.139 | 3.190
5 | 6.806 | 2.549
6 | 8.472 | 1.564
7 | 10.139 | 0.612
8 | 11.806 | 0.056
9 | 13.472 | 0.110
10 | 15.139 | 0.751

## Slide 47: Converting voltage to COMP values
Sample 0: (you determine this)
  Duty cycle:
  = 1.736 volts / 3.3 volts
  = 53%
  COMP = Duty cycle * COUNTERTOP:
  = 1.736 / 3.3 * 26667
  = 14031
Sample | Time (ms) | Value (Volts)
1 | 0.139 | 1.736
2 | 1.806 | 2.688
3 | 3.472 | 3.244
4 | 5.139 | 3.190
5 | 6.806 | 2.549
6 | 8.472 | 1.564
7 | 10.139 | 0.612
8 | 11.806 | 0.056
9 | 13.472 | 0.110
10 | 15.139 | 0.751

## Slide 48: Resulting COMP values
So sequence_data values will be: {14031, 21725, 26213, 25781, 20595, 12636, 4942, 454, 886, 6072}
Sample | Time (ms) | Value (Volts) | Value (Duty Cycle) | Value (COMP)
1 | 0.139 | 1.736 | 53% | 14031
2 | 1.806 | 2.688 | 81% | 21725
3 | 3.472 | 3.244 | 98% | 26213
4 | 5.139 | 3.190 | 97% | 25781
5 | 6.806 | 2.549 | 77% | 20595
6 | 8.472 | 1.564 | 47% | 12636
7 | 10.139 | 0.612 | 19% | 4942
8 | 11.806 | 0.056 | 2% | 454
9 | 13.472 | 0.110 | 3% | 886
10 | 15.139 | 0.751 | 23% | 6072
Chart: Time (ms)
Series2 | 1.7364 | 2.6884 | 3.2438 | 3.1904 | 2.5487 | 1.5636 | 0.61162 | 0.056222 | 0.10959 | 0.75135

## Slide 49: Resulting signal
Blue lines are the actual PWM signal we generate
Green lines are the averaged voltage output of the PWM
  Faster sampling rate would better represent the signal
Note: if exact start time of wave matters, need to start PWM a little early (half a sample)
Chart: Time (ms)
3 | 1.7364 | 1.7364 | 2.6884 | 2.6884 | 3.2438 | 3.2438 | 3.1904 | 3.1904 | 2.5487 | 2.5487 | 1.5636 | 1.5636 | 0.61162 | 0.61162 | 0.056222 | 0.056222 | 0.10959 | 0.10959 | 0.75135 | 0.75135
Chart: Time (ms)
| -0.69461111111111107 | 0.18250990841738279 | 0.18251090841738271 | 0.97205455555555564 | 0.97205555555555556 | 2.3300931014955948 | 2.3300941014955949 | 2.6387212222222223 | 2.6387222222222224 | 4.2773203984341608 | 4.2773213984341609 | 4.3053878888888892 | 4.3053888888888894 | 5.917027174374307 | 5.9170281743743072 | 5.9720545555555553 | 5.9720555555555555 | 7.2595111912405814 | 7.2595121912405807 | 7.6387212222222223 | 7.6387222222222215 | 8.4285992026937286 | 8.4286002026937279 | 9.3053878888888875 | 9.3053888888888867 | 9.6143493429488469 | 9.6143503429488462 | 10.972054555555555 | 10.972055555555555 | 11.000455379343617 | 11.000456379343616 | 12.638721222222221 | 12.638722222222221 | 12.694081936736804 | 12.694082936736804 | 14.305387888888889 | 14.305388888888888 | 15.18250990841738 | 15.182510908417381 | 15.971388888888889
 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0 | 3.3 | 3.3 | 0 | 0

## Slide 50: Outline
Digital-to-Analog Converters
Pulse-Width Modulation
nRF52 PWM
Using PWM