## Slide 1: Lecture 13 Other Protocols
CE346 – Microcontroller System Design
Branden Ghena – Fall 2025
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Final Project Details
A bunch of little posts on Piazza with details
  Some might apply to your project
  Details on grading that you might be interested in
  Link so you can make a private repo for your code
Two big notes
  You MUST cite work you use
  Don’t use Lab1 (MMIO GPIO) or Lab2 (Virtual Timers) in your final project

## Slide 3: Other final project stuff
I’ll be doing ordering roughly weekly at this point
Lab this Friday will be office hours instead!
  You are not required to attend
  But I’ll be there to answer project questions if you have any
  You’re welcome to just come and work too
Next week Friday will be project check-ins
  More details to come

## Slide 4: Today’s Goals
Discuss more advanced wired communication protocols
  With a little less detail
  Just give a taste of what they are like
Think a little about higher-layer concerns like data routing, interpretation, and reliability
Explore concept of bit-banging protocols that hardware doesn’t support

## Slide 5: Outline
USB
CAN
Bit-banging
  1-wire
  Neopixel LED strips
Video Protocols
  VGA
  HDMI

## Slide 6: USB references
USB in a NutShell
  https://www.beyondlogic.org/usbnutshell
Other stuff I found useful
  https://www.usbmadesimple.co.uk/
  http://kofa.mmto.arizona.edu/stm32all/blue_pill/usb/an57294.pdf
  https://en.wikipedia.org/wiki/USB

## Slide 7: Universal Serial Bus (USB)
Pervasive wired communication protocol
  Universal accurately applies!
  Targets predominantly external devices over a plug/cable
Good combination of simple and capable
  Base version for simple devices does not require too much in terms of pins or resources
  More complex versions can transfer a significant amount of data
    These grew organically over time though
Great support for interoperability
  Generic device profiles that allowed for plug-and-play
  Supported by OS initiatives to include driver software

## Slide 8: USB is a layered protocol
USB protocol describes how to:
  Electrically send bits
  Send frames of multiple bytes
  Communicate data between two devices
  Communicate specific application data (through device classes)
Much more complicated, compared to others
  SPI: only how to electrically send bits
  UART and I2C: how to send frames of bytes

## Slide 9: Roles and topology
Hosts and Devices
  USB On-The-Go allows host negotiation
    Added later. Supports devices like smartphones
Host is in charge of communication (“Upstream”)
Devices provide various capabilities Host can interact with (“Downstream”)
Tiered star topology
  Host connects to hubs, which connect to devices
  Up to 127 devices per hub. Up to 5 layers of hubs

## Slide 10: USB Outline
Low-layer details
  How are bits sent
  How are packets (collections of bits) sent
Higher-layer details
  How do we interact with devices
  How do we determine what devices are and how they work

## Slide 11: USB signals
Four signals
  Vbus (5 volts, can power devices)
  D+
  D-
  Ground
D+/D- are a differential pair
  Signals are inverses of each other
    Usually, occasionally act separately to signal special conditions
    Increases voltage difference between states (5 - -5 = 10 volts)
  Wires are twisted to avoid interference

## Slide 12: Synchronizing data
No clock signal!! How is USB so fast?
  Partially EE magics: better receivers, matched wire impedance
  Partially easier to distinguish signal states
  Also guaranteed transitions, which allow resynchronization
Transitions are used to denote data (non-return-to-zero inverted)
  With guaranteed transition in within every 8 bits (bit stuffing)
  Allows clocks on the two devices to synchronize

## Slide 13: USB speeds
USB 1.0
  Low Speed: 1.5 Mbps
    Not clear if this is used anymore
  Full Speed: 12 Mbps
    Microcontrollers tend to support Full Speed
    We’re focusing on details from it
USB 2.0
  High Speed: 480 Mbps
USB 3.0+
  Super Speed: 5-20 Gbps
  Adds multiple parallel data connections
Pull-up resistors allow for detection of a plugged device
Also identify speed

## Slide 14: USB interactions
General transaction format
  Host sends a Token packet: identifies transfer direction and device
  Host or Device send data depending on direction
  Other side acknowledges receipt of data
Like a maxed-out version of the I2C transaction pattern
  Host always initiates communication
Reading data from Device
Writing data to Device

## Slide 15: USB token packets
Packet fields
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Token type: Setup device, Read from device, or Write to device
  Address+Endpoint to identify Device
  CRC, (Cyclical Redundancy Check) to detect bit errors
    5-bit CRC

## Slide 16: USB data packets
Packet fields
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Data: application data
  Data, up to 1023 bytes (full speed, often capped at 64 for microcontrollers, probably bigger for modern USB versions)
  CRC, (Cyclical Redundancy Check) to detect bit errors
    16-bit CRC

## Slide 17: Cyclic Redundancy Check (CRC)
Determines if the data received matches the data sent
  CRC value is calculated on original data and appended to message
  CRC value is recalculated on the received data
  Value appended to message and value recalculated MUST match
Essentially some kind of hash operation
  Turns many bits into some smaller number of bits that are unique-ish
CRC algorithms are:
  Particularly good at single bit errors AND contiguous bit errors
  Relatively simple to calculate
  Very widely used in communication

## Slide 18: Break + Question
Why have two CRC values?
Reading data from Device
Writing data to Device

## Slide 19: Break + Question
Why have two CRC values?
  Devices that aren’t addressed want to be able to determine that right away without reading all of the data
  For reading, data is sent by two different devices, so it needs two CRCs
    Keep writes the same for symmetry
Reading data from Device
Writing data to Device

## Slide 20: USB Outline
Low-layer details
  How are bits sent
  How are packets (collections of bits) sent
Higher-layer details
  How do we interact with devices
  How do we determine what devices are and how they work

## Slide 21: Interacting with USB devices
Each Device is given a separate address on the bus
Each Device also has a number of Endpoints
  Logical communication channels
  Direct data and guide communication patterns

## Slide 22: USB endpoint types
Interrupt transfers
  Guaranteed latency, small amounts of data
  Important sensor data (mice and keyboards)
  Polled frequently by Host
Bulk transfers
  Sporadic large transfers, reliable communication
  General reading/writing of data (flash drives and USB serial)
  Polled by Host whenever there is available bandwidth
Isochronous transfers
  Guaranteed data rate, unreliable communication
  Continuous data streaming (audio and webcams)
  Polled frequently by host

## Slide 23: USB control endpoint
Every USB Device has a special Control endpoint as well
Used for setting up the USB Device driver on the Host
Initializing a Device
  Host sends SETUP transaction requesting device descriptor
  Host performs IN transaction to read device descriptor
  Host performs OUT transaction to write device status

## Slide 24: USB device descriptors
Tree structure describing the device
  Interfaces it provides
  Endpoints associated with each interface
  Transmitted as an array of bytes
Secretly the best part of USB: devices tell the computer what they are (and how to use them)

## Slide 25: Example Microbit
Interface: Communications, Abstract (modem), CDC
  Endpoint: 3, IN, Interrupt
Interface: CDC Data, CDC DATA interface
  Endpoint: 1, IN, Bulk
  Endpoint: 2, OUT, Bulk
Interface: Vendor Specific Class, Subclass, Protocol
  Endpoint: 5, IN, Bulk
  Endpoint: 4, OUT, Bulk
Interface: Mass Storage, SCSI, MSD interface
  Endpoint: 7, IN, Bulk
  Endpoint: 6, OUT, Bulk
SEGGER JTAG interface
Virtual serial device
USB external filesystem

## Slide 26: lsusb output
lsusb
  List USB devices
Combine with –s flag to select a single device
Combine with -v flag for verbose mode with more information

## Slide 27: Minimal virtual serial USB Device
Virtual Serial Device
  Endpoint 0: Control, IN/OUT
    Respond to IN requests by setting up OUT with a buffer of descriptor data of the correct size
  Endpoint 1: Interrupt, IN
    Needed for serial modem controls, just ignore it
  Endpoint 2: Bulk, OUT
    Connect to buffer from _write() (just takes raw characters)
  Endpoint 3: Bulk, IN
    Connect buffer to _read() (just provides raw characters)

## Slide 28: HID USB Device (Human Interface Device)
Used for human interaction devices, like keyboard/mouse
“Report” structure is provided over Interrupt IN endpoint
  Or on demand via Control IN endpoint
Example mouse with x,y and three buttons

## Slide 29: USB summary
Specification for fast data communication
Specification for interacting with abstract device types
  Connects correct driver to interpret and send data
Pros
  Very fast
  Very interoperable
Cons
  Hardware and software are way more complex than simple protocols like UART, SPI, and I2C
  Not very energy efficient

## Slide 30: nRF52 USBD
Implements USB Device (not Host)
  Control endpoint
  14 bulk/interrupt (7 IN, 7 OUT)
    64-byte transfers
  2 isochronous (1 IN, 1 OUT)
    1023-byte transfers
Full-speed USB
  With 5 volt signals

## Slide 31: Break + Question
What are the ramifications of many USB devices sharing a bus?
  Consider: throughput and latency
What if I really had 127 USB mice on a single USB hub?
  What if it was microphones instead?

## Slide 32: Break + Question
What are the ramifications of many USB devices sharing a bus?
  Consider: throughput and latency
    Devices need to share bandwidth
    Also devices are “polled” one-at-a-time
What if I really had 127 USB mice on a single USB hub?
  What if it was microphones instead?
    Certainly latency would be really bad
    You might saturate the data throughput capabilities!

## Slide 33: Outline
USB
CAN
Bit-banging
  1-wire
  Neopixel LED strips
Video Protocols
  VGA
  HDMI

## Slide 34: Controller Area Network (CAN bus)
Designed for highly reliable interactions within a vehicle
Multi-master with arbitration
  Similar to I2C
Mechanism for sending messages with “identifiers”
  Identifies the data in the message, not the device its for
  Lower value identifiers have high priority
  All messages are received by all CAN nodes
    Which can decide at higher levels which identifiers they care about

## Slide 35: CAN physical connections
Two differential, wired-AND signal lines
  Transitions are used to transmit bits (non-return-to-zero) with bit-stuffing
  Combines aspects of USB and I2C
  125 kHz – 5 Mbps speeds

## Slide 36: CAN packet format
11-bit identifier
  Check bits as they are sent to see if you win arbitration
Up to 8 bytes (64 bits) of data
  Very small messages! (other versions of CAN provide more data)
CRC for bit error detection
Acknowledgement
  Like I2C, let the line float and see if another device responds
  If not, explicitly retransmit!

## Slide 37: CAN message types
Data frame
  Transmission of data for a certain identifier
Remote frame
  Requests data transmission of a certain identifier
Error frame
  Transmitted when an error is detected with the previous message
Overload frame
  Transmitted by a node that is too busy to respond right now

## Slide 38: CAN reliability design – detecting errors
Check for errors everywhere and appropriately handle
  Bit error
    If the value found on the bus differs from the one sent
  Stuff error
    If 6 consecutive bits of the same type are found
  CRC error
    If CRC does not match
  Form error
    Format field has unexpected values
  Acknowledgement error
    No ACK received
Devices detecting an error broadcast a message signifying it!
  Multiple devices sending the same message works without arbitration loss
  Previous message is then retransmitted

## Slide 39: CAN reliability design – handling errors
Each node accepts the possibility that maybe it is the faulty one
Track errors and successes and change device state
  Passive: limited error signaling and transmissions
  Bus off: does not transmit in any way
Idea is that the CAN controller hardware can be faulty but still detect it in some cases

## Slide 40: CAN summary
Designed for reliable vehicular communication
Multi-master bus with serial communication
Pros
  Highly reliable
  Extensible to many devices
Cons
  Special-purpose design. Whole system has to agree on identifiers
  Relatively slower throughput

## Slide 41: Break + Open Question
Why is CAN a good choice for vehicles (historically)?
What problems is CAN facing today?

## Slide 42: Break + Open Question
Why is CAN a good choice for vehicles (historically)?
  High reliability
  A few low-data-rate sensors scattered throughout the car
What problems is CAN facing today?
  Camera data doesn’t fit in 8-byte packets…

## Slide 43: Outline
USB
CAN
Bit-banging
  1-wire
  Neopixel LED strips
Video Protocols
  VGA
  HDMI

## Slide 44: Controlling a protocol without a peripheral
If your microcontroller doesn’t have a hardware peripheral to control a certain protocol, you could still emulate it
  Known as bit-banging
Example: use GPIO to create a UART
  Set high/low values with certain timings to make start, data, and stop bits
    Probably based on an interrupt if microcontroller is fast enough
    Or maybe is hard-coded with delays
  For reading the UART, instead read bits from the bus at a given rate
    Expect start/stop bits, but ignore them

## Slide 45: Two bit-banging examples
1-Wire Protocol
Neopixel LED strip

## Slide 46: 1-Wire Protocol
Similar to I2C, but without a clock line
Devices can optionally power themselves off the data line

## Slide 47: 1-wire read operations
Controller drives line low then releases, and samples 15 μs later
  Falling edge wakes up peripheral devices
  Peripheral device either drives low for a 0 or also releases for a 1
Peripheral writes 0
Peripheral writes 1
Controller samples at ~15 μs
Controller samples at ~15 μs
Controller pulling data line low
Peripheral pulling data line low
Resistor pullup

## Slide 48: Controlling 1-wire with a UART
1-wire is not supported by most microcontrollers
  Instead, it must be emulated either with GPIO or with another protocol
Example: UART plus an external transistor can emulate 1-wire
  Run UART way faster than 1-wire: each UART byte is one 1-wire bit
  Connect TX to a transistor which can connect to Ground or disconnect
  Connect RX to the data line
  To read, write data 0xFF
    Start bit pulls line low to trigger peripheral device
    8 data bits do not affect data line (disconnected)
    RX line will match 0xFF for reading a 1, or will be anything else for a 0

## Slide 49: Two bit-banging examples
1-Wire Protocol
Neopixel LED strip

## Slide 50: Neopixel LED strips
LEDs on a long strip connected in series
  Often capable of RGB control
Custom protocol for driving them

## Slide 51: Neopixel protocol
32 bits for each LED
  After the first LED gets its data, all the next bits are forwarded down the chain
Each bit is represented by an amount of time high and low

## Slide 52: Emulating Neopixel protocol with SPI
Idea: configure SPI speed so N bits line up with the period of the bit
  For example, 8 bits per period
To send a 0 bit: 0xE0 (0b11100000)
To send a 1 bit: 0xF8 (0b11111000)
From the Neopixel perspective, that data is just the square wave it wanted
Warning: I don’t promise the actual numbers here are correct. Just the overall idea. Recalculate the numbers yourself based on timing requirements

## Slide 53: Emulating Neopixel protocol with PWM
Idea: these are just differing duty-cycle square waves i.e., PWM
  Set PWM period to equal the period for sending a bit
  Needs to be a left-aligned PWM signal
To send a 0 bit: 30% duty cycle
To send a 1 bit: 70% duty cycle
Driver translates colors into a byte array, then bits in the array into duty cycles, then just plays the duty cycles
Warning: I don’t promise the actual numbers here are correct. Just the overall idea. Recalculate the numbers yourself based on timing requirements

## Slide 54: Details on NeoPixels
Datasheets:
  https://cdn-shop.adafruit.com/product-files/2757/p2757_SK6812RGBW_REV01.pdf
  https://cdn-shop.adafruit.com/datasheets/WS2812B.pdf
Good writeups on using NeoPixels:
  https://github.com/japaric/ws2812b/blob/master/firmware/README.md
  https://wp.josh.com/2014/05/13/ws2812-neopixels-are-not-so-finicky-once-you-get-to-know-them/

## Slide 55: Outline
USB
CAN
Bit-banging
  1-wire
  Neopixel LED strips
Video Protocols
  VGA
  HDMI

## Slide 56: Controlling video output
Not very common for embedded systems
  Either directly connected to a screen over SPI/I2C, or not at all
Very common for traditional computing though
  And while we’re talking about protocols, let’s look at them!
Reminder: memory is a huge embedded systems concern here
  640 x 480 pixels @ 18-bit color = 675 kB
  nRF52833 RAM: 128 kB, Flash: 512 kB

## Slide 57: Old-school VGA display design
Screen lights up when hit with electrons
  Separate Red, Green, and Blue activation areas
System directs electrons at each pixel of the screen on a loop

## Slide 58: VGA connector
All data goes to the display (write-only)
Horizontal and Vertical sync lines
  Timing control
  Horizontal: when each row restarts
  Vertical: when the entire screen restarts
Red/Green/Blue lines
  Analog voltage for intensity: 0-0.7 volts
  Requires a high-speed DAC (RAMDAC)
Ground pins
  To connect ground between devices

## Slide 59: Example display: 640x480 at 60 Hz
Send each pixel in a row at 20 MHz (40 ns per pixel)
  25 μs for the entire 640 pixel row
6.35 μs pause before next row
After all 480 rows, 1.43 ms pause before next frame
High resolution devices would have to go faster
  Possibly MUCH faster
https://digilent.com/reference/learn/programmable-logic/tutorials/vga-display-congroller/start

## Slide 60: More modern VGA devices
Protocol doesn’t really make any sense for a digital device
  But it already existed and was very popular
  So LCD monitors and projectors implemented it too
ADC reads in analog voltages for Red, Green, and Blue into a memory
Data from the memory is displayed on the screen
Bits -> DAC -> Wire -> ADC -> Bits
  That’s a lot of unnecessary work

## Slide 61: VGA Extension - Display Data Channel (DDC)
Uses extra wires in the VGA connector
  Originally “4-bit monitor ID”, but rarely used in practice
  Instead uses two pins as I2C data and clock lines
Monitor is always a peripheral device at address 0x50
Provides a “Extended Display Identification Data” payload
  128-256 bytes of data
  “Descriptor” for the display, like USB descriptors
  Identifies manufacturer, resolution(s), refresh rate(s), timing requirements

## Slide 62: HDMI
Clock plus three data “channels”
  Transition-Minimized Differential Signaling (TMDS)
  Similar to USB with twisted pair wiring
  Send data packets to display
I2C data and clock for Display Data Channel (DDC)
  Adapted from VGA
Consumer Electronics Control (CEC) enables control of devices
  Only uses 1-wire to reduce pin count
  Protocol: simplified async I2C

## Slide 63: Outline
USB
CAN
Bit-banging
  1-wire
  Neopixel LED strips
Video Protocols
  VGA
  HDMI