## Slide 1: Lecture 16: Embedded OS
CE346 – Microcontroller System Design
Branden Ghena – Fall 2025

## Slide 2: Administrivia
See you all tomorrow for project check-ins
Last quiz this coming Tuesday
  I promise to grade Quiz 3 this weekend. Sorry about the delay

## Slide 3: Today’s Goals
Introduce embedded OS concerns and how they are different from general-purpose computing, particularly in security.
Describe Tock Operating System goals and design
Introduce Rust programming language
Explore example OS device driver stackup from Tock
Sidebar: I promise not to quiz you on specific Tock details
  Although I might ask you about embedded OS in general

## Slide 4: General Tock resources
https://github.com/tock/tock
https://www.tockos.org/
“Multiprogramming a 64 kB Computer Safely and Efficiently” Levy et al. 2017. Symposium on Operating Systems Principles. https://brandenghena.com/projects/tock/levy17multiprogramming.pdf
"Tock: From Research to Securing 10 Million Computers“ Schuermann et al. 2025. Symposium on Operating System Principles. https://brandenghena.com/projects/tock/2025-sosp-tock-decade.pdf

## Slide 5: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design

## Slide 6: What is an operating system?
Hardware
Steam
Chrome
Powerpoint
QEMU
Spotify
User processes
Physical computer

## Slide 7: What is an operating system?
Hardware
Steam
Chrome
Powerpoint
QEMU
Spotify
User processes
Operating System
Physical computer

## Slide 8: What is an operating system?
Hardware
Steam
Chrome
Powerpoint
QEMU
Spotify
User processes
File System
Process Manager
Network
Virtual Memory
Operating System
Device Drivers
Interrupt Handlers
Boot and Init
Physical computer

## Slide 9: What is an operating system?
Hardware
Steam
Chrome
Powerpoint
QEMU
Spotify
User processes
File System
Process Manager
Network
Virtual Memory
Operating System
Device Drivers
Interrupt Handlers
Boot and Init
Hardware Abstraction Layer
Application Interface
Physical computer

## Slide 10: Operating systems goals
OSes make advancing technology available to rapidly evolving applications. They do so with two major goals:
  Provide abstractions to applications to enable hardware compatibility
    Why: allow reuse of common features, avoid low-level details
    Challenges: What are the correct abstractions?
  Manage sharing of resources across many applications
    Why: protect applications, enforce fair access
    Challenges: What are the mechanisms and what are the policies?
Good operating systems do these quickly, efficiently, and securely

## Slide 11: How does this differ from what we’ve been doing?
Often our application and driver logic were coordinated and in some cased co-mingled
  We didn’t consider “sharing” of resources between multiple stakeholders
We did abstract away interfaces to hardware
  But we didn’t consider how to do so in a way that allowed hardware to be interchangeable

## Slide 12: Userspace versus kernel distinction
Kernel has full control over the system
  Manages resources
Userspace has partial control (whatever the kernel allows it)
  Uses resources granted to achieve some goal
When userspace wants access to something, it needs to request it from the kernel
  Uses “system calls” to do so
  Trigger a software interrupt, with some values to describe what it wants
    Kernel takes action (or denies action) and returns back to application

## Slide 13: Linux system calls
Example system calls
  https://man7.org/linux/man-pages/man2/syscalls.2.html
Number | Name | Description
0 | read | Read file
1 | write | Write file
2 | open | Open file
3 | close | Close file
4 | stat | Get info about file
57 | fork | Create process
59 | execve | Execute a program
60 | _exit | Terminate process
62 | kill | Send signal to process

## Slide 14: Embedded needs its own operating systems
Can’t use normal Linux!
  Too little memory and processing in embedded hardware
  Too much concern about power in embedded applications
  Microcontrollers don’t have the necessary hardware features (virtual memory)
Important: Linux is never going to be the solution
  Capabilities of general computers are orders of magnitude better
  Embedded systems are gaining more capabilities
  But new lower-power, lower-cost systems keep emerging too

## Slide 15: Linux is useful for many edge devices though
Raspberry Pi is a great example
If your device is powerful enough to run Linux, maybe that’s a good idea!
  Essentially gives you a normal computer platform to run stuff on
  Easier to do big things: Webcam -> Python -> OpenCV
But there will always be smaller, cheaper, less capable devices where Linux doesn’t make sense
  Or even bigger, capable systems that need to be precisely controlled

## Slide 16: A variety of embedded OSes exist with different designs
TinyOS (2000-2012-ish) was designed to support extremely low-capability devices with 2 KB of RAM total
FreeRTOS (2003-today) was designed to real-time tasks with a very small kernel, around 8 source files

## Slide 17: Zephyr (2016-today)
Linux Foundation embedded OS project
  Developed in C
  Lots of industry buy-in
Features (in their words)
  Extensive suite of kernel services
    Multi-threading, memory allocation, IPC, power management, etc.
  Multiple scheduler choices
  Highly configurable and modular
  Cross architecture

## Slide 18: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design

## Slide 19: Two needs not met by traditional embedded OSes
Security
  Protect the core platform from applications
Multiprogramming
  Run multiple, unrelated applications (securely)

## Slide 20: Challenge for secure embedded: no virtual memory
No hardware support for virtual memory
  So all addresses on the system are real physical addresses
Nothing prevents applications from
  Manipulating kernel data structures
  Directly accessing hardware
All applications on the system must be trusted
  Devices do have one single purpose
  But any weak link leaves the whole system broken

## Slide 21: Embedded devices are a weak link
Custom, application-specific code written in C
  Limited code-reuse
  Low testing coverage
All code on the system is trusted
  No isolation: any code can directly access hardware registers
  Little distinction between “kernel” and “application”

## Slide 22: Reminder: Mirai botnet (2016)
Takes control of up to 600,000 insecure connected devices
  IP-attached cameras, DVRs, routers, printers

## Slide 23: Weak devices provide network entry points
IoT devices can be used as a network entry point
  Step one: hack the device
  Step two: use the device to access information on the private network
Example: casino high-rollers database obtained through an IoT fish tank thermostat
  https://interestingengineering.com/a-casinos-database-was-hacked-through-a-smart-fish-tank-thermometer
See also: Mirai botnet

## Slide 24: Modern systems increasingly need support for multiprogramming
Example: USB authentication key
  Universal Second Factor (U2F)
  HMAC One-time Password (HOTP)
  GPG Key (GNU Privacy Guard)

## Slide 25: Security layering is desirable
Different domains with different expectations
  Applications, services, and platform

## Slide 26: Platform layer
Core kernel plus microcontroller-specific code
  ~10 developers
  Trusted compute base
Goal: possible to correctly and safely extend

## Slide 27: Services layer
Device drivers, networking, libraries
  ~100 developers
  Auditable, but possibly still buggy
Goal: protect kernel from safety violations

## Slide 28: Applications layer
End-user functionality
  ~1000 developers
  Third-party applications, potentially malicious
Goal: end-users can install 3rd-party apps

## Slide 29: Break + Question
What are challenges for updating IoT device firmware?

## Slide 30: Break + Question
What are challenges for updating IoT device firmware?
  Manufacturer needs to create update (still exist AND care)
    Software is usually closed source, so others can’t update it
  Update needs to get to the device
    Either the device needs an internet connection to check
    Or consumer needs to be aware of update and have a mechanism to upload it

## Slide 31: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design

## Slide 32: Tock
Embedded OS designed for secure multiprogramming
  Kernel written in Rust programming language
  Applications written in any language
  Runs on multiple hardware platforms
Open-source research project
  2015 collaboration between Stanford, UC Berkeley, and Michigan
    Since expanded to 6-7 universities (Princeton, UCSD, Northwestern)
    Plus several companies (Google, Microsoft, Western Digital)
https://github.com/tock/tock
https://tockos.org/

## Slide 33: Tock Features
A preemptive embedded OS (runs on microcontrollers)
  ARM Cortex-M and RISC-V supported now
Has separate kernel and user space
  Most embedded OS have the one piece software philosophy
  Runs untrusted apps in user space
  Uses memory protection on applications (hardware support required)
Kernel (and drivers) written in Rust
Apps written in C/C++ or Rust (any language is possible)

## Slide 34: Tock software organization
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
System Calls
6LoWPAN
SI7021
SD Card
Console
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf
Syscall Interface

## Slide 35: Tock’s isolation mechanisms
Processes
Standalone executable in any language
  C, C++, Rust, Lua
Isolation enforced at runtime
Higher overhead
Applications
Capsules
Rust code linked into kernel
Isolation enforced at compile-time
Lower overhead
Used for device drivers, protocols, timers...
Trusted for liveness, not safety
Totally untrusted

## Slide 36: What does the Tock core kernel include?
Managing Processes
  Loading, stopping
Scheduling
  Determining which process is running at which time
  Handling hardware events
Memory Management
  Mostly giving chunks to processes
  Also memory protections
Syscalls
  Connecting processes to device drivers

## Slide 37: Device drivers
Much larger percentage of the code in Tock
Split into groups
  Capsules are microcontroller-agnostic (above the core kernel)
    Syscall drivers connect syscalls to specific devices
    Control for generic systems: GPIO, LED, Timers, etc.
    External devices: connected over buses
      I2C: Temperature, Pressure, Humidity, Light, IMU
      SPI: Screen, Memory
  Chip drivers are microcontroller-specific (below the core kernel)
    Implement various peripherals within those microcontrollers

## Slide 38: Userspace applications
Written and compiled entirely separately from the kernel
  Load the kernel into flash
  Individually write each application to flash as as well
Written in any language
  C is the major one, Rust also big
  C++ and Lua exist
System calls to the kernel to make device requests

## Slide 39: How do applications access devices?
System calls are used to access devices
  All device interactions are non-blocking (start now, finish later)
Three generic syscalls
  Command – takes a 32-bit numerical argument
  Allow – takes a pointer to a buffer to read/write
  Subscribe – takes a pointer to a function to callback
First two arguments to all syscalls
  Driver number (the driver it wants to interact with)
  Minor number (driver-specific identifier)

## Slide 40: Example: console capsule (driver number: 1)
Command syscall values
  Transmit from buffer, argument is length
  Receive into buffer, argument is length
  Cancel request
Allow syscall values
  Pointer to buffer for sending
  Pointer to buffer for receiving
Subscribe syscall values
  Send complete handler
  Receive complete handler
Writing bytes to console:
uint8_t buffer[20] = {…data…}
Allow(1, 1, buffer)
Command(1, 1, 20)

## Slide 41: Event-driven programming
Tock adopts an event-driven model to avoid concurrency issues
  Single core system, so the source of concurrency is interrupts
  Exposed to applications through “subscribe” callbacks
Callbacks never occur during normal operation
  Even if application is descheduled due to timeslice
Additional syscall: yield – no arguments
  Application pauses until a callback is ready for it
  Once one or more events are ready
    Call the callback handlers, one at a time
    Return from yield statement

## Slide 42: Yield example
void sensor_callback (int value) { printf("Got sensor reading %i\n", value); }
int main () { sensor_register(sensor_callback); // calls allow sensor_sample(); // calls command yield(); }

## Slide 43: Real Tock applications
Practically, these syscalls are wrapped in library code rather than exposed raw like that
  Except for yielding
Libtock-C design (C userspace)
  Libtock – async libraries
  Libtocksync – sync libraries (built using async libraries)

## Slide 44: Example Tock application
https://github.com/tock/libtock-c/blob/master/examples/tests/microbit_v2/main.c

## Slide 45: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design

## Slide 46: Tock threat model
Kernel security
  Secrets may not be accessed by applications or capsules.
  Applications and capsules may not modify kernel data except through exposed APIs.
In normal operating systems, drivers are run in kernel mode
  Full access to memory and hardware on the system
So how do we do better than that without moving drivers into userspace applications

## Slide 47: Tock solution: use language features
Tock uses the Rust programming language for the kernel
Systems language
  Represents how hardware actually interacts
  Strong type system and memory safety
  Runtime behavior similar to C
Result: capsules cannot access memory they do not own
  Cannot access application secrets
  Cannot modify other kernel structures (even by accident)

## Slide 48: Basic Rust syntax
let a: i32 = 1;
  Creates a variable a which is a 32-bit signed integer. Sets value to 1
let mut b: u8 = 0;
  Creates a variable b which is an 8-bit unsigned integer. Sets value to 0
  Mutable variables can be modifed later in code
fn add2(x: f64, y: f64) -> f64 {
// implicit return (no semicolon)
x + y
}
  Function that takes two double arguments and returns a double

## Slide 49: Rust Structs and Impl
// Define a struct named 'Point' with fields 'x' and 'y'
struct Point {
x: f64,
y: f64,
}
// Implementation block for the 'Point' struct
impl Point {
// Define a method that calculates the distance between two points
fn distance_to(&self, other: &Point) -> f64 {
// Calculate the distance using the Euclidean distance formula
((self.x - other.x).powi(2) + (self.y - other.y).powi(2)).sqrt()
}
}
let distance = point1.distance_to(&point2);
Later in code:

## Slide 50: What problems is Rust trying to solve?
Memory lifetime
  Use-after-free
  Common example: pass a reference into a function, then free it
Data races
  Multiple access to data and at least one modifies it
  Problems we were solving with locks
Generally: have the compiler handle for you whatever it can

## Slide 51: Rust has a strong notion of “ownership”
Ownership is a notion of managing memory and sharing.
Rust ownership rules
  Each value has a variable that’s called its owner.
  There can only be one owner at a time.
  When the owner goes out of scope, the value is dropped.
Last one is straightforward:
  Values on the stack go away at the end of the function (or any block { })
  This lifetime works just like C or C++

## Slide 52: Example: ownership with strings
Rust ownership rules
  Each value has a variable that’s called its owner.
  There can only be one owner at a time.
let s1 = String::from("hello");
let s1 = String::from("hello"); let s2 = s1;

## Slide 53: Ownership is transferred through function calls
fn main() { let s = String::from("hello"); // s comes into scope takes_ownership(s); // s's value moves into the function... // s is no longer valid here } // Here, s goes out of scope. But because s's value // was moved, nothing special happens.
fn takes_ownership(some_string: String) { // some_string comes into scope println!("{}", some_string); } // Here, some_string goes out of scope and `drop` is called. // The backing memory is freed.

## Slide 54: Ownership model prevents data races
References allow multiple read-only access to a value
  For example: passing a value into a function by reference
  Any number of references may exist to a value
Requesting a writable (mutable) reference requires sole ownership
  No other references may exist
  Original owner cannot access value
This is enforced by the compiler!!!
  So there is no runtime cost
  And programmers cannot do bad things by accident

## Slide 55: My feelings about writing code in Rust
Three steps of Rust acceptance
You are confused about little weird syntax things.
You are frustrated by so many compilation errors.
You realize your code mostly works if it compiles.

## Slide 56: Tock downside: all drivers must be written in Rust
Why hasn’t every OS taken the “language support” path?
  Primarily, it wasn’t really available. C or C++ were the only real options.
Also, the vast majority of developers know C but not Rust
  And the vast majority of existing code is in C and not Rust
One of Tock’s major challenges is that things like networking stacks need to be re-written in Rust
  BLE, 802.15.4, WiFi

## Slide 57: Sidebar: the future of Rust
Rust is still growing in popularity but still fairly young
  Many people are excited to have a safe alternative to C
  But there is a steep learning curve to using Rust
  And a vast body of existing code already in C
How dominant would it have to be to switch our curriculum?
  Unclear. We’ve taught C for decades.
  Certainly considering it for CS211, but no immediate plan to change
    Still can’t stop teaching C (too useful)
    Rust in 5 weeks at the end of CS211 would be much harder than C++

## Slide 58: Learning Rust
Slowly creeping into the Systems curriculum at Northwestern
You’ll likely need to learn it on your own
  https://www.rust-lang.org/learn
  https://doc.rust-lang.org/book/
  https://serokell.io/blog/learn-rust
  https://learnxinyminutes.com/docs/rust/ (5 minute overview)

## Slide 59: Break + Programming languages personified
https://leftoversalad.com/c/015_programmingpeople/

## Slide 60: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design

## Slide 61: Driver “stack”
Driver code does a lot of work internally
Externally provides a simpler abstract interface to the device
Some drivers build on top of other drivers
  Snake game
  Builds on top of LED Matrix driver
  Builds on top of GPIO and Timers

## Slide 62: Typical software stack in Tock
Application(s)
Libtock-c Library
Syscall Driver
Hardware Interface Layer (HIL)
Chip Driver
Additional Capsules (zero or more)

## Slide 63: Layer connections
Each layer can communication with the one above and below it
Within the kernel each layer
  Has a reference to the thing below and can call functions on it directly
  Has a “client” reference to thing above
    Allows responding upwards when action is complete
    Usually one function: callback()
Application(s)
Libtock-c Library
Syscall Driver
Hardware Interface Layer (HIL)
Chip Driver
Additional Capsules (zero or more)

## Slide 64: Example: Tock temperature stack on Microbit
Let’s revisit our favorite temperature sensor
  Degrees Celsius in 0.25 degree increments
Register interface
  TASKS_START
    Start a measurement
  INTENSET
    Enable interrupts
  EVENTS_DATARDY
    Check if temperature value is ready
  TEMP
    Read temperature value
Application(s)
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
nRF52 TEMP Driver

## Slide 65: Temperature chip driver
https://github.com/tock/tock/blob/master/chips/nrf5x/src/temperature.rs
Accesses registers to interact with Temperature peripheral
Demonstrates Tock register interface
Implements the TemperatureDriver HIL
Application(s)
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
nRF52 TEMP Driver

## Slide 66: Senors Hardware Interface Layer
Rust “trait” that a struct can implement
  Allows shared behavior by multiple underlying implementations
TemperatureDriver
  set_client(&TemperatureClient)
  read_temperature() -> Result<(), ErrorCode>
TemperatureClient
  callback(Result<i32, ErrorCode>)
https://github.com/tock/tock/blob/master/kernel/src/hil/sensors.rs
Application(s)
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
nRF52 TEMP Driver

## Slide 67: Temperature capsule
https://github.com/tock/tock/blob/master/capsules/extra/src/temperature.rs
Implements Syscall driver
  Commands
    0 – check if this exists
    1 – read temperature
  Subscribe
    Get callbacks with temperature values
Tracks “busy” status of sensor
  But allows multiple applications to be notified when value is ready
Application(s)
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
nRF52 TEMP Driver

## Slide 68: Libtock-c Temperature Library
https://github.com/tock/libtock-c/blob/master/libtock/sensors/temperature.c
libtock_temperature_read(callback)
Actual syscalls in a separate file
  https://github.com/tock/libtock-c/blob/master/libtock/sensors/syscalls/temperature_syscalls.c
Application(s)
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
nRF52 TEMP Driver

## Slide 69: Example: Microbit Inertial Measurement Unit (IMU)
Capsule for LSM303AGR chip
  Uses generic I2C capsule below it
  Provides interface for Ninedof above it
Allows LSM303AGR driver to be reused on multiple boards
  Each which could have different microcontrollers
Application(s)
Libtock-c Ninedof
Ninedof Capsule
Sensors HIL (Ninedof)
LSM303AGR Capsule
I2C HIL (I2CDevice)
…

## Slide 70: Full LSM303AGR stack
LSM303AGR provides two interfaces
  Ninedof
  Temperature!
Beneath it gets a bit messy
  I2CDevice
    Concept of a device with an address
  I2CMaster
    Implementation
Application(s)
Libtock-c Ninedof
Ninedof Capsule
Sensors HIL (Ninedof)
LSM303AGR Capsule
Libtock-c Temperature
Temperature Capsule
Sensors HIL (TemperatureDriver)
I2C HIL (I2CDevice)
Virtual I2C Capsule
I2C HIL (I2CMaster)
nRF52 I2C Driver

## Slide 71: Capsules can have multiple drivers beneath them too
Application(s)
Libtock-c SDCard
SDCard Capsule
SPI HIL (SpiMasterDevice)
nRF52 SPI Driver
Virtual SPI Capsule
SPI HIL (SpiMaster)
Time HIL (Alarm)
nRF52 Timer Driver
GPIO HIL (InterruptPin)
nRF52 GPIO Driver

## Slide 72: General Tock resources
https://github.com/tock/tock
https://www.tockos.org/
“Multiprogramming a 64 kB Computer Safely and Efficiently” Levy et al. 2017. Symposium on Operating Systems Principles. https://brandenghena.com/projects/tock/levy17multiprogramming.pdf
"Tock: From Research to Securing 10 Million Computers“ Schuermann et al. 2025. Symposium on Operating System Principles. https://brandenghena.com/projects/tock/2025-sosp-tock-decade.pdf

## Slide 73: Outline
Embedded Operating Systems
Embedded Security Challenges
Tock Overview
Rust Programming
Tock Driver Design