## Slide 1: Lecture 02 Microcontrollers
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Class Updates
Reminder: fill out lab hardware survey ASAP
  The link is on Campuswire
Starting orders after class
  Let me know when people start receiving stuff
My office hours 1-2pm today
  Feel free to swing by

## Slide 3: Today’s Goals
Explore microcontrollers
  Their purpose
  Their capabilities
  Design tradeoffs
Describe history and state-of-the-art for microcontrollers
Explore the microcontroller(s) on our Microbits

## Slide 4: Outline
Microcontroller Background
Microcontroller Design
Microcontroller History
Microbit microcontroller

## Slide 5
Source: iFixit
Notes: Fitbit, Wearables, microcontrolles

## Slide 6
Source: iFixit
Samsung K3LK4K40BM-BGCN 12 GB LPDDR5 RAM layered over Qualcomm 865 SoC
Samsung Galaxy S20 Ultra
Notes: SoC, LOTS of microcontrollers and accelerators, multiple things all on one die (often the CPU, an accelerator of some kind for example to speed up video processing, and a comms unit like a Wifi or BLE chip).

## Slide 7
Source: iFixit
LR35902 4.19 Mhz CPU …Z80 Microprocessor
The Nintendo Game Boy was initially released in Japan on April 21, 1989

## Slide 8
…computing everywhere!

## Slide 9: Categories of computer chips
Microprocessor (MPU or Processor)
  CPU + Bus/Pins
  No memory or peripherals
Microcontroller (MCU)
  CPU + Pins + Memory + Peripherals
  Peripherals: separate hardware units within chip
    Often I/O interfaces
System on a Chip (SoC)
  Microcontroller + Extensive Peripherals
  Example: Radios or ML Accelerators
  Essentially multiple chips combined
Evolution of increased complexity over time

## Slide 10: Outline
Microcontroller Background
Microcontroller Design
Microcontroller History
Microbit microcontroller

## Slide 11: Generic microcontroller block diagram
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 12: Processor
Microcontroller needs to execute software instructions
Emphasis: simple and reliable
  i.e. not x86 CISC
Often simple, in-order, short-pipeline RISC architectures
  Literally a three-stage pipeline you likely learned in CS361
Many different ISAs are possible
  Custom ISAs and ARM (ARMv7E-M) are both common

## Slide 13: Reminder: Instruction Set Architecture
ISA includes the actual instructions as well as the model for how the computer interacts with memory
Does the ISA for a microcontroller matter if you’re not programming in assembly?

## Slide 14: Reminder: Instruction Set Architecture
ISA includes the actual instructions as well as the model for how the computer interacts with memory
Does the ISA for a microcontroller matter if you’re not programming in assembly?
  Yes
  Differences in instruction efficiency and amount are important
  Differences in compiler support are VERY important

## Slide 15: Processor design choices
How many bits is the architecture?
  8-bit and 16-bit not uncommon
  64-bit is very rare (who has that much memory?)
What instructions are supported?
  Normal stuff yes
  What about single-cycle multiply?
  What about floating-point operations?
  Vector instructions?
How fast does it run?
  1-100 MHz is common on modern systems (faster is more energy cost)
  Occasionally MUCH slower (think 32 KHz)

## Slide 16: Memory
Common memory hierarchy
What’s missing? Why?
Registers
RAM
ROM

## Slide 17: Memory
Common memory hierarchy
What’s missing? Why?
  Cache
  Makes timing unreliable
Registers
RAM
ROM
More modern microcontrollers often have optional instruction caches
Can be enabled by software

## Slide 18: Volatile memory: SRAM
Same design as registers in traditional computer systems
  No need to refresh it -> lower energy costs
Tradeoff:
  More expensive
  Physically larger

## Slide 19: Non-Volatile memory: Flash (usually)
Same design as SSDs and Flash drives
Memory is stored with no energy costs
  Reading is lowish energy and quick
  Writing is high energy and very slow
    Writing also has to occur in blocks (e.g. 512 bytes)
Concern: Flash has a limited lifetime ~10,000 writes
  Only writing to Flash when you load code? Essentially forever
  Recording data to Flash every second? 2.8 hours

## Slide 20: SRAM (RAM) versus Flash (ROM) memory
Size and time difference between non-volatile and volatile memory is significantly reduced from traditional computing
  Non-volatile store 2-10x larger than volatile
  Single-cycle RAM. Maybe two-cycles to Flash (to read)
Major difference: energy and writability
  SRAM is low-energy to read and write (no refresh needed)
  Flash is lowish-energy to read, but very high energy to write
Hierarchical structure is not enforced
  Same address space for RAM and Flash (very different from traditional)
  Run instructions right inside of Flash
  Keep variables in RAM (or const variables in Flash)

## Slide 21: Memory design choices
How much memory can we fit without making it too high cost or too high power?
  The answer has slowly increased over time
  15 years ago: 2 KB RAM – 32 KB Flash
  Today: 256 KB RAM – 1 MB Flash
How to provide memory safety?
  Usually no virtual memory (all addresses are real addresses)
  Nothing stops arbitrary memory overwriting
  Modern systems: Memory Protection Unit
    Specify a small number of ranges and permissions

## Slide 22: Peripherals
Hardware modules the perform some action
Common examples
  Control digital input and output pins
  Read analog inputs
  Send messages in a given wire protocol (UART, SPI, I2C)
  Set and check timers
Less common examples
  Cryptography accelerators
  Complicated wire protocols (USB, CAN)
  Wireless radios (BLE, 802.15.4, WiFi)
We’ll spend most of class learning various peripherals

## Slide 23: Peripheral design choices
More peripherals mean more use cases
  But also means more cost for the chip
  Peripherals occupy silicon
  Most peripherals will go unused for a given application…
Flexibility within a given peripheral
  One capability is easier to use
  Many capabilities are more useful
Apple A8 SoC

## Slide 24: Pins
Peripherals need to electrically connect to outside world
  Attach to pins on the exterior of the chip
More pins allow for more connections
  At increased cost and size
Pin layouts can add more pins for cheaper
  But make soldering and debugging difficult

## Slide 25: Internal connections to pins
Peripherals need to connect to external pins
  Can any peripheral connect to any pin, or are there limited mappings?
  Modern microcontrollers allow any-to-any connections
Older MCUs had mapping tables and pin selection was more challenging

## Slide 26: What haven’t we talked about?
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 27: What haven’t we talked about?
Power
Programming
Others?
  Clocks
  Antennas
Microcontroller
Processor
Memory
Peripherals
Pins

## Slide 28: Powering microcontrollers
Usually require a specific voltage
  E.g. 5 volts, 3.3 volts, 1.8 volts
  Must be stable and supply enough current (or MCU “browns out”)
  Noisy power supply can be an issue
Some microcontrollers have wider ranges of acceptable voltages
  Need to pay attention to acceptable range on I/O though

## Slide 29: Programming microcontrollers
JTAG (Joint Test Action Group)
  Hardware built into the microcontroller for testing purposes
  Can arbitrarily read/write memory
  Can single step process too, at runtime!
    GDB can connect to it! (sort of)
Bootloaders
  Software runs on the microcontroller at boot that waits a short time for someone to contact it and upload code
    Via I/O pins
  Convenient, but sometimes unreliable

## Slide 30: Outline
Microcontroller Background
Microcontroller Design
Microcontroller History
Microbit microcontroller

## Slide 31: Older microcontrollers (90s-00s)
Focus: cheap, small computer systems
PIC
  8, 16, and 24-bit MIPs architecture
  PICAXE available with Basic interpreter
AVR
  8-bit custom architecture (AVR architecture)
  Used in Arduinos
  AT Tiny 4: $0.30 per unit
    4 I/O pins, 32 Bytes RAM, 512 Bytes ROM

## Slide 32: More capable microcontrollers (00s-10s)
Focus: diversify into extreme low power and more capable systems
MSP430
  16-bit custom architecture (MSP430 architecture)
  Capable, but also extremely low power
    <1 μA sleep current
STM32, Atmel SAM series (Cortex-M0, M3, M4, M4F)
  32-bit ARM architecture (ARMv7)
    Leverage success of ARM on smartphones
  Every peripheral under the sun. Plus a variety of memory choices

## Slide 33: Cortex M Series
A number of options for increasing capabilities
In practice:
  Cortex-M0+ for low-end systems
  Coretx-M4 for high capability systems

## Slide 34: Modern system-on-chips (10s-?)
Focus: increase memory and capability
  Include radios in the same chip
nRF51 and nRF52 series
  32-bit ARM microcontrollers (Cortex M)
  Include 2.4 GHz radio: Bluetooth Low Energy and 802.15.4/Thread
Others have followed this same path
  TI CC26XX
  Apollo3
  STM32WL

## Slide 35: Future microcontrollers
Multi-core systems
  Not for performance, but for separation of concerns
    Run radio code on one core
    Application code goes on the other core
  Also allows BIG.little architecture
    Higher performance core when interpreting data
    Lower performance core for sampling sensors
  nRF53 series is already doing this
    But support is still nascent

## Slide 36: Popular components rarely die
Majority of popular older options still exist
  Designers can trade off cost, capability, and efficiency alongside “modern features”
Upgrading for an existing product is unlikely
  Large cost, little benefit
Example: Arduino still primarily uses AVR
  Works just fine for its needs
  Also releases new boards with nRF52s (Arduino Nano 33 BLE)

## Slide 37: Outline
Microcontroller Background
Microcontroller Design
Microcontroller History
Microbit microcontroller

## Slide 38: Micro:bit v2
Circuit board
  Entire thing
  a.k.a “Dev Board”
  a.k.a PCB (Printed Circuit Board)
Microcontroller
  The computer on it
  Microbit has two
    One as a programmer
    One for applications
Microcontrollers

## Slide 39: KL27Z – Programmer on the Micro:bit v2
32-bit ARM Cortex-M0+ microcontroller
  48 MHz core, 16 KB RAM, 256 KB Flash
Acts as a programming interface to nRF52833
  Connects to USB and to JTAG (SWD)

## Slide 40: nRF52833 – Microcontroller on the Micro:bit v2
32-bit ARM Cortex-M4F microcontroller
  64 MHz core, 128 KB RAM, 512 KB Flash
  Floating point support
  2.4 GHz Radio: Bluetooth Low energy / 802.15.4
  Various peripherals
    ADC, PWM
    I2C, UART, SPI, USB
    RNG, 32-bit Timers, Watchdog, Temperature
    Up to 42 I/O pins

## Slide 41: To the datasheet!
nRF52833 Product Specification
  Online: https://infocenter.nordicsemi.com/index.jsp?topic=%2Fps_nrf52833%2Fkeyfeatures_html5.html
  PDF: https://infocenter.nordicsemi.com/pdf/nRF52833_PS_v1.3.pdf

## Slide 42: Outline
Microcontroller Background
Microcontroller Design
Microcontroller History
Microbit microcontroller(s)