## Slide 1: Lecture 04 Input and Output
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Today’s Goals
How does a microcontroller interact with peripherals to perform input and output operations?
  Memory-Mapped I/O
  Interrupts
  DMA
Explore reliable use of MMIO
Discuss interaction patterns for Interrupts and DMA

## Slide 3: Outline
I/O Motivation
Memory-Mapped I/O
Interrupts
DMA

## Slide 4: Devices are the point of computers
Traditional systems need to receive input from users and output responses
  Keyboard/mouse
  Disk
  Network
  Graphics
  Audio
  Various USB devices
Embedded systems have the same requirement, just more types of IO
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 5: Devices are core to useful general-purpose computing
Computer
Mouse
Keyboard
Ethernet
Bluetooth
Monitor
Headphones
Ethernet
Bluetooth
Input
Output

## Slide 6: Devices are essential to cyber-physical systems too
Computer
Lidar
Inertial Measurement Unit
Camera
CAN
Throttle Control
Brake Control
Wheel Rotation
CAN
Input
Output

## Slide 7: Device access rates vary by many orders of magnitude
Rates in bit/sec
System must be able to handle each of these
  Sometimes needs low overhead
  Sometimes needs to not wait around
Device | Behavior | Partner | Data Rate (Kb/s)
Keyboard | Input | Human | 0.2
Mouse | Input | Human | 0.4
Microphone | Output | Human | 700.0
Bluetooth | Input or Output | Machine | 20,000.0
Hard disk drive | Storage | Machine | 100,000.0
Wireless network | Input or Output | Machine | 300,000.0
Solid state drive | Storage | Machine | 500,000.0
Wired LAN network | Input or Output | Machine | 1,000,000.0
Graphics display | Output | Human | 3,000,000.0

## Slide 8: Outline
I/O Motivation
Memory-Mapped I/O
Interrupts
DMA

## Slide 9: How does a computer talk with peripherals?
A peripheral is a hardware unit within a microcontroller
  Sort of a “computer-within-the-computer”
  Performs some kind of action given input, generates output
We interact with a peripheral’s interface
  Called registers (actually are from EE perspective, but you can’t use them)
  Read/Write like they’re data
How do we read/write them?
  Options:
    Special assembly instructions
    Treat like normal memory

## Slide 10: Memory-mapped I/O (MMIO): treat devices like normal memory
Certain physical addresses do not actually go to memory
Instead they correspond to peripherals
  And any instruction that accesses memory can access them too!
Every microcontroller I’ve ever seen uses MMIO
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 11: Memory map on nRF52833
Flash 0x00000000
SRAM 0x20000000
APB peripherals 0x40000000
  Everything but GPIO
AHB peripherals 0x50000000
  Just GPIO
UICR – User Information Config
FICR – Factory Information Config

## Slide 12: Example nRF52 peripheral placement
0x1000 is plenty of space for each peripheral
  1024 registers, each 32 bits
  No reason to pack them tighter than that

## Slide 13: TEMP on nRF52833 example
Internal temperature sensor
  0.25° C resolution
  Range equivalent to microcontroller IC (-40° to 105° C)
  Various configurations for the temperature conversion (ignoring)

## Slide 14: MMIO addresses for TEMP
What addresses do we need? (ignore interrupts for now)
  0x4000C000 – TASKS_START
  0x4000C100 – EVENTS_DATARDY
  0x4000C508 - TEMP

## Slide 15: Example code
To the terminal!

## Slide 16: Example code

## Slide 17: Using structs to manage MMIO access
Writing simple C code and access peripherals is great!
Problems:
  Need to remember all these long addresses
  Need to make sure compiler doesn’t stop us!
Solution:
  Wrap entire access in a struct!
  Compilers turn it into the same thing in the end anyways

## Slide 18: C structs
Collection of variables placed together in memory
  typedef struct {
  uint32_t variable_one;
  uint32_t variable_two;
  uint32_t array[2];
  } example_struct_t;
Placement rules - Variables are placed adjacent to each other in memory except:
  Variables are always placed at a multiple of their size
  Padding added to the end to make the total size a multiple of the biggest member
  Microcontrollers can usually ignore these: all registers are the same size!

## Slide 19: Temperature peripheral MMIO struct
  typedef struct {
  } temp_regs_t;

## Slide 20: Temperature peripheral MMIO struct
  typedef struct {
  uint32_t TASKS_START;
  uint32_t TASKS_STOP;
  uint32_t _unused_A[62];
  uint32_t EVENTS_DATARDY;
  uint32_t _unused_B[64+64+1];
  uint32_t INTENSET;
  uint32_t INTENCLR;
  uint32_t _unused_C[64+64];
  uint32_t TEMP;
  } temp_regs_t;
  volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);

## Slide 21: Temperature peripheral MMIO struct
  typedef struct {
  uint32_t TASKS_START;
  uint32_t TASKS_STOP;
  uint32_t _unused_A[62];
  uint32_t EVENTS_DATARDY;
  uint32_t _unused_B[64+64+1];
  uint32_t INTENSET;
  uint32_t INTENCLR;
  uint32_t _unused_C[64+64];
  uint32_t TEMP;
  } temp_regs_t;
  volatile temp_regs_t* TEMP_REGS = (temp_regs_t*)(0x4000C000);
  // code to access
  TEMP_REGS->TASKS_START = 1;
  while (TEMP_REGS->EVENTS_DATARDY == 0);
  float temperature = ((float)TEMP_REGS->TEMP)/4.0;

## Slide 22: Outline
I/O Motivation
Memory-Mapped I/O
Interrupts
DMA

## Slide 23: What do interactions with devices look like?
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
This is the “polling” model of I/O.
“Poll” the peripheral in software repeatedly to see if it’s ready yet.

## Slide 24: Waiting can be a waste of CPU time
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
Imagine a keyboard device
  CPU could be waiting for minutes before data arrives
  Need a way to notify CPU when an event occurs
    Interrupts!

## Slide 25: Interrupts
What is an interrupt?
  Some event which causes the processor to stop normal execution
  The processor instead jumps to a handler for that event
What causes interrupts?
  Hardware exceptions
    Divide by zero, Undefined Instruction, Memory bus error
  Software
    Syscall, Software Interrupt (SWI)
  External hardware
    Input pin, Timer, various “Data Ready”

## Slide 26: Interrupts, visually
Some code that’s executing

## Slide 27: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code

## Slide 28: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code
Continue original code

## Slide 29: ARM Nested Vectored Interrupt Controller (NVIC)
Manages interrupt requests (IRQ)
  Stores all callee saved registers on the stack
    So the handler code doesn’t overwrite them
  Moves the PC to the proper handler, a.k.a. Interrupt Service Routine (ISR)
  Restores registers after handler returns and moves PC back
Interrupts can preempt other interrupts!
Jump directly to the interrupt handler
Handles interrupt entry and exit
Stacking
Unstacking
Priorities

## Slide 30: ARM Vector table
List of function pointers to handler for each interrupt/exception
First 15 are architecture-specific exceptions
After that are microcontroller interrupt signals

## Slide 31: Vector table in software
Placed in its own section
  LD file puts it first in Flash
Reset_Handler determines where software starts executing
After that are all exception and interrupt handlers
  All function pointers to some C code somewhere

## Slide 32: NVIC functionality
NVIC functions
  NVIC_EnableIRQ(number)
  NVIC_DisableIRQ(number)
  NVIC_SetPriority(number, priority)
    Technically 256 priorities
    Only 8 are implemented
Must enable interrupts in two places!
  Enabling interrupt in the peripheral will generate the signal
  Enabling interrupt in the NVIC will cause signal to jump to handler
Priority determines which interrupt goes first
  And determines how interrupts are nested

## Slide 33: Nested interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler
Continue original code
Higher priority Interrupt triggers!
continues
Interrupt handler

## Slide 34: Outline
I/O Motivation
Memory-Mapped I/O
Interrupts
DMA

## Slide 35: Direct Memory Access (DMA)
Even with interrupts, providing data to the peripheral is time consuming
  Need to be interrupted every byte, to copy the next byte over
DMA is an alternative method that uses hardware to do the memory transfers for the processor
  Software writes address of the data and the size to the peripheral
  Peripheral reads data directly from memory
  Processor can go do other things while read/write is occurring

## Slide 36: General-purpose DMA

## Slide 37: Special-purpose DMA
nRF52 uses “EasyDMA”, which is built into individual peripherals
  Only capable of transferring data in/out of that peripheral
  Easier to set up and use in practice
  Only available on some peripherals though (no DMA for TEMP)
Warning: addresses for DMA MUST be in RAM!

## Slide 38: Full peripheral interaction pattern
Configure the peripheral
Enable peripheral interrupts
Set up peripheral DMA transfer
Start peripheral
Continue on to other code
Interrupt occurs, signaling DMA transfer complete
Set up next DMA transfer
Continue on to other code, and repeat

## Slide 39: Outline
I/O Motivation
Memory-Mapped I/O
Interrupts
DMA