## Slide 1: Lecture 05 Digital Circuits
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Today’s Goals
Understand the basics of digital circuitry
  Enough to be able to interact with the Microbit
Explore how the Microbit controls digital inputs and outputs

## Slide 3: Outline
Digital circuits
Controlling digital signals
  GPIO
  GPIOTE

## Slide 4: Digital signals
Exist in two states:
  High (a.k.a. Set, a.k.a. 1)
  Low (a.k.a. Clear, a.k.a. 0)
Simpler to interact with
  Constrained to two voltages
  With quick transitions between the two
  No math for voltage level
    Either high or low

## Slide 5: Digital signals map to voltage ranges
Upper range is high signal
  ~0.7*VDD
Bottom range is low signal
  ~0.3*VDD
Middle is undefined
  Only exists during transitions
http://www.sharetechnote.com/html/Electronics_CMOS.html

## Slide 6: Digital circuits
Connecting components together with digital signals
  Mostly ICs
  Also buttons/switches and LEDs
Way simpler than analog circuits
  Mostly connecting boxes with wires
  Plus a few resistors here and there
An abstraction
  Not sufficient for fully understanding electronics behavior, but close

## Slide 7: Switches
Single Pole, Double Throw switch
  Middle pin (Pole) connects to one of two outer pins (Throws)
For controlling microcontrollers
  Often connect outer pins to VCC and Ground respectively
  Input then goes High or Low depending on switch state
https://learn.sparkfun.com/tutorials/button-and-switch-basics/

## Slide 8: Buttons
Single Pole, Single Throw switch
  Pole pin either connects to Throw pin or is disconnected
  Come in normally-closed (connected) and normally-open (disconnected)

## Slide 9: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?

## Slide 10: Disconnected circuits
When button is pushed, input signal is low
What is the value of the input when the button is unpressed?
  Floating! Could be any voltage
  Solution: connect weakly to either high or low voltage

## Slide 11: Current flows through the “path of least resistance”
Simplification
  Works well for the types of circuits we use
Pull-up resistor
  When button is open (disconnected), the only path is through the resistor
  When button is closed (connected) the least resistance path is through the button to Ground

## Slide 12: Pull-up resistors and pull-down resistors
Resistor sets the “default” value of a wire
  Pull-up connects to VCC
  Pull-down connects to Ground
  Usually 10-100 kΩ
When button is open (disconnected)
  Connection through the resistor sets signal
When button is closed (connected)
  Signal is directly connected to a voltage source
  Much lower resistance means that signal dominates

## Slide 13: Buttons on the Microbit
Normally open buttons
  Disconnected by default
Active low signal
  Activating (pushing) button creates a low signal
Pull-up resistors
  Set button signal high by default

## Slide 14: LEDs
Light Emitting Diodes
  Generate light as current passes through them
  Various colors available
Diodes
  Only allow current to go through one way
  Not particularly relevant for LEDs
    Treat as a digital component
Connect anode to high voltage and cathode to ground
  Plus a resistor to limit the total amount of current
https://learn.sparkfun.com/tutorials/light-emitting-diodes-leds

## Slide 15: Active state for LEDs
LEDs can be active high or active low depending on configuration
  Active high is how people assume they work
  Active low is often used instead
    GPIO pins can usually sink more current than they can source

## Slide 16: LEDs on the Microbit
Microphone LED
  Active high
Simple to use
Ignore this other part for now

## Slide 17: LEDs on the Microbit
Use two GPIO pins to control each LED
  Row high as VDD
  Column low as Ground
Remember, connections only exist where there are dots

## Slide 18: Controlling the LED matrix
Cannot individually control all LEDs simultaneously
  Need to light one row at a time
  Iterate rows quickly to make them appear on all the time
We’ll have a lab on these later
  Combine GPIO and timers

## Slide 19: Outline
Digital circuits
Controlling digital signals
  GPIO
  GPIOTE

## Slide 20: General Purpose Input/Output (GPIO)
Read/write from/to external pins on the microcontroller
  Two possible values: high (1) or low (0)
Basic unit of operation for microcontrollers
  Allows them to interact with buttons and LEDs
  Every microcontroller has GPIO

## Slide 21: GPIO on nRF52833

## Slide 22: GPIO on nRF52833
Abstract model of the pin.
This isn’t really how the hardware is implemented. But it’s a reasonable model for users.

## Slide 23: GPIO on nRF52833
Inputs and outputs to/from the peripheral.
GPIO could be controlled by other peripherals. Controlling a pin in use by other peripherals is bad.

## Slide 24: GPIO on nRF52833
Registers within the GPIO peripheral. Configure various things about setup.

## Slide 25: GPIO on nRF52833
Peripheral contents are duplicated for each output pin.
Each pin has its own registers (or portions thereof).

## Slide 26: Multiple ports
nRF52833 has up to 42 I/O pins
  But only 32 can fit in a single word
  Splits them into two “ports”
Pins are named based on port
  P0.14 – Button A, P0.23 – Button B
  P1.04 – LED column 4

## Slide 27: GPIO on nRF52833
External pin on the microcontroller

## Slide 28: GPIO on nRF52833
Output chain. Signal comes from OUT register, through output buffer, to external pin.

## Slide 29: GPIO Output
Outputs a high or low signal
Output configurations
  High drive output (either for high, low, or both)
    Sources or sinks additional current
      For powering external devices
    Normal drive: ~2 mA
    High drive: ~10 mA
  Disconnect (a.k.a. High Impedance or High-Z)
    Wired-OR or Wired-AND scenarios

## Slide 30: GPIO on nRF52833
Input chain. Signal goes from pin, through input buffer, to IN register.

## Slide 31: GPIO Input
Reads in a signal as either high or low
Input Configurations
  Input buffer connect/disconnect
    Allows the pin to be disabled if not being read from
  Pull
    Disabled, Pulldown, Pullup
    Connects an internal pull up/down resistor (~13 kΩ)
    Sets default value of input

## Slide 32: Electrical specifications
High voltage range: 0.7*VDD to VDD (~2.3 volts)
Low voltage range: Ground to 0.3*VDD (~1 volt)
GPIO are extremely fast
  Transition time is <25 ns
  Connected directly to memory bus for faster interactions
  This allows complicated signal patterns to be replicated in software
    If they aren’t implemented as a hardware peripheral
    Known as bit-banging

## Slide 33: Set/Clear registers
OUT works traditionally: write a 1 for high, 0 for low
OUTSET write a 1 to set that pin (high) zero has no effect
OUTCLR write a 1 to clear that pin (low) zero has no effect
  Lets you modify a pin without modifying the others (or reading first)

## Slide 34: Outline
Digital circuits
Controlling digital signals
  GPIO
  GPIOTE

## Slide 35: Handling interrupts from GPIO
Separate peripheral, GPIOTE (GPIO Task/Event)
  Manages up to 8 individual pins
    Can read inputs and trigger interrupts
    Can also connect outputs from events on other peripherals (PPI)
  Can trigger interrupts for a “Port event” as well
    Software checks which pin(s) caused the event to occur
    Very low power operation (works with system clocks off)
Unclear why this is a separate peripheral
  Presumably too complicated/expensive to have 42 of them

## Slide 36: Configuring individual input interrupts
Pick an available GPIOTE channel (0-7)
Configure it
  Port and Pin number
  Task (output), Event (input), or Disabled
  Polarity for input events
    Low-to-high
    High-to-low
    Toggle (both directions)
Enable interrupts for channel in GPIOTE (and in NVIC!)
Clear event in interrupt handler
  Doesn’t happen automatically

## Slide 37: Sensing port events
Uses the “Detect” signal. Generated from pin Sense configuration

## Slide 38: Configuring port input interrupts
Configure the Sense for each pin
  High or Low
  Allows different pins to have different “active” states
Select detect mode
  Direct connection to pins
  Latched version (saved even if pin later changes back)
Enable interrupts for port in GPIOTE (and in NVIC!)
Clear event in interrupt handler and value in Latch register
  Doesn’t happen automatically

## Slide 39: Outline
Digital circuits
Controlling digital signals
  GPIO
  GPIOTE

## Slide 40: Outline
Bonus: thoughts on energy use

## Slide 41: Ohm’s Law
  V = I x R
Volts = Current times Resistance
  P = I x V
Power = Current times Voltage
These two equations govern most of the circuit math we’ll need in this course
  Work with resistive circuits

## Slide 42: Thinking about energy
Batteries often list energy in mA*h (milliamp – hours)
  Coin cell battery: 3v at 220 mAh
  2x AA battery: 3v at 2000 mAh
  iPhone 11 battery: 3.7v at 3000 mAh
nRF52833 active current: 5.6 mA (at 3v)
  Coin cell: 40 hours -> ~2 days
  2x AA: 360 hours -> ~15 days
  iPhone 11: 535 hours -> ~22 days
So how does any of this work???

## Slide 43: Microcontroller sleep modes
Sleep mode
  Processor stops running
  Most peripherals are disabled
  Continues until an interrupt occurs and wakes the microcontroller
    Usually a timer or GPIO input
nRF52833 sleep mode current: 1.8 μA (GPIO port event only)
  Coin cell: 122222 hours -> ~5000 days -> ~14 years
Low-power systems shoot for less than 1% duty cycle
  Average current of ~100 μA or less
  Warning: other stuff on the board counts!!
    LEDs are 1-10 mA each… Power is not a concern of the Microbit