## Slide 1: Lecture 06 Timers
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Today’s Goals
Understand the role of clocks in a microcontroller
Explore functionality of various timer peripherals on the Microbit

## Slide 3: Outline
Clocks
Timers
Real-Time Counter
Watchdog

## Slide 4: What are clocks?
Clock signals, in the microcontroller context, are oscillating square wave signals used to latch inputs
A clock MUST be running for (almost) anything on a microcontroller to function (processor and peripherals)
  Exceptions:
    Low-power input interrupts
      GPIOTE port interrupt, Analog LPCOMP interrupt, NFC sense interrupt, USB power interrupt
    Reset signal

## Slide 5: Generating clocks
External crystal oscillator
  Creates clock signal
  Chunk of quartz
  Behaves like RLC circuit but uses less energy
Internal mechanisms
  RC oscillator
    Creates clock signal
    Less accurate and higher energy than crystal
  Phase-Locked Loop (PLL)
    Multiply input to create new higher frequency clocks

## Slide 6: Microbit crystal for nRF52833

## Slide 7: Clocks and energy
Fundamental tradeoff
  Faster clock gets things done faster but uses more energy
  Slower clock uses less energy but gets things done slower
  Which to use depends on the situation
    CPU bound: faster clock, IO bound: slower clock
Chiang et al. “Power Clocks: Dynamic Multi-Clock Management for Embedded Systems” EWSN 2021
Example of clock selection for a mixed load (part IO, part CPU)
Energy consumed becomes a horizontal line when the task is completed

## Slide 8: Controlling clocks
Some microcontrollers provide extremely fine-grained control over clocks
  Really complicated section of code to get working
  Many combinations are invalid
  Manually enable/disable clocks as needed
nRF52 instead gives almost no control but is easier to use
  One 64-MHz clock for processor
  Multiple peripheral clocks, but (most) peripherals are hardwired to one
    16 MHz for almost all peripherals (PDM and I2S are 32 MHz)
  Low-frequency 32 kHz clock for low-power peripherals
  Automatically enables/disables clocks

## Slide 9: nRF52833 clocks
Optional: for lower energy and higher accuracy

## Slide 10: Electrical characteristics
Active power of clocks
  32 kHz crystal run current: 0.23 μA
  32 kHz RC oscillator run current: 0.70 μA
  32 MHz crystal average run current: 300-700.00 μA
  32 MHz standby current: 110.00 μA
Startup time for external crystals
  32 kHz crystal: 250-500 ms (milliseconds!!!)
  32 MHz crystal: 60-200 μs
  Beware: switching can lead to delays and instability
    nRF52 uses RC oscillator while crystal is not yet ready

## Slide 11: Outline
Clocks
Timers
Real-Time Counter
Watchdog

## Slide 12: Timer peripherals
Common need for embedded systems: sense of time
  Start this behavior after a certain amount of time
  Stop this behavior after a certain amount of time
  Measure how much time passed between two events
Timer peripherals
  Input is one of the system clocks
  Counts up a register at each clock tick
    Looking at register at start and end can give real-world duration
  Compare to saved value and trigger interrupt on match
    Allows interrupts to be scheduled in the future

## Slide 13: Timer peripheral on nRF52833

## Slide 14: Input and Prescaler
𝑓TIMER =
Prescaler is a 4-bit number
  Possible timer input clocks: 16 MHz – 488 Hz
Ticks counted with (up to) 32-bit internal Counter:
  Minimum 268 seconds until overflow (at 62.5 ns per tick)
  Maximum 101 days until overflow (at 2.04 ms per tick)

## Slide 15: Alternate input source for counter mode
Counter mode works with non-timer inputs
  E.g. GPIO input event
Count anything!

## Slide 16: Capture/Compare registers (CC)
32-bit storage registers (each timer has multiple)
  Uses: capturing or comparing
On Capture[n] event
  Internal Counter value copied to CC[n]
Capture used to measure durations of events
  Capture can be triggered by software or by Events from other peripherals
  Multiple registers to measure multi-part events

## Slide 17: Comparing with CC registers
When internal Counter value equals a CC register
  Corresponding Compare[n] event is triggered
  Can trigger interrupts
Usually written to in advance to start/stop behavior
  Toggle LED every second
  Sample sensor every five minutes
  Refresh LED matrix every 1/60 seconds

## Slide 18: The nRF52833 has multiple Timer instances

## Slide 19: Bonus concept: shorts
Reminder: Tasks are inputs and Events are outputs
Shorts connect an Event to a Task within a peripheral
  Tasks and Events are fairly nRF specific
Timer shorts
  Connect Compare[n] to Clear
  Connect Compare[n] to Stop

## Slide 20: Usage: how do we set a one second timer?
Assume timer is already running
Get current time from timer
Add 1 second worth of ticks to it
  is the number of ticks per second
Set an unused Compare register to value
Enable interrupts for that Compare event
Warning: what if you’re setting a 1 us timer instead? Or a 100 ns timer?
Timer could expire before software writes it to the peripheral.

## Slide 21: Check your understanding
Prescaler value is 4
Current internal Counter value is 0x1000
Want a 0.5 second timer
What do you set the CC[0] register to? (32-bits)
𝑓TIMER =

## Slide 22: Check your understanding
Prescaler value is 4
Current internal Counter value is 0x1000
Want a 0.5 second timer
What do you set the CC[0] register to? (32-bits)
  1 MHz Timer frequency -> 500,000 ticks in 0.5 seconds
  500000 -> 0x7A120
  Plus initial value of counter = 0x7B120
𝑓TIMER =

## Slide 23: Outline
Clocks
Timers
Real-Time Counter
Watchdog

## Slide 24: Real-time Counter
Low-power (32 kHz) version of Timer
  Only a 24-bit internal Counter
Note: abbreviated RTC, but that already means something else (Real-Time Clock)

## Slide 25: Differences between Real-Time Counter and Timer
Runs off of LFCLK instead of HFCLK
  With smaller prescaler value (4096 vs 32768)
24-bit counter vs 32-bit counter for Timer
Can read the Counter value directly
  No need for Capture task
Otherwise extremely similar. Just a low-power version of Timer

## Slide 26: Time resolution for Real-Time Counter
𝑓TIMER =
Resolution
  Minimum: 30.517 μs, overflows in 512 seconds (24-bit Counter)
  Maximum: 125 ms, overflows in 582 hours
Not as precise as the Timer (62.5 ns best precision)
  Possible design: use both
    Real-Time Counter for most of the waiting
    Chained into Timer for precise remaining amount of time

## Slide 27: Outline
Clocks
Timers
Real-Time Counter
Watchdog

## Slide 28: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
  Why?

## Slide 29: Reliable systems
What’s the most common way to solve computer problems?
  Turn it off and turn it on again.
  Why?
  Resets “state” to original values, which are likely good
    Startup is often well-tested
    It’s long-running code interacting in unexpected ways that leaves systems in a broken state

## Slide 30: Watchdog timer (WDT)
Focused on failures where the system “hangs” forever
  Maybe software, maybe hardware!
Can’t know for certain the system is hung, but can know practically
  Select a timeout that is the maximum amount of time you expect the system to ever go without looping in main()
  Multiply it by 2-10
  Set a watchdog timer to that value
If watchdog timer ever expires, it resets the system (in hardware)

## Slide 31: Watchdog configuration
timeout (seconds) =
Configure watchdog
  Can choose whether to count down during Sleep mode or Debug mode
Set a Counter Reload Value (CRV, 32-bits)
Start the watchdog timer
  Loads internal Counter to CRV value
  Starts counting down at 32 kHz

## Slide 32: Running applications with a watchdog timer
Need to periodically reset the watchdog to keep it from expiring
  Known as “feeding” the watchdog or “kicking” the watchdog
Reload Request register
  Must write sequence 0x6E524635 to reload watchdog
  Incredibly unlikely to happen by accident
While running, watchdog is protected from modification
  Configure once, run forever (at least until a reboot)
  Only option is to make periodic Reload Requests
Default off on the nRF52833 (default on for the MSP430!)

## Slide 33: Outline
Clocks
Timers
Real-Time Counter
Watchdog