## Slide 1: Lecture 10 Prototyping
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley), Project Lead The Way

## Slide 2: Administrivia
Quiz 2 due tonight
Reminder on my office hours today:
  After class 11-12
  Normal office hours 1-2

## Slide 3: Today’s Goals
Discuss issues to consider when prototyping systems
Understand how to use breadboards for prototyping
Explore various components and how you might use them with a breadboard

## Slide 4: Outline
Overview of Prototyping
Breadboarding Components

## Slide 5: Prototyping goals
Does this thing work at all?
  Particular IC
  Circuit layout
  Software design
  etc.
Sometimes before doing something more serious with it
  Design a PCB, Make a product, etc.
  Not uncommon that the prototype is as far as you’ll get

## Slide 6: Isolating tests
The goal when prototyping is to isolate the question at hand
Do consider
  New sensor/IC/component/whatever
Do not consider
  Power
  Interference
  Enclosure
  Stable microcontroller
  Soldering skills

## Slide 7: Buying Parts
Prototyping vendors
  Where you look for cool stuff to buy
  Sparkfun
  Adafruit
Electronics vendors
  Where you buy parts when you know what you need
  Digikey
  Mouser

## Slide 8: Prototyping methods
Breadboarding
  Plug and connect components as needed
  Build up arbitrarily complex designs from nothing
Development kits
  Pre-fabricated systems design for testing components
Small-scale test PCBs
  Design a PCB that demonstrates the thing you’re interested in
    Making a PCB is less hard than some might think (Eagle, Fritzing, etc.)
    $20-30 for small, low-speed PCBs from batch services like OSHPark

## Slide 9: Breadboards for prototyping
Reusable platform for temporary circuits
Plug in jumper wires and through-hold components

## Slide 10: How a breadboard works
Component leads and wires are inserted into holes in the breadboard
Half-rows of five holes are connected
Vertical columns are connected for power/ground
Holes to
insert wires

## Slide 11: Breadboard LED example
Uses button to control LED

## Slide 12: Breadboard guidelines
Long wires in large bird nests makes debugging very difficult
  Shorter, constrained wires are easier to understand
  In this class, we’ll only have large jumper wires though…
Use the minimum jumpers necessary, mostly use breadboard for connections
Better
Bad

## Slide 13: More permanent breadboards
Breadboards are also known as “Solderless Breadboards”
Protoboard allows configurable circuits
  Solder jumper wires between locations
  Solder adjacent pads to form connection
Usually not worth it (just make a PCB)
  Does solve core problem of breadboards: things getting unintentionally unplugged

## Slide 14: When to not use breadboards
Breadboards work great for digital circuits and simple analog!
High voltage/current are bad for breadboards
  Honestly, anything above 12 volts DC shouldn’t be in a breadboard
  Also avoid high-power applications above a few Watts
  Never put AC in a breadboard
Sensitive analog circuits
  Particularly anything sensitive to capacitance may not work right
  Sets of metal holes with strips connecting them function as capacitors
Anything in long term use

## Slide 15: Outline
Overview of Prototyping
Breadboarding Components

## Slide 16: Prototyping with a breadboard
What kinds of things might you use with a breadboard?
Jumper wire
Microbit!
Resistors/Capacitors
LEDs
Buttons/Switches
Analog Sensors
Various other through-hole components
  Transistors, Op-Amps, other ICs
https://www.adafruit.com/product/2975

## Slide 17: Jumper wires
Connect two rows in the breadboard together
Recommendation:
  Peel off sets of 2-4 wires and keep them stuck together
  Often want to run multiple at once

## Slide 18: Microbit
Always connect LED matrix side up
Breaks out various pins from board
  Need to consult table to know which pins
  https://tech.microbit.org/hardware/schematic/
https://www.sparkfun.com/products/13989
https://learn.sparkfun.com/tutorials/microbit-breakout-board-hookup-guide

## Slide 19: Resistors
Surface Mount Resistors
Variable Resistors
(potentiometer)
Carbon Film Resistors
4 Bands

## Slide 20: Resistor color codes
Colored bands on resistors label the resistance value of the part
First and second bands are the digits
Third band is multiplier
Fourth band is tolerance
  Usually gold: +/- 5%

## Slide 21: Example: determine the resistor

## Slide 22: Example: determine the resistor
56 x 10 Ω = 560 Ω (5%)

## Slide 23: Potentiometers
Vary resistance between zero and some maximum
  1 kΩ, 10 kΩ, 100 kΩ common
Connect middle and an edge for just a changeable resistor
Middle terminal is a movable resistor divider
  Knob changes middle output if outer pins are VCC and Ground

## Slide 24: LEDs
Directional component: only allows current to flow one way
Shorter side is the negative one
  i.e. where current flows to
Larger metal component
inside of case or case flat spot is cathode or
negative (-) lead
Shorter wire is cathode or
negative (-) lead
Negative ( - ) lead
Schematic Symbol

## Slide 25: RGB LED
Three different colors of LED in a single large diffuser
Short leads are negative ends
  One for each color
Long lead is common power
  Common anode
Combinations of LEDs give other colors
  Cyan, Yellow, Violet, White
https://cdn-shop.adafruit.com/datasheets/FLR-100WAS-RGB.pdf

## Slide 26: Sensors
Thermistor
Photoresistor

## Slide 27
Breadboard demo!

## Slide 28
Breadboard demo!
RGB LED
  Plus resistors
Control LED with
  Switch
  Potentiometer
  Photoresistor

## Slide 29: Outline
Overview of Prototyping
Breadboarding Components