## Slide 1: Lecture 14 USB
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Today’s Goals
Discuss more advanced wired communication protocols
  With a little less detail
Think about higher-layer concerns like data routing, interpretation, and reliability

## Slide 3: Outline
I2C (wrapup)
USB
CAN

## Slide 4: I2C overview
SDA – Serial Data
SCL – Serial Clock
  Usually 100 kHz or 400 kHz
Communication is a shared bus between all controller(s) and peripheral(s)
Pull-up resistors for open-drain communication

## Slide 5: I2C transactions
Start and Stop Conditions: change SDA while SCL is low
Address + R/W bit, then data byte(s)
Common pattern:
  Write to device to choose an internal data (known as registers)
  Repeated-start, followed by read to get data value

## Slide 6: Real-world I2C transactions

## Slide 7: Sparkfun Qwiic connect system
System for wiring multiple prototyping boards together
Four-pin connector
  VCC (3.3 volts)
  Ground
  SDA
  SCL
Daisy-chains through boards
  Actually connects to chips in parallel as a bus
https://www.sparkfun.com/qwiic

## Slide 8: I2C use cases
Various sensors
  Usually low to medium speed
  Even relatively high speed stuff often has I2C for convenience
    Accelerometers and microphones
    Often with intelligent filtering built in
Communication between microcontrollers
  Either can act as the Controller when necessary
Commonly exists internally within smartphones and laptops too
  Light sensors, Temperature sensors, etc.

## Slide 9: System Management Bus (SMBus)
Related communication specification
  A little more strict in places, but generally interoperable
Adds ability to broadcast or unicast messages
  Generic addresses for Controller and various peripherals (Battery)
Adds an open-drain shared interrupt signal
  High-impedance or pull low, just like SDA and SCL
  Allows any device to alert a controller
    Controller has to probe bus to determine which device wants attention

## Slide 10: nRF TWI peripherals
TWIM – for I2C Controller
  This is the common case
  Provide buffer to write from and/or read into for DMA
  Configure registers, perform interaction, repeat
TWIS – for I2C peripheral
  Less common for microcontroller to be a peripheral
  Supports dual-mode where you are switching between states
  Provide up to two addresses that will be matched against
  When interrupted with write data
    Change buffer connected to read DMA (as appropriate)
    Possibly stretching clock to make it all work

## Slide 11: I2C Pros and Cons
Pros
  Wiring is simple
  Only uses two pins
  Very widely supported
Cons
  Relatively slow communication rate
  Speed versus power use tradeoff (due to pull-down resistor)
  Open collector makes debugging difficult

## Slide 12: Outline
I2C
USB
CAN

## Slide 13: USB references
USB in a NutShell
  https://www.beyondlogic.org/usbnutshell
Other stuff I found useful
  https://www.usbmadesimple.co.uk/
  http://kofa.mmto.arizona.edu/stm32all/blue_pill/usb/an57294.pdf
  https://en.wikipedia.org/wiki/USB

## Slide 14: Universal Serial Bus (USB)
Pervasive wired communication protocol
  Universal accurately applies!
  Targets predominantly external devices over a plug/cable
Good combination of simple and capable
  Base version for simple devices does not require too much in terms of pins or resources
  More complex versions can transfer a significant amount of data
    These grew organically over time though
Great support for interoperability
  Generic device profiles that allowed for plug-and-play
  Supported by OS initiatives to include driver software

## Slide 15: USB is a layered protocol
USB protocol describes how to:
  Electrically send bits
  Send frames of multiple bytes
  Communicate data between two devices
  Communicate specific application data (through device classes)
Much larger compared to others
  SPI: only how to electrically send bits
  UART and I2C: how to send frames of bytes

## Slide 16: Roles and topology
Hosts and Devices
  USB On-The-Go allows host negotiation
    Added later. Support devices like smartphones
Host is in charge of communication (“Upstream”)
Devices provide various capabilities Host can interact with (“Downstream”)
Tiered star topology
  Host connects to hubs, which connect to devices
  Up to 127 devices per hub. Up to 5 layers of hubs

## Slide 17: USB signals
Four signals
  Vbus (5 volts, can power devices)
  D+
  D-
  Ground
D+/D- are a differential pair
  Signals are inverses of each other
    Usually, occasionally act separately to signal special conditions
    Increases voltage difference between states (5 - -5 = 10 volts)
  Wires are twisted to avoid interference

## Slide 18: Synchronizing data
No clock signal!! How is USB so fast?
  Partially EE magics: better receivers, matched wire impedance
  Partially easier to distinguish signal states
  Also guaranteed transitions, which allow resynchronization
Transitions are used to denote data (non-return-to-zero inverted)
  With guaranteed transition in within every 8 bits (bit stuffing)
  Allows clocks on the two devices to synchronize

## Slide 19: USB speeds
USB 1.0
  Low Speed: 1.5 Mbps
    Not clear if this is used anymore
  Full Speed: 12 Mbps
    Microcontrollers tend to support Full Speed
    We’re focusing on details from it
USB 2.0
  High Speed: 480 Mbps
USB 3.0+
  Super Speed: 5-20 Gbps
  Adds multiple parallel data connections
Pull-up resistors allow for detection of a plugged device
Also identify speed

## Slide 20: USB data frames
General packet format
  Sync field, allows transmitter and receiver clocks to synchronize
  Packet ID, determines what type of packet is being sent
    Token, setup Device or read/write data from/to Device
    Data, application data
    Handshake, acknowledgement (or explicit NAK)
  Address+Endpoint, for Token packets to identify Device
  Data, up to 1023 bytes (full speed, often capped at 64 for microcontrollers)
  CRC, (Cyclical Redundancy Check) to detect bit errors
  End-of-packet

## Slide 21: USB transactions
All transmissions are initiated by the Host, which can periodically request reading from a Device if desired
Reading data from Device
Writing data to Device

## Slide 22: Interacting with USB devices
Each Device is given a separate address on the bus
Each Device also has a number of Endpoints
  Logical communication channels
  Direct data and guide communication patterns

## Slide 23: USB endpoint types
Interrupt transfers
  Guaranteed latency, small amounts of data
  Important sensor data (mice and keyboards)
  Polled frequently by Host
Bulk transfers
  Sporadic large transfers, reliable communication
  General reading/writing of data (flash drives and USB serial)
  Polled by Host whenever there is available bandwidth
Isochronous transfers
  Guaranteed data rate, unreliable communication
  Continuous data streaming (audio and webcams)
  Polled frequently by host

## Slide 24: USB control endpoint
Every USB Device has a special Control endpoint as well
Used for setting up the USB Device driver on the Host
Initializing a Device
  Host sends SETUP transaction requesting device descriptor
  Host performs IN transaction to read device descriptor
  Host performs OUT transaction to write device status

## Slide 25: USB device descriptors
Packed version of tree structure describing the device
  Interfaces it provides
  Endpoints associated with each interface

## Slide 26: Example Microbit
Interface: Communications, Abstract (modem), CDC
  Endpoint: 3, IN, Interrupt
Interface: CDC Data, CDC DATA interface
  Endpoint: 1, IN, Bulk
  Endpoint: 2, OUT, Bulk
Interface: Vendor Specific Class, Subclass, Protocol
  Endpoint: 5, IN, Bulk
  Endpoint: 4, OUT, Bulk
Interface: Mass Storage, SCSI, MSD interface
  Endpoint: 7, IN, Bulk
  Endpoint: 6, OUT, Bulk
SEGGER JTAG interface
Virtual serial device
USB external filesystem

## Slide 27: Minimal virtual serial USB Device
Virtual Serial Device
  Endpoint 0: Control, IN/OUT
    Respond to IN requests by setting up OUT with a buffer of descriptor data of the correct size
  Endpoint 1: Interrupt, IN
    Needed for serial modem controls, just ignore it
  Endpoint 2: Bulk, OUT
    Connect to buffer from _write() (just takes raw characters)
  Endpoint 3: Bulk, IN
    Connect buffer to _read() (just provides raw characters)

## Slide 28: HID USB Device (Human Interface Device)
Used for human interaction devices, like keyboard/mouse
“Report” structure is provided over Interrupt IN endpoint
  Or on demand via Control IN endpoint
Example mouse with x,y and three buttons

## Slide 29: USB summary
Specification for fast data communication
Specification for interacting with abstract device types
  Connects correct driver to interpret and send data
Pros
  Very fast
  Very interoperable
Cons
  Hardware and software are way more complex than simple protocols like UART, SPI, and I2C
  Not very energy efficient

## Slide 30: nRF52 USBD
Implements USB Device (not Host)
  Control endpoint
  14 bulk/interrupt (7 IN, 7 OUT)
    64-byte transfers
  2 isochronous (1 IN, 1 OUT)
    1023-byte transfers
Full-speed USB
  With 5 volt signals

## Slide 31: Outline
I2C
USB
CAN

## Slide 32: Controller Area Network (CAN bus)
Designed for highly reliable interactions within a vehicle
Multi-master with arbitration
  Similar to I2C
Mechanism for sending messages with “identifiers”
  Identifies that data in the message, not the device
  Lower value identifiers have high priority
  All messages are received by all CAN nodes
    Which can decide at higher levels which identifiers they care about

## Slide 33: CAN physical connections
Two differential, wired-AND signal lines
  Transitions are used to transmit bits (non-return-to-zero) with bit-stuffing
  Combines aspects of USB and I2C
  125 kHz – 5 Mbps speeds

## Slide 34: CAN packet format
11-bit identifier
  Check bits as they are sent to see if you win arbitration
Up to 8 bytes (64 bits) of data
CRC for checking
Acknowledgement
  Like I2C, let the line float and see if another device responds
  If not, explicitly retransmit!

## Slide 35: CAN message types
Data frame
  Transmission of data for a certain identifier
Remote frame
  Requests data transmission of a certain identifier
Error frame
  Transmitted when an error is detected with the previous message
Overload frame
  Transmitted by a node that is too busy to respond right now

## Slide 36: CAN reliability design – detecting errors
Check for errors everywhere and appropriately handle
  Bit error
    If the value found on the bus differs from the one sent
  Stuff error
    If 6 consecutive bits of the same type are found
  CRC error
    If CRC does not match
  Form error
    Format field has unexpected values
  Acknowledgement error
    No ACK received
Devices detecting an error broadcast a message signifying it!
  Multiple devices sending the same message works without arbitration loss
  Previous message is then retransmitted

## Slide 37: CAN reliability design – handling errors
Each node accepts the possibility that maybe it is the faulty one
Track errors and successes and change device state
  Passive: limited error signaling and transmissions
  Bus off: does not transmit in any way
Idea is that the CAN controller hardware can be faulty but still detect it in some cases

## Slide 38: CAN summary
Designed for reliable vehicular communication
Multi-master bus with serial communication
Pros
  Highly reliable
  Extensible to many devices
Cons
  Special-purpose design. Whole system has to agree on identifiers
  Relatively slower throughput

## Slide 39: Outline
I2C
USB
CAN