## Slide 1: Lecture 17 Energy Management
CE346 – Microprocessor System Design
Branden Ghena – Spring 2021
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley), Brandon Lucia (Carnegie Mellon)

## Slide 2: Administrivia
Quiz 4 is available
  Due Friday
Demo details coming on Wednesday
~9 days to complete your project

## Slide 3: Today’s Goals
Consider energy and microcontroller systems
  What are the energy sources?
  What are the energy sinks?
Understand sleep mode on a microcontroller
Discuss software for low-energy operation

## Slide 4: Outline
Energy Sources
Energy Management
  Sleep
  Intermittent computing

## Slide 5: Energy sources
Need some way to gain energy to power system
Choices affect mobility, lifetime, software design, and capabilities
  Is the device tied to its power source?
  Must a human manually provide more energy?
  How do I write software to ensure “progress” is made?
  What sensors/actuators can the device run?

## Slide 6: Measuring energy use
Base equations
  Power = Current * Voltage (Watts)
  Energy = Power * Time (Joules)
Energy = volts * amps * seconds
  Voltage is usually constant for a system
  Time is how long you are running for / measurement period
  Current changes based on activities being done
    Often energy is presented as a current draw
    Maybe an average current draw
    With Voltage and Time implicit

## Slide 7: Example current trace during wireless communication

## Slide 8: Wired power through USB
Provides 5v at up to 500 mA (USB 2.0) or 900 mA (USB 3.0)
  Or power delivery specifications, which can do far more power
Must be converted to different voltage to use
  Voltage regulator takes in 5v and spits out 3.3v
  Has its own maximum current!
System is limited by the minimum of USB or regulator power
  Microbit: regulator gives 3.3v at up to 600 mA
    USB 2.5 Watts, Regulator 1.98 Watts ⇨ System 1.98 Watts
    This is a max! Stay 15-30% below regulator limit

## Slide 9: Thinking about energy
Batteries often list energy in mA*h (milliamp – hours)
  Coin cell battery: 3v at 220 mAh
  2x AA battery: 3v at 2000 mAh
  iPhone 11 battery: 3.7v at 3000 mAh
Also usually limited by regulator
  Sometimes just directly connected to system
  We can run at 3v just fine! (3.7v is no good though)
Voltage can vary with charge
  But only a little, right before battery is depleted
  Example: coin cell goes down to ~2.7 volts

## Slide 10: How are batteries measured?
Measuring energy remaining is a difficult problem
  Many questions to be handled
    How much did it start with?
    How much energy has been used?
    What type of battery is it?
  Energy is not as constant a quantity as one would hope
    Pulling out lots at once has an overhead penalty
Coulomb Counter (aka Battery Fuel Gauge)
  Designed for a specific battery “chemistry”
  Monitors charge flowing in each direction
  I2C interface for reading battery state
Accuracy is not exact, more of an educated guess

## Slide 11: How are batteries managed?
Usually a dedicated IC for charging and managing battery packs
  Recharges battery with appropriate amount of current
  Monitors issues of battery health
    Various status monitoring
      Overcharge, undercharge
      Overcurrent
      Overtemperature, undertemperature
    Will go so far as to cut off the system to protect the battery
Takeaway: complicated problem, approach with caution!
  Best to reuse an existing design, if possible

## Slide 12: Microbit only uses battery energy in a simple way
Battery input connects directly to regulator
  No protection for battery health
  No battery charging capabilities
Usually this is fine for simple, low-power systems

## Slide 13: Energy harvesting
Grab energy from the environment and use that!
  Could augment with a battery and use energy to recharge
  Could go entirely batteryless and live on harvested energy alone
Sources
  Light (outdoor or indoor. most successful)
  Airflow (outdoor or air vents)
  Motion (on human body)
  Temperature differential (difficult in practice)
  RF (very low energy source)

## Slide 14: Temperature harvesting from hot pipes
Peltier junctions create a voltage from temperature differential
  Challenge: needs a large differential for more energy

## Slide 15: Managing harvested energy
Often uses an IC to pull in energy and provide to system
Harvested voltage/current are often very small
  Signal in millivolts is pretty common
  Need to accumulate over time to power system
    Fill up a capacitor
Need particular load for maximum power
  ICs often implement Maximum Power Point Tracking (MPPT)
  Varies load automatically to always harvest the most possible energy

## Slide 16: Outline
Energy Sources
Energy Management
  Sleep
  Intermittent computing

## Slide 17: Thinking about energy
Battery energy
  Coin cell battery: 3v at 220 mAh
  2x AA battery: 3v at 2000 mAh
  iPhone 11 battery: 3.7v at 3000 mAh
nRF52833 active current: 5.6 mA (at 3v)
  Coin cell: 40 hours -> ~2 days
  2x AA: 360 hours -> ~15 days
  iPhone 11: 535 hours -> ~22 days
So how does any of this work???

## Slide 18: Sleep mode power draw

## Slide 19: Microcontroller sleep modes
Sleep mode
  Processor stops running
  Most peripherals are disabled
  Continues until an interrupt occurs and wakes the microcontroller
    Usually a timer or GPIO input
nRF52833 sleep mode current: 1.8 μA (GPIO port event only)
  Coin cell: 122222 hours -> ~5000 days -> ~14 years
Low-power systems shoot for less than 1% duty cycle
  Average current of ~100 μA or less
  Warning: other stuff on the board counts!!
    LEDs are 1-10 mA each… Power is not a concern of the Microbit

## Slide 20: Microbit current draw (microcontroller)
Active CPU
  5.6 mA (executing from Flash)
  1.8 μA (sleep mode with RAM retention)
Transmitting RF packet
  15.5 mA (+8 dBm)
Other peripherals
  SAADC: 1.37 mA
  Timer: 729 μA (for any Timer peripheral)
  I2C: 6.6 mA (pull-down resistors when transmitting 0 bit)
  Everything else is handfuls of μA

## Slide 21: Microbit current draw (non-microcontroller)
KL27 (JTAG interface microcontroller)
  2 μA sleep, 8 mA active
Speaker
  0-27.5 mA (changes with input signal)
Microphone
  0-120 μA (activated with GPIO pin)
Accelerometer/Magnetometer
  2-212 μA (depends on sensing rates, 200 is magnetometer)
LEDs
  0-230 mA (can be activated individually)
Everything else
  0-1 mA (mostly due to pull-up resistors)

## Slide 22: Max and min current for Microbit
Maximum current: 280 mA at 3.3 volts (~1 W)
  With everything active
  Well within limits of regulator
Minimum current
  ~15 mA (always-on power LED)
  If you removed the power LED:
  <100 μA (with everything off)

## Slide 23: nRF52 sleep mode
Triggered with assembly instruction
  WFI (Wait For Interrupt) or WFE (Wait For Event)
Stops processor until woken by interrupt, exception, or event
On nRF52 automatically disables high frequency clock if unneeded

## Slide 24: Software stops when the processor does, but peripherals continue
Problem: when the processor is off, no code is running
Solutions
  Peripherals can wake it up again
    Can probably go for milliseconds to minutes without any actions
    Timer interrupt can wake processor to do things
  Have hardware handle some parts in the background without the processor’s involvement
    DMA
    PPI

## Slide 25: Controlling peripherals while processor sleeps
DMA (Direct Memory Access)
  Set up a pointer to memory and a length
  Peripheral can load/store memory without processor’s involvement
  Usually use completion interrupt to wake processor
PPI (Programmable Peripheral Interconnect)
  Any Event can be tied to any Task within the nRF52
  Allows for complicated actions to be chained together

## Slide 26: nRF52 Tasks and Events
Tasks are used to perform some operation
  Often written to by software
Events change value when some change in status occurs
  Often used to trigger interrupts
PPI peripheral can connect any TASK to any EVENT
Example: Timer peripheral

## Slide 27: nRF52 PPI peripheral
Connects Events to Tasks via hardware
Each channel gets one Event pointer and up to two Task pointers
  Must point to Event/Task registers

## Slide 28: Example PPI use case
Automatic high-speed ADC sampling
Software configures and sleeps
  ADC (buffer and enable)
  Timer (prescaler, compare value, short from compare to clear, and start)
PPI: When Timer fires (EVENTS_COMPARE[0]),
  Sample ADC (TASKS_SAMPLE)
PPI: When ADC buffer full (EVENTS_END),
  Stop Timer (TASKS_STOP)
  Fork: wake processor (via software interrupt from EGU)

## Slide 29: Outline
Energy Sources
Energy Management
  Sleep
  Intermittent computing

## Slide 30: Reducing energy consumption even further
If sleep isn’t enough, you can power things off completely
  Transistor can be used to turn off the sensor

## Slide 31: Energy harvesting can lead to intermittent computing

## Slide 32: Disabling the microcontroller
Even 2 μA sleep current might be too much for energy harvesting
  Can turn off microcontroller periodically
  Enable it again once VCC returns
Problem: how do you write software to deal with intermittency?
  Run-to-completion with relatively quick code
    Initialize, sample sensor, send packet, turn off again
  Code checkpointing
    Save state from code and restore when power resumes
    Might be as little as which state the system is in, plus some samples
    Might be as much as saving entire stack state
    Needs low-energy, nonvolatile storage (FRAM or MRAM help!)

## Slide 33
Programs may not finish
Execution Time
count++
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.
Make capy bigger

## Slide 34
Programs may not finish
Execution Time
count++
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
count++;
buf[count] = accel()
.
.
.
Power fail
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 35
Programs may not finish
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 36
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
Power fail
Checkpoint
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 37
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
buf[count] = accel()
avg = sum(buf)/count
transmit-
Power fail
Power fail
Checkpoint
Checkpoint
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 38
Checkpointing enables progress
Execution Time
count++
buf[count] = accel()
count++;
buf[count] = accel()
Power fail
int process() {
count++;
buf[count] = accel();
avg = sum(buf)/count;
transmit(avg);
}
Power fail
.
.
.
Need to latch execution state periodically!
count++
buf[count] = accel()
buf[count] = accel()
avg = sum(buf)/count
transmit-
Power fail
Power fail
Checkpoint
Checkpoint
transmit(avg)
Execute with checkpoints
Notes: More detailed explanation WHY volatile/non-volatile etc. Perhaps split to two slides
Add callout saying we need latch, etc.

## Slide 39: Checkpointing goals
Have the compiler automatically insert checkpoints as needed
  Human doesn’t have to think about them when programming
Limit checkpointing overhead while maximizing forward progress
  Checkpointing will take time to perform, so want to do it rarely
  Rarer checkpoints mean more progress is lost in average outage
  Need to compromise on the two based on available energy

## Slide 40: Outline
Energy Sources
Energy Management
  Sleep
  Intermittent computing