## Slide 1: Lecture 06 Sensors
CE346 – Microcontroller System Design
Branden Ghena – Spring 2026
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Project Proposals due later this week
  Feel free to chat with me if you’ve got any questions about ideas
  Emailed project groups already
    If you’re still looking for a group, or another group member, let me know
  Goal to get you feedback next week
  Will likely focus on groups I’m concerned about though
    No news is good news

## Slide 3: Campus resources for prototyping
Ford Prototyping Lab has lots of resources that could be useful
  Machine shop and hand tools
  Laser cutters
  3D printing
  https://design.northwestern.edu/about/design-facilities/prototyping-lab.html
Mudd Library has 3D printing support as well
  Often free to use for classes
  https://www.library.northwestern.edu/use-the-libraries/technology-multimedia/makerlab-3d-printing/

## Slide 4: Today’s Goals
Think about sensing and sensors
Explore a variety of sensor types, how they are made, and what their capabilities are
Discuss output devices as well: actuators
Generally: do an overview of what exists and how it works
  Embedded systems is a mile wide and an inch deep
  Goal is to have a basic understanding of many things
    And then build a deeper understanding of the stuff you use

## Slide 5: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 6: Definitions
A sensor is a device that measures a physical quantity
  Temperature sensor
  Light sensor
  Microphone
An actuator is a device that modifies a physical quantity
  Heater
  Motor
  Speaker

## Slide 7: Analog signals
Exist in infinite states
  From a maximum to a minimum
Often used for interactions with the real world
  Sensors usually generate analog signals
Microbit example: microphone

## Slide 8: Sensors transform quantity into an electric signal
Microcontrollers can interact with analog signals
  Generating an analog signal proportional to physical quantity makes the quantity able to be sensed
  Microcontrollers will transform this analog signal into a binary value with an analog-to-digital converter
How do we generate an electrical signal?
  Ohm’s Law: V = I * R (Voltage = Current * Resistance)
  Vary any one of these three and an analog signal is created
    Resistive sensors are common
    As are sensors that produce a voltage/current

## Slide 9: Resistive sensors
  L: length of the conductor
  A: area of the conductor
  ρ: resistivity of the conductor material
Various materials have resistivity that is itself a function
  Based on temperature, light, strain, etc.

## Slide 10: Force-sensitive resistor
Vary resistance based on pressure or flex
  Various shapes and sizes

## Slide 11: Using a resistive sensor
Place in series with another resistor
  Between VCC and ground
Measure voltage between the two relative to ground
Forms a “voltage divider”

## Slide 12: Voltage divider
  Vin is a voltage source
  R1 and R2 are resistors
If R1 == R2
  Vout = Vin/2
Smaller R1 means larger Vout
  Vout approaches Vin
Important! Learn this

## Slide 13: Generating voltage via piezoelectric effect
Compression of the material generates a voltage
Various sources of compression:
  Air Pressure
  Acceleration
  Strain
Alternative to resistive sensors. But, a voltage is still the output

## Slide 14: Understanding sensor voltage
Once you get a voltage, what do you do with it?
Need to understand the transfer function between voltage and the sensed quantity
  Examples for an accelerometer: senses acceleration
Hopefully, function is linear
  Frequently, function is NOT

## Slide 15: Affine sensor model (for linear sensors)
x is the quantity being sensed
F(x) is a voltage proportional to that quantity
Parameters
  a: sensitivity, units Volts/quantity
    Change in voltage per change in quantity
  b: bias, units Volts
    Offset in voltage for zero of the quantity

## Slide 16: Bias and sensitivity example
Accel
x(g)
Vreadout (V)
F(x)
-3.6
3.6
0
0
1.5
3.0
F(x) = ax+b
b = 1.5
a = 1.5/3.6 = 0.417 V/g

## Slide 17: Break + Question
Accelerometer
  Measures 0-5 g
  Over a 0-5v range
What is sensitivity?
What is bias?
What acceleration is the voltage reading 3.5 volts?
  x is the quantity being sensed
  F(x) is a voltage proportional to that quantity
  a: sensitivity, units Volts/quantity
    Change in voltage per change in quantity
  b: bias, units Volts
    Offset in voltage for zero of the quantity

## Slide 18: Break + Question
Accelerometer
  Measures 0-5 g
  Over a 0-5v range
What is sensitivity? 1 v/g
What is bias? 0 v
What acceleration is the voltage reading 3.5 volts?
  3.5 v = 1v/g * x + 0v -> 3.5 g
  x is the quantity being sensed
  F(x) is a voltage proportional to that quantity
  a: sensitivity, units Volts/quantity
    Change in voltage per change in quantity
  b: bias, units Volts
    Offset in voltage for zero of the quantity

## Slide 19: Understanding transfer function: ADXL330 datasheet
Sensitivity and Bias are listed values
Ratiometric
  Relative to voltage the system is powered at

## Slide 20: Understanding transfer function: ADXL330 datasheet
Bandwidth
  ≈Data update speed of the sensor
  Data changes above 1600 Hz are less detectable
Various other features listed that you may or may not care about

## Slide 21: Active and passive sensing
Passive Sensing
Active Sensing

## Slide 22: Active and passive sensing
We usually focus on passive sensing
  Cheaper and lower energy costs!
Active sensing examples
  Flash photography
  Ultrasonic distance sensing
  Lidar and Radar

## Slide 23: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 24: Digital temperature sensor
Thermostat
  Original meaning of the word
Heat bends a strip of two different metals
Switches circuit on/off based on the temperature

## Slide 25: Thermo-electric temperature sensing
Thermocouple generates a voltage based on temperature
Can be used to harvest energy to run system

## Slide 26: Thermocouples are used in an RTG to power Mars rovers
Radioisotope Thermoelectric Generator
  Nuclear source creates heat
  Thermocouples convert heat to electricity
Reliable energy source for space!
  Solar panels get dusty on Mars, and sunlight has reduced energy at great distances
  In first year: 125 W
  After 14 years: 100 W
    Curiosity has been running this long
Used for other deep-space missions too
  Voyager, New Horizons, Cassini, Dragonfly
http://large.stanford.edu/courses/2012/ph240/belanger2/
https://en.wikipedia.org/wiki/Multi-mission_radioisotope_thermoelectric_generator

## Slide 27: Resistive temperature sensing
Thermistor varies resistance based on temperature
Set up as a voltage divider to measure
Advantages: extremely cheap and easy to use
Disadvantages: non-linear transfer function
Chart: Temperature (C)

## Slide 28: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 29: Measuring light
Lux: unit of illuminance
Beware spectrum sensitivity

## Slide 30: Resistive light sensing
Photocell changes resistance with light (non-linear)
Kit version:
10 kΩ when dark
1 kΩ when light

## Slide 31: Photodiodes leak current based on light levels
When voltage is applied in reverse to an ideal diode, no current flows
But some small amount of current leaks for real-world diodes
  Proportional to light levels!
LEDs can be used as (crappy) photodiodes as well!
  Apply reverse voltage
  Read in leak current as voltage across a resistor using ADC
https://wiki.analog.com/university/courses/electronics/electronics-lab-led-sensor

## Slide 32: Light color sensing
Respond to specific light colors separately
Intelligent sensor: photodiodes combined with ADCs and a wired interface (I2C)
Allows interrupting based on comparator too

## Slide 33: Passive Infrared (PIR) sensor
Detect movement in the environment
  By detecting change in IR levels
  “Motion” sensor
Often come with plastic lens cover to improve field of view and range

## Slide 34: PIR sensors come in digital and analog forms
Digital includes a preconfigured comparator

## Slide 35: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 36: Inertial Measurement Unit (IMU)
IMUs (a.k.a 9 degree-of-freedom, 9DOF) are used for tracking motion of a device
  Acceleration (X, Y, Z axes)
  Rotation (X, Y, Z axes)
  Magnetism (X, Y, Z axes)
  Sometimes 6DOF with Acceleration + one of the others
Intelligent sensing: combines multiple sensors, ADCs, and computation with a wired interface
  9 analog inputs would otherwise be too many
Can be used to track motion, determine transportation method
  Smartphones, Robotics, etc.

## Slide 37: Sensing acceleration
Goal: create a voltage that changes based on force

## Slide 38: Microelectromechanical Systems (MEMS)
Same concept, but within an IC and 1 to 100 micrometers in size

## Slide 39: Using accelerometers
Accelerometers usually measure in g’s
  Where 1 g equals acceleration due to Earth gravity
Determining distance from acceleration is possible
  But messy. Error is squared when integrating
  Needs careful filtering and is only accurate over short periods
  Often fills in gaps between GPS samples (or other localization systems)
Accelerometers also work as tilt sensors
  Constantly sensing pull of gravity

## Slide 40: Gyroscopes
Measures angular velocity
  Usually lower limit than you might hope
  <10 rotations per second
Usually, we want angle instead of rotation speed
  Integrate signal to determine current angle
  Combine noise and DC bias with integration and you get a continuously accumulating error: drift

## Slide 41: Magnetometer
Measures the magnetic field
Usually used in devices as a compass
  Detect Earth’s magnetic field orientation
Problem: Earth’s magnetic field often overwhelmed by local magnetism when indoors
  Large chunks of metal in walls, for example
  Or other metal parts nearby on the circuit board!!
Satellites can use magnetometers for localization

## Slide 42: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 43: Intelligent sensors
Many embedded sensors are more intelligent than simple analog
Combine it with a built-in ADC (analog-to-digital converter)
  Can be more finely tuned and calibrated for accuracy
  Now gives digital output over some wired communication mechanism
Combine it with additional circuitry / computation
  Automatically filter data
  Detect specific signal patterns and interrupt
I point most groups at intelligent sensors for projects
  More expensive but easier to use

## Slide 44: Example of Intelligent Sensor: QWIIC sensors
https://www.sparkfun.com/qwiic
  Adafruit has compatible parts it calls “STEMMA” https://www.adafruit.com/category/620
Sensors have a standard, wired interface
  Power, Ground, I2C (wired communication protocol)
Removes electrical/wiring issues
  Transforms into a software issue of what the correct commands to send to the device are
  Our usual plan: use an existing driver to guide creation of our own

## Slide 45: Other sensors (may or may not be intelligent)
Environment: Pressure, Humidity, Air Velocity, Air Quality
Distance: Ultrasonic, Lidar, or Radar
Biometric: Pulse Oximeter, Heart Rate
Agricultural: Soil moisture
Let’s do a quick tour of some more!

## Slide 46: Distance measurement with ultrasonic
Sound travels much slower than light
  About one foot per millisecond
Ultrasonic transmitters use high-frequency sound that humans can’t hear
  And measure the time for it to bounce off an object and return
Gives centimeter accurate distance
  But works best for solid objects

## Slide 47: Gesture sensor
Actually senses light colors (RGB channels)
  Four sensors aligned in a pattern
Comes with an LED that shines
  Uses reflections to determine direction a hand is moving over it

## Slide 48: Pulse sensor
Photo sensor that provides an analog output
When pressed tightly against a finger, the blood flow is detectable and corresponds with your pulse
  Counting peaks gives heartrate

## Slide 49: RFID Cards and Readers
Not a sensor at all, just a radio
  Provides energy to the tag and gets a wireless data packet in response
Useful for projects as it can distinguish between different RFID tags
  Usually cards
  Also capsules that can be embedded in various objects

## Slide 50: Break + Open Question
How are new sensors discovered/created?

## Slide 51: Water Quality Sensor
https://hackaday.com/2021/02/18/internet-of-clams/

## Slide 52: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 53: Capacitive Touch Sensor
Pull-up resistors connected to metal pads
  Also connected to GPIO pin
Acts as a capacitor connected to ground

## Slide 54: The touch pad recharges on its own
If you drive the GPIO pin attached to it low, touchpad clears low
If you make the GPIO pin an input (high impedance)
  The touchpad gets pulled high, which takes some amount of time
The more capacitance the longer this takes!
And fingers are GIANT capacitors
Low Capacitance
High Capacitance

## Slide 55: Capacitive touch sensing method
Drive GPIO pin low
  Connects the pad to ground
Set GPIO pin as input and enable low-to-high interrupt
  Gets an interrupt when the pad finally becomes high on its own
  Use a timer to determine time until interrupt
    ~70 μs with no finger, <= milliseconds with finger
  Needs to timeout after a few milliseconds to declare “touched” as there might be enough capacitance to never go fully high
Repeat periodically (a few times a second is probably good enough)
Sudden large increase in rise time ⇨ someone is touching!
  Finger acts as a large capacitor

## Slide 56: Capacitive touch works on any metal surface
Idea: Microbit door handle sensor
Connect a wire and a pull-up resistor to a metal door handle to sense when someone is touching it!
  Timing will be very different from capacitive pad, but should be repeatable and capable of distinguishing human touch

## Slide 57: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 58: What if you want to make an output?
More varied in their nature
  Typically: send an electrical signal in some form
  Actuator transforms electrical signal into some other mechanism
    Movement, heat, light, sound, etc.
Can also be intelligent actuators
  Communicate bits/bytes over some protocol about which actions to take
  Example: displays
Let’s do an overview of some outputs too

## Slide 59: Audio outputs
Microbit can do this natively! It has a speaker
  We’ll use it in lab 5
  Not a very good speaker…
    Great for beeps
    Bad at being loud or higher-quality audio
Alternative:
  External speaker driver hardware
  You provide it an audio signal (future lecture)
  It amplifies it and sends it to speakers
  Often supports multiple channels
    Left and Right channel audio

## Slide 60: Light outputs
Microbit has the 5x5 LED Matrix
But we can use additional LEDs
  High-power, super-bright LEDs
  RGB LED rings and strips
Challenge: need additional power
  Usually an external 5v supply
LED strips use a custom control protocol too (future lecture)

## Slide 61: Screens
Various sizes and capabilities
  Biggest are a couple inches and color
  Expect a LOW refresh rate
Intelligent systems with complicated protocols for initializing and transferring data
Probably the most complicated devices teams use
  But also, many teams use them successfully each quarter

## Slide 62: Motors
Simplest form are little buzzers that vibrate
  “Vibratory motors” for haptic feedback
Controlling more complicated motors usually gets in the real of electrical engineering
  H-bridge to drive the motors
  Pretty well-documented online at least
Motors often need external power
  It takes a lot of energy to move a motor and a load

## Slide 63: Servos
Simpler motors that come with built-in control
Some can spin like motors
Others move to fixed angles on command
We’ll control a simple servo in Lab4

## Slide 64: Thermal printer
Common use case: printing receipts
  Just an arbitrary printer though
Operation
  Special paper darkens if heated
  Print head has a row of dots that can be individually heated as paper moves over them
Communication
  Usually a UART (serial) protocol
  With a library of commands for positioning and selecting characters
https://www.dfrobot.com/product-1799.html

## Slide 65: Outline
Sensing Overview
Types of Sensors
  Temperature
  Light
  Inertial
  Others
Capacitive Touch Sensing
Actuators

## Slide 66: Bonus
Research case study

## Slide 67: PowerBlade current sensing
Example of creating a custom sensor
PowerBlade goals
  Sense current and voltage in real-time
  Be small enough to be deployable
Problem
  To measure current, you usually have to break the circuit
  But PowerBlade attaches in parallel

## Slide 68: Measuring current
Coil of wire in a changing electric/magnetic field produces a voltage
One way to make inductors is as a coil of wire wrapped horizontally around a magnetic core
Re-purpose horizontally wire-wound inductor as current sensor!

## Slide 69: Sensor placement
Is in the middle or close to a prong the best choice?
Turns out it’s closer to a prong
  Decreases with distance squared
Angled like the magnetic field is

## Slide 70: Measuring sensor values
Sensor output is very small
Amplify to make output large enough to accurately measure with ADC
Need to pick sampling rate
  AC: 60 cycles per second in US
  Need N * 60 measurements per second
  N=42 (as fast as we can measure)
    2520 measurements per second

## Slide 71: At first, our output signal was this green line

## Slide 72: Measurement into current
Search coil measures the derivative of current!!
Need to integrate to get signal and apply sensitivity and bias