## Slide 1: Lecture 10 Wired Communication: UART
CE346 – Microcontroller System Design
Branden Ghena – Spring 2026
Some slides borrowed from: Alexis Shuping (Northwestern), Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley), Alanson Sample (Michigan)

## Slide 2: Administrivia
Quiz today (warn your project members if they aren’t here)
Reminder: place hardware orders ASAP
  First round of orders due end-of-day Friday for all teams
  Placing first orders now
  I’ll start bringing hardware to class next week
    I don’t want give away my Microbit breakouts before Lab6

## Slide 3: Today’s Goals
Explore tradeoffs in wired communication
  Signals, Speed, Timing, Topology
Describe a wired serial communication protocol: UART
Discuss nRF52 implementation of UART

## Slide 4: Outline
Wired Communication
UART
nRF52 UARTE

## Slide 5: Purpose of communication
Goal: convey digital information between two devices
Simple solution
  Digital I/O pin – 1-bit of information
Complex solution
  Send multiple bits (arbitrarily many)
  While also minimizing
    Time, Energy, Pins, Errors, etc.

## Slide 6: Wired versus wireless communication
Wired
  Send digital signals across one or more wires
  Advantages: Reliable, Low energy, Often simpler topology
  Disadvantages: Physically limiting
Wireless
  Send digital signals across another medium (usually RF)
  Advantages: Physically flexible,
  Disadvantages: Unreliable, High energy, Usually broadcast

## Slide 7: Wired versus wireless communication
Wired
  Send digital signals across one or more wires
  Advantages: Reliable, Low energy, Often simpler topology
  Disadvantages: Physically limiting
  Today + next two lectures: UART, I2C, SPI, USB
Wireless
  Send digital signals across another medium (usually RF)
  Advantages: Physically flexible,
  Disadvantages: Unreliable, High energy, Usually broadcast
  After that: Wireless Communication

## Slide 8: Tradeoffs in Wired Communication
What It Affects:
Communication Speed
System Cost
What We Control:
Number of Signals
Timing of Signals
Network topology

## Slide 9: Effect: Communication Speed
Round-trip-time inherently limited by the speed of light
  Speed of electricity 50-99% of that
  29 cm (11.4 in) = 1 nanosecond
    Totally relevant for memory latency within computers
Also limited by interference
  Faster signals are harder to distinguish
  More susceptible to interference (matters less for wired comms)
Limited by whether the other device can keep up
  Might need some flow-control signaling to slow down when not ready

## Slide 10: Example communication speed
Internal, low-energy communication
  UART, 1-1000 kbps
  I2C, 100-400 kbps
  SPI, 1-100 Mbps
External (mostly serial) communication
  USB, 1-20000 Mbps
  Ethernet, 1-40000 Mbps
  HDMI, 4-48 Gbps
Internal parallel communication
  PCI, 8-32 Gbps
  RAM, 12-25 Gbps
Note: Speeds are always measured in bits per second

## Slide 11: Effect: System Cost
Difficult to speak in specific terms, as every project and implementation is unique
However, certain methodologies are more expensive than others
  General rule: simpler architectures are cheaper!
As we scale up, even small changes in per-unit cost can become very significant

## Slide 12: Other Effects
We’ll mostly look at protocols in terms of cost and speed in this lecture
However, there are many other tradeoffs to consider, as well!
  Power usage
    Very important for battery-powered devices
  Reliability
    Critical for medical, aerospace, and other life-sustaining applications
  Longevity
  And many others!

## Slide 13: Tradeoffs in Wired Communication
What It Affects:
Communication Speed
System Cost
What We Control:
Number of Signals
Timing of Signals
Network topology

## Slide 14: Tradeoff: number of signals
Serial interface
  Single wire
  Transmit data as a “series” of bits separated by time
Parallel interface
  Multiple wires
    How many depends on the system
  Transmit data across multiple “parallel” wires simultaneously
  Still separate by time for more data than wires
Transmitter
Transmitter

## Slide 15: Serial versus parallel
Serial
  Cheaper to use less wires
  Slower to transmit data
  Examples
    RS-232, UART, I2C, USB (2.0)
Parallel
  More expensive for more pins and wires
  Faster to transmit data
  Examples
    Internal buses, PCI, USB (3.0)

## Slide 16: Tradeoffs in Wired Communication
What It Affects:
Communication Speed
System Cost
What We Control:
Number of Signals
  Serial Parallel
Timing of Signals
Network topology

## Slide 17: Tradeoff: timing of signals
Synchronous communication
  Clock signal sent along with data
  Data is captured at edge of clock signal (rising or falling)
  Advantage: send signals very fast
  Disadvantage: extra pin and wire
Asynchronous communication
  Agree upon timing in advance and read data at that rate
  Advantage: no need for clock signal
  Disadvantage: clock synchronization
DATA
CLK
Transmitter
Receiver
b0
b1
b2
b3
b4
b5
b7
b6
D0
D1
D2
D3
D4
D5
D6
D7
CLK
Transmitter
Receiver
b0
b0
b0
b0
b0
b0
b1
b2
b3
b4
b5
b6
b7
Synchronous systems can be Serial (top) or Parallel (bottom)

## Slide 18: Compromise: combining signals and clocks
There is a method of recovering the clock from the signal
  Either the clock is directly encoded in the signal
  Or the signal will have mandatory high/low changes to synchronize
https://en.wikipedia.org/wiki/Clock_recovery
https://en.wikipedia.org/wiki/Self-clocking_signal

## Slide 19: Tradeoffs in Wired Communication
What It Affects:
Communication Speed
System Cost
What We Control:
Number of Signals
  Serial Parallel
Timing of Signals
  Sync Async
Network topology

## Slide 20: How to connect: point-to-point networks
How do we connect computers in a network?
  This is a question of “network topology”
  Simple option: just connect them directly
Problem: what if I find a third computer?

## Slide 21: How to connect: bus networks
Connect everything to one wire in parallel
  Actually a “multidrop bus”
  Scales pretty well to many computers
Problem: which computer gets to transmit when?
  Simultaneous transmissions conflict
  Need a scheme for “arbitration”, deciding who transmits when

## Slide 22: How to connect: ring networks
Connect everything with point-to-point connections
  Connect the last computer back to the first computer
  Also known as Daisy-Chain (without the last connection back to the start)
Problem: what if a computer stops sending?

## Slide 23: How to connect: star networks
Connect to a hub with point-to-point connections
  Hub connects all computers
  Hub is a simple computer with one job: transfer communications between computers
    Hopefully more reliable than any of the computers

## Slide 24: Microcontrollers are often hubs of star networks
Connect to multiple different sensors
Sometimes a few sensors are connected on a bus

## Slide 25: Summary: Tradeoffs in Wired Communication
What It Affects:
Communication Speed
System Cost
What We Control:
Number of Signals
  Serial Parallel
Timing of Signals
  Sync Async
Network topology
  Point Bus Ring Star

## Slide 26: Break + Open Question
What network topology is WiFi?
  Point-to-Point
  Shared Bus
  Ring
  Star

## Slide 27: Break + Open Question
What network topology is WiFi?
  Point-to-Point
  Shared Bus
  Ring
  Star
Any wireless device can hear any other wireless device (in range)
  BUT, it tries to emulate a Star topology, where each device only talks to the router

## Slide 28: Outline
Wired Communication
UART
nRF52 UARTE

## Slide 29: UART Overview
Universal Asynchronous Receiver Transmitter
  Serial communication between two devices
  Two wires: transmit and receive
  Simple to implement and very common on microcontrollers
Tradeoff choices: Serial, Asynchronous, Point-to-Point
Most frequently used to send text data between devices
  Microcontroller printf() output
  GPS to microcontroller
  Radio AT commands to/from microcontroller
Serial Async Point

## Slide 30: UART: chip-to-chip communication
Usually implemented as a two-wire interface
  TXD: Transmits data
  RXD: Receives data
  Optionally two additional pins for flow control
  No clock signal! Asynchronous
Note: TX connects to RX (you’ll always get this wrong on the first try)
Serial Async Point
Ground must be connected too. We just assume this to be true for internal busses

## Slide 32: Serial communication - DB9 connector
Common pattern in cables
  Ground (must be common), often VCC
  Communication pin(s)
  Plus extra wires for signaling metadata
Signal voltage not compatible with modern microcontrollers!
  Up to +/- 15 volts

## Slide 33: Protocol Timing Diagrams
Demonstrate how a digital signal changes over time
Options
  Low
  High
  Whichever the data value is (hexagons)
Time

## Slide 34: UART data frame
Signal is high by default

## Slide 35: UART data frame
Signal is high by default
Goes low to trigger Start

## Slide 36: UART data frame
Signal is high by default
Goes low to trigger Start
Send each data bit (high=1, low=0), plus optionally parity bit

## Slide 37: UART data frame
Signal is high by default
Goes low to trigger Start
Send each data bit (high=1, low=0), plus optionally parity bit
Goes high to trigger Stop

## Slide 38: UART example, transmitting 0x32 and 0x3C

## Slide 39: A few other aspects of UARTs
Transmission Rate (Baud Rate)
Sampling Rate
Flow Control
Error Handling and Detection

## Slide 40: UART baud rates
Baud rate is a measure of “symbols per second”
  Typically 1 bit per symbol, but not always
  UART is 1 bit per symbol, but 8 data bits per 10/11 symbols

## Slide 41: Most common UART baud rates
Any baud rate is possible
  But there are a handful of normal configurations
  115200 and 9600 are most common
We use 38400 for labs!
  That’s the number you’ve been typing in
  115200 was too fast to keep up with
  9600 was pretty slow though…

## Slide 42: UART sampling rate
How do we make asynchronous communication work?
  Both sides must agree on the baud rate
  Listen for start bit
  Conceptually:
    Only need to sample 9-10 more times at baud rate spacing (once per bit)
    Short enough that clocks should not diverge too much
  Realistically:
    Sample 8 or 16 times per bit
    Determine boundaries between bits
    Select most common value between boundaries

## Slide 43: UART flow control
How do we ensure that the other device is ready for the message?
  Add two pins for “hardware flow control” (uncommon in practice)
  Ready To Send (RTS) output, signals that you want to send data
  Clear to Send (CTS) input, signals that other device is ready to receive
Software flow control is possible too
  Send special byte that means pause or resume transmissions
  Only works with ASCII though (otherwise, byte might be valid data)

## Slide 44: UART error conditions
Parity failure
  Bit error when receiving data
Overrun
  New data arrived and overwrote buffer in peripheral before it was read
Framing
  Did not see Stop Bit when expected (should be guaranteed “1”)
Break condition
  Signal is low for entire message (Zero data plus Framing Error)
  Often used as a signal between devices

## Slide 45: Detecting errors with parity
If enabled, choose one configuration for all UART messages
  Even parity: total number of “1” bits in data is even
  Odd parity: total number of “1” bits in data is odd
Parity bit: set to 1 or 0 based on configuration and message data
  If message doesn’t match parity configuration at receiver, there was a bit error (single error detecting)
Example: Data = 10101011 (five “1” bits)
  Odd parity: set parity bit to zero
  Even parity: set parity bit to one

## Slide 46: UART Pros and Cons
Pros
  Only uses two wires
  No clock signal is necessary
  Can do error detection with parity bit
Cons
  Data frame is limited to 8 bits out of 10 bits (20% signaling overhead)
  Doesn’t support multiple device interactions (point-to-point only)
  Relatively slow to ensure proper reception

## Slide 47: Longer Decoding Example (no parity bits)
How many bytes are transmitted here?
Notes: REMINDER: animation messed up here

## Slide 48: Longer Decoding Example (no parity bits)
START
STOP
START
STOP
START
STOP
How many bytes are transmitted here? 3 bytes

## Slide 49: Break + Longer Decoding Example
START
START
START
STOP
STOP
STOP
How many bytes are transmitted here? 3 bytes
What is the data for the first byte?
  Remember: least significant bit is first
What message is sent here?

## Slide 50: Break + Longer Decoding Example
 |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
START
START
START
STOP
STOP
STOP
How many bytes are transmitted here? 3 bytes
What is the data for the first byte? 0b01001000 -> 0x48
  Remember: least significant bit is first
What message is sent here?

## Slide 51: Break + Longer Decoding Example
 |  |  | 0 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  |  | 1 | 0 | 0 | 1 | 0 | 0 | 1 | 0 |  |  | 1 | 0 | 0 | 0 | 0 | 1 | 0 | 0 |  |  | 
START
START
START
STOP
STOP
STOP
How many bytes are transmitted here? 3 bytes
What is the data for the first byte? 0b01001000 -> 0x48
  Remember: least significant bit is first
What message is sent here? 0x48, 0x49, 0x21
  In ASCII: HI!

## Slide 52: Real-world signals don’t have the guides
Assume the smallest step you ever see is the bit length
  Check that the start/stop bits are where you expect
  Calculate the values
Logic analyzers are tools to automatically do this protocol decoding

## Slide 53: UART to USB bridge
Microcontrollers typically use a UART for printf()
  Need to translate UART into something a computer can read (USB)
FTDI makes the most common chip to do this (FT232)
Microbit uses a microcontroller to do this!
  Secondary microcontroller connects to USB
  Also connects to nRF52833 via UART and JTAG
  ttyACM0 is a “virtual serial device” on top of USB, miniterm is a serial console

## Slide 54: Typical UART configurations
Baud rate 115200
No parity
No flow control
Probably covers ~70% of UART communication
  Baud rate 9600, No parity, No flow control covers another 15%
We are the rare case of an unusual baudrate 38400
  It was as fast as the Microbit could keep up with

## Slide 55: Outline
Wired Communication
UART
nRF52 UARTE

## Slide 56: Which UART peripheral?
Two peripherals in the nRF52 documentation
UART peripheral
  Standard UART without DMA
  Deprecated (as in, they strongly suggest not using it)
UARTE peripheral
  Standard UART with DMA
Their registers overlap
  They are two different ways of using the same hardware
  Only one at a time can be “active”

## Slide 57: UARTE Peripheral
Configurations
  Pins: TXD, RXD, and optionally RTS, CTS
  Baudrate, Parity, Flow control
Actions
  Transmit via DMA
    Provide a pointer to RAM (not Flash) and a length
  Receive via DMA
    Provider a pointer to RAM and a length

## Slide 58: UARTE peripheral

## Slide 59: UARTE peripheral
Pins: RX, TX, (optional) CTS and RTS

## Slide 60: UARTE peripheral
Receive connects directly to buffer in RAM

## Slide 61: UARTE peripheral
Transmit connects directly from buffer in RAM (not flash!)

## Slide 62: UARTE baudrates
Choose from standard, preconfigured baudrates
That values are 32-bit numbers implies other baudrates are possible…

## Slide 63: UARTE driver code
Pretty straightforward to implement driver for this
  Definitely could have been a lab
DMA is exactly what you want
  Pointer to buffer of data (in RAM)
  Length
  Go!
More interesting: how does printf() use the UART?

## Slide 64: boards/microbit_v2/microbit_retarget.c
printf() eventually calls _write()with formatted data
Converts stdio calls into UART TX and RX
  Blocking functions
Library just sets DMA and starts Tx

## Slide 65: Outline
Wired Communication
UART
nRF52 UARTE