## Slide 1: Lecture 15 Wrapup + Microprocessors
CE346 – Microcontroller System Design
Branden Ghena – Spring 2026
Some slides borrowed from: Josiah Hester (Northwestern), Prabal Dutta (UC Berkeley)

## Slide 2: Administrivia
Project check-ins this Friday
I can do a last round of orders this weekend
  After that, anything but Amazon will take too long to arrive
  Part of the check-ins: is there any remaining hardware you need?
Project Demo Scheduling
  Form link sent out through Ed
  Half of the class from 11:00-1:30 and half from 2:00-4:30
  Demos will be continuous during that period and open to the public!

## Slide 3: More administrivia
Last quiz today!
  Tell your friends

## Slide 4: Less administrivia
You’re using pin numbers wrong in your project
  Yes you
  (maybe)
Several groups forgot to switch to I2C_QWIIC_SDA (and SCL) when configuring their I2C
Bigger issue: several groups are just using numbers as if they mean output pins
  EDGE_P19 is NOT the same as 19
  EDGE_P8 is NOT the same as 8
  Use definitions in microbit_v2.h instead!!

## Slide 5: Today’s Goals
Discuss remaining parts of the Microbit and nRF52833
  Realize that we’ve covered almost everything on the system!!
Compare and contrast other microcontrollers and other similar hardware platforms

## Slide 6: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Other microcontroller peripherals
  Microprocessors

## Slide 7: Microbit
Used almost all of this!
Remaining:
  Batteries
  Wireless
  KL27Z I2C

## Slide 8: Internal Microbit connections

## Slide 9: KL27 I2C Interface
Device information
  Version of board and JTAG firmware
  Power state of board
    USB, Battery, both
    Voltage values for battery and VIN
  USB connection state
  Disable the power LED!!
Flash Storage
  128 kB of the KL27’s Flash is readable/writable over I2C
https://github.com/microbit-foundation/spec-i2c-protocol/blob/main/spec/index.md

## Slide 10: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Other microcontroller peripherals
  Microprocessors

## Slide 11: nRF52833 Peripherals
Tour of the nRF52833 peripherals
With some details on the ones we haven’t talked about
  Wireless
  Crypto
  Audio

## Slide 12: nRF52833 Peripherals
Cortex-M4F processor
32-bit ARM core
Floating point
Includes Interrupt control and SysTick (an extra timer)

## Slide 13: nRF52833 Peripherals
Memory buses

## Slide 14: nRF52833 Peripherals
JTAG and Debugging
Allows code updates
Allows GDB to step through code

## Slide 15: nRF52833 Peripherals
Volatile memory
SRAM, 128 kB

## Slide 16: nRF52833 Peripherals
Nonvolatile memory
Flash, 512 kB
Non-Volatile Memory Controller

## Slide 17: nRF52833 Peripherals
Power and Clock management

## Slide 18: nRF52833 Peripherals
GPIO pins

## Slide 19: nRF52833 Peripherals
Various timers
Watchdog Timer
Real-Time Counter
Timer peripheral

## Slide 20: nRF52833 Peripherals
Programmable Peripheral Interconnect
  Event->Task chaining
Random Number Generator
Temperature sensor

## Slide 21: nRF52833 Peripherals
Wireless radio
  Bluetooth Low Energy
  802.15.4 (Zigbee or Thread)
Cryptography
  ECB (AES mode)
  CCM (AES mode)
  AAR (Accelerated Address Resolver)
    For BLE random addresses

## Slide 22: nRF52833 Peripherals
Wired communication protocols
USB Device
SPI
  Controller/Peripheral
TWI (I2C)
  Controller/Peripheral
UART

## Slide 23: nRF52833 Peripherals
Inter-IC Sound (I2S)
  Wired communication bus explicitly for audio data
  Unrelated to I2C
Like a synchronous UART
  Clock, data in, data out
Additional signals
  MCK – synchronization
  LRCK – left/right channel select

## Slide 24: nRF52833 Peripherals
NFC
  Near-Field Communication
Close-range wireless communication protocol
“Tap-to-pay” systems

## Slide 25: nRF52833 Peripherals
GPIOTE
  GPIO interrupts

## Slide 26: nRF52833 Peripherals
Analog inputs
Comparator
Low-Power Comparator
Successive Approximation Analog-to-Digital Converter

## Slide 27: nRF52833 Peripherals
Quadrature Decoder peripheral
Detects rotation speeds and direction
  Usually for motors

## Slide 28: Quadrature Encoding
Usually two receivers and disks: A & B That gets you direction and speed

## Slide 29: nRF52833 Peripherals
Pulse Width Modulation
Pulse Density Modulation
  Similar idea to PWM
  Input-only peripheral
  Targets microphones

## Slide 30: nRF52833 is complete
That’s just about everything!
First 550 out of 600 pages of nRF52833 datasheet
  Remaining 50 are hardware details
    Pinout for different packages
    Recommended circuit layout
    Soldering details

## Slide 31: Break + Open Question
What doesn’t the nRF52833 have a peripheral for? (i.e., what could you imagine a peripheral for that it doesn’t have)

## Slide 32: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Other microcontroller peripherals
  Microprocessors

## Slide 33: Microcontroller knowledge is transferrable
Your knowledge of microcontrollers applies to almost all of them
  They have similar peripherals that work in similar ways
The exact names and configurations will definitely be different
  But the fundamentals stay the same
Let’s prove this with a quick view of two microcontrollers
  Atmel SAM4L
  Texas Instruments MSP430

## Slide 34: Atmel SAM4L Microcontroller
ARM Cortex M4F (same processor!)
Lots of very configurable peripherals
  USART, SPI, TWI, I2S, DAC, ADC, Timer, …
  Kind of a “do-everything” microcontroller

## Slide 35: SAM4L GPIO
GPIO register map (heavily abbreviated)

## Slide 36: Setting or clearing individual bits
Actually, each register appears four times in a row
  Read/write version
  Set version (like nRF *SET)
  Clear version (like nRF *CLR)
  Toggle version

## Slide 37: SAM4L Timers
Three 16-bit timers
  Each of which can have multiple inputs clock signals with prescaler values
  Timers can be chained together to make up to a 48-bit timer
One register for reading counter
Three registers for “compare interrupts”

## Slide 38: SAM4L PWM
PWM peripheral is essentially built into Timer peripheral
Timer peripheral also supports a “Waveform” mode where it generates an output GPIO signal, i.e. PWM
One comparison point is low-to-high transition, another is high-to-low transition

## Slide 39: Texas Instruments MSP430 (MSP430FR59xx)
Example of a very different microcontroller
16-bit custom architecture processor
2 kB RAM
64 kB FRAM
  Non-volatile, byte-writable

## Slide 40: MSP430 GPIO register map
Registers are a single byte in size
Oddly, some have an “undefined” reset state 😱

## Slide 41: Example MSP430 GPIO register: OUT
Example 8-bit register. Controls 8 pins in a GPIO “port”

## Slide 42: MSP430 Timer peripheral
A choice of input clocks goes through dividers to run a 16-bit timer
  Five total timers available on the system
  Some can trigger external output pins, some are only internal

## Slide 43: MSP430 PWM
The MSP430 Timer peripheral handles PWM as well!

## Slide 44: Bonus: nRF54L15
ARM Cortex-M33
  128 MHz
RISC-V EMC
  128 MHz
  Co-processor
  “Soft Peripherals”
    Load code so this acts like an arbitrary peripheral
Memory
  256 KB RAM
  1524 KB RRAM (non-volatile)

## Slide 45: nRF54L15 Temperature Peripheral

## Slide 46: nRF54L15 peripherals
GPIO (very similar) and GPIOTE (very similar)
  Three ports now, split by: low-power, normal, or high-speed
TIMER (very similar), improved RTC (1 μs ticks, 52 bits)
LPCOMP, COMP, and SAADC (all very similar)
PWM (basically identical)
UART, TWI, SPI (very similar)

## Slide 47: nRF54L15 changes
Power domains
  Makes it very clear which peripherals are active in different active/sleep modes
Peripheral interconnect
  nRF52 allows chaining Tasks and Events together
  nRF54 expands this to a full publish/subscribe architecture
    Timer event -> trigger ADC
    Timer OR GPIO event -> disable GPIO and Timer

## Slide 48: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Other microcontroller peripherals
  Microprocessors

## Slide 49: Microprocessor system design
What about modern microprocessors? (really SoC’s)
  Similar idea, but a LOT more stuff
Various peripherals, which might not be focused on sensor I/O
  Less ADCs and I2C more Ethernet and Graphics
External memory busses
  Microprocessors expect external memory to exist on the system
  Which means that they need pins for an external memory bus

## Slide 50: Beaglebone
Cheap, single board computer
  Like Raspberry Pi
Gross diagram that’s actually in their datasheet

## Slide 51: Resources on the Beaglebone and its microprocessor
https://beagleboard.org/bone-original
https://beagleboard.org/static/beaglebone/BEAGLEBONE_SCHEM_A3.pdf
https://transistor-man.com/files/emu/beaglebone_hardware/BONE_SRM.pdf
https://www.ti.com/product/AM3358

## Slide 52: AM3358 processor
ARM Cortex A8
  32-bit processor
  1 GHz clock
  300 pins!!
Internal memory
  176 kB ROM
  64 kB RAM
External memory
  DDR2/3, 400 MHz RAM
  NAND or NOR Flash

## Slide 53: AM3358 peripherals
Advanced peripherals
  Graphics
  Ethernet
  USB, CAN
Regular peripherals
  GPIO, Timers
  ADC
  UART, SPI, I2C

## Slide 54: How much bigger is a microprocessor?
nRF52833 datasheet:
  600 pages total
AM3358 datasheet:
  250 pages of electrical information
  5000 pages of peripheral information
    Lots of peripherals + very complicated peripherals
  And it’s not that the basic peripherals are much larger
    UART: 60 pages (okay, maybe a little longer)
    I2C: 20 pages
    Four different timers at ~30 pages each

## Slide 55: Memory interface - DDR
Double Data Rate (DDR)
Address bits
  17 pins (3 bank, 14 address)
  Bank + Address selects a 2 kB chunk out of 2 GB
Data bits
  16 pins
Clocks, Chip select
Various sequencing signals
Pinout on the Beaglebone

## Slide 56: Break + Question
Wires (traces) for high-speed busses like memory must be match, to ensure that all are exactly the same length. Why?

## Slide 57: Break + Question
Wires (traces) for high-speed busses like memory must be match, to ensure that all are exactly the same length. Why?
Speed of electricity in the wires matters
If one wire is a foot longer than the others, its signal arrives 1 ns late
  Even fractions of nanoseconds could matter for high-speed communication

## Slide 58: Flash interface - MMC
Multi-media Card interface
  Used to communicate with SD Cards
  Also for eMMC Flash chips (which act like SD Cards, but soldered in place)
For SD cards SPI can usually be used
For eMMC 4-bit version of interface
  Clock
  Command
  Data 0, 1, 2, 3
Pinout on the Beaglebone

## Slide 59: Ethernet interface - RMII
Reduced Media-Independent Interface (RMII)
Pinout on the Beaglebone

## Slide 60: Other processor pinouts on the Beaglebone
Lots of acronyms that we recognize!
Analog inputs
UARTs
I2C
GPIOs
Timers

## Slide 61: Outline
What haven’t we talked about?
  Microbit
  nRF52833
Other hardware systems
  Other microcontroller peripherals
  Microprocessors

## Slide 62: Outline
Bonus: Other hardware systems
  FPGAs

## Slide 63: FPGA systems
When else might you run into large busses like memory?
On an FPGA!
  Field-Programmable Gate Array (FPGA)
  Configurable hardware
    Engineers write a description of the hardware (Verilog or VHDL)
    FPGA implements that hardware
  Much faster than software, but still slower than a custom chip

## Slide 64: Combined FPGA + Microcontroller

## Slide 65: Busses: AHB vs APB
Advanced High-performance Bus (AHB)
  Multiple bus controllers
  Pipelined operation
  Burst transfers of data
  Used for high-speed memory operations
Advanced Peripheral Bus (APB)
  Simpler interface
  Lower power
  Used for most peripheral communication

## Slide 66: APB usage
Bus has three states
  IDLE
    Nothing is happening
    Default
  SETUP
    A transfer of data is about to happen
    Address and configuration signals are set
  ACCESS
    Data is actually transferred over the bus

## Slide 67: Example APB write operation
Setup phase begins
with this rising edge
Setup
Phase
Access
Phase

## Slide 68: Example APB read operation
Setup
Phase
Access
Phase
Setup phase begins
with this rising edge

## Slide 69: With an FPGA you can create your own peripherals
Busses can be exposed to the FPGA for it to use
Example use case
  Custom camera with selectable pixel lines and an ADC
  Don’t want to manually control it with software (too slow)
  Create a hardware peripheral on the FPGA that takes software commands like “grab a frame” and implements them

## Slide 70: Example register map
Verilog HDL that describes a register map
Reads in the address from the bus to determine which register is written to
Modifies internal registers based on the bits of the data

## Slide 71: Performing peripheral operations
On every clock edge, check status registers
If they are active, iterate through a state machine
  Possibly many states to make the actual operation occur