## Slide 1: Lecture 02 Representations
CS213 – Intro to Computer Systems
Branden Ghena – Fall 2023
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Announcements
Homework 1 will be posted sometime later today
  Practice problems on binary-to-hex-to-decimal conversion, integer encodings, and memory
  Today’s lecture will finish the content you need for it
  Due Tuesday October 3rd
    I need to create Gradescope so you can submit it. Should happen this weekend

## Slide 3: Today’s Goals
Complete introduction to binary and hexadecimal
Discuss data representation in memory
Explore data representations
  Integers, signed and unsigned
  Different bit widths
  Translating between encoding schemes
  Other encodings besides integers

## Slide 4: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 5: Learning binary
To understand how a computer really works we need to understand that data it operates on
Computers hold data in memory as individual ones and zeros
  These ones and zeros make up binary values
So, we’re going to need to understand binary
  Binary will definitely come up again in this and other classes

## Slide 6: Positional Numbering Systems
The position of a numeral (e.g., digit) determines its contribution to the overall number
  Makes arithmetic simple (compared to, say, roman numerals)
  Any number has one canonical representation
Example: base 10
  1045610 = 1*104 + 0*103 + 4*102 + 5*101 + 6*100
  Usually, we leave out the zeros:
    1*104 + 4*102 + 5*101 + 6*100

## Slide 7: Base 2 Example
Computer Scientists use base 2 a LOT (especially in computer systems)
Let’s convert 13810 to base 2
We need to decompose 13810 into a sum of powers of 2
  Start with the largest power of 2 that is smaller or equal to 13810
  Subtract it, then repeat the process
13810 – 12810 = 1010
1010 – 810 = 210
210 – 210 = 010
13810 = 1×128 + 0×64 + 0×32 + 0×16 + 1×8 + 0×4 + 1×2 + 0×1
13810 = 100010102
13810 = 1×27 + 0×26 + 0×25 + 0×24 + 1×23 + 0×22 + 1×21 + 0×20

## Slide 8: Binary practice
Convert 1012 to decimal
  = 1×22 + 0×21 + 1×20
  = 4 + 0 + 1
  = 510
Convert 410 to binary: 1002 (one less than 5)

## Slide 9: Why computers use Base 2
Simple electronic implementation
  Easy to store with bi-stable elements
  Reliably transmitted on noisy and inaccurate wires
Straightforward implementation of arithmetic functions
(Pretty much) all computers use base 2
0.0V
0.5V
2.8V
3.3V
0
1
0
Voltage
Time

## Slide 10: Why don’t computers use Base 10?
Because implementing it electronically is a pain
  Hard to store
    ENIAC (first general-purpose electronic computer) used 10 vacuum tubes / digit
  Hard to transmit
    Need high precision to encode 10 signal levels on single wire
  Messy to implement digital logic functions
    Addition, multiplication, etc.
    (See CE203 for details)

## Slide 11: Base 16: Hexadecimal
Writing long sequences of 0s and 1s is tedious and error-prone
  And takes up a lot of space on a page!
So we’ll often use base 16 (also called hexadecimal)
Base 2 = 2 symbols (0, 1) Base 10 = 10 symbols (0-9) Base 16, need 16 symbols
  Use letters A-F once we run out of decimal digits
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 12: Base 16: Hexadecimal
16 = 24, so every group of 4 bits becomes a hexadecimal digit (or hexit)
  If we have a number of bits not divisible by 4, add 0s on the left (always ok, just like base 10)
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
1 0 1 0 0 1 0 1 1 1 1 0 1 1
0x297B
0 0
“0x” prefix = it’s in hex

## Slide 13: Break + Practice problem
Convert 0x42 to decimal
Steps
  Convert 0x42 to binary:
  Convert binary to decimal:
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 14: Break + Practice problem
Convert 0x42 to decimal
Steps
  Convert 0x42 to binary:
    0x4 -> 0b0100 0x2 -> 0b0010
    0x42 -> 0b 0100 0010
  Convert binary to decimal:
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
“0b” prefix = it’s in binary

## Slide 15: Break + Practice problem
Convert 0x42 to decimal
Steps
  Convert 0x42 to binary:
    0x4 -> 0b0100 0x2 -> 0b0010
    0x42 -> 0b 0100 0010
  Convert binary to decimal:
    1*26 + 1*21 = 64 + 2 = 66
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111
“0b” prefix = it’s in binary

## Slide 16: Direct hex-to-decimal conversion is possible, but unnecessary
Convert 0x42 to decimal
Alternate method:
  0x42
  = 4×161 + 2×160
  = 64 + 2
  = 66
But you’re honestly better off converting hex to binary first
  It’s good practice!

## Slide 17: Specific bit widths
Since computers are hardware, cannot have arbitrary bit lengths
  Must be some specific number of bits
  We’ll say “this is a 16-bit number” or this is a “9-bit number”
What if the number of bits isn’t divisible by four, can it still be hex?
  Yes! All non-existent bits MUST be zero
Example: translate 0x35 to a 6-bit binary number
  0b0011 0101 -> 0b11 0101
  If it had been 0x75 (0b111 0101) writing as a 6-bit binary number would be impossible (converting could happen, but we’d have overflow)

## Slide 18: Bytes
A single bit doesn’t hold much information
  Only two possible values: 0 and 1
  So we’ll typically work with larger groups of bits
For convenience, we’ll refer to groups of 8 bits as bytes
  And usually work with multiples of 8 bits at a time
  Conveniently, 8 bits = 2 hexits
Some examples
  1 byte: 0b01100111 = 0x67
  2 bytes: 11000100 001011112 = 0xC42F
“0b” prefix = it’s in binary
“0x” prefix = it’s in hex

## Slide 19: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 20: Byte-oriented memory organization
We’ve seen how sequences of bits can express numbers
  And how we usually work with groups of 8 bits (bytes) for convenience
  Variables are almost always some multiple number of bytes (1 byte, 2 bytes, 8 bytes, etc.)
In a computer system, bytes can be stored in memory
  Conceptually, memory is a very large array of bytes
  Each byte has its own address (≈ pointer)
Compiler + run-time system control allocation
  Where different program objects should be stored
  Multiple mechanisms, each with its own region: static, stack, and heap
• • •
00•••0
FF•••F

## Slide 21: Most/least significant bits/bytes
When working with sequences of bits (or sequences of bytes), need to be able to talk about specific bits (bytes)
  Most Significant bit (MSb) and Most Significant Byte (MSB)
    Have the largest possible contribution to numeric value
    Leftmost when writing out the binary sequence
  Least Significant bit (LSb) and Least Significant Byte (LSB)
    Have the smallest possible contribution to numeric value
    Rightmost when writing out the binary sequence
10110110 01101010 10101010 01111100
Most significant bit
Most significant byte
Least significant byte
Least significant bit

## Slide 22: Addressing and byte ordering
For data that spans multiple bytes, need to agree on two things
  1. What should be the address of the object? (each byte has its own!)
    And by extension, given an address, how do we find the relevant bytes (same question!)
  2. How should we order the bytes in memory?
    Do we put the most or least significant byte at the first address?

## Slide 23: There isn’t always one correct answer
Different systems can pick different answers! (mostly for 2nd Q)
  Very nice illustration of two overarching principles in systems: You need to know the specifics of the system you’re using!
    Many questions don’t really have right or wrong answers!
    Instead, they have tradeoffs. What the “right” answer is depends on context!
  Different answers across systems is perfectly fine
    But all the parts of a given system must agree with each other!

## Slide 24: 1. Addressing data in memory
All addresses refer to one or more bytes
  Never bits
For multi-byte objects, the lowest address refers to the entire object
  Addresses of successive objects differ by 4 (32-bit) or 8 (64-bit)
Systems pretty much universally use the address of the first byte as the address for the whole object
  I’m not aware of any system that does otherwise
  But there could be some weirdo systems out there (or historically)
32-bit
Bytes
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
Addr.
0012
0013
0014
0015
64-bit
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008
Notes: For objects that span multiple bytes we need to agree on two things
- what would be the address of the object?
- how would we order the bytes in memory?

## Slide 25: 2. Byte ordering
How to order bytes within a multi-byte object in memory
  Only relevant when working with data larger than a byte!
Conventions
  Big Endian: Oracle/Sun (SPARC), IBM (PowerPC), Computer Networks
    Most significant byte has lowest address (comes first)
  Little Endian: Intel (x86, x86-64)
    Least significant byte has lowest address (comes first)
Example
  4-byte piece of data: 0x01234567
  Address of that data is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01
Increasing memory addresses
Notes: most significant comes first -> big endian
Little and big endian comes from Jonathan Swifts’ Guilliver’s Travels where two groups couldn’t agree as to how a soft-boiled egg should be opened (big or little end first)
Anecdote: little endian was developed by intel to keep backwards compatibility with cashier’s machines that were streaming data in the proper order for computation (LSB in first).
The CTC Datapoint 2200 was designed using simpler bit-serial logic in which little-endian address and data formats facilitate carry propagation. When Intel implemented the 8008 for Datapoint, they kept the little-endian architecture. However, Datapoint never used the 8008 chip, using an MSI equivalent implementation as Intel was unable to deliver the 8008 in time. After renegotiation, CTC kept its money and Intel kept the rights to 8008. That was the beginning of the x86 architecture.

## Slide 26: Practice: reading memory
Assume memory is Little Endian
  So the Least Significant Byte comes first
What is the four-byte value at 0x2010?
What is the two-byte value at 0x2014?
What is the one-byte value at 0x2016?
Address | Value
0x2010 | 0x37
0x2011 | 0x1A
0x2012 | 0xBE
0x2013 | 0x98
0x2014 | 0x0C
0x2015 | 0x80
0x2016 | 0x42

## Slide 27: Practice: reading memory
Assume memory is Little Endian
  So the Least Significant Byte comes first
What is the four-byte value at 0x2010?
What is the two-byte value at 0x2014?
What is the one-byte value at 0x2016?
Address | Value
0x2010 | 0x37
0x2011 | 0x1A
0x2012 | 0xBE
0x2013 | 0x98
0x2014 | 0x0C
0x2015 | 0x80
0x2016 | 0x42
0x98BE1A37
0x800C
0x42

## Slide 28: Practice: reading memory
Assume memory is Little Endian
  So the Least Significant Byte comes first
What is the four-byte value at 0x2010?
What is the two-byte value at 0x2014?
What is the one-byte value at 0x2016?
Address | Value
0x2010 | 0x37
0x2011 | 0x1A
0x2012 | 0xBE
0x2013 | 0x98
0x2014 | 0x0C
0x2015 | 0x80
0x2016 | 0x42
0x98BE1A37
0x800C
0x42

## Slide 29: Practice: reading memory
Change: assume memory is Big Endian
  So the Most Significant Byte comes first
What is the four-byte value at 0x2010?
What is the two-byte value at 0x2014?
What is the one-byte value at 0x2016?
Address | Value
0x2010 | 0x37
0x2011 | 0x1A
0x2012 | 0xBE
0x2013 | 0x98
0x2014 | 0x0C
0x2015 | 0x80
0x2016 | 0x42
0x371ABE98
0x0C80
0x42
Note: endianness doesn’t affect one-byte values!

## Slide 30: Tables of memory
Method of displaying large chunks of memory
  8 bytes per row
  Data values in hexadecimal
Memory addresses labeled on the left and byte offset on the top
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x1040 | 2E | E2 | BD | 62 | EF | A0 | CD | 93
0x1048 | A4 | 75 | 61 | 2F | 0F | DB | 64 | A4
0x1050 | 54 | 7A | F2 | 60 | 6E | 47 | B0 | 92
0x1058 | DA | 72 | 8F | A8 | E5 | 15 | 18 | CE
0x1060 | 86 | BF | 6A | 6A | 92 | 99 | CF | 6C

## Slide 31: Tables of memory
To find an address: deconstruct into:
  base address (left) + offset (top)
Remember: addresses are in hexadecimal!
  0x1048+2 = 0x104A
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x1040 | 2E | E2 | BD | 62 | EF | A0 | CD | 93
0x1048 | A4 | 75 | 61 | 2F | 0F | DB | 64 | A4
0x1050 | 54 | 7A | F2 | 60 | 6E | 47 | B0 | 92
0x1058 | DA | 72 | 8F | A8 | E5 | 15 | 18 | CE
0x1060 | 86 | BF | 6A | 6A | 92 | 99 | CF | 6C

## Slide 32: Tables of memory
Practice: what value is at address 0x1050?
  0x54 (0x1050 + 0)
Practice: what value is at address 0x105F?
  0xCE (0x1058 + 8)
Address | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
0x1040 | 2E | E2 | BD | 62 | EF | A0 | CD | 93
0x1048 | A4 | 75 | 61 | 2F | 0F | DB | 64 | A4
0x1050 | 54 | 7A | F2 | 60 | 6E | 47 | B0 | 92
0x1058 | DA | 72 | 8F | A8 | E5 | 15 | 18 | CE
0x1060 | 86 | BF | 6A | 6A | 92 | 99 | CF | 6C

## Slide 33: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 34: Big Idea: What do bits and bytes mean in a system?
The answer is: it depends!
Depending on the context, the bits 11000011 could mean
  The number 195
  The number -61
  The number -19/16
  The character ‘├’
  The ret x86 instruction
You have to know the context to make sense of any bits you have!
  Looking at the same bits in different contexts can lead to interesting results
  Information = bits + context!
An encoding is a set of rules that gives meaning to bits

## Slide 35: An example encoding: ASCII characters
ASCII = American Standard Code for Information Interchange
  Standard dating from the 60s
Maps 8-bit* bit patterns to characters
  (* the standard is actually 7-bit, leaving the 8th bit unused)
  We already know how to go from sequences of bits (base 2) to integers
  Need to take one more step, and interpret these integers as characters
Examples
  0100 00012 = 0x41 = 6510 = ‘A’
  0100 00102 = 0x42 = 6610 = ‘B’
  0011 00002 = 0x30 = 4810 = ‘0’
  0011 00012 = 0x31 = 4910 = ‘1’
Reference: https://www.asciitable.com/

## Slide 36: Full ASCII table
Values listed in:
Decimal
Hexadecimal
Octal
HTML
Character

## Slide 37: Encodings are just determined by people
There’s no inherent truth in the design of an encoding
  Although some encodings are nice or annoying for various reasons
  Example: it’s nice in ASCII that letters are in alphabetical order
You could come up with an entirely new way of encoding characters
  The hard part would be getting everyone else to agree to use it

## Slide 38: Open Question + Break
What things might we want to encode?

## Slide 39: Open Question + Break
What things might we want to encode?
  Numbers
    Signed and unsigned integers
    Real numbers
    Mathematical symbols: ∞ 𝛑
  Language
    Characters in various different languages ΩͶݽ서北
    Emoji 😱😡😁😭🤷🦃🎶🎂✨🐱‍🏍🍢
  Colors, Playing Cards, User Actions, anything!

## Slide 40: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 41: Integer types in C
C type provides both size and encoding rules
Integer types in C come in two flavors
  Signed: short, signed short, int, long, …
  Unsigned: unsigned char, unsigned short, unsigned int, ...
And in multiple different sizes
  1 byte: signed char, unsigned char
  2 bytes: short, unsigned short
  4 bytes: int, unsigned int
  Etc.

## Slide 42: Sizes of C types are system dependent
Portability
  Some programmers assume an int can be used to store a pointer
  OK for most 32-bit machines, but fails for 64-bit machines!
How I program
  Use fixed width integer types from <stdint.h>
  int8_t, int16_t, int32_t
  uint8_t, uint16_t, uint32_t
C Data Type | Intel IA32 | x86-64 | C Standard* (C99)
char | 1 | 1 | ≥1
short | 2 | 2 | ≥2
int | 4 | 4 | ≥2
long | 4 | 8 | ≥4
long long | 8 | 8 | ≥8
float | 4 | 4 | 
double | 8 | 8 | 
pointer | 4 | 8 | Widths for data, code pointers may differ!
CS213 uses this
Notes: Note that short int use 2-bytes, unqualified int is 4B and long int uses the full word size (4 or 8)
Also note two different floating-point formats – single and double precision
There are differences among same architectures of different width, different archs of same width, and the standard is in lala land

## Slide 43: Expressing C types in bits
Two families of encodings to express integers using bits
  Unsigned encoding for unsigned integers
  Two’s complement encoding for signed integers
Each encoding will use a fixed size (# of bits)
  For a given machine
  Size + encoding family determine which C type we’re representing
    Reverse is also true: a C type specifies both size and encoding
  Fixed size is because computers are finite!

## Slide 44: Unsigned integer encoding
Just write out the number in binary
  Works for 0 and all positive integers
Example: encode 10410 as an unsigned 8-bit integer
  10410 = 0×27 + 1×26 + 1×25 + 0×24 + 1×23 + 0×22 + 0×21 + 0×20
⇒ 01101000
⇒ 0x68
(Binary To Unsigned)

## Slide 45: Bounds of unsigned integers
For a fixed width w, a limited range of integers can be expressed
  Smallest value (we will call UMin):
    all 0s bit pattern: 000…0, value of 0
  Largest value (we will call UMax):
    all 1s bit pattern: 111...1, value of 2w – 1
    2w – 1 = 1×2w-1 + 1×2w-2 + ... + 1×21 + 1×20 = 11111...
Maximum 8-bit number = 28-1 = 256-1 = 255

## Slide 46: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 47: Encoding signed integers
What’s different about representing a signed number?
  It can be negative!
So, we’re going to have to somehow represent values that are negative and positive
There are actually many different encodings capable of doing this
  This is when that “nice encoding” versus “annoying encoding” matters

## Slide 48: Doesn’t work: attempting signed encoding
Goal: encode integers that can be positive or negative
First attempt: we can use the most significant bit for sign
  “Sign-and-magnitude” encoding
  In 8-bits:
    +4 = 00000100
    -4 = 10000100
+0 = 00000000
-0 = 10000000
+127 = 01111111
-127 = 11111111
Annoying problem: we have two representations of zero!
Also annoying: hardware to do math with signed and unsigned numbers gets complicated…

## Slide 49: Does work: Two’s complement encoding
Bad news: need to make the encoding more complicated
Good news: it will actually work
Plan:
  Start with unsigned encoding, but make ONLY the largest power negative
  Example: for 8 bits, most significant bit is worth -27 not +27 (other bits are still positive)
To encode a negative integer
  First, set the most significant bit to 1 to start with a big negative number
  Then, add positive powers of 2 (the other bits) to “get back” to number we want
Example: encode -6 as a 4-bit two’s complement integer
  -610 =
1 × -23
+ 0 × 22 + 1 × 21 + 0 × 21
⇒ 0b1010
⇒ 0xa

## Slide 50: Two’s complement examples
Encode -100 as an 8-bit two’s complement number
  -10010 =
Problem becomes: encode +28 as a 7-bit unsigned number
1 × -27
-128
+ 0 × 26
+ 0
+ 0 × 25
+ 0
+ 1 × 24
+ 16
+ 1 × 23
+ 8
+ 1 × 22 + 0 × 21 + 0 × 20
+4 +0 +0
-10010 = 0b10011100 = 0x9C
Shortcut: determine positive version of number, flip it, and add one
  10010 = 0b01100100
  Flipped = 0b10011011
  Plus 1 = 0b10011100 = 0x9C We’ll talk about binary addition next lecture

## Slide 51: Interpreting binary signed values
Converting binary to signed:
Note: most significant bit still tells us sign!! 1-> negative
  Checking if a number is negative is just checking that top bit
Zero problem is solved too
  0b00000000 = 0 0b10000000 = -128
-1: 0b111…1 = -1 (regardless of number of bits!)
Sign bit

## Slide 52: Bounds of two’s complement integers
For a fixed width w, a limited range of integers can be expressed
  Smallest value, most negative (we will call TMin):
    1 followed by all 0s bit pattern: 100…0 = -2w-1
  Largest value, most positive (we will call TMax):
    0 followed by all 1s bit pattern: 01...1, value of 2w-1 – 1
Beware the asymmetry! Bigger negative number than positive

## Slide 53: Ranges for different bit amounts
Observations
  |TMin | = TMax + 1
    Asymmetric range
  UMax = 2 * TMax + 1
C Programming
  #include <limits.h>
  Declares constants, e.g.,
    ULONG_MAX
    LONG_MAX
    LONG_MIN
  Values are platform specific
Notes: Note the asymmetry on the 2’s-complement range, a source of bugs; why the asymmetry? 0 is nonnegative which means it can represent one less positive number
Note also that UMax is just over 2 TMax (Umax = 2*Tmax+1)

## Slide 54: Unsigned & Signed Numeric Values
Equivalence
  Same encodings for non-negative values
Uniqueness
  Every bit pattern represents unique integer value
  Each representable integer has unique bit encoding
 Can Invert Mappings
  Can go from bits to number and back, and vice versa
  U2B(x) = B2U-1(x)
    Bit pattern for unsigned integer
  T2B(x) = B2T-1(x)
    Bit pattern for two’s complement integer
X
B2T(X)
B2U(X)
0000
0
0001
1
0010
2
0011
3
0100
4
0101
5
0110
6
0111
7
–8
8
–7
9
–6
10
–5
11
–4
12
–3
13
–2
14
–1
15
1000
1001
1010
1011
1100
1101
1110
1111
0
1
2
3
4
5
6
7

## Slide 55: Practice + Break
What range of integers can be represented with 5-bit two’s complement?
    A -31 to +31
    B -15 to +15
    C 0 to +31
    D -16 to +15
    E -32 to +31

## Slide 56: Practice + Break
What range of integers can be represented with 5-bit two’s complement?
    A -31 to +31 No asymmetry and 6-bits
    B -15 to +15 No asymmetry
    C 0 to +31 Unsigned
    D -16 to +15 Correct
    E -32 to +31 6-bits

## Slide 57: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 58: Casting signed to unsigned
C allows conversions from signed to unsigned (and vice versa)
Resulting value
  Not based on a numeric perspective: keep the bits and reinterpret them!
  Non-negative values unchanged
    ux = 15213
  Negative values change into (large) positive values (and vice versa)
    uy = 50323
Warning: Casts can be implicit in assignments or function calls!
  More on that in a few slides
short int x = 15213;
unsigned short int ux = (unsigned short) x;
short int y = -15213;
unsigned short int uy = y; /* implicit cast! */

## Slide 59: Mapping Signed  Unsigned (4 bits)
Signed
0
1
2
3
4
5
6
7
-8
-7
-6
-5
-4
-3
-2
-1
Unsigned
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Bits
0000
0001
0010
0011
0100
0101
0110
0111
1000
1001
1010
1011
1100
1101
1110
1111
=
+ 16 (i.e., 24)
- 16 (i.e., 24)
Large negative factor becomes
large positive!

## Slide 60: Signed vs Unsigned in C
Constants
  By default constants are considered to be signed integers
  Unsigned with “U/u” as suffix: 0U, 4294967259U
Expression evaluation
  If there is a mix of unsigned and signed in a single expression, signed values are converted to unsigned
  Including comparison operations!! <, >, ==, <=, >=
Can lead to surprising behavior!
  -1 < 0U ⇒ false!
  -1 gets converted to unsigned
  All 1s bit pattern ⇒ UMax! Definitely not less than 0!

## Slide 61: Example
Convert signed 8-bit number -120 into an unsigned number
Convert -120 into binary
Convert binary back into unsigned decimal

## Slide 62: Example
Convert signed 8-bit number -120 into an unsigned number
Convert -120 into binary -120 = -128 + 8 =
Convert binary back into unsigned decimal

## Slide 63: Example
Convert signed 8-bit number -120 into an unsigned number
Convert -120 into binary -120 = -128 + 8 = 1x(-128) + 0x64 + 0x32 + 0x16 + 1x8 + 0x4 + 0x2 + 0x1
Convert binary back into unsigned decimal

## Slide 64: Example
Convert signed 8-bit number -120 into an unsigned number
Convert -120 into binary -120 = -128 + 8 = 1x(-128) + 0x64 + 0x32 + 0x16 + 1x8 + 0x4 + 0x2 + 0x1 0b 1000 1000
Convert binary back into unsigned decimal
  1x128 + 0x64 + 0x32 + 0x16 + 1x8 + 0x4 + 0x2 + 0x1
  128 + 8 = 136

## Slide 65: Code Security Example
Simplified example of code found in FreeBSD’s implementation of getpeername
There are legions of experts trying to find vulnerabilities in programs, not all with good intentions
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 66: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf(“%s\n”, mybuf);
}

## Slide 67: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE];
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
int len = KSIZE < maxlen ? KSIZE : maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}
/* Declaration of library function memcpy */
void *memcpy(void *dest, void *src, size_t n);
size_t is unsigned!

## Slide 68: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 69: Truncation
May want to convert between numeric types of different sizes
Going from a larger to a smaller number of bits is easy
  Truncation: drop bits from the most significant side until we fit
    Values that can be represented by both types are preserved!
      Including negative values!
    Values that can’t be represented by the smaller type are mapped to some that can (modular (= modulo) behavior)
Example
  16 bits → 8 bits: 10110010 01001000 →
  Unsigned: 4564010 → 7210
    7210 = 4564010 modulo 28
  Signed: -5266410 → 7210
    7210 = -5266410 modulo 28
01001000
This can cause bugs!!
See Ariane 5 explosion…

## Slide 70: Extension
Going from smaller to larger: what to do with the “new” bits?
  These “new” bits go on the most significant side
Unsigned: easy, pad with 0s!
  Always safe to add 0s on the most significant end: 1521310 = 0001521310
  Example: 8 bits → 16 bits: 01001000 →
    7210 = 7210
  Value is preserved!
01001000
00000000

## Slide 71: Sign Extension
Extending signed encodings takes more effort to preserve the value
Duplicate the Most significant bit when extending
  If it’s a zero, extend with zeros. If it’s a one, extend with ones.
• • •
X
X’
• • •
• • •
• • •
w
w
k

## Slide 72: Example sign extension
Extend -128 from an 8-bit to bigger versions
8-bit version:
  -128 + 0 = 1x(-128) + all zeros = 0b1000 0000
9-bit version:
  -256 + 128 = 1x(-256) + 1x128 + all zeros = 0b1 1000 0000
10-bit version:
  -512 + 256 + 128 = 0b11 1000 0000

## Slide 73: Sign Extension Examples
Converting from smaller to larger integer data type
C automatically performs sign extension for signed types
  If cast changes both sign and size, extends based on source signedness
  But less confusing to write code that makes the types (and casts) explicit
signed short x = 15213;
signed int ix = (int) x;
signed short y = -15213;
signed int iy = (int) y;
Decimal
Hex
Binary
x
15213
3B 6D
00111011 01101101
ix
15213
00 00 3B 6D
00000000 00000000 00111011 01101101
y
-15213
C4 93
11000100 10010011
iy
-15213
FF FF C4 93
11111111 11111111 11000100 10010011

## Slide 74: Justification for sign extension
Prove correctness by induction on k
  Induction Step: extending by single bit maintains value
Look at weight of high-order bits:
  X: -2w–1 xw–1
  X’: -2w xw–1 + 2w–1 xw–1 = (-2w-1+1)xw–1 + 2w–1 xw–1 = (-2×2w-1 + 2w-1 )xw–1 = -2w–1 xw–1
-
• • •
X
X’
-
+
• • •
w+1
w
extending
truncating
Notes: Truncating from a w-bit number to a k-bit one – drop the high-order w-k bits; clearly can alter its value

## Slide 75: Break + Practice
Convert 16-bit 0x3427 to an 8-bit signed integer
Convert 8-bit 0xF0 to a 16-bit signed integer
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 76: Break + Practice
Convert 16-bit 0x3427 to an 8-bit signed integer
  Process: truncate extra bits
  Answer is 0x27
Convert 8-bit 0xF0 to a 16-bit signed integer
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 77: Break + Practice
Convert 16-bit 0x3427 to an 8-bit signed integer
  Process: truncate extra bits
  Answer is 0x27
Convert 8-bit 0xF0 to a 16-bit signed integer
  Process: sign extend. Is the most-significant bit one? Yes!
  Answer is 0xFFF0
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 78: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings

## Slide 79: Encoding strings (The C way)
Represented by array of characters
  Each character encoded in ASCII format
  NULL character (code 0) to mark the end
Compatibility
  Byte ordering not an issue (data all single-byte!)
  ASCII text files generally platform independent
    Except for different conventions of line termination character(s)!
char S[6] = "18243";
Big-Endian
Little-Endian
0x31
0x38
0x32
0x34
0x33
0x00
0x31
0x38
0x32
0x34
0x33
0x00

## Slide 80: Encoding color
RGB colors
  3-byte values
  First byte is Red, then Green, then Blue
Usually specified in hexadecimal
  #FF0000 -> maximum red, zero green or blue
  #4E2A84 -> 1/4 red, 1/8 blue, 1/2 green (Northwestern Purple)
224 possible colors = 16777216 colors

## Slide 81: Interpreting file contents
Collections of data
  Usually in permanent storage on your computer
Regular files
  Arbitrary data
  Think of as a big array of bytes
Non-regular files would be directories, symbolic links, or other less used things

## Slide 82: What about different types of regular files?
Text files versus Executables versus Tar files
  All just differing patterns of bytes!
  It really is just all data. The meaning is in how you interpret it.
Executable File
Archive (tar)

## Slide 83: Identifying regular files
file in Linux command line can help determine the type of a file
  https://github.com/file/file

## Slide 84: Encoding time
Unix time:
  32-bit signed integer counting seconds elapsed since initial time
  Initial time was January 1st at midnight UTC, 1970
Current Unix time (as of last editing this slide): 1672850392
  Negative numbers would mean times before 1970
Problem: when does Unix time hit the maximum value?
  2147483647 seconds from January 1st 1970
  Result: January 19th, 2038
  This is the “Year 2038 Problem”

## Slide 85: Bonus xkcd comic
https://xkcd.com/2697/

## Slide 86: Outline
Binary and Hex
Memory
Encoding
Integer Encodings
  Signed Integers
  Converting Sign
  Converting Length
Other encodings