## Slide 1: Lecture 18 Input/Output Devices
CS213 – Intro to Computer Systems
Branden Ghena – Fall 2023
Slides adapted from: Hester, Tarzia (Northwestern), Bryant, O’Hallaron (CMU), Dutta, Garcia, Weaver (UC Berkeley), Venkataraman (Wisconsin), Singh (Princeton)

## Slide 2: Administrivia
Homework 4 due today!
  Don’t forget about it
  Good practice for midterm 2
SETI Lab due on Thursday!
  Beware, it’ll take quite a while to get feedback close to the deadline
  Run seti-eval as sparingly as possible
  It will give you very similar results to seti-perf

## Slide 3: Common SETI Lab Errors
Straight line performance
  Often better than 1.02x right away and graph does not have a curve shape
  Doesn’t vary thread count per the program argument
Stuck at 0.3x
  Usually didn’t optimize
  Or maybe just optimized p_band_scan.c but not anything it relies on
No Carrier Match
  Your code output didn’t match the original band_scan
No Alien Match
  You didn’t correctly determine which of your generated signals is alien

## Slide 4: Administrivia
Midterm 2 next week Wednesday
  12:00-1:20 pm in this classroom (Tech Auditorium)
  Allowed two sheets of standard paper, front and back, for notes
    You may reuse your notes from last time as the first sheet if you want or you can make entirely new notes sheets
  Material from weeks 5 and onwards
    x86-64 Assembly Procedures through I/O & Networks (Thursday)
    Homeworks 3 and 4
    Bomb Lab, Attack Lab, and SETI Lab

## Slide 5: Today’s Goals
Introduce Input and Output (I/O) in computer systems
Consider application-level I/O details
Explore OS / microcontroller approaches to I/O
  How to talk to devices
  Interaction patterns with devices
  Device drivers

## Slide 6: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 7: Devices are the point of computers
Traditional systems need to receive input from users and output responses
  Keyboard/mouse
  Disk
  Network
  Graphics
  Audio
  Various USB devices
Embedded systems have the same requirement, just more types of IO
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 8: Devices are core to useful general-purpose computing
Computer
Mouse
Keyboard
Ethernet
Bluetooth
Monitor
Headphones
Ethernet
Bluetooth
Input
Output

## Slide 9: Devices are essential to cyber-physical systems too
Computer
Lidar
Inertial Measurement Unit
Camera
CAN
Throttle Control
Brake Control
Wheel Rotation
CAN
Input
Output

## Slide 10: Device access rates vary by many orders of magnitude
Rates in bit/sec
System must be able to handle each of these
  Sometimes needs low overhead
  Sometimes needs to not wait around
Device | Behavior | Partner | Data Rate (Kb/s)
Keyboard | Input | Human | 0.2
Mouse | Input | Human | 0.4
Microphone | Output | Human | 700.0
Bluetooth | Input or Output | Machine | 20,000.0
Hard disk drive | Storage | Machine | 100,000.0
Wireless network | Input or Output | Machine | 300,000.0
Solid state drive | Storage | Machine | 500,000.0
Wired LAN network | Input or Output | Machine | 1,000,000.0
Graphics display | Output | Human | 3,000,000.0

## Slide 11: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 12: Linux abstraction: everything is a file!
Application-level: treat devices like files
  They can be read and written
  They may be created or destroyed (plugged/unplugged)
  They can be created in hierarchies. Example:
    SATA devices
      SSD
    USB devices
      Webcam
      Microphone

## Slide 13: Linux device classes
Character devices
  Accessed as a stream of bytes (like a file)
  Example: Webcam, Keyboard, Headphones
Block devices
  Accessed in blocks of data (like a disk)
  Can hold entire filesystems
  Example: Disks, Flash drives
Network interfaces
  See CS340 (Computer Networking)
  Accessed through transfer of data packets
dev
char
block
net
Serial
Parallel
SATA
SCSI
Ethernet
WiFi
video
2D
3D

## Slide 14: Communication with devices
Must ask the OS to communicate with the device for us
  This is a job for system calls!
Which system calls? File I/O ones!
  Open/Close
  Read/Write
  Seek, Flush
  Ioctl
  And various others

## Slide 15: Accessing devices
Open/Close
  Inform device that something is using it (or not)
  Argument is path to device (like path to file)
  Get a file descriptor that the other operations act on
“/dev” directory is populated with devices

## Slide 16: Interacting with devices
Same read/write system calls you’ve seen before
Read
  ssize_t read(int fd, void *buf, size_t count);
Write
  ssize_t write(int fd, const void *buf, size_t count);
Seek doesn’t really make sense for most devices…

## Slide 17: Arbitrary device interactions
ioctl – I/O Control
  int ioctl(int fd, unsigned long request, ...);
Request number followed by an arbitrary list of arguments
  “request” may be broken in fields: command, size, direction, etc.
Catch-all for device operations that don’t fit into file I/O model
  Combine with “magic numbers” to form some special action
  Reset device, Start action, Change setting, etc.
  Read the device documentation to find these

## Slide 18: ioctl example - sounds through console
Simplified from: http://www.johnath.com/beep/beep.c
void play_beep(unsigned int repeats, float frequency) {
/* try to snag the console */
int console_fd = open("/dev/console", O_WRONLY);
for (unsigned int i=0; i<repeats; i++) { /* start beep */
if(ioctl(console_fd, KIOCSOUND, (int)(CLOCK_TICK_RATE/frequency)) < 0) {
perror("ioctl");
}
usleep(1000); /* wait... */
ioctl(console_fd, KIOCSOUND, 0); /* stop beep */
usleep(1000); /* wait... */
}
close(console_fd);
}

## Slide 19: Break + Open Question
What are some downsides of “everything is a file”?

## Slide 20: Break + Open Question
What are some downsides of “everything is a file”?
  Doesn’t allow devices to send data to us. Data needs to be requested
  Slow turnaround time for detecting some action by a device
    Like a mouse click
  Not all devices map to files well
    Microphone/Webcam work okay, just chunks of data to be read
    Input devices not so much: keyboard, mouse, touchscreen
      These are often handled directly by the OS instead

## Slide 21: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 22: Going deeper: how to talk to devices
What if you are writing the OS? How does it talk to devices?
Or what if you don’t have an OS at all and want to control devices directly?
  Example: embedded systems

## Slide 23: How to interact with I/O devices
A device is really a miniature computer-within-the-computer
  Has its own processing, memory, software
We can mostly ignore that and deal with its interface
  Called registers (actually are from EE perspective, but you can’t use them)
  Read/Write like they’re data

## Slide 24: Example powered device: Real Time Clock
Battery-backed up clock on computer motherboard
Keeps sense of time when computer is off
Resynchronized when the computer is awake
Index | Contents | Range
0x00 | Seconds | 0-59
0x02 | Minutes | 0-59
0x04 | Hours | 0-23 in 24-hour mode, 1-12 in 12-hour mode, highest bit set if PM
0x06 | Weekday | 1-7, Sunday =1
0x07 | Day of Month | 1-31
0x08 | Month | 1-12
0x09 | Year | 0-99
https://www.singlix.com/trdos/archive/pdf_archive/real-time-clock-nmi-enable-paper.pdf
Registers:

## Slide 25: Two options for reading/writing device registers
Special assembly instructions
Treat like normal memory

## Slide 26: Two options for reading/writing device registers
Special assembly instructions
Treat like normal memory

## Slide 27: Port-Mapped I/O (PMIO): special assembly instructions
x86 IN and OUT instructions
  Privileged instructions (kernel mode only)
  Two arguments: destination and data register
Each device is mapped to some port address
  IN and OUT instructions interact with interface
  IN <PORT NUMBER>, <REGISTER>
  OUT <REGISTER>, <PORT NUMBER>

## Slide 28: Example powered device: Real Time Clock
Example: read current value from real-time clock
// read seconds
mov $0, %al out %al, $0x70 in $0x71, %al
Index | Contents | Range
0x00 | Seconds | 0-59
0x02 | Minutes | 0-59
0x04 | Hours | 0-23 in 24-hour mode, 1-12 in 12-hour mode, highest bit set if PM
0x06 | Weekday | 1-7, Sunday =1
0x07 | Day of Month | 1-31
0x08 | Month | 1-12
0x09 | Year | 0-99
https://www.singlix.com/trdos/archive/pdf_archive/real-time-clock-nmi-enable-paper.pdf
Port Address

## Slide 29
Example I/O port map
This isn’t standardized, but these are some typical values.
https://wiki.osdev.org/Can_I_have_a_list_of_IO_Ports

## Slide 30: Check your understanding – PMIO in C
How would you access PMIO from a C program?

## Slide 31: Check your understanding – PMIO in C
How would you access PMIO from a C program?
  Need to use assembly!
  Hopefully with C function wrapper, like System Calls

## Slide 32: Annoying parts of Port-Mapped I/O
Special assembly instructions are hard to write in C
  Need some wrapper function that actually calls them
  Not really that big of an issue, but a little weird
Feels sort of like memory read/write, but isn’t
  Why not?
  Can we just put the “port address space” somewhere in memory?
    Could be a problem if we don’t have enough memory
    But today we have tons of extra physical address space laying around

## Slide 33: Two options for reading/writing device registers
Special assembly instructions
Treat like normal memory

## Slide 34: Memory-mapped I/O (MMIO): treat devices like normal memory
Certain physical addresses do not actually go to RAM
Instead, they correspond to I/O devices
  And any instruction that accesses memory can access them too!
x86-64 being the historical amalgamation that it is, uses both PMIO or MMIO depending on the device
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 35: Other details about MMIO
Devices are mapped into physical memory
  Usually only accessible by the operating system
  But could be directly placed in virtual memory for a process in very special cases
Devices are NOT memory though
  Need to be careful not to cache them
    Values being read could change, or reading could have an effect
  Cannot let compiler mess with our reads/writes either
    volatile keyword in C
Conceptually not really very different from PMIO
  Both just read/write to specific addresses the device is mapped to

## Slide 36: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 37: Simpler Memory-Mapped IO example: a microcontroller
A microcontroller is a single chip with a processor and memory
  Used for simple devices such as embedded systems
  Example use case: a Fitbit
Fitbit flex (circa 2013)
Features
  Counts your steps
  Reports via Bluetooth Low Energy
  Lights up some LEDs based on your goals
  Vibrates when its battery is low

## Slide 38: Fitbit teardown
https://www.ifixit.com/Teardown/Fitbit+Flex+Teardown/16050
Notes: Fitbit, Wearables, microcontrolles

## Slide 39: Fitbit circuit board front
Red (top)
  STMicro 32L151C6 Microcontroller
Blue (left)
  TI BQ24040 Battery Charger
Yellow (right)
  STMicro LIS2DH Accelerometer
Orange (bottom)
  Nordic nRF8001 Bluetooth Low Energy Radio
The back is uninteresting

## Slide 40: Fitbit as a computer
Computers usually need
  Processor
  Memory (RAM)
  Storage (Flash/SSD)
  External communication
    USB, Thunderbolt, SATA, HDMI, WiFi
  Power management
    Maybe batteries and charging
  Something to connect it all: motherboard
  Microcontroller
  Bluetooth radio
  Vibratory motor
  Battery and power management
  Circuit board

## Slide 41: Example microcontroller memory map
0x1000 bytes is plenty of space for each device (a.k.a. peripheral)
  1024 registers, each 32 bits
  No reason to pack them tighter than that
nRF52833 microcontroller

## Slide 42: Example: TEMP device on nRF52833 microcontroller
Internal temperature sensor
  0.25° C resolution
  Range equivalent to microcontroller chip (-40° to 105° C)
  Various configurations for the temperature conversion (ignoring)

## Slide 43: MMIO addresses for TEMP
What addresses do we need? (ignore interrupts for now)
  0x4000C000 – TASKS_START
  0x4000C100 – EVENTS_DATARDY
  0x4000C508 - TEMP

## Slide 44: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;

## Slide 45: Accessing addresses in C
What does this C code do?
*(uint32_t*)(0x4000C000) = 1;
  0x4000C000 is cast to an uint32_t* (a 32-bit unsigned integer pointer)
  Then dereferenced
  And we write 1 to it
  “There are 32-bits of memory at 0x4000C000. Write a 1 there.”

## Slide 46: Example code
To the terminal!
Let’s write it from scratch

## Slide 47: Example code (temp_mmio app)

## Slide 48: Break + relevant xkcd
https://xkcd.com/138/

## Slide 49: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 50: What do interactions with devices look like?
while STATUS==BUSY; Wait
  (Need to make sure device is ready for a command)
Write value(s) to DATA
Write command(s) to COMMAND
while STATUS==BUSY; Wait
  (Need to make sure device has completed the request)
Read value(s) from Data
This is the “polling” model of I/O.
“Poll” the peripheral in software repeatedly to see if it’s ready yet.

## Slide 51: Waiting can be a waste of CPU time
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
Imagine a keyboard device
  CPU could be waiting for minutes before data arrives
  Need a way to notify CPU when an event occurs
    Interrupts!

## Slide 52: Interrupts
What is an interrupt?
  Some event which causes the processor to stop normal execution
  The processor instead jumps to a software “handler” for that event
    Then returns back to what it was doing afterwards
What causes interrupts?
  Hardware exceptions
    Divide by zero, Undefined Instruction, Memory bus error
  Software
    Syscall, Software Interrupt (SWI)
  External hardware
    Input pin, Timer, various “Data Ready”

## Slide 53: Interrupts, visually
Some code that’s executing

## Slide 54: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code

## Slide 55: Interrupts, visually
Some code that’s executing
Interrupt triggers!
Interrupt handler code
Continue original code
Interrupts are a form of exceptional control flow

## Slide 56: Hardware devices can generate interrupts
Each device maps to some number of hardware interrupts
Done at system boot time for x86-64
  Discover devices
  Map devices into address space
  Map interrupts for devices
Hardcoded into hardware for microcontrollers

## Slide 57: Interrupts allow waiting to happen asynchronously
Prior code example was synchronous
  Nothing else continued on the processor until access was complete
  Good for very fast devices (like the real-time clock, that just returns data)
  We call this “Polling”
With interrupts, device handling is now asynchronous
  Access occurs in the background and processor can do something else
  Good for very slow devices (Disk)
  Comes with all the downsides of concurrency though…

## Slide 58: Microcontroller TEMP device supports interrupts!
Can either loop while checking the EVENTS_DATARDY register
Or could enable an interrupt from the device
  And only bother reading data when it is ready

## Slide 59: When should a system use polling versus interrupts?
Polling
  Great if the device is going to respond immediately (like 1 cycle)
  Important if we need to respond very quick (less than a microsecond)
Interrupts
  Great if we’ll need to wait a long time for status to change
  Still responds pretty quickly, but not immediately
    Needs to context switch from running code to interrupt handler

## Slide 60: Check your understanding – writing to GPU
Let’s say that a GPU has MMIO registers for an entire 4 KB page
  Takes 100 ns to write each word (8 bytes) of memory
Assuming that we’re just writing all zeros (ignore reading from memory), how long does it take to write a page to MMIO?

## Slide 61: Check your understanding – writing to GPU
Let’s say that a GPU has MMIO registers for an entire 4 KB page
  Takes 100 ns to write each word (8 bytes) of memory
Assuming that we’re just writing all zeros (ignore reading from memory), how long does it take to write a page to MMIO?
  4 KB / 8 B = 512 writes * 100 ns / write = 51 µs
    (For a 3 GHz processor, that’s ~150,000 cycles)

## Slide 62: Direct Memory Access (DMA)
Even with interrupts, providing data to the peripheral is time consuming for transferring lots of data
  Need to be interrupted every byte, to copy the next byte over
DMA is an alternative method that uses hardware to do the memory transfers for the processor
  Software writes address of the data and the size to the peripheral
  Peripheral reads data directly from memory
  Processor can go do other things while read/write is occurring

## Slide 63: Programmed I/O versus Direct Memory Access
SATA Controller
SATA Controller
Disk
Disk

## Slide 64: General-purpose DMA

## Slide 65: Full peripheral interaction pattern
Configure the peripheral
Enable peripheral interrupts
Set up peripheral DMA transfer
Start peripheral
Continue on to other code
Interrupt occurs, signaling DMA transfer complete
Set up next DMA transfer
Continue on to other code, and repeat

## Slide 66: Break + Open Question
What kinds of peripherals/devices should you use the DMA for?

## Slide 67: Break + Open Question
What kinds of peripherals/devices should you use the DMA for?
  Anything where there is a lot of data coming in over a period of time
    Either a big buffer of lots of data, like a radio message
    Or a bunch of individual samples, coming in quickly
  Devices
    Canonical example from general computing: disks (HDD/SSD)
    Messages to/from other devices (radios, wired busses)
    Sensor readings (if read quickly)

## Slide 68: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers

## Slide 69: What is a device driver?
A device driver is the software in the Operating System that manages a specific device
  Modern computers come with MANY of these pre-installed
  And have the ability to automatically find many others if needed
Can be generic “keyboard driver” or very specific “Ricoh IM C3000 printer driver”
Source of many bugs in the in Operating System
  Due to amount and variety of them

## Slide 70: How should we write driver software?
There are various knobs available to us from hardware
  Polling, Interrupts, DMA
There are also various software interface design
  Synchronous
  Asynchronous Callbacks

## Slide 71: Synchronous device drivers
Synchronous functions
  Function call issues a command
  Does not return until action is complete and result is ready
Example: most functions we’re used to
  sqrt() for example
  printf() also usually works this way (with some exceptions)
For microcontrollers: Arduino interfaces are usually like this!
  Easy to get started with and understand

## Slide 72: Downside of synchronous code: the waiting
How long will it take until the function returns?
  Immediately, seconds, minutes?
What if there’s an error and the device never responds?
  More advanced interface could include a timeout option
Synchronous designs require other synchronous designs
  We can build synchronous interfaces from asynchronous ones
  But we can’t go the other way

## Slide 73: Asynchronous drivers
Goal: let the hardware run on its own and have the code get back to it later
Challenge: programmers don’t think that way
Other challenge: how do we “get back to it later”?
  One solution: Callbacks

## Slide 74: Callbacks
Callbacks reuse a similar idea to interrupts
  When the event occurs, call this function
General pattern
  Call driver function with one argument being a function pointer
  Driver sets up interaction and returns immediately
  Later the event happens and the driver calls the function pointer

## Slide 75: Callback functions
uint32_t timer_start( uint32_t microseconds, void (*callback_fn)(void*), void* context );
timer_start(duration, my_timer_handler, context);
“Context” is often provided as well (void*)
  Ability for caller to pass an argument for the callback function
  Often a pointer to a position in a structure or a shared variable to modify
  Similar to idea of closures in other languages

## Slide 76: Example with callbacks (could be temp driver)
…

## Slide 77: CE346 – Microprocessor System Design
Embedded Systems
  How does hardware work?
  How do we write drivers to interact with hardware from software?
  Sensing and sensors
Big open-ended project: anything with inputs and outputs
Project demos: Tuesday of exam week (12/5) from 11-5 in Mudd 3514
  Public! Anyone is welcome to stop in
  Not formal presentations, just demos you can play with

## Slide 78: Outline
Input/Output Motivation
Application-Level Input/Output
Talking to Devices
  MMIO Example
Device Interaction Patterns
Device Drivers