## Slide 1: Lecture 03 Data Operations
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2023
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
You should all have access to Piazza and Gradescope
  Contact me via email immediately if you don’t!!
Office hours are now running
  See Canvas homepage for office hours times
  Mix of in-person (M/W/F) and online (T/R) hours
  Today: Elder 30 2-4pm, Tech M128 5-8pm
    Each staffed by 3+ PMs

## Slide 3: Administrivia
Homework 1 due by end-of-day Wednesday
  Submit on Gradescope
Pack Lab should be out later today!
  Sometime this evening
You’ll do Pack Lab on one of the EECS servers
  Usually we use Moore, but any should be fine for this lab
  SSH + Command Line interface
  See Piazza post for details on remote access
  See Piazza post for tutorials on command line

## Slide 4: Today’s Goals
Explore operations we can perform on integers and more generally on binary numbers
Understand the edge cases of those operations

## Slide 5: C versus the hardware
Operations you can perform on binary numbers have edge conditions
  Usually going above or below the bit width
If we say what happens in that scenario, it’ll be what “the hardware” (i.e., a computer) does
  In today’s examples, pretty much every computer does the same thing
That is not the same as what C does
  Unclear choices are left as: UNDEFINED BEHAVIOR 😱
  Which is to say, the compiler can make any choice it wants

## Slide 6: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 7: Unsigned Addition
Like grade-school addition, but in base 2, and ignores final carry
  If you want, can do addition in base 10 and convert to base 2. Same result! But here we’re going to understand what the hardware is doing.
Example: Adding two 4-bit numbers
  510 + 310 = 810 ✔
0101
+ 0011
1
0
0
0
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 8: Unsigned Addition and Overflow
What happens if the numbers get too big?
Example: Adding two 4-bit numbers
  1310 + 310 = 1610
    Too large for 4 bits! Overflow
    Result is the 4 least significant bits (all we can fit): so 010
    Gives us modular (= modulo) behavior: 16 modulo 24 = 0
1101
+ 0011
0
0
0
0
1
1
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 9: Modulo behavior in binary numbers
1000
0000
0100
1100
0011
0010
0001
0111
0110
0101
1011
1010
1001
1111
1110
1101
+1
-1
10000

## Slide 10: Unsigned addition is modular
Implements modular arithmetic
  UAddw(u , v) = (u + v) mod 2w
Need to drop carry bit, otherwise results will keep getting bigger
  Example in base 10: 8010 + 4010 = 12010 (2-digit inputs become a 3-digit output!)
Warning: C does not tell you that the result had an overflow!
  Unsigned addition in C silently behaves like modular arithmetic
• • •
• • •
u
v
+
• • •
u + v
• • •
True Sum: w+1 bits
Operands: w bits
UAdd Result: w bits
UAddw(u , v)
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 11: Signed (2’s Complement) Addition
Works exactly the same as unsigned addition!
  Just add the numbers in binary, and the result will work out
Signed and unsigned sum have the exact same bit-level representation
  Computers use the same machine instruction and the same hardware!
  That’s a big reason 2’s complement is so nice! Shares operations with unsigned
Notes: The w-bit two’s complement sum of two numbers has the exact same bit-level representation as the unsigned sum; most computers use the same machine instruction

## Slide 12: Signed addition example
Same addition method as unsigned
Example: Adding two 4-bit signed numbers
  -510 + 310 = -210 ✔
1011 (-8 + 3 = -5)
+ 0011 ( +3)
1 (-8 + 6 = -2)
0
1
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 13: Combining negative and positive numbers
Overflow sometimes makes signed addition work!
Example: Adding two 4-bit signed numbers
  -310 + 310 = 010
    Too large for 4 bits! Drop the carry bit
    Result is what we expect as long as we truncate
1101 (-8 + 5 = -3)
+ 0011 ( +3)
0
0
0
0
1
1
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 14: Signed addition and overflow
Overflow can still happen in signed addition though
Example: Adding two 4-bit signed numbers
  510 + 310 = -810 (+8 is too big to fit)
  Remember, this was also unsigned 510 + 310 = 810
0101
+ 0011
1
0
0
0
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 15: Signed addition and negative overflow
Overflow also happens in the negative direction
Example: Adding two 4-bit signed numbers
  -510 + -510 = +610 (-10 was too small to fit)
1011
+ 1011
10
0
1
1
1
1
1
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 16: Overflow: hardware vs C standard
Hardware implementations for unsigned and signed addition are the same
  Both implement modular arithmetic
Unsigned overflow in C is defined as modular arithmetic
Signed overflow in C is UNDEFINED BEHAVIOR
  Compiler probably does modular result
  But there are no promises about this and it can make assumptions
  So don’t rely on it

## Slide 17: Special boss in Chrono Trigger
Dream Devourer
  Special boss in the Nintendo DS edition
Wanted to make it even more challenging
  32000 hit points
  Takes forever to defeat
Hit points stored as a 16-bit signed integer
  Range: -32768 to +32767
How do speedrunners defeat the boss?

## Slide 18: Chrono Trigger signed overflow bug
Solution: heal it
Hit points go negative and it dies

## Slide 19: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 20: Negating a number
In C:
  x = -y;
Operation
  Determine the negative, signed version of the number (two’s complement)
  Hardware method: flip it and add one

## Slide 21: Negating via Complement & Increment
Claim: The following is true for 2’s complement
  ~x + 1 == -x
Complement
  Observation: ~x + x == 1111…112 == -1
Increment
  ~x + 1 == ~x + x - x + 1 == -1 - x + 1 == -x
  ~x + 1 == -x
Example, 4 bits: 610 = 01102
  Complement: 10012 → Increment = 10102 = -8 + 2 = -610
1
0
0
1
0
1
1
1
x
0
1
1
0
1
0
0
0
~x
+
1
1
1
1
1
1
1
1
-1

## Slide 22: Subtraction in two’s complement
Subtraction becomes addition of the negative number
  5 – 3 = 5 + -3 = 2
Both unsigned and signed subtraction
  Convert subtractor to its two’s complement negative form
    i.e., negate it
  Then do addition
  Treat result as an unsigned number
0101 (+5)
+ 1101 ( -3)
10
0
0
1
1
1
1

## Slide 23: C rules vs hardware rules
Exact same overflow rules apply
Unsigned subtraction can wrap below zero to make a large number
  Modular arithmetic
Signed subtraction is UNDEFINED BEHAVIOR
  And therefore should not be trusted

## Slide 24: Break + practice
Adding two 8-bit numbers:
  Also determine the decimal version of the result
00010101
+ 10110001

## Slide 25: Break + practice
Adding two 8-bit numbers:
  Also determine the decimal version of the result
00010101
+ 10110001
1
1
1
1
0
1
0
0
1
0
1
128+64+4+2 = 198
128+32+16+1 = 177
16+4+1 = 21
OR
-128+64+4+2 = -58
-128+32+16+1 = -79
16+4+1 = 21
Unsigned encoding
Signed encoding

## Slide 26: Break + practice
Adding two 8-bit numbers:
  Also determine the decimal version of the result
00010101
+ 10110001
1
1
1
1
0
1
0
0
1
0
1
128+64+4+2 = 198
128+32+16+1 = 177
16+4+1 = 21
OR
-128+64+4+2 = -58
-128+32+16+1 = -79
16+4+1 = 21
Unsigned encoding
Signed encoding
What about unsigned subtraction 21-79?
That would apply modulo arithmetic and result in the value 198

## Slide 27: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 28: Multiplication
Goal: Compute the Product of w-bit numbers x, y
  Either signed or unsigned
But, exact results can be bigger than w bits
  Double the size (2w), in fact!
  Example in base 10: 5010 * 2010 = 100010
    (2-digit inputs become a 4-digit output!)
As with addition, result is truncated to fit in w bits
  Because computers are finite, results can’t grow indefinitely

## Slide 29: Unsigned Multiplication
Standard Multiplication Function
  Equivalent to grade-school multiplication
  But ignores most significant w bits of the result
  As a person, we can do base 10 multiplication, convert to base 2, then truncate
Implements modular arithmetic like addition does
  UMultw(u , v) = (u · v) mod 2w
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
UMultw(u , v)
• • •

## Slide 30: Unsigned multiplication
Example: Multiplying two 4-bit numbers
                210 * 510 = 1010 ✔
0010
x 0101
0010
0000
0010
+ 0000
0001010
0
00
000
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 31: Signed (2’s Complement) Multiplication
Standard Multiplication Function
  Ignores most significant w bits
  Lower bits still give the correct result
    So we can use same machine instruction for both!
    Again, that’s one reason why 2’s complement is so nice
In C, signed overflow is undefined
  ...but probably you’ll see the two’s complement behavior
• • •
• • •
u
v
*
• • •
u · v
• • •
True Product: 2*w bits
Operands: w bits
Discard w bits: w bits
TMultw(u , v)
• • •

## Slide 32: Signed multiplication
Example: Multiplying two’s complement 5-bit numbers
11110
x 00011
11110
0
+ 11110
What are these two 5-bit numbers?
-2
3
What is the result of this addition?
0
1
0
0
1
1
1
1011010
-210 * 310 = -610 ✔
Notes: If u + v < 2^w, the leading bit in the w+1-bit representation of the sum will be 0 so discarding it doesn’t change anything
If u + v > 2^w, the leading bit will equal 1 and discarding it will be the same as subtracting 2^w

## Slide 33: What about divide?
Annoying operation, not going to discuss in this class
  Similar to long division process
  Tedious and complicated to get right
I’ve worked on computers that don’t have hardware support for division at all!!
Important thing to remember is that integers don’t have fractional parts
  In C: 1/2 == 0
  We’ll need a new encoding for fractional numbers: floating point

## Slide 34: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 35: Boolean algebra
You’ve programmed with and and or in earlier classes
  Written && and || in C and C++
Boolean algebra is a generalization of that
  A mathematical system to represent (propositional) logic
  2 truth values: true = 1, false = 0
  3 operations: and = &, or = |, not (or complement) = ~

## Slide 36: Performing Boolean algebra
Follow the rules for each operation to compute results
  Rules are the like those you know from programming
  OR: | AND: & NOT: ~ 1: True 0: False
(1 | 0) & 0
1 & 0
0
(1 & 1) & ~(0 | 0)
1 & ~(0)
1 & 1
1

## Slide 37: Truth tables for Boolean algebra
For each possible value of each input, what is the output
  Column for each input
  Column for the output operation
A & B |  | 
A | B | A & B
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1
A ¦ B |  | 
A | B | A ¦ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
~A | 
A | ~A
0 | 1
1 | 0

## Slide 38: Exclusive Or
Some operations aren’t available as C logical operators (confused students to think it wasn’t available in c at all)
  Xor ^ - either A or B, but not both
We can build Xor out of &, |, and ~
  A^B = (~A & B) | (A & ~B)
    (exactly one of A and B is true)
  A^B = (A | B) & ~(A & B)
    (either is true but not both are true)
  The two definitions are equivalent
    Produce the same Truth Table
A ^ B |  | 
A | B | A ^ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0

## Slide 39: Practice problem
(A & B) ¦ B |  | 
A | B | (A&B)¦B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 

## Slide 40: Practice problem
(A & B) ¦ B |  | 
A | B | (A&B)¦B
0 | 0 | 
0 | 1 | 
1 | 0 | 
1 | 1 | 
0
0
1
1

## Slide 41: Practice problem
(A & B) ¦ B |  | 
A | B | (A&B)¦B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 0
1 | 1 | 1
This is equivalent to B (A has no influence on the solution)

## Slide 42: De Morgan’s Law
We can express Boolean operators in terms of the others
De Morgan’s laws: allow swapping & with |
  A & B = ~(~A | ~B) → ~(A & B) = ~A | ~B
    (neither A nor B is false)
  A | B = ~(~A & ~B) → ~(A | B) = ~A & ~B
    (A and B are not both false)
  Useful for simplifying logical statements

## Slide 43: Generalized Boolean algebra
Boolean operations can be extended to work on vectors of bits (i.e., bytes)
Operations are applied one bit at a time: bitwise
All of the properties of Boolean algebra still apply
  Relationships between operations, etc.
Bitwise operations are usable in C: &, |, ~, ^
  Can operate on any integer type (long, int, short, char, signed or unsigned)
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01000001
01111101
00111100
10101010

## Slide 44: Warning: bitwise operations are NOT logical operations
Logical operations in C: ||, &&, ! (logical Or, And, and Not)
  Only operate on a single bit
    View 0 as “False”
    View anything nonzero as “True”
    Always return 0 or 1
  Short-circuit evaluation: only checks the first operand if that is sufficient
Examples
  !0x41 -> 0x00 !0x00 -> 0x01 !!0x41 -> 0x01
  0x59 && 0x35 -> 0x01
  (p != NULL) && *p (short circuit avoids null pointer access)
Don’t confuse the two!! It’s a common C mistake
Useful for turning many bits into 1 bit

## Slide 45: Break + Practice
0x37 | 0xAA
0x06 ^ 0xFF
A ^ B |  | 
A | B | A & B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A ¦ B |  | 
A | B | A ¦ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 46: Break + Practice
0x37 | 0xAA
0x06 ^ 0xFF
00110111
| 10101010
10111111
00000110
^ 11111111
11111001
A ^ B |  | 
A | B | A & B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 0
A ¦ B |  | 
A | B | A ¦ B
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1
Hex | Decimal | Binary
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 47: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 48: Left Shift: x << y
Shift bit-vector x left by y positions
  Throw away extra bits on left
  Fill empty bits with 0
    Same behavior for signed or unsigned
Equivalent to multiplying by 2y
  And then taking modulo (i.e. truncating overflow bits)
Undefined behavior in C when:
  y < 0, or y ≥ bit_width(x)
  Also when some non-0 bits get shifted off (probably they get truncated)
00000010
Argument x
00010000
<< 3
10100010
Argument x
00010000
<< 3
00000010000
00000010000
10100010000
10100010000
Notes: For x << k, what is the effect of the shift if k >= w, the number of bits of x data type?
e.g.
x << 32
x >> 36
x >> 40
For C, nothing standard but most commonly use lower log_2 w bits of the shift; for Java that’s a rule; effectively that’s k mod w, so for a 32b data type
x << 32 same as x << 0
x >> 36 same as x >> 4
x >> 40 same as x >> 8

## Slide 49: Right Shift: x >> y
Shift bit-vector x right y positions
  Throw away extra bits on right
But how to fill the new bits that open up?
  Will depend on signed vs unsigned
Unsigned: Logical shift
  Always fill with 0’s on left
Signed: Arithmetic shift
  Replicate most significant bit on left
  Necessary for two’s complement integer representation (sign extension!)
Undefined behavior in C when:
  y < 0, or y ≥ bit_width(x)
01100010
Argument x
00011000
Logi. >> 2
00011000
Arith. >> 2
10100010
Argument x
00101000
Logi. >> 2
11101000
Arith. >> 2
00011000
00011000
00011000
00011000
00101000
11101000
00101000
11101000
Notes: For x << k, what is the effect of the shift if k >= w, the number of bits of x data type?
e.g.
x << 32
x >> 36
x >> 40
For C, nothing standard but most commonly use lower log_2 w bits of the shift; for Java that’s a rule; effectively that’s k mod w, so for a 32b data type
x << 32 same as x << 0
x >> 36 same as x >> 4
x >> 40 same as x >> 8

## Slide 50: Practice shifting in C
unsigned char x = 0b10100010;
x << 3 = ?
0b00010000
Note:
GCC supports the prefix 0b for binary literals (like 0x… for hex) directly in C.
This is not part of the C standard! It may not work on other compilers.
0b00101000
0b11101000
signed char x = 0b10100010;
x >> 2 = ?
unsigned char x = 0b10100010;
x >> 2 = ?
Steps:
0b10100010000
0b10100010000
Steps:
0b0010100010
0b0010100010
Steps:
0b1110100010
0b1110100010

## Slide 51: Concept: Not all operations are equally expensive!
Some operations are pretty simple to perform in hardware
  E.g., addition, shifting, bitwise operations
  Also true of doing the same by hand on paper
Others are much more involved
  E.g., multiplication, or even more so division
  Consider long multiplication / long division; quite tedious!
  Hardware is not doing the exact same thing, but similar principle
Trick: try to replace expensive operations with simple ones!
  Doesn’t work in all cases, but often does when mult/div by constants

## Slide 52: Shift to divide
Division by powers of two could be shifts
  unsigned int x = y / 2; unsigned int x = y >> 1;
Even more important because division is a complicated operation
  Multiply is implemented in (relatively) simple hardware on most systems
  Compiler might actually translate your divide by powers of two into shift operations though!
Warning: rounding needs to be handled correctly for signed numbers and division
  See bonus slides

## Slide 53: Compilers automatically chose the best operations
Should you use shifts instead of multiply/divide in your C code?
  NO
Just write out the math
  Math is more readable if that’s what you meant
  Compiler automatically converts code for you for best performance
These two mean the same thing, but one is way more understandable
    int x = y * 32;
    int x = (y << 5);

## Slide 54: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 55: Bit Masking
How do you manipulate certain bits within a number?
Combines some of the ideas we’ve already learned
  ~, &, |, <<, >>
Steps
  Create a “bit mask” which is a pattern to choose certain bits
  Use & or | to combine it with your number
  Optional: Use >> to move the bits to the least significant position

## Slide 56: Bit mask values
Selecting bits, use the AND operation
  1 means to select that bit
  0 means to not select that bit
Writing bits
  Writing a one, use the OR operation
    1 means to write a one to that position
    0 is unchanged
  Writing a zero, use the AND operation
    0 means to write a zero to that position
    1 is unchanged
Select bottom four bits:
num & 0x0F
Set 6th bit to one:
num | (1 << 6)
num | (0b01000000)
Clear 6th bit to zero: num & (~(1 << 6))
num & (~(0b01000000))
num & (0b10111111)

## Slide 57: Example: swap nibbles in byte
Nibble - 4 bits (one hex digit)
  Input: 0x4F -> Output 0xF4
  Method:
    1. Shift and select upper four bits
    2. Shift and select lower four bits
    3. Combine the two nibbles
    uint8_t lower = input >> 4;
    uint8_t upper = input << 4; // lower bits zeros
    uint8_t output = upper | lower; // combines two halves
What are the values of the new upper bits?
Unsigned -> Will be zero
Shifting implicitly zero’d out irrelevant bits. Otherwise we would have needed an & operation.

## Slide 58: Example: selecting bits
Select bits 2 and 3 from a number
Input: 0b01100100
0b01100100
Mask: 0b00001100
0b01100100
& 0b00001100
0b00000100
Finally, shift right by two to get the values in the least significant position:
0b00000001
In C: result = (input & 0x0C) >> 2;

## Slide 59: Outline
Integer Operations
  Addition
  Negation and Subtraction
  Multiplication and Division
Binary Operations
  Boolean Algebra
  Shifting
  Bit Masks

## Slide 60: Outline
Dividing with bit shift
Bonus material isn’t required and won’t be on an exam
  Unless it becomes main lecture material in a different lecture
Usually the material is just for students who want more depth
  As is the case here

## Slide 61: Unsigned Power-of-2 Divide with Right Shift
Quotient of unsigned by power of 2
  u >> k gives  u / 2k 
  Uses logical shift
  Pink part would be remainder / fractional part (right of the point)
    Shift just drops it: equivalent to rounding down
0
0
1
0
0
0
•••
u
2k
/
u / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
0
0
•••
•••
 u / 2k 
•••
Result:
0
0
0
0
•••
0
.
Binary Point
 x  : round x down
 x  : round x up

## Slide 62: Signed Power-of-2 Divide with Shift (Almost)
Quotient of signed by power of 2
  x >> k gives  x / 2k 
  Uses arithmetic shift
  Also rounds down, again by dropping bits
    But signed division should round towards 0! (that’s its math definition)
    That means rounding up for negative numbers!
Example, 4 bits: -6 / 4 = -1.5 (should round towards 0, to -1)
  10102 >> 2 = 11102 = -210
  Rounds the wrong way!
0
0
1
0
0
0
•••
x
2k
/
x / 2k
Division:
Operands:
•••
k
•••
•••
•••
0
•••
•••
RoundDown(x / 2k)
•••
Result:
.
Binary Point
0
•••

## Slide 63: Correct Signed Power-of-2 Divide
Want  x / 2k  (round towards 0)
  Math identity: x / y =  (x + y - 1) / y 
  Compute negative case as (x+2k-1)/ 2k  → gets us correct rounding!
  Computing both cases in C: (x<0 ? (x + (1<<k)-1) : x) >> k
    Biases dividend toward 0
Case 1: No rounding
Example, 4 bits: -8 / 22 = -2 bias = (1<<2)-1 = 3
  (1000 + 0011) >> 2 = 1011 >> 2 = 1110 = -210 (correct, no rounding)
Divisor:
Dividend:
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
0
0
0
•••
1
•••
0
1
1
•••
.
Binary Point
1
0
0
0
1
1
1
•••
+2k –1
•••
1
1
1
•••
1
•••
1
1
1
•••
    Biasing has no effect; all affected bits are dropped
all bits at positions 0...(k-1) are 0
Notes: Ceiling (x / y) = floor (x + y - 1) / y)

## Slide 64: Correct Signed Power-of-2 Divide (Cont.)
Example, 4 bits: -6 / 22 = -1 bias = (1<<2)-1 = 3
  (1010 + 0011) >> 2 = 1101 >> 2 = 1111 = -110 (correct, rounds towards 0)
Compiler does that for you (but you need to be able to read it!)
Divisor:
Dividend:
Case 2: Rounding
0
0
1
0
0
0
•••
x
2k
/
 x / 2k 
•••
k
1
•••
•••
1
•••
0
1
1
•••
1
0
0
0
1
1
1
•••
+2k –1
•••
1
•••
•••
    Biasing adds 1 to final result; just what we wanted
•••
Incremented by 1
Incremented by 1
.
Binary Point
some bits at positions 0...(k-1) are 1