## Slide 1: Lecture 11 Memory Hierarchy
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2023
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Business as usual
  Homework 3 due Wednesday
  Attack Lab due next week Wednesday
Topics remaining in class
  Memory System (Hierarchy, Caches, Virtual Memory)
  Applications (Concurrency, Processes, Virtual Memory)
  Other Systems Topics (Compilers, Networks)

## Slide 3: Changing the focus of CS213
So far in class we’ve focused on how computers do things
  Represent data
  Run instructions
Now we’re focusing on how to improve those things
  Secure (last lecture plus some stuff in two weeks)
  Efficient (today and next week)
As we’ll show today, the most important thing to speed up is memory
  It is possible and hardware does so already
  Software can be designed to take advantage of this

## Slide 4: Today’s Goals
Explore the memory systems available in modern computers
  Understand capabilities and limitations of each
Discuss the memory hierarchy
  How it improves performance through caching
Describe software patterns that caching is designed to support
Bonus: assembly-to-transistors deep-dive

## Slide 5: Outline
Memory Technologies
Memory Hierarchy
Caches
Locality of Reference

## Slide 6: Storage in a Computer System
Data can be stored in different places
  Registers, caches, memory, disk, etc.
Hugely different characteristics
  Storage size
    x86-64: 16 registers. 128 B total (not including FP registers, etc.)
    Memory is measured in GB, disks in TB
  Latency (i.e., time to access data)
    Registers are really fast, memory less so, disk is incredibly slow
  Cost per byte
    Registers are really expensive, disks are really cheap, memory somewhere in the middle
Each serves a different purpose in a system
  Can design systems to get the best of all worlds (in most cases)

## Slide 7: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus

## Slide 8: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Registers and Caches

## Slide 9: Register storage
x86-64
  16 registers (general-purpose) with 8 bytes each
  32 registers (special-purpose) with up to 64 bytes each
  Plus some other odds and ends (%rip, flags, segments, etc.)
128 bytes for general purpose registers
Order 2-3 kB for everything
Accesses are very fast. Within a single processor cycle
  Usually, 0.25-4 cycles per instruction

## Slide 10: Register technology: SRAM
Static RAM (SRAM)
  Each cell stores a bit in a bi-stable circuit, typically a six-transistor circuit
  Static – no need for periodic refreshing; keeps data while powered
  Relatively insensitive to disturbances such as electrical noise
    Energetic particles (alpha particles, cosmic rays) can flip stored bits
Fastest memory on computer
  Also most expensive and takes up most space per bit
  Typically used for registers and cache memories

## Slide 11: Caches
Memory in the processor that duplicates portions of RAM
  Goal: speed up accesses to frequently used data
  Complicated part: what’s in the cache at any given moment
    Many configurations to try to improve the “hit rate” on data
Not general-purpose memory
  Can’t be directly accessed and doesn’t have memory addresses
  Hardware automatically chooses what’s in the cache
Cache sizes
  Kilobytes to Megabytes of storage: ~1-10 MB total in modern processors

## Slide 12: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
RAM

## Slide 13: Main memory
The “RAM” in your computer
  Random Access Memory
  Can access any byte you want in “random” order
Typically measured in GB
  1-128 GB
  Some special purpose systems may have MUCH less
This is the “array of bytes” we’ve been using in assembly
  Program memory lives in RAM

## Slide 14: Main memory technology: DRAM
Dynamic RAM (DRAM)
  Each cell stores a bit as a charge in a capacitor
  Capacitors lose charge; each cell must be refreshed every 10-100 ms
  More sensitive to disturbances (EMI, radiation, …) than SRAM
Slower than SRAM, but cheaper and denser
  ~100x slower than registers
Typically used for main memory

## Slide 15: Accessing DRAM
Read entire row of data at a time
  Large in practice, kilobytes
Select actual bytes that are wanted
  Possibly modifying those bits
Write row back to memory
  Must always happen!
  Reading is destructive

## Slide 16: Connecting main memory and the processor
Data flows between main memory and processor over “buses”
  A collection of parallel wires that carry address, data, and control signals
  Typically shared by multiple devices
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
memory bus
Includes memory controller
movl A, %eax (load)
Processor writes address A to the bus
Memory writes data to the bus
Processor reads data from the bus
movl %eax, A (store)
Processor writes address A to the bus
Processor writes data to the bus
Memory reads data from the bus
system bus

## Slide 17: Sidebar: memory security is important
Data in RAM disappears without power
  But the rate depends on temperature, minutes to decay if frozen
  Cold Boot Attack: freeze RAM to remove from computer and steal contents

## Slide 18: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Disk: Hard drive or SSD

## Slide 19: Disk storage
Workhorse storage devices
  Terabytes in size in modern computers
  Milliseconds to read
    100,000x longer than reading from RAM
    10,000,000x longer than reading from registers
Used for filesystem storage
  Running programs do not directly use disk except when interacting with files
IBM 350 Disk Storage Unit
First disk drive, 1956
WD Red 6TB NAS, 2015
101.6mm
146.99mm
Storage?
5MB!
Basic mechanisms the same!

## Slide 20: Disk types

## Slide 21: Hard disk drive operation
The disk surface
spins at a fixed
rotational rate
(5400-15000 RPM)
spindle
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 22: Animation of Disk Access

## Slide 23: Writing bits to the platters
Note: most disks can only move the entire set of arms, not two sets of them

## Slide 24: Disk heads read/write data to the platters

## Slide 25: Accessing data on disk
Three-step process
  Read head needs to move to the right cylinder: seek time
  Platter turns until start of sector under the read head: rotational latency
  Sector passes under read head and data is read: transfer time
Time cost dominated by seek time and rotational latency
  Consequence: reading first bit of a sector is expensive
  But reading the rest of the sector is basically free!
When using disks, best to favor large sequential reads/writes
  Terrible for random access! (reading a little bit here, a little bit there)
  Fits file access well (read/write in order)
    But overall still really slow compared to main memory or registers

## Slide 26: Disk types

## Slide 27: Floating-gate transistors
Concept behind transistor-based non-volatile memory
  EPROM, EEPROM, and Flash
  High voltage on control gate creates charge on floating gate
  Charge on floating gate activates/deactivates transistor
High voltage degrades structure, leading it to eventually fail after enough writes

## Slide 28: Solid State Drives (SSDs)
Flash memory
  Just like Flash Drives
Pages: 2KB to 512KB, Blocks: 32 to 128 pages
Data read/written in units of pages
Page can be written only after its block has been erased
  Need to copy rest of the data to not lose it. Expensive!
A block wears out after repeated writes (10k – 100k writes) and can no longer be used
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
Notes: SSD based on flash memory (non-volatile memory based on EEPROM – electrically erasable programmable ROM)
Plugs into a standard disk slot – typically USB or SATA
Made of a few chips and a flash translation layer, a hw/firmware piece similar to a disk controller

## Slide 29: SSDs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    Order petabyte (1015 bytes) of random writes before they wear out
  More expensive per byte (but getting cheaper)
    2022: HDD $0.013 per GB, SSD $0.05 per GB (last year was $0.02 vs $0.09)
Applications
  Portable electronics (phones, tablets, etc.)
  Began to appear in desktops and servers circa 2007
  Now common on laptops as well
Biggest speed improvement to your computer:
Get an SSD

## Slide 30: Reading memory from disk
Data from disk is always read into Main Memory
Direct Memory Access (DMA)
  Processor starts a read and then returns to programs
  Disk performs the read, transfers data, then notifies processor when done
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface

## Slide 31: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus

## Slide 32: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works

## Slide 33: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works
  Secretly make it larger than it claims to be
    e.g. 200 GB when it claims to be 100 GB
  Behind the scenes move around memory as necessary so the device can still hold 100 GB even if half of the flash is
    Maintain a mapping of which data is located where

## Slide 34: Outline
Memory Technologies
Memory Hierarchy
Caches
Locality of Reference

## Slide 35: Computing timescales
Assuming 4 GHz processor, Instruction (with registers): 0.25 ns
Jeff Dean (Google AI): “Numbers Everyone Should Know”
Reminder:
1,000,000,000 ns per second

## Slide 36: Jim Gray’s storage latency analogy
How “far” is data for the CPU, converted to human scale
Storage
Distance
Time
Registers
On-chip cache
On-board cache
Main memory
Disk
Tape
In my apartment
Across the street
A few blocks away
In Milwaukee
On Mars
On Kepler-76b
~1 minute
2-4 minutes
10 minutes
1.5 hours
2 years
2000 years (at speed of light)
Jim Gray
Turing Award 1998

## Slide 37: The CPU-Memory gap
Increasing gap between DRAM, disk, and CPU speeds.
SRAM roughly keeping up
DRAM, disk and CPU
performance gap widening
Split reflects the introduction of multicores
Disk
DRAM
CPU
SSD
SRAM
Notes: In early 21st century computer manufacturers discover they couldn’t keep increasing CPU clock freq. because chips would consume too much power; answer was multicore – there you see the cycle times getting slower but effective cycle times keeping about the same improvement rate

## Slide 38: The CPU-Memory Gap
CPUs outspeed memory
  But they can’t compute on data they don’t have!
  If the CPU has to wait for data to reach it, it just sits idle!
    All these GHz don’t look so useful anymore, do they?
Challenge: get data to the CPU despite “slow” memory
  So the CPU can work at full speed, without waiting for data
Two-pronged strategy
  Memory hierarchy: keep data we need closer to the CPU
  Locality of reference: predict which data we’re likely to need

## Slide 39: Memory hierarchy
Some fundamental and enduring properties of systems
  The faster the storage, the more expensive ($) it is
  The faster the storage, the smaller (capacity) it is
  The gap between processor and main memory speed is widening
Key idea: keep the data you need the most in fast memory!
  Data you only need from time to time can be in slow memory, no big deal
  Most used data goes in registers
  Least used data goes to disk
Analogy: kitchen ingredients I use
  Salt, all the time: it sits out on the counter
  Oregano, frequently: front of the cabinet
  Onion powder, occasionally: back of the cabinet
  Brown sugar, sometimes: somewhere in the pantry
  Saffron, never: I can go buy some if I do need it

## Slide 40: Memory hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
Main memory holds disk
blocks retrieved from local
disks.
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from main memory.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 41: Outline
Memory Technologies
Memory Hierarchy
Caches
Locality of Reference

## Slide 42: Caching, general principle
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device
  Data lives in both places (typically)
  When the consumer (e.g., CPU) reads the data, it gets it from the smaller, faster storage
  If the data we want is not in the cache, we pay the full cost of bringing it over from the larger, slower storage into the smaller, faster storage
    The hope: we don’t need to do it too often
Fundamental idea in systems. Shows up all over!
  Memory hierarchies
  Content delivery networks (CDNs) on the Internet (Akamai, Cloudflare, etc.)

## Slide 43: Caching in a memory hierarchy
Fundamental idea of a memory hierarchy
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1
    L2 cache memory as a cache for main memory
    Main memory as a cache for disk, etc.
  Each level stores some of the most frequently accessed data
  The closer the cache is to the processor, the “hotter” the cached data

## Slide 44: Memory hierarchies make memory fast and large
Why do memory hierarchies work?
  Programs tend to access the data at level k more often than they access the data at level k+1
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit
Net effect:
  A large pool of memory that costs as little as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top
  Best of both worlds!

## Slide 45: Caching in a memory hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
Blocks cannot be stored in an arbitrary location!
They can only live at one of a fixed set of locations.
In this example: they must be in the same “column” for both levels.

## Slide 46: General caching concepts
Request
14
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
14
4*
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14

## Slide 47: General caching concepts
12
Request
12
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14
Cache miss
  b is not at level k, so the level k cache must fetch it from level k+1, e.g., block 12
  If the level-k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Here, we pick 4; same column as 12
    4 is “dirty”, need to write back to k+1
    More on this next lecture
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
12
4*
Request
12
4*
4*
12
12
“ * ” means the block is dirty (i.e., it has been modified)

## Slide 48: Cache Misses Taxonomy
Cold (compulsory) miss
  Cold misses occur when a block is accessed for the first time
  No one ever accessed it, so there wasn’t any reason to bring it into cache
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
  There’s no way the working set can all fit in the cache, so there will be misses
Conflict miss
  In most caches, blocks cannot be stored in any available slot
  If two blocks need to go in the same slot, need to evict the old one to store the new!
  If after that, we need to access the old block, conflict miss!
    We had a conflict, evicted a block, and now we miss trying to access that block
  Note: can happen even when there is “room” elsewhere in the cache!

## Slide 49: Break + Video
How do you remember which cache miss is which?
  Mr. Bean can help you tell the difference! (video)

## Slide 50: Outline
Memory Technologies
Memory Hierarchy
Caches
Locality of Reference

## Slide 51: Locality
Goal: predict which data the CPU will want to access
  So we can bring it to (and keep it in!) fast memory
  Problem: memory is huge! (billions of bytes) how do you decide which to save?
Principle of Locality
  Programs tend to reuse/use data items recently used or nearby those recently used
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time

## Slide 52: Types of locality practice
Temporal locality
  Recently referenced items are likely to be referenced in the near future
Spatial locality
  Items with nearby addresses tend to be referenced close together in time
Quiz: what kind of locality?
  Data
    Reference array elements in succession:
    Reference sum each iteration:
  Instructions
    Execute instructions in sequence:
    Cycle through loop repeatedly:
sum = 0;
for (i = 0; i < n; i++)
sum += a[i];
return sum;
Spatial locality
Spatial locality
Temporal locality
Temporal locality

## Slide 53: Locality example
Can get a sense for whether a function has good locality just by looking at its memory access patterns
Does this function have good locality?
Yes!
  Array is accessed in same row-major order in which it is stored in memory
  a through a+3 , a+4 through a+7, a+8 through a+11, etc.
int sumarrayrows(int a[M][N]){
int sum = 0;
for (int i = 0; i < M; i++) {
for (int j = 0; j < N; j++) {
sum += a[i][j];
}
}
return sum;
}
Temporal or spatial locality?
Spatial: accesses to array
Temporal: accesses to sum
Notes: sum: both
a: mostly spatial
loop body instructions: both

## Slide 54: Locality example
Does this function have good locality?
No!
  Scans array column-wise instead of row-wise
  a through a+3, then a+4*N through a+4*N+3, etc.
  Holy jumping around memory Batman!
More on that in a couple of lectures
int sumarraycols(int a[M][N]){
int sum = 0;
for (int j = 0; j < N; j++) {
for (int i = 0; i < M; i++) {
sum += a[i][j];
}
}
return sum;
}
Notes: sum: both
instructions: both
a: nope!

## Slide 55: Locality to the Rescue!
How can we exploit locality to bridge the CPU-memory gap?
  Use it to determine which data to put in a cache!
Spatial locality
  When level k needs a byte from level k+1, don’t just bring one byte
  Bring neighboring bytes as well!
  Good chances we’ll need them too in the near future
Temporal locality
  When you bring something into the cache, try to keep it there
  Good chances we’ll need it again in the near future
Result: most accesses should be cache hits!
  Memory system: size of largest memory, with speed close to that of fastest memory
We’ll see how that works in detail next time

## Slide 56: Lecture BONUS Assembly to Transistors
CS213 – Intro to Computer Systems
Branden Ghena
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 57: Assembly into machine code
Machine code are the numerical versions of each instruction
Number breaks down into parts
  Operation
  Source
  Destination
Immediates are stored in the instruction encoding

## Slide 58: Machine code ideas
Example:
  ADD $0x4351FF23, %rax
  ADD with destination %rax translates into 0x05
  Immediate is appended on to that
  Machine code: 0x0523FF5143
Number of bytes for each instruction is variable
  1-15 bytes depending on instruction and operands
Translation in complicated
  We’re not going to do it by hand, although Attack Lab touches it a bit

## Slide 59: Representing instructions as numbers
Why represent instructions as numbers?
Everything in memory is “just a number”
  And instructions go in memory
Hardware can “decode” number to figure out what to do
  Break number apart into bits (just like floating point)
  Some bits pick operation
  Some bits pick register or specify immediate

## Slide 60: Computer Processor (in five easy steps)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 61: These steps are relatively easy (we’ll skip them)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 62: This is extremely complicated for x86-64 (skip it too)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 63: We can talk about what execution means though!
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 64: Arithmetic Logic Unit (ALU)
Piece of hardware
Takes in two operands
  Source and Destination values
Takes in an Opcode
  Which operation to run
Performs operation and outputs result

## Slide 65: What can an ALU do?
All the basic arithmetic operations
  Add
  Subtract
  Bitwise And
  Bitwise Or
  Bitwise Xor
  Arithmetic Shift Right
  Logical Shift Right
  Logical Shift Left
Complex operations are separate hardware
  Multiply, Divide, Anything floating point

## Slide 66: Let’s zoom in

## Slide 67: Inside an ALU
Input values go into separate hardware blocks for each operation
Every operation occurs in parallel, simultaneously
  We are in hardware so this doesn’t take any additional time
ALU Inputs

## Slide 68: Inside an ALU – selecting the correct output
Selector
ALU Output
ALU Inputs
Opcode
Selects ALU output based on Opcode

## Slide 69: Let’s zoom in

## Slide 70: How is an ALU made?
All of those arithmetic operations can be broken down into a series of 1-bit Boolean operations
  Add is XOR for result + AND for carry
  Subtract is Flip bits (NOT), Add one (XOR + AND), then Add (XOR + AND)
  And/Or/Xor are just their respective operations
  Shifts are just move the bits around (simple in hardware, just move wires)

## Slide 71: 32-bit OR operation
Perform OR operation on each individual bit
  Pictured is a series of 1-bit OR gates

## Slide 72: 32-bit ADD operation
Below is the 1-bit version with carry-in/out
  Two 1-bit AND, two 1-bit XOR, one 1-bit OR
  Repeat 32 times, connecting carries together

## Slide 73: Let’s zoom in

## Slide 74: Logic gates can be created with transistors
CMOS implementation of logic gates
  Complementary Metal-Oxide Semiconductor
Transistors are just on/off switches

## Slide 75: Let’s zoom in

## Slide 76: Transistors are made out of silicon and other materials
Turning gate on/off causes source and drain to connect or disconnect
  Acts as a switch
We can make very small transistors

## Slide 77: That’s the bottom

## Slide 78: Zooming out again
Transistors make logic gates
1-bit AND gate
F
~6 transistors

## Slide 79: Zooming out again
Logic gates make operations
1-bit AND gate
1-bit ADD operation
~30 transistors

## Slide 80: Zooming out again
1-bit operations make 32-bit operations
1-bit ADD operation
~1000 transistors

## Slide 81: Zooming out again
Operations make an ALU
Selector
ALU Output
ALU Inputs
Opcode
~20K transistors

## Slide 82: ALU allows us to execute operations
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 83: All the way back to software
Machine code specifies what should be executed
Assembly translates into machine code
C compiles into assembly

## Slide 84: A processor is just a lot of transistors connected very carefully
ALU plus other operations make up a Core
  Decode logic, floating point, registers, etc.
Multiple cores plus caches make up a Processor
  And other stuff these days like graphics

## Slide 85: Outline
Memory Technologies
Memory Hierarchy
Caches
Locality of Reference
Bonus: Assembly to Transistors