## Slide 1: Lecture 16 Virtual Memory
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2023
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Homework 4 due tonight
  Very similar problems will be on the exam
SETI Lab
  Due next week Wednesday
  See the pinned Piazza posts
    Getting Started
    Testing Performance

## Slide 3: Today’s Goals
Understand goals and application of virtual memory
Explore how virtual memory resolves memory problems
Practice translating virtual addresses to physical addresses
Bonus: Practice problems at the end
  Also some bonus details on multi-level page tables we won’t test you on

## Slide 4: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 5: The Illusion!
CPU
RAM
Process A
I am the ONLY PROCESS accessing memory, and I don’t have to share it with anyone!

## Slide 6: The Reality!
CPU
RAM
Process A
Process B
Process A
Process B
Process C
Process C
DISK

## Slide 7: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?

## Slide 8: Multiple applications share RAM
CPU
RAM
Process A
Process B
Both processes assume they start at the beginning of RAM and use as much as they need

## Slide 9: Multiple applications share RAM
CPU
RAM
Process A
Process A
Process B

## Slide 10: Multiple applications share RAM
CPU
RAM
Process A
SWITCH
Process A
Process B

## Slide 11: Multiple applications share RAM
CPU
RAM
Process A
Process B
Process A
Process B

## Slide 12: Multiple applications share RAM
CPU
RAM
Process A
Process B
There’s enough RAM for both. Why should we have to swap?
Challenge here is that programs are compiled with specific addresses…
Process A
Process B

## Slide 13: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?

## Slide 14: Memory fragmentation
CPU
RAM
Process A
Process B
Process A
Process B
Process C
Process C

## Slide 15: Memory fragmentation
CPU
RAM
Process A
Process A
Process C
Process C

## Slide 16: Memory fragmentation
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
Hmm… There’s enough space, but not all together!

## Slide 17: Memory fragmentation
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
There we go!

## Slide 18: Memory fragmentation
CPU
RAM
Process A
Process A
Process C
Process C
Process D
Process D
Wait… This isn’t my data?

## Slide 19: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?
  How do we support processes bigger than RAM?

## Slide 20: Processes might be bigger than RAM
CPU
RAM
Process A
Memory for Process A

## Slide 21: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?
  How do we support processes bigger than RAM?
  How do we protect processes from each other?

## Slide 22: Processes can’t be trusted
CPU
RAM
Process A
Process B
Process A
Process B
Please give me Process A’s data! For I am evil!

## Slide 23: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?
  How do we support processes bigger than RAM?
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is?

## Slide 24: Computing timescales
Assuming 4 GHz processor, Instruction (with registers): 0.25 ns
Jeff Dean (Google AI): “Numbers Everyone Should Know”
Jim Gray’s analogy:
Registers are in your apartment
Disk is on Mars

## Slide 25: Caching disks
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
off-chip L2
cache (SRAM)
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices
Main memory should act as a cache for disk!

## Slide 26: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?
  How do we support processes bigger than RAM?
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is?
Virtual memory addresses all of these problems!

## Slide 27: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 28: Virtual memory concept
Disconnect reality of RAM from illusion of main memory
Processes work with the illusion
  They use virtual addresses to reference where their memory is
Computer (and OS) work with the reality
  They use physical addresses that are real locations in RAM
The hardware/OS translates virtual addresses into physical addresses

## Slide 29: A system using physical addresses
Main memory - An array of M contiguous byte-sized cells, each with a unique physical address
Physical addressing
  Most natural way to access it
    Addresses used by the CPU correspond to bytes in memory
  Used in simple systems like early PCs and embedded microcontrollers
0:
1:
M-1:
Main memory
CPU
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
4
Notes: Main memory is organized as an array of contiguous byte-sized cells, starting at address 0; given that, physical addressing is the most natural way for the CPU to use it.

## Slide 30: A system using virtual addresses
The CPU generates virtual address
  Address translation is done by dedicated hardware (memory management unit) via OS-managed lookup table (a Page Table)
  Resulting physical address is used to access memory hierarchy
Modern processors use virtual addresses
  All addresses your programs work with are virtual!
0:
1:
M-1:
Main memory
Memory Management Unit
2:
3:
4:
5:
6:
7:
Physical address
(PA)
Data word
8:
...
CPU
Virtual address
(VA)
CPU Chip
4
4100

## Slide 31: Your experiences with Virtual Memory
In Attack Lab, what was the address of touch2?
  0x40000-ish, right?
  The same each time you run it too
But multiple of you were running separate ctarget processes at the same time on Moore
  0x40000-ish was a Virtual Address
Really, each process’s code was at a totally different Physical Address in Moore’s actual RAM

## Slide 32: Virtual Memory
From here on out, we’ll be working with two different memory spaces:
  Virtual Memory (VM): A large (~infinite) space that a process believes it, and only it, has access to
  Physical Memory (PM): The limited RAM space your computer must share among all processors
This idea is independent of physical caches
  There are still multiple layers of memory caches in the CPU
  They might use virtual or physical addresses
    We’ll usually assume caches use physical addresses for this class

## Slide 33: Break + Review
https://wizardzines.com/comics/virtual-memory/

## Slide 34: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 35: File data is stored on disk
Physical memory: how much RAM does a computer actually have
  These days, a handful of gigabytes is typical
Address space: 264 possible addresses on x86-64!
  That’s 264 possible bytes of memory, or 17,179,869,184 GB!
  (In reality, architecture limits addresses to 48 bits, soon 57. Still huge!)
Across all your programs, may need more data than fits in physical memory, so some of it is in disk

## Slide 36: VM as a Tool for Caching
Solution: use physical memory as a cache! (called: DRAM cache)
  Store the bulk of your data on disk (very large, very cheap, but very slow)
  And store the currently-used data in main memory (very fast by comparison)
  Get the best of both worlds! Large capacity and fast access!
DRAM cache organization driven by the enormous miss penalty
  DRAM is about 100x slower than SRAM
  Disk is about 100,000x slower than DRAM

## Slide 37: Picking Cache Design Parameters
Block size?
  Disks are better at transferring large chunks of data (the first byte incurs a long delay, the rest come really fast afterwards)
  Large block size: typically 4-8 KB
Associativity?
  DRAM cache misses incur enormous penalties; have to go to disk. Yikes!
  Associativity is high to minimize miss rate
    Fully associative (one huge set): any block can go anywhere in cache
    Requires a “large” mapping function – but managed in software, so ok
Write-back or write-through?
  Disk cannot keep up with a firehose of small writes
  Use write-back (only write to disk when a page is evicted)
Replacement algorithms?
  Not limited by hardware; hardware strongly favors simple methods
  Highly sophisticated, expensive, open-ended replacement algorithms

## Slide 38: DRAM Cache Analogy to Cache Memory
+
=
0
1
2
B-1
tag
v
0
1
2
B-1
tag
v
0
1
2
B-1
tag
v
0
1
2
B-1
tag
v
0
1
2
B-1
tag
v
…
tag
v
tag
v
tag
v
tag
v
tag
v
…
0
1
2
B-1
0
1
2
B-1
0
1
2
B-1
0
1
2
B-1
0
1
2
B-1
…
tag
v
tag
v
…
Page Table
(in DRAM)
Main Memory (DRAM)
Page
Every virtual address ALWAYS maps to some entry!

## Slide 39: Locating an object in DRAM Cache: Page Tables
A page table maps virtual pages to physical pages
  One page table entry (PTE) per virtual page (possible page in VM)
    Fully-associative → one big set. Use the ”tag” to index into table!
  Each PTE specifies either a physical page (in DRAM) or a disk address
    Valid bit tells us which
    Instead of data in the “cache block”, “pointer” to where data is
null
null
Page table (Memory resident - DRAM)
Physical memory (DRAM Cache)
VP 7
VP 4
Disk Memory
Valid
0
1
0
1
0
1
0
1
Physical page number or disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Some pages are unallocated (i.e., no data there)

## Slide 40: Page Hit
Page hit: reference to a VM word that is in physical memory (hit on the DRAM cache)
null
null
Memory resident
page table
(DRAM)
Physical memory (DRAM)
VP 7
VP 4
Disk memory
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
VP 2
Page table has an entry for each
virtual page, so index with “tag”
(VPN) instead!

## Slide 41: Page Fault
Page fault: reference to VM word that is not in physical memory (DRAM cache miss)
null
null
Memory resident
page table
(DRAM)
VP 7
VP 4
Valid
0
1
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
0
Physical memory (DRAM)
Disk memory

## Slide 42: Handling Page Fault
Page miss causes page fault (a HW exception, OS code kicks in to handle)
null
null
Memory resident
page table
(DRAM)
VP 7
VP 4
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
Physical memory (DRAM)
Disk memory

## Slide 43: Handling Page Fault
Page miss causes page fault (a HW exception, OS code kicks in to handle)
Page fault handler selects a victim to be evicted (here VP 4)
null
null
Memory resident
page table
(DRAM)
VP 7
VP 4
Valid
0
1
0
1
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
Eviction decision is made by software. So can be pretty sophisticated! (Beyond scope of this class)
→ fewer page faults (if we do it right)
Physical memory (DRAM)
Disk memory

## Slide 44: Handling Page Fault
Page miss causes page fault (a HW exception, OS code kicks in to handle)
Page fault handler selects a victim to be evicted (here VP 4)
The victim page is swapped with the disk block of the requested address
null
null
Memory resident
page table
(DRAM)
VP 7
VP 3
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
Requires a disk read! (Slow!)
OS suspends process in the meantime.
Resumes it once memory access finishes.
Physical memory (DRAM)
Disk memory

## Slide 45: Handling Page Fault
Offending instruction is restarted: page hit this time!
null
null
Memory resident
page table
(DRAM)
VP 7
VP 3
Valid
0
1
1
0
0
1
0
1
Physical page
number or
disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
Virtual address
VPN
Offset
How does anything ever get done?
Locality to the rescue!
Physical memory (DRAM)
Disk memory

## Slide 46: Locality saves the day (as usual)
At any point in time, programs tend to access a small set of active virtual pages called the working set
  Programs with higher temporal locality will have smaller working sets
If (working set size < main memory size)
  High performance for one process after compulsory misses
  Fully-associative cache, so no conflicts. Only capacity matters.
  Life is good!
If ( SUM(working set sizes) > main memory size )
  Thrashing: Performance meltdown where pages are swapped to and from disk continuously
  When cache memory is thrashing, CPU runs at the speed of memory. Ow.
  When virtual memory is thrashing, CPU runs at the speed of disk. Yikes!
    Hope you enjoy the commute to Pluto. Because that’s where your data is

## Slide 47: Break + Question
Computer has:
  8 pages of Virtual Memory
  4 pages of Physical Memory
How many entries (rows) does a page table have?
How many entries can be valid at any time?

## Slide 48: Break + Question
Computer has:
  8 pages of Virtual Memory
  4 pages of Physical Memory
How many entries (rows) does a page table have? 8 entries
How many entries can be valid at any time? 4 valid
Page Table translates Virtual to Physical
  It needs an entry for each virtual page, so 8 entries
  Rows are valid if they point at physical memory
    So only four entries can be valid (unless they share a physical page)

## Slide 49: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 50: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get?
  How do we move memory around?
  How do we support processes bigger than RAM?
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is? ✔
  Use RAM as a cache for disk

## Slide 51: Which addresses do processes get?
Programs can use whatever virtual addresses they want
  Usually a fixed mapping for a given OS
OS controls physical addresses
  Decides which parts of RAM are used for which things
Shared libraries
Heap
Code (text)
Data
User stack
%rsp
Process
virtual
memory
brk
Kernel Virtual Memory
0x400000
0x80000000000
Dynamic segments
0x0007FFFFFFFFFFFF
0x0000000000000000

## Slide 52: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get? ✔ Whatever virtual addresses they want
  How do we move memory around?
  How do we support processes bigger than RAM?
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is? ✔
  Use RAM as a cache for disk

## Slide 53: How do we move memory around?
Just change the page table entry!
null
null
Page table (Memory resident - DRAM)
Physical memory (DRAM Cache)
Disk Memory
Valid
0
1
0
1
0
1
0
1
Physical page number or disk address
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
null
null
null

## Slide 54: How do we move memory around?
Just change the page table entry!
  Same virtual address points at a different physical address
Usually only happens when pages are swapped to disk and then later brought back
null
null
Page table (Memory resident - DRAM)
Physical memory (DRAM Cache)
Disk Memory
Valid
0
1
0
1
0
1
0
1
Physical page number or disk address
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3
null
null
null

## Slide 55: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get? ✔ Whatever virtual addresses they want
  How do we move memory around? ✔ Update page table entries
  How do we support processes bigger than RAM?
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is? ✔
  Use RAM as a cache for disk

## Slide 56: How do we support processes bigger than RAM?
Just leave some pages for that process on disk
Page table entry still exists for each virtual page
Hopefully working set is smaller than program memory
null
null
Page table (Memory resident - DRAM)
Physical memory (DRAM Cache)
VP 7
VP 4
Disk Memory
Valid
0
1
0
1
0
1
0
1
Physical page number or disk address
PTE 0
PTE 7
PP 0
VP 2
VP 1
PP 3
VP 1
VP 2
VP 4
VP 6
VP 7
VP 3

## Slide 57: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get? ✔ Whatever virtual addresses they want
  How do we move memory around? ✔ Update page table entries
  How do we support processes bigger than RAM? ✔ Leave some pages on disk
  How do we protect processes from each other?
  How do we deal with how incredibly slow disk is? ✔
  Use RAM as a cache for disk

## Slide 58: How do we protect processes from each other?
Each process has separate virtual memory spaces
  No way to access another process’s physical memory unless it is mapped to one of your virtual addresses
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
PP 12
...
0
M-1
Address
translation

## Slide 59: Enabling shared libraries
We could share some physical pages across processes to enable shared libraries or shared memory
Virtual Address Space for Process 1:
Physical
Address
Space (DRAM)
0
N-1
(e.g., read-only
library code)
Virtual Address Space for Process 2:
VP 1
VP 2
...
0
N-1
VP 1
VP 2
...
PP 2
PP 6
PP 8
...
0
M-1
Address
translation

## Slide 60: VM as a Tool for Memory Protection
What if we want better protection?
  Mark a page as read-only
  Keep a page in memory, but only the OS can touch it
Extend PTEs with permission bits!
  Page fault handler checks these before remapping
HW enforces this protection (trap into OS if violation occurs)
Process i
Address
READ
WRITE
PP 6
Yes
No
PP 4
Yes
Yes
PP 2
Yes
VP 0:
VP 1:
VP 2:
•
•
•
Process j
Yes
SUP
No
No
Yes
Address
READ
WRITE
PP 9
Yes
No
PP 6
Yes
Yes
PP 11
Yes
Yes
SUP
No
Yes
No
VP 0:
VP 1:
VP 2:
Physical Address Space
PP 2
PP 4
PP 6
PP 8
PP 9
PP 11
Must be running in kernel (supervisor mode)
EXEC
Yes
No
•
•
•
No
EXEC
No
Yes
No
Notes: If process i is running in user mode it can read vp0 and read/write vp1 but cannot access vp2 (must run in SUPervisor mode)

## Slide 61: Memory problems
What are the challenges to supporting this reality?
  Which addresses does each process get? ✔ Whatever virtual addresses they want
  How do we move memory around? ✔ Update page table entries
  How do we support processes bigger than RAM? ✔ Leave some pages on disk
  How do we protect processes from each other? ✔ Don’t overlap virtual address spaces + permission bits
  How do we deal with how incredibly slow disk is? ✔
  Use RAM as a cache for disk

## Slide 62: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 63: Address Translation
Goal: Given virtual address, find corresponding physical address
  (Or get a page fault if the page is not in memory)
  Translation done by Memory Management Unit (hardware)
  But mapping itself is maintained by OS (software)
    Just a table in memory!
Basic Parameters
  N = 2n : Number of addresses in virtual address space
  M = 2m : Number of addresses in physical address space. m ≤ n (usually much less)
  P = 2p : Page size (bytes)
Components of the virtual address (VA)
  Virtual page number (VPN)
  Page Offset
Components of the physical address (PA)
  Physical page number (PPN)
  Page Offset (same offset as VA)

## Slide 64: Address Translation With a Page Table
Virtual page number (VPN)
Page offset
Physical page number (PPN)
Page Offset
Virtual address
Physical address
Valid
Physical page number (PPN)
Page table base register (PTBR)
CR3 on x86-64
(OS-only register)
Page table (in memory)
Page table address
for process
Valid bit = 0:
page not in memory
(page fault)
0
p-1
p
n-1
0
p-1
p
m-1
If Valid bit = 1 &&
access mode allowed:
page in memory
(page hit)
VPN is the index into the page table
Access
Access rights mismatch:
prohibited access by process
(protection violation fault)

## Slide 65: Memory Access: Page Hit
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) MMU sends physical address to cache/memory
5) Cache/memory sends data word to processor
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE address
PTE
1
2
3
4
5

## Slide 66: Memory Access: Page Fault
1) Processor sends virtual address to MMU
2-3) MMU fetches PTE from page table in cache/memory
4) Valid bit is zero, so MMU triggers page fault exception
5) Handler identifies victim (and, if dirty, pages it out to disk)
6) Handler pages in new page and updates PTE in memory
7) Handler returns to original process, restarting faulting instruction
MMU
Cache/
Memory
CPU
VA
CPU Chip
PTE address
PTE
1
2
3
4
5
Disk
Page fault handler (OS code)
Victim page
New page
Exception
6
7

## Slide 67: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
How do we split Virtual Addresses into VPN and Offset?
Mapping can be anything, which is bigger doesn’t really matter!
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0

## Slide 68: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
How do we split Virtual Addresses into VPN and Offset?
  Offset is based on page size: 64-bytes ⇨ 6 bits. All the rest are VPN
How big are Physical Page Numbers?
Mapping can be anything, which is bigger doesn’t really matter!
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 

## Slide 69: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
How do we split Virtual Addresses into VPN and Offset?
  Offset is based on page size: 64-bytes ⇨ 6 bits. All the rest are VPN
How big are Physical Page Numbers? 16-6 = 10 bits
Mapping can be anything, which is bigger doesn’t really matter!
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 

## Slide 70: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x3F0
  VPN:
  Offset:
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 

## Slide 71: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x3F0
  VPN: 0b001111
  Offset: 0b110000
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 

## Slide 72: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x3F0
  VPN: 0b001111
  Offset: 0b110000
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN:
Offset:

## Slide 73: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x3F0
  VPN: 0b001111
  Offset: 0b110000
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN: 0b01 1111 0000
Offset: 0b110000
Physical address:

## Slide 74: Virtual memory example
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x3F0
  VPN: 0b001111
  Offset: 0b110000
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN: 0b01 1111 0000
Offset: 0b110000
Physical address:
  0b0111110000110000
  0x7C30

## Slide 75: Break + Question
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x500
  VPN:
  Offset:
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN:
Offset:
Physical address:

## Slide 76: Break + Question
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x500
  VPN: 0b010100
  Offset: 0b000000
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN: INVALID
Offset:
Physical address:
  Page Fault

## Slide 77: Break + Practice again
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x0D6
  VPN:
  Offset:
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN:
Offset:
Physical address:

## Slide 78: Break + Practice again
Parameters
  Virtual addresses are 12-bits
  Physical addresses are 16-bits
  Page size is 64 bytes
Translate:
Virtual address: 0x0D6
  VPN: 0b000011
  Offset: 0b010110
11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
15 | 14 | 13 | 12 | 11 | 10 | 9 | 8 | 7 | 6 | 5 | 4 | 3 | 2 | 1 | 0
Physical Page Number |  |  |  | Virtual Page Number |  |  |  |  |  | Page Offset |  |  |  |  | 
VPN | PPN | Valid
0x00 | 0x123 | 1
0x01 | 0x156 | 1
0x02 | 0x143 | 1
0x03 | 0x16F | 1
0x04 | 0x1FF | 0
0x05 | 0x107 | 0
0x06 | 0x100 | 0
0x07 | 0x1C0 | 0
0x08 | 0x1D8 | 0
0x09 | 0x1BF | 0
0x0A | 0x000 | 1
0x0B | 0x3FF | 1
0x0C | 0x308 | 0
0x0D | 0x3FD | 0
0x0E | 0x111 | 1
0x0F | 0x1F0 | 1
VPN | PPN | Valid
0x10 | 0x237 | 1
0x11 | 0x236 | 1
0x12 | 0x2B0 | 1
0x13 | 0x280 | 0
0x14 | 0x120 | 0
Continues on… |  | 
PPN: 0b010 110 1111
Offset: 0b010110
Physical address:
  0b0101101111010110
  0x5BD6

## Slide 79: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 80: Accessing page tables is slow
Problem: page tables are in memory
  And we need to access them to find our address to access memory
  Two memory accesses per access!!! 😱
Page table entries (PTEs) are cached in L1, L2, etc, like any other data in memory
  PTEs may be evicted by other data references. Oops.
  PTE access still requires average effective memory access delay

## Slide 81: Speeding up Translation with a TLB
Solution: Translation Lookaside Buffer (TLB)
  Small hardware cache memory inside MMU
  Contains page table entries for a small number of pages
  Maps virtual page numbers to physical page numbers
  Reduces issues with data kicking PTEs out of caches!
Like cache memories, uses set indices, tags, and valid bits
  VPN split into: TLB tag and TLB index (just like caches, because it is one!)
  No need for a block offset equivalent (PTEs have a single value)

## Slide 82: TLB Hit
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
4
5
A TLB hit eliminates a memory access
TLB
VPN
3
Notes: After the miss, PTE goes into the TLB (like any cache access)

## Slide 83: TLB Miss
MMU
Cache/
Memory
PA
Data
CPU
VA
CPU Chip
PTE
1
2
5
6
TLB
VPN
4
PTEA
3
A TLB miss incurs an additional memory access (the PTE)
Fortunately, TLB misses are rare. Why?
Locality. It’s always locality.
Notes: A: locality!

## Slide 84: Address translation process
hardware
hardware or OS software
OS software
Virtual Address
TLB
Lookup
Page Table
Access
Update
TLB
Page Fault
(OS loads page)
Protection
Check
Physical
Address
TLB Miss
TLB Hit
Page not
in Mem
Access
Denied
Access
Permitted
Protection
Fault
SEGFAULT
Page
in Mem
Check cache
Find in Disk
Find in Mem
Notes: Need to restart instruction.
Soft and hard page faults.

## Slide 85: Outline
Memory Problems
Virtual Memory Concept
Main Memory as a Cache
Memory Problems Solved
Address Translation
Caching Page Table Entries

## Slide 86: Outline
Bonus: Memory System Practice Problems

## Slide 87: Simple Memory System Example
Addressing
  14-bit virtual addresses
  12-bit physical address
  Page size = 64 bytes
13
12
11
10
9
8
7
6
5
4
3
2
1
0
11
10
9
8
7
6
5
4
3
2
1
0
VPO
PPO
PPN
VPN
Virtual Page Number
Virtual Page Offset
Physical Page Number
Physical Page Offset

## Slide 88: Simple Memory System: Page Table
We only show a few entries (out of 256)
1
0D
0F
1
11
0E
1
2D
0D
0
–
0C
0
–
0B
1
09
0A
1
17
09
1
13
08
Valid
PPN
VPN
0
–
07
0
–
06
1
16
05
0
–
04
1
02
03
1
33
02
0
–
01
1
28
00
Valid
PPN
VPN
0
-
2E
Valid
PPN
VPN
…
…

## Slide 89: Simple Memory System: TLB
16 entries
4-way associative
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
0
–
02
1
34
0A
1
0D
03
0
–
07
3
0
–
03
0
–
06
0
–
08
0
–
02
2
0
–
0A
0
–
04
0
–
02
1
2D
03
1
1
02
07
0
–
00
1
0D
09
0
–
03
0
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Valid
PPN
Tag
Set

## Slide 90: Simple Memory System: L1 Cache
16 lines, 4-byte block size
Physically addressed
Direct mapped
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
BO
CI
CT
03
DF
C2
11
1
16
7
–
–
–
–
0
31
6
36
F0
72
1D
1
0D
5
09
8F
6D
43
1
32
4
–
–
–
–
0
36
3
08
04
02
00
1
1B
2
–
–
–
–
0
15
1
11
23
11
99
1
19
0
B0
B1
B2
B3
Valid
Tag
Idx
–
–
–
–
0
14
F
D3
1B
77
83
1
13
E
15
34
96
04
1
16
D
–
–
–
–
0
12
C
–
–
–
–
0
0B
B
3B
DA
15
93
1
2D
A
–
–
–
–
0
2D
9
89
51
00
3A
1
24
8
B0
B1
B2
B3
Valid
Tag
Idx

## Slide 91: Address Translation Example #1
Virtual Address: 0x03D4
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  BO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
BO
CI
CT
0
0
1
0
1
0
1
1
1
1
0
0
0
0
0x0F
0x3
0x03
Y
N
0x0D
0
0
0
1
0
1
0
1
1
0
1
0
0
0x5
0x0D
Y
0x36
(using the Page Table, TLB, and L1 cache shown in the preceding slides)
Address space: 14-bit VAddr, 12-bit PAddr, 64-byte page TLB: 16 entries, 4-way
L1 Cache: 16 lines, 4-byte block, direct mapped,
    Physically addressed
movb (%rcx), %al
Notes: Write VPN, TLBI, … on the board and do example in class

## Slide 92: Address Translation Example #2
Virtual Address: 0x0B8F
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  BO ___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
BO
CI
CT
1
1
1
1
0
0
0
1
1
1
0
1
0
0
0x2E
2
0x0B
N
Y
TBD
(using the Page Table, TLB, and L1 cache shown in the preceding slides)
Likely invalid page. Maybe needs to read from disk. Either way we don’t know the PPN.

## Slide 93: Address Translation Example #3
Virtual Address: 0x0020
  VPN ___ TLBI ___ TLBT ____ TLB Hit? __ Page Fault? __ PPN: ____
Physical Address
  BO___ CI___ CT ____ Hit? __ Byte: ____
13
12
11
10
9
8
7
6
5
4
3
2
1
0
VPO
VPN
TLBI
TLBT
11
10
9
8
7
6
5
4
3
2
1
0
PPO
PPN
BO
CI
CT
0
0
0
0
0
1
0
0
0
0
0
0
0
0
0x00
0
0x00
N
N
0x28
0
0
0
0
0
0
0
0
0
1
1
1
0
0x8
0x28
N
Mem
(using the Page Table, TLB, and L1 cache shown in the preceding slides)
Cache miss, so needs to read byte values from main memory

## Slide 94: Outline
Bonus: Multi-level Page Tables

## Slide 95: Multi-Level Page Tables
Suppose:
  4KB (212) page size, 48-bit address space, 8-byte PTE
How big is the page table?
  Would need a 512 GB page table!
    248 * 2-12 * 23 = 239 bytes
  That’s just meta-data! Where does the data go?
Common solution:
  Multi-level page tables
  Split the VPN into multiple pieces, 1 per level
  Example: 2-level page table
    Level 1 table: each PTE points to a level 2 page table (always memory resident)
    Level 2 table: each PTE points to a page (paged in and out like any other data, maybe not even allocated!)
Level 1
Table
...
Level 2
Tables
...

## Slide 96: A Two-Level Page Table Hierarchy
Level 1 page table
...
Level 2 page tables
VP 0
...
VP 1023
VP 1024
...
VP 2047
Gap
0
PTE 0
...
PTE 1023
PTE 0
...
PTE 1023
1023 null
PTEs
PTE 1023
1023
unallocated
pages
VP 9215
Virtual
memory
(1K - 9)
null PTEs
PTE 0
PTE 1
PTE 2 (null)
PTE 3 (null)
PTE 4 (null)
PTE 5 (null)
PTE 6 (null)
PTE 7 (null)
PTE 8
2K allocated VM pages
for code and data
6K unallocated VM pages
1023 unallocated pages
1 allocated VM page
for the stack
32 bit addresses, 4KB pages, 4-byte PTEs
If you’re not using most of the address space
(which you’re not), don’t need most level 2
page tables! So don’t allocate them!
1 table
1024 entries
3 tables, NOT 1024!
1024 entries each

## Slide 97: Multi-level page table: Core i7
CR3
Physical
address
of page
Physical
address
of L1 PT
9
VPO
9
12
Virtual
address
L4 PT
Page
table
L4 PTE
PPN
PPO
40
12
Physical
address
Offset into
physical and
virtual page
VPN 3
VPN 4
VPN 2
VPN 1
L3 PT
Page middle
directory
L3 PTE
L2 PT
Page upper
directory
L2 PTE
L1 PT
Page global
directory
L1 PTE
9
9
40*
/
40*
/
40*
/
40*
/
40*
/
12
/
512 GB
region
per entry
1 GB
region
per entry
2 MB
region
per entry
4 KB
region
per entry
*aligned to a 4K-boundary

## Slide 98: End-to-end Core i7 Data Address Translation
CPU
VPN
VPO
36
12
TLBT
TLBI
6
30
...
L1 d-TLB (64 sets, 4 entries/set)
VPN1
VPN2
9
9
PTE
CR3
PPN
PPO
40
12
Page tables
L1 d-TLB miss
L1 d-TLB hit
Physical
address
(PA)
Result
32/64
...
CT
CO
40
6
CI
6
L2, L3, and
main memory
L1 d-cache
(64 sets, 8 lines/set)
L1 hit
L1 miss
Virtual address (VA)
VPN3
VPN4
9
9
PTE
PTE
PTE
L2 TLB
L2 TLB hit
L2 TLB miss
VPN
VPN
data