## Slide 1: Lecture 14 Concurrency
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2024
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Attack Lab due Today
Homework 4 is out now
  Due next week Thursday, only covers cache materials
SETI Lab releases soon
  Today’s lecture has 90%+ of the information you need for it
    And everything you need to get started
  Tuesday’s lecture will add a few more details about optimization
  Due last Thursday of class

## Slide 3: Today’s Goals
Discuss goals of concurrency and how it is achieved in software
Understand the challenges of writing parallel software
Explore how to practically use parallelism for simple examples

## Slide 4: Outline
Need for Parallelism
Processes and Threads
Concurrency Challenges
Using Threads

## Slide 5
It’s the mid 1990s and you work at Microsoft.
You need to double the speed of Excel in two years.
What do you do?

## Slide 6
It’s the mid 1990s and you work at Microsoft.
You need to double the speed of Excel in two years.
What do you do? Take a vacation

## Slide 7: Moore’s Law – CPU transistors counts
“Number of transistors in a chip doubles every 18 months”
Transistors are getting exponentially smaller!
How small? Today: 7nm!
< ½ the size of most viruses!
Notes: Gordon Moore – first version of the law – ’65: double every year; restated in ‘75: double every two years
Was simplified to “every 18 months”

## Slide 8: Processors kept getting faster too

## Slide 9: Power is a major limiting factor on speed
We could make processors go very fast
  But doing so uses more and more power
More power means more heat generated
  And chips typically work up to around 100°C
  Hotter than that and things stop working
We add heat sinks and fans and water coolers to keep chips cool
  But it’s hard to remove heat quickly enough from chips
So, power consumption ends up limiting processor speed

## Slide 10: Denard Scaling
Moore’s Law corollary: Denar Scaling
  As transistors get smaller, the power density stays the same
  Which is to say that the power-per-transistor decreases!
Making the processor clock speed faster uses more power
  But the two balance out for roughly net even power
  So not only do we get more transistors, but chip speed can be faster too
From our Excel example:
  In two years, new hardware would run the existing software twice as fast

## Slide 11: Then they stopped getting faster
~2006: Leakage current becomes significant
Now smaller transistors doesn’t mean lower power

## Slide 12: So… now what?
In summary:
Making transistors smaller doesn’t make them lower power,
so if we were to make them faster, they would take more power,
which will eventually lead to our processors melting…
and because of that, we can’t reliably make performance better by waiting for clock speeds to increase.
How do we continue to get better computation performance?

## Slide 13: Exploit parallelism!

## Slide 14: Update: 2010-2021
Still growing!
Stable
Stable
Small improvement
Still growing for servers

## Slide 15: Parallelism Analogy
I want to peel 100 potatoes as fast as possible:
  I can learn to peel potatoes faster
  OR
  I can get 99 friends to help me
Whenever one result doesn’t depend on another, doing the task in parallel can be a big win!

## Slide 16: Parallelism versus Concurrency
Two processes A and B
B
A
B
A
B
A
B
A
OR
time
time
time
time
Serial execution
Parallel execution
Concurrent execution

## Slide 17: Parallelism versus Concurrency
Parallelism
  Two things happen strictly simultaneously
Concurrency
  More general term
  Two things happen in the same time window
    Could be simultaneous, could be interleaved
  Concurrent execution occurs whenever two processes are both active
B
A
OR
time
time
OR
time

## Slide 18: Outline
Need for Parallelism
Processes and Threads
Concurrency Challenges
Using Threads

## Slide 19: How do we apply parallelism to software?
Goal: make computer faster by performing multiple tasks
Need multiple different software tasks
Two particular ways of creating a software task
  Processes
  Threads

## Slide 20: View of a process
Process: a program that is currently being run
Contents:
Address Space
Registers
code
static data
heap
stack
~ FFFF FFFFhex
~ 0hex
%r8d
%r8
%r9d
%r9
%r10d
%r10
%r11d
%r11
%r12d
%r12
%r13d
%r13
%r14d
%r14
%r15d
%r15
%rsp
%esp
%eax
%rax
%ebx
%rbx
%ecx
%rcx
%edx
%rdx
%esi
%rsi
%edi
%rdi
%ebp
%rbp
Instruction Pointer
Condition Codes
Etc.

## Slide 21: Process use case: separate programs
Right now I am running:
  Powerpoint
  Chrome
  Notion
Each is a separate process
  Have their own memory
  Have their own registers
  Operating System manages them
No need for communication between them

## Slide 22: Multiprocessor Systems (in pictures)
Core 0
Control
Datapath
RIP
Registers
(ALU)
Memory
Bytes
Processor 0 Memory Accesses
Core 1
Control
Datapath
RIP
Registers
(ALU)
Processor 1 Memory Accesses
Actually parallel!

## Slide 23: Alternate view of a process
Process: code and data, plus a thread
Thread: execution state
  Each process has at least one thread
Registers
%r8d
%r8
%r9d
%r9
%r10d
%r10
%r11d
%r11
%r12d
%r12
%r13d
%r13
%r14d
%r14
%r15d
%r15
%rsp
%esp
%eax
%rax
%ebx
%rbx
%ecx
%rcx
%edx
%rdx
%esi
%rsi
%edi
%rdi
%ebp
%rbp
Instruction Pointer
Condition Codes
Stack
Code and Data

## Slide 24: Alternate view of a process
A process could have multiple threads
  Each with its own registers and stack
Code and Data
Threads have separate:
  Instruction Pointer
  Registers
  Stack Memory
  Condition Codes
Threads share:
  Code
  Global variables

## Slide 25: Thread use case: web browser
Let’s say you’re implementing a web browser:
You want a tab for each web page you open:
Each tab is its own thread
The same code loads each website (shared code section)
The same global settings are shared by each tab (shared data section)
Each tab does have separate state (separate stack and registers)
Disclaimer: Actually, modern browsers use separate processes for each tab for a variety of reasons including performance and security. But they used to use threads.

## Slide 26: Process address space with multiple threads
Stack (T1)
Code
Static Data
Heap
Stack (T2)
Stack (T3)
Thread 1
Thread 3
Thread 2
%RIP (Thread 1)
%RIP (Thread 3)
%RIP (Thread 2)
Data
Segment

## Slide 27: Multithreading processors
Basic idea: Processor resources are expensive and should not be left idle
Long memory latency to memory on cache miss?
  Hardware switches threads to bring in other useful work while waiting for cache miss
  Swapping between threads in a process takes less time than waiting for memory, so we get back to work sooner!

## Slide 28: Multithreading processor
Memory
Bytes
Processor
Control
Datapath
RIP 0
Registers 0
(ALU)
RIP 1
Registers 1
Two copies of RIP and Registers inside processor hardware
Looks like two processors to software (hardware thread 0, hardware thread 1)
Control logic decides which thread to execute an instruction from next (concurrent, but NOT parallel)
28

## Slide 29: Multithreading, multicore processors
Combine capabilities of both designs
Run two processes each with two threads
Or run one process with four threads
Memory
Bytes
Processor 0 Memory Accesses
Processor 1 Memory Accesses
Processor
Control
Datapath
RIP 0
Registers 0
(ALU)
RIP 1
Registers 1
Processor
Control
Datapath
RIP 0
Registers 0
(ALU)
RIP 1
Registers 1

## Slide 30: Example: i7 processor
4 total cores
Each capable of 2 threads
≈ 8 processors

## Slide 31: Break + Open Question
How many “cores” does a computer need?

## Slide 32: Break + Open Question
How many “cores” does a computer need?
  Depends on the workload
  Personal computer
    ~2-10 processes running at once in the foreground
    Plus ~100 in the background
  Server
    Could be serving thousands of requests simultaneously
    Moore: 48 cores, Hanlon: 40 cores

## Slide 33: Outline
Need for Parallelism
Processes and Threads
Concurrency Challenges
Using Threads

## Slide 34: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 35: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 36: Speedup Example
Imagine a program that takes 100 seconds to run
95 seconds in the blue part
5 seconds in the green part
We’re going to speed up the green part and take a look at the net result
95 s | 5 s

## Slide 37: Speedup from improvements
95 s | 5 s
Speedup with Improvement | = | Execution time without improvement
 |  | Execution time with improvement
5 s -> 2.5 s: Speedup = 100/97.5 = 1.026
5 s -> 1 s: Speedup = 100/96 = 1.042
5 s -> 0.001s: Speedup = 100/95.001 = 1.053
The impact of a performance improvement is relative to the importance of the part being improved!

## Slide 38
Speedup =
F = Fraction of execution time speed up S = Scale of improvement
(1 - F) + F
S
Non-speed-up part
Speed-up part
1
1
0.75 + 0.25
2
1
0.75 + 0.125
=
=
1.14
Example: 2x improvement to 25% of the program
Equivalent to prior equation
Amdahl’s Law

## Slide 39: Amdahl’s Law (in pictures)
The amount of speedup that can be achieved through parallelism is limited by the non-parallel portion of your program! 😭
  And every program has at least some non-parallel parts
Parallel
portion
Serial
portion
Time
Number of Processors
1
2
3
4
5
Speedup
Number of Processors

## Slide 40: Challenges to concurrency
Concurrency is great! We can do so many things!!
But what’s the downside…?
How much speedup can we get from it?
How hard is it to write parallel programs?

## Slide 41: Concurrency problem: data races
Consider two threads with a shared global variable: int count = 0
count could end up with a final value of 1 or 2. How?
Thread 1:
void thread_fn(){
count += 1;
}
Thread 2:
void thread_fn(){
count += 1;
}

## Slide 42: Concurrency problem: data races
Consider two threads with a shared global variable: int count = 0
count could end up with a final value of 1 or 2. How?
These instructions could be interleaved in any way.
Thread 1:
void thread_fn(){
mov $0x8049a1c, %edi
mov (%edi), %eax
add $0x1, %eax
mov %eax, (%edi)
}
Thread 2:
void thread_fn(){
mov $0x8049a1c, %edi
mov (%edi), %eax
add $0x1, %eax
mov %eax, (%edi)
}
Assuming “count” is in memory location 0x8049a1c

## Slide 43: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | ???
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 0
Before this code starts

## Slide 44: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 0
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 0
Assuming “count” is in memory location pointed to by %edi

## Slide 45: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 0
Assuming “count” is in memory location pointed to by %edi

## Slide 46: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 1
Assuming “count” is in memory location pointed to by %edi

## Slide 47: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | 1
Memory | 
Variable | Value
count | 1
Assuming “count” is in memory location pointed to by %edi

## Slide 48: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | 2
Memory | 
Variable | Value
count | 1
Assuming “count” is in memory location pointed to by %edi

## Slide 49: Data race example – Count = 2
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | 2
Memory | 
Variable | Value
count | 2
Assuming “count” is in memory location pointed to by %edi

## Slide 50: Theads do not have guaranteed ordering
BUT, there’s no guarantee that the instructions occur in that order!
Since the two threads are running in parallel, the instructions could be interleaved in any way (both threads are really running simultaneously)

## Slide 51: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | ???
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 0
Before this code starts
Remember, each thread has its own separate registers!

## Slide 52: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 0
Thread 2 | 
Register | Value
%eax | ???
Memory | 
Variable | Value
count | 0

## Slide 53: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 0
Thread 2 | 
Register | Value
%eax | 0
Memory | 
Variable | Value
count | 0

## Slide 54: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 0
Thread 2 | 
Register | Value
%eax | 1
Memory | 
Variable | Value
count | 0

## Slide 55: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 0
Thread 2 | 
Register | Value
%eax | 1
Memory | 
Variable | Value
count | 1

## Slide 56: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | 1
Memory | 
Variable | Value
count | 1

## Slide 57: Data race example – Count = 1
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Time
Assuming “count” is in memory location pointed to by %edi
Thread 1 | 
Register | Value
%eax | 1
Thread 2 | 
Register | Value
%eax | 1
Memory | 
Variable | Value
count | 1

## Slide 58: Data race comparison
Thread 1 | Thread 2
mov (%edi), %eax | 
add $0x1, %eax | 
mov %eax, ($edi) | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
Time
Thread 1 | Thread 2
mov (%edi), %eax | 
 | mov (%edi), %eax
 | add $0x1, %eax
 | mov %eax, (%edi)
add $0x1, %eax | 
mov %eax, (%edi) | 
Final value of count: 2
Final value of count: 1
Assuming “count” is in memory location pointed to by %edi

## Slide 59: Data race explanation
Thread scheduling is non-deterministic
  There is no guarantee that any thread will go first or last or not be interrupted at any point
If different threads write to the same variable
  The final value of the variable is also non-deterministic
  This is a data race
Avoid incorrect results by:
  Not writing to the same memory address!! OR
  Synchronizing reading and writing to get deterministic behavior

## Slide 60: Data race explanation
Thread scheduling is non-deterministic
  There is no guarantee that any thread will go first or last or not be interrupted at any point
If different threads write to the same variable
  The final value of the variable is also non-deterministic
  This is a data race
Avoid incorrect results by:
  Not writing to the same memory address!! OR
  Synchronizing reading and writing to get deterministic behavior
We’ll pick this one for CS213
CS343 explores this in depth

## Slide 61: Avoiding shared memory data races
Ensure that no two threads write to the same memory address
Multiple threads reading from the same memory address is fine
  As long as no thread writes to that memory
Where do you put results then? Simple solution:
  Make an array with a slot for each thread
  Each thread only writes to their own slot in the array
  After all threads are done, main thread iterates the array and determines the final result

## Slide 62: Question + Break
Consider three threads with a shared global variable: int count = 0
What are the possible values of count?
Thread 1:
void main(){
count += 1;
}
Thread 2:
void main(){
count -= 1;
}
Thread 3:
void main(){
count += 2;
}

## Slide 63: Question + Break
Consider three threads with a shared global variable: int count = 0
What are the possible values of count? -1, 0, 1, 2, 3
How are you supposed to reason about this?! Need mechanisms for sharing memory.
Thread 1:
void main(){
count += 1;
}
Thread 2:
void main(){
count -= 1;
}
Thread 3:
void main(){
count += 2;
}

## Slide 64: Outline
Need for Parallelism
Processes and Threads
Concurrency Challenges
Using Threads

## Slide 65: Thread operations
Create threads
  Shares all memory with all threads of the process.
  Scheduled independently of parent
Join thread
  Waits for a particular thread to finish
  Can’t continue computation until all threads finish
That’s it! Don’t really need anything else (for this class)
  Library also includes synchronization primitives to solve data races
Can communicate between threads by reading/writing (shared) global variables
  But we’re only going to read from shared variables for safety
  We’ll write to separate memory locations

## Slide 66: POSIX Threads Library: pthreads
https://man7.org/linux/man-pages/man7/pthreads.7.html
int pthread_create(pthread_t* thread, const pthread_attr_t* attr, void* (*start_routine)(void*), void* arg);
  Thread is created executing start_routine with arg as its sole argument.
  Returning from the start routine exits the thread
void pthread_exit(void* value_ptr);
  Terminates the thread and makes value_ptr available to any successful join
int pthread_join(pthread_t thread, void** value_ptr);
  Suspends execution of the calling thread until the target thread terminates.
  On return with a non-NULL value_ptr the value passed to pthread_exit() by the terminating thread is made available in the location referenced by value_ptr.

## Slide 67: Basic thread example
Main thread
Peer thread
return NULL;
Main thread waits for
peer thread to terminate
exit()
Terminates
main thread and
any peer threads
call Pthread_create()
call Pthread_join()
Pthread_join() returns
printf()
Peer thread
terminates

## Slide 68: Example: parallel sum of array
double array[LEN] = {1, 2, 3, …, LEN};
// determine result sequentially double sequential_sum = 0;
for (int i=0; i<LEN; i++) {
sequential_sum += array[i];
}

## Slide 69: Example: parallel sum of array
double array[LEN] = {1, 2, 3, …, LEN};
Parallelization Plan
Create num_threads different threads
Threads create “partial” sums for their portion of the work
  Each thread does (LEN/num_threads) work
  Create an array for results with one slot per thread
Wait until done, then sum the partial results
  Main thread calls join() to wait for each thread to complete
  Main thread adds up results

## Slide 70: Example: parallel sum of array
Create num_threads different threads
pthread_t tid[num_threads];
for (long i=0; i<num_threads; i++) {
pthread_create(&(tid[i]), NULL, worker, (void*)i);
}
Arguments to pthread_create
  thread_handle, attributes, thread_function, function_argument
Main Thread

## Slide 71: Example: parallel sum of array
2. Threads create “partial” sums for their portion of the work
void* worker(void* arg) {
long i = (long)arg;
int mystart = i * (LEN/num_threads);
int myend = (i+1) * (LEN/num_threads);
partial_sum[i] = 0;
for (int j=mystart; j<myend; j++) {
partial_sum[i] += array[j];
}
pthread_exit(NULL); // Thread work is complete
}
Decide which portion of work this thread should do
Worker Threads

## Slide 72: Example: parallel sum of array
2. Threads create “partial” sums for their portion of the work
void* worker(void* arg) {
long i = (long)arg;
int mystart = i * (LEN/num_threads);
int myend = (i+1) * (LEN/num_threads);
partial_sum[i] = 0;
for (int j=mystart; j<myend; j++) {
partial_sum[i] += array[j];
}
pthread_exit(NULL); // Thread work is complete
}
Do the work
Puts result in its own slot in the partial_sum array (avoids data races)
Worker Threads

## Slide 73: Example: parallel sum of array
3. Wait until done, then sum the partial results
for (int j=0; j<num_threads; j++) {
pthread_join(tid[j], NULL); // second argument is return result
}
double parallel_sum = 0;
for (int k=0; k<num_threads; k++) {
parallel_sum += partial_sum[k];
}
Main Thread

## Slide 74: Trying this out for yourself
See SETI Lab for example code you can run yourself
We just went through a slightly simplified version of parallel-sum-ex.c

## Slide 75: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
Array of 200 million length
No threads created
Only the sequential version is run. Takes about ~878 million cycles to run

## Slide 76: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
$ ./parallel-sum-ex 1 1 200000000
Sequential sum: 19999999900000000 ( 902438479 cycles)
Parallel sum: 19999999900000000 (1169222739 cycles)
Array of 200 million length
1 to thread created. No parallelism for a speedup. Actually, it takes LONGER to run.
Starting threads takes time! Need to make sure they’re doing enough work to be worth it.

## Slide 77: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
$ ./parallel-sum-ex 1 1 200000000
Sequential sum: 19999999900000000 ( 902438479 cycles)
Parallel sum: 19999999900000000 (1169222739 cycles)
$ ./parallel-sum-ex 8 8 200000000
Sequential sum: 19999999900000000 ( 888810917 cycles)
Parallel sum: 19999999900000000 (1033659530 cycles)
Array of 200 million length
8 threads actually has some parallelism
Starts doing better than one thread but needs more parallelism for a big win.

## Slide 78: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
$ ./parallel-sum-ex 1 1 200000000
Sequential sum: 19999999900000000 ( 902438479 cycles)
Parallel sum: 19999999900000000 (1169222739 cycles)
$ ./parallel-sum-ex 8 8 200000000
Sequential sum: 19999999900000000 ( 888810917 cycles)
Parallel sum: 19999999900000000 (1033659530 cycles)
$ ./parallel-sum-ex 16 16 200000000
Sequential sum: 19999999900000000 ( 895258209 cycles)
Parallel sum: 19999999900000000 ( 693511997 cycles)
Array of 200 million length
16 threads starts to win!
I don’t actually have that many cores, but the system is swapping threads whenever memory reads stall to improve performance

## Slide 79: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
$ ./parallel-sum-ex 1 1 200000000
Sequential sum: 19999999900000000 ( 902438479 cycles)
Parallel sum: 19999999900000000 (1169222739 cycles)
$ ./parallel-sum-ex 8 8 200000000
Sequential sum: 19999999900000000 ( 888810917 cycles)
Parallel sum: 19999999900000000 (1033659530 cycles)
$ ./parallel-sum-ex 16 16 200000000
Sequential sum: 19999999900000000 ( 895258209 cycles)
Parallel sum: 19999999900000000 ( 693511997 cycles)
$ ./parallel-sum-ex 32 32 200000000
Sequential sum: 19999999900000000 ( 886174224 cycles)
Parallel sum: 19999999900000000 ( 609774231 cycles)
$ ./parallel-sum-ex 64 64 200000000
Sequential sum: 19999999900000000 ( 898098616 cycles)
Parallel sum: 19999999900000000 ( 426420305 cycles)
Array of 200 million length
32 and 64 threads are really cruising
Down to half the time for the computation

## Slide 80: Running the parallel sum application
$ ./parallel-sum-ex 0 1 200000000
Sequential sum: 19999999900000000 ( 878576632 cycles)
Parallel sum: 0 (44 cycles)
$ ./parallel-sum-ex 1 1 200000000
Sequential sum: 19999999900000000 ( 902438479 cycles)
Parallel sum: 19999999900000000 (1169222739 cycles)
$ ./parallel-sum-ex 8 8 200000000
Sequential sum: 19999999900000000 ( 888810917 cycles)
Parallel sum: 19999999900000000 (1033659530 cycles)
$ ./parallel-sum-ex 16 16 200000000
Sequential sum: 19999999900000000 ( 895258209 cycles)
Parallel sum: 19999999900000000 ( 693511997 cycles)
$ ./parallel-sum-ex 32 32 200000000
Sequential sum: 19999999900000000 ( 886174224 cycles)
Parallel sum: 19999999900000000 ( 609774231 cycles)
$ ./parallel-sum-ex 64 64 200000000
Sequential sum: 19999999900000000 ( 898098616 cycles)
Parallel sum: 19999999900000000 ( 426420305 cycles)
$ ./parallel-sum-ex 128 128 200000000
Sequential sum: 19999999900000000 ( 891919128 cycles)
Parallel sum: 19999999900000000 ( 493951974 cycles)
Array of 200 million length
128 threads is basically the same as 64 threads
Further parallelism isn’t helping very much. (technically worse than 64, but it’s within error bounds on timing)

## Slide 81: Outline
Need for Parallelism
Processes and Threads
Concurrency Challenges
Using Threads

## Slide 82: Outline
Bonus: SIMD Instructions

## Slide 83: SIMD Architectures
Data-Level Parallelism (DLP): Executing one operation on multiple data streams
  SIMD: Single Instruction Multiple Data
Example: Multiplying a coefficient vector by a data vector (e.g. in filtering)
y[i] := c[i] × x[i], 0≤i<n
Sources of performance improvement:
  One instruction is fetched & decoded for entire operation
  Multiplications are known to be independent
  Pipelining/concurrency in memory access as well

## Slide 85: Example SIMD Instructions
To improve performance, Intel’s SIMD instructions
  Fetch one instruction, do the work of multiple instructions
  MMX (MultiMedia eXtension, Pentium II processor family)
  SSE (Streaming SIMD Extension, Pentium III and beyond)
Notes: hardware/assembly language solution

## Slide 86: Example: SIMD Array Processing
for each f in array
f = sqrt(f)
pseudocode
SISD
SIMD
for each f in array {
load f to the floating-point register
calculate the square root
write the result from the register to memory
}
for each 4 members in array {
load 4 members to the SSE register
calculate 4 square roots in one operation
write the result from the register to memory
}

## Slide 87: SIMD in the Real World
Today’s compilers can generate SIMD code!
  But in some cases we get better results by hand
Intel’s x86 implements many SIMD instructions
  Which have the benefit of being usable on lab machines
  (and most of our own personal computers)

## Slide 89: Intel SIMD has been continuously extended

## Slide 90: And it has increased in size a lot

## Slide 91: Intel SIMD Data Types

## Slide 92: SSE Instruction Categories for Multimedia Support
SSE-2+ supports wider data types to allow 16 × 8-bit and 8 × 16-bit operands
Notes: 64 bits operated on simultaneously!

## Slide 93: How do we use these SIMD instructions?
Intrinsics:
  “function calls” that actually just execute an assembly instruction
Example:
_mm_add_epi32(first_values, second_values);
WHAT????

## Slide 94: _mm_add_epi32(first_values, second_values)
MultiMedia extension (They all start with this)
Arguments are Extended Packed Integers, each 32-bits in size (signed)
first_values
second_values
+

## Slide 95
Sooooooo fast

## Slide 96
int add_no_SSE(int size, int *first_array, int *second_array) {
for (int i = 0; i < size; ++i) {
first_array[i] += second_array[i];
}
}
int add_SSE(int size, int *first_array, int *second_array) {
for (int i=0; i + 4 <= size; i+=4) { // only works if (size%4) == 0
// load 128-bit chunks of each array
__m128i first_values = _mm_loadu_si128((__m128i*) &first_array[i]);
__m128i second_values = _mm_loadu_si128((__m128i*) &second_array[i]);
// add each pair of 32-bit integers in the 128-bit chunks
first_values = _mm_add_epi32(first_values, second_values);
// store 128-bit chunk to first array
_mm_storeu_si128((__m128i*) &first_array[i], first_values);
}
...
}
https://www.cs.virginia.edu/~cr4bd/3330/F2017/simdref.html

## Slide 97: You can do this with floating point numbers too!
Packed Double (PD)
Scalar Double (SD)

## Slide 98: Example: Reversing an array in 7 steps (animated)