## Slide 1: Lecture 11 Memory Hierarchy
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2025
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Administrivia
Business as usual
  Bomb Lab due today
  Homework 3 releases later today (maybe tomorrow)
  Attack Lab is out now
Reminder on Attack Lab partnership survey if you want a partner!
Topics remaining in class
  Memory System (Hierarchy, Caches, Virtual Memory)
  Applications (Concurrency, Virtual Memory, Processes)
  Other Systems Introductions (Compilers, Networks)

## Slide 3: Changing the focus of CS213
So far in class we’ve focused on how computers do things
  Represent data
  Run instructions
Now we’re focusing on how to improve those things
  Secure (last lecture plus some stuff in two weeks)
  Efficient (today and next week)
As we’ll show today, the most important thing to speed up is memory
  It is possible and hardware does so already
  Software can be designed to take advantage of this

## Slide 4: Today’s Goals
Hardware day!!
Describe what’s going on inside a processor
  Assembly-to-transistors deep-dive
Explore the memory systems available in modern computers
  Understand capabilities and limitations of each
Discuss the memory hierarchy
  How it improves performance through caching

## Slide 5: Outline
What’s in a processor? Assembly-to-Transistors
Memory Technologies
Memory Hierarchy
Caching Concept

## Slide 6: Assembly into machine code
Machine code are the numerical versions of each instruction
Number breaks down into parts
  Operation
  Source
  Destination
Immediates are stored in the instruction encoding

## Slide 7: Representing instructions as numbers
Why represent instructions as numbers?
Everything in memory is “just a number”
  And instructions go in memory
Hardware can “decode” number to figure out what to do
  Break number apart into bits (just like floating point)
  Some bits pick operation
  Some bits pick register or specify immediate

## Slide 8: Machine code ideas
Example:
  ADD $0x4351FF23, %rax
  ADD with destination %rax translates into 0x05
  Immediate is appended on to that
  Machine code: 0x0523FF5143
Number of bytes for each instruction is variable
  1-15 bytes depending on instruction and operands
  So the processor reads it byte-by-byte to figure out the meaning
Translation is tedious
  We’re not going to do it by hand, although Attack Lab touches it a bit

## Slide 9: Computer Processor (in five easy steps)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 10: These steps are relatively easy (we’ll skip them)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 11: This is extremely complicated for x86-64 (skip it too)
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 12: We can talk about what execution means though!
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 13: Arithmetic Logic Unit (ALU)
Piece of hardware
Takes in two operands
  Source and Destination values
Takes in an Opcode
  Which operation to run
Performs operation and outputs result

## Slide 14: What can an ALU do?
All the basic arithmetic operations
  Add
  Subtract
  Bitwise And
  Bitwise Or
  Bitwise Xor
  Arithmetic Shift Right
  Logical Shift Right
  Logical Shift Left
Complex operations are separate hardware
  Multiply, Divide, Anything floating point

## Slide 15: Let’s zoom in

## Slide 16: Inside an ALU
Input values go into separate hardware blocks for each operation
Every operation occurs in parallel, simultaneously
  We are in hardware so this doesn’t take any additional time
ALU Inputs
64-bit
AND
64-bit
OR
64-bit
ADD/SUB
64
64
64
64
64

## Slide 17: Inside an ALU – selecting the correct output
Selector
ALU Output
ALU Inputs
Opcode
Selects ALU output based on Opcode
64-bit
AND
64-bit
OR
64-bit
ADD/SUB
64
64
64
64
64

## Slide 18: Let’s zoom in

## Slide 19: How is an ALU made?
All of those arithmetic operations can be broken down into a series of 1-bit Boolean operations
  Add is XOR for result + AND for carry
  Subtract is Flip bits (NOT), Add one (XOR + AND), then Add (XOR + AND)
  And/Or/Xor are just their respective operations
  Shifts are just move the bits around (simple in hardware, just move wires)

## Slide 20: 64-bit OR operation
Perform OR operation on each individual bit
  Pictured is a series of 1-bit OR gates
64-bit
OR
A62 B62 A63 B63
Result62
Result63
64
64
64

## Slide 21: 64-bit ADD operation
Below is the 1-bit version with carry-in/out
  Two 1-bit AND, two 1-bit XOR, one 1-bit OR
  Repeat 64 times, connecting carries together
A62 B62
A63 B63
Result62
Result63

## Slide 22: Let’s zoom in

## Slide 23: Logic gates can be created with transistors
CMOS implementation of logic gates
  Complementary Metal-Oxide Semiconductor
Transistors are just on/off switches

## Slide 24: Let’s zoom in

## Slide 25: Transistors are made out of silicon and other materials
Turning gate on/off causes source and drain to connect or disconnect
  Acts as a switch
We can make very small transistors
  Handfuls of nanometers in size

## Slide 26: That’s the bottom

## Slide 27: Zooming out again
Transistors make logic gates
1-bit AND gate
F
~6 transistors

## Slide 28: Zooming out again
Logic gates make operations
1-bit AND gate
1-bit ADD operation
~30 transistors

## Slide 29: Zooming out again
1-bit operations make 64-bit operations
1-bit ADD operation
~1000 transistors
A62 B62
A63 B63
Result62
Result63

## Slide 30: Zooming out again
Operations make an ALU
Selector
ALU Output
ALU Inputs
Opcode
~20K transistors
A62 B62
A63 B63
Result62
Result63
64
64
64
64
64
64-bit
AND
64-bit
OR

## Slide 31: ALU allows us to execute operations
Reads instruction from memory
Decodes it into an Operation plus Configurations
  Immediates, Registers, Memory, etc.
Reads from source (based on configuration)
Executes that operation
Writes to destination (based on configuration)

## Slide 32: All the way back to software
Machine code specifies what should be executed
Assembly translates into machine code
C compiles into assembly

## Slide 33: Break + Open Question
We hit roughly 20 thousand transistors for an ALU, but a modern processor has more than 1 billion transistors. Where are all the rest going?

## Slide 34: Break + Open Question
We hit roughly 20 thousand transistors for an ALU, but a modern processor has more than 1 billion transistors. Where are all the rest going?
  Decoding instructions
  Multiple processor cores (each with multiple ALUs and decoders)
  Graphics
  Other peripheral devices
    USB, HDMI, Ethernet, etc.
  Memory!
    Registers and Caches (especially caches)

## Slide 35: A processor is just a lot of transistors connected very carefully
ALU plus other operations make up a Core
  Decode logic, floating point, registers, etc.
Multiple cores plus caches make up a Processor
  And other stuff these days like graphics

## Slide 36: Outline
What’s in a processor? Assembly-to-Transistors
Memory Technologies
Memory Hierarchy
Caching Concept

## Slide 37: Reminder: metric unit prefixes
Going to talk about nanometers and nano/micro/milliseconds today
Also we do frequently mention bytes, kilobytes, megabytes, gigabytes, etc.
For perspective
  1 Megasecond ≈ 11 days
  1 Gigasecond ≈ 31 years
Prefix | Symbol | Power | Decimal Value
Peta | P | 1015 | 1 000 000 000 000 000
Tera | T | 1012 | 1 000 000 000 000
Giga | G | 109 | 1 000 000 000
Mega | M | 106 | 1 000 000
Kilo | k | 103 | 1 000
- |  | 100 | 1
milli | m | 10-3 | 0.001
micro | μ | 10-6 | 0.000 001
nano | n | 10-9 | 0.000 000 001
pico | p | 10-12 | 0.000 000 000 001

## Slide 38: Storage in a Computer System
Data can be stored in different places
  Registers, caches, memory, disk, etc.
Hugely different characteristics
  Storage size
    x86-64: 16 registers. 128 B total (not including FP registers, etc.)
    Memory is measured in GB, disks in TB
  Latency (i.e., time to access data)
    Registers are really fast, memory less so, disk is incredibly slow
  Cost per byte
    Registers are really expensive, disks are really cheap, memory somewhere in the middle
Each serves a different purpose in a system
  Can design systems to get the best of all worlds (in most cases)

## Slide 39: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus

## Slide 40: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Registers and Caches

## Slide 41: Register storage
x86-64
  16 registers (general-purpose) with 8 bytes each
  32 registers (special-purpose) with up to 64 bytes each
  Plus some other odds and ends (%rip, flags, segments, etc.)
128 bytes for general purpose registers
Order 2-3 kB for everything
Accesses are very fast. Within a single processor cycle
  Usually, 0.25-4 cycles per instruction

## Slide 42: Register technology: SRAM
Static RAM (SRAM)
  Each cell stores a bit in a bi-stable circuit, typically a six-transistor circuit
  Static – no need for periodic refreshing; keeps data while powered
  Relatively insensitive to disturbances such as electrical noise
    Energetic particles (alpha particles, cosmic rays) can flip stored bits
Fastest memory on computer
  Also most expensive and takes up most space per bit
  Typically used for registers and cache memories

## Slide 43: Cache memories (a.k.a. caches)
Memory in the processor that duplicates portions of main memory
  Goal: speed up accesses to frequently used data
  Complicated part: what’s in the cache at any given moment
    Many configurations to try to improve the “hit rate” on data
Not general-purpose memory
  Can’t be directly accessed and doesn’t have memory addresses
  Hardware automatically chooses what’s in the cache
Cache sizes
  Kilobytes to Megabytes of storage: ~1-100 MB total in modern processors

## Slide 44: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
RAM

## Slide 45: Main memory
The “RAM” in your computer
  Random Access Memory
  Can access any byte you want in “random” order
Typically measured in GB
  1-128 GB
  Some special purpose systems may have MUCH less or more
This is the “array of bytes” we’ve been using in assembly
  Program memory lives in RAM

## Slide 46: Main memory technology: DRAM
Dynamic RAM (DRAM)
  Each cell stores a bit as a charge in a capacitor
  Capacitors lose charge; each cell must be refreshed every 10-100 ms
  More sensitive to disturbances (EMI, radiation, …) than SRAM
Slower than SRAM, but cheaper and denser
  ~100x slower than registers
Typically used for main memory

## Slide 47: Accessing DRAM
Read entire row of data at a time
  Large in practice, kilobytes
Select actual bytes that are wanted
  Possibly modifying those bits
Write row back to memory
  Must always happen!
  Reading is destructive

## Slide 48: Connecting main memory and the processor
Data flows between main memory and processor over “buses”
  A collection of parallel wires that carry address, data, and control signals
  Typically shared by multiple devices
main
memory
I/O
bridge
bus interface
ALU
register file
CPU chip
memory bus
Includes memory controller
movl A, %eax (load)
Processor writes address A to the bus
Memory writes data to the bus
Processor reads data from the bus
movl %eax, A (store)
Processor writes address A to the bus
Processor writes data to the bus
Memory reads data from the bus
system bus

## Slide 49: Sidebar: memory security is important
Data in RAM disappears without power
  But the rate depends on temperature, minutes to decay if frozen
  Cold Boot Attack: freeze RAM to remove from computer and steal contents

## Slide 50: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Disk: Hard drive or SSD

## Slide 51: Disk storage
Workhorse storage devices
  Terabytes in size in modern computers
  Milliseconds to read
    100,000x longer than reading from RAM
    10,000,000x longer than reading from registers
Used for filesystem storage
  Running programs do not directly use disk except when interacting with files
IBM 350 Disk Storage Unit
First disk drive, 1956
Seagate 24TB HDD, 2025
4 inches (102 mm)
Storage?
5MB! (these slides are 8 MB)
Basic mechanisms the same!
5.75 inches (146 mm)

## Slide 52: Disk types

## Slide 53: Hard disk drive operation
The disk surface
spins at a fixed
rotational rate
(5400-15000 RPM)
spindle
By moving radially, the arm can position the read/write head over any track.
The read/write head
is attached to the end
of the arm and flies over
the disk surface on
a thin cushion of air.
spindle
spindle
spindle
spindle
arm
read/write heads
move in unison
from cylinder to cylinder
spindle

## Slide 54: Disk heads read/write data to the platters

## Slide 55: Animation of Disk Access

## Slide 56: Writing bits to the platters
Note: most disks can only move the entire set of arms, not two sets of them

## Slide 57: Accessing data on disk
Three-step process
  Read head needs to move to the right cylinder: seek time
  Platter turns until start of sector under the read head: rotational latency
  Sector passes under read head and data is read: transfer time
Time cost dominated by seek time and rotational latency
  Consequence: reading first bit of a sector is expensive
  But reading the rest of the sector is basically free!
When using disks, best to favor large sequential reads/writes
  Terrible for random access! (reading a little bit here, a little bit there)
  Fits file access well (read/write in order)
    But overall still really slow compared to main memory or registers

## Slide 58: Disk types

## Slide 59: Floating-gate transistors
Concept behind transistor-based non-volatile memory
  EPROM, EEPROM, and Flash
  High voltage on control gate creates charge on floating gate
  Charge on floating gate activates/deactivates transistor
High voltage degrades structure, leading it to eventually fail after enough writes

## Slide 60: Solid State Drives (SSDs)
Flash memory
  Just like Flash Drives
Pages: 2KB to 512KB, Blocks: 32 to 128 pages
Data read/written in units of pages
Page can be written only after its block has been erased
  Need to copy rest of the data to not lose it. Expensive!
A block wears out after repeated writes (10k – 100k writes) and can no longer be used
Flash
translation layer
I/O bus
Page 0
Page 1
Page P-1
…
Block 0
…
Page 0
Page 1
Page P-1
…
Block B-1
Flash memory
Solid State Disk (SSD)
Requests to read and
write logical disk blocks
Notes: SSD based on flash memory (non-volatile memory based on EEPROM – electrically erasable programmable ROM)
Plugs into a standard disk slot – typically USB or SATA
Made of a few chips and a flash translation layer, a hw/firmware piece similar to a disk controller

## Slide 61: SSDs vs Rotating Disks
Advantages
  No moving parts  faster, less power, more rugged
Disadvantages
  Have the potential to wear out
    Mitigated by “wear leveling logic” in flash translation layer
    Order petabyte (1015 bytes) of random writes before they wear out
  More expensive per byte (but getting cheaper)
    2025: HDD $0.012 per GB, SSD $0.042 per GB (about 4x the cost)
Applications
  Portable electronics (phones, tablets, etc.)
  Began to appear in desktops and servers circa 2007
  Now common on laptops as well
Biggest speed improvement to your computer:
Get an SSD

## Slide 62: Reading memory from disk
Data from disk is always read into Main Memory
Direct Memory Access (DMA)
  Processor starts a read and then returns to programs
  Disk performs the read, transfers data, then notifies processor when done
main
memory
ALU
register file
CPU chip
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
bus interface

## Slide 63: Tour of computer memory
Main
memory
I/O
bridge
Processor
System bus
Memory bus
Disk
controller
Graphics
adapter
USB
controller
Mouse
Keyboard
Display
Disk
I/O bus
Disk: Hard drive or SSD
RAM
Registers and Caches

## Slide 64: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works

## Slide 65: Break + Question
How do you make an SSD with a longer lifetime (more writes)?
  Without changing any of the physics of how it works
  Secretly make it larger than it claims to be
    e.g. 200 GB when it claims to be 100 GB
  Behind the scenes move around memory as necessary so the device can still hold 100 GB even if half of the flash is
    Maintain a mapping of which data is located where

## Slide 66: Outline
What’s in a processor? Assembly-to-Transistors
Memory Technologies
Memory Hierarchy
Caching Concept

## Slide 67: Computing timescales
Assuming 4 GHz processor, Instruction (with registers): 0.25 ns
Jeff Dean (Google AI): “Numbers Everyone Should Know”
Reminder:
1,000,000,000 ns per second

## Slide 68: Jim Gray’s storage latency analogy
How “far” is data for the CPU, converted to human scale
Storage
Distance
Time
Registers
On-chip cache
On-board cache
Main memory
Disk
Tape
In my apartment
Across the street
A few blocks away
In Milwaukee
On Mars
On Kepler-76b
~1 minute
2-4 minutes
10 minutes
1.5 hours
2 years
2000 years (at speed of light)
Jim Gray
Turing Award 1998

## Slide 69: The CPU-Memory gap
Increasing gap between DRAM, disk, and CPU speeds.
SRAM roughly keeping up
DRAM, disk and CPU
performance gap widening
Split reflects the introduction of multicores
Disk
DRAM
CPU
SSD
SRAM
Notes: In early 21st century computer manufacturers discover they couldn’t keep increasing CPU clock freq. because chips would consume too much power; answer was multicore – there you see the cycle times getting slower but effective cycle times keeping about the same improvement rate

## Slide 70: The CPU-Memory Gap
CPUs outspeed memory
  But they can’t compute on data they don’t have!
  If the CPU has to wait for data to reach it, it just sits idle!
    All that engineering effort, just sitting around waiting…
Challenge: get data to the CPU despite “slow” memory
  So the CPU can work at full speed, without waiting for data
Two-pronged strategy
  Memory hierarchy: keep data we need closer to the CPU
  Locality of reference: predict which data we’re likely to need

## Slide 71: Memory hierarchy
Some fundamental and enduring properties of systems
  The faster the storage, the more expensive ($) it is
  The faster the storage, the smaller (capacity) it is
  The gap between processor and main memory speed is widening
Key idea: keep the data you need the most in fast memory!
  Data you only need from time to time can be in slow memory, no big deal
  Most used data goes in registers
  Least used data goes to disk
Analogy: kitchen ingredients I use
  Salt, all the time: it sits out on the counter
  Oregano, frequently: front of the cabinet
  Onion powder, occasionally: back of the cabinet
  Brown sugar, sometimes: somewhere in the pantry
  Saffron, never: I can go buy some if I do need it

## Slide 72: Memory hierarchy
registers
on-chip L1
cache (SRAM)
main memory
(DRAM)
local secondary storage
(local disks)
Larger,
slower,
and
cheaper
(per byte)
storage
devices
remote secondary storage
(distributed file systems, Web servers)
Local disks hold files retrieved from disks on remote network servers.
Main memory holds disk
blocks retrieved from local
disks.
off-chip L2
cache (SRAM)
L1 cache holds cache lines retrieved from the L2 cache memory.
CPU registers hold words retrieved from L1 cache.
L2 cache holds cache lines retrieved from main memory.
L0:
L1:
L2:
L3:
L4:
L5:
Smaller,
faster,
and
costlier
(per byte)
storage
devices

## Slide 73: Outline
What’s in a processor? Assembly-to-Transistors
Memory Technologies
Memory Hierarchy
Caching Concept

## Slide 74: Caching, general principle
Cache: A smaller, faster storage device that acts as a staging area for a subset of the data in a larger, slower device
  Data lives in both places (typically)
  When the consumer (e.g., CPU) reads the data, it gets it from the smaller, faster storage
  If the data we want is not in the cache, we pay the full cost of bringing it over from the larger, slower storage into the smaller, faster storage
    The hope: we don’t need to do it too often
Fundamental idea in systems. Shows up all over!
  Memory hierarchies
  Content delivery networks (CDNs) on the Internet (Akamai, Cloudflare, etc.)

## Slide 75: Caching in a memory hierarchy
Fundamental idea of a memory hierarchy
  For each k, the faster, smaller device at level k serves as a cache for the larger, slower device at level k+1
    L2 cache memory as a cache for main memory
    Main memory as a cache for disk, etc.
  Each level stores some of the most frequently accessed data
  The closer the cache is to the processor, the “hotter” the cached data

## Slide 76: Memory hierarchies make memory fast and large
Why do memory hierarchies work?
  Programs tend to access the data at level k more often than they access the data at level k+1
  Thus, the storage at level k+1 can be slower, and thus larger and cheaper per bit
Net effect:
  A large pool of memory that costs as little as the cheap storage near the bottom, but that serves data to programs at the rate of the fast storage near the top
  Best of both worlds!

## Slide 77: Caching in a memory hierarchy
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Larger, slower, cheaper storage
device at level k+1 is partitioned
into blocks.
Data is copied between
levels in block-sized transfer units
8
9
14
3
Smaller, faster, more expensive
device at level k caches a
subset of the blocks from level k+1
Level k:
Level k+1:
Blocks cannot be stored in an arbitrary location!
They can only live at one of a fixed set of locations.
In this example: they must be in the same “column” for both levels.

## Slide 78: General caching concepts
Request
14
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
14
14
4*
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14

## Slide 79: General caching concepts
12
Request
12
Program needs object d, which is stored in some block b
Cache hit
  Program finds b in the cache at level k e.g., block 14
Cache miss
  b is not at level k, so the level k cache must fetch it from level k+1, e.g., block 12
  If the level-k cache is full, then some current block must be replaced (evicted). Which one is the “victim”?
    Here, we pick 4; same column as 12
    4 is “dirty”, need to write back to k+1
    More on this next lecture
9
3
0
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
Level
k:
Level
k+1:
14
12
4*
Request
12
4*
4*
12
12
“ * ” means the block is dirty (i.e., it has been modified)

## Slide 80: What causes a cache miss?
Cold (compulsory) miss
  Cold misses occur when a block is accessed for the first time
  No one ever accessed it, so there wasn’t any reason to bring it into cache
Capacity miss
  Occurs when the set of active cache blocks (working set) is larger than the cache
  There’s no way the working set can all fit in the cache, so there will be misses
Conflict miss
  In most caches, blocks cannot be stored in any available slot
  If two blocks need to go in the same slot, need to evict the old one to store the new!
  If after that, we need to access the old block, conflict miss!
    We had a conflict, evicted a block, and now we miss trying to access that block
  Note: can happen even when there is “room” elsewhere in the cache!
  We’ll show examples of this next lecture

## Slide 81: Break + Question
When you first start up a program, it runs really slowly for a few seconds. What kind of cache misses are occurring?
When you have too many browser tabs open and active, all of the tabs run more slowly. What kind of cache misses are occurring?
Miss types: Cold, Capacity, Conflict

## Slide 82: Break + Question
When you first start up a program, it runs really slowly for a few seconds. What kind of cache misses are occurring?
  Cold (aka Compulsory) misses. The data has never been loaded before!
When you have too many browser tabs open and active, all of the tabs run more slowly. What kind of cache misses are occurring?
  Capacity misses. You have too much data to fit it all in the cache
    Could be Conflict misses as well, but probably not
Miss types: Cold, Capacity, Conflict

## Slide 83: Outline
What’s in a processor? Assembly-to-Transistors
Memory Technologies
Memory Hierarchy
Caching Concept