## Slide 1: Lecture 05 Intro to x86-64 Assembly
CS213 – Intro to Computer Systems
Branden Ghena – Winter 2026
Slides adapted from: St-Amour, Hardavellas, Bustamente (Northwestern), Bryant, O’Hallaron (CMU), Garcia, Weaver (UC Berkeley)

## Slide 2: Reminders
Homework 1
  Due by 11:59 pm on Thursday (January 22), submit on Gradescope
  No late submissions!
Pack Lab
  Due in one week from today (Tuesday, January 27)
  If you haven’t yet, get started right away!
    Lots of conceptually difficult parts to understand
    Lots of C code to write, which you may have forgotten
  Especially, make sure you don’t have issues logging into Moore
    Takes ~24 hours to fix and we won’t be giving extensions for it
  This assignment is 12% of your overall course grade, and takes at least that much effort
    Not an “easier first assignment”

## Slide 3: Midterm Exam 1
Tuesday, January 27th (one week from today)
  In this classroom
  We’ll start handing out exams at 2pm, so be here on time
  Bring one 8.5”x11” notes sheet with whatever you want on front/back
    And a pencil or two!
Contents
  Lectures 1-4: Introduction, Data Representations, Data Operations, Floating Point
  Assembly will not be on this exam
Prior exams posted on Canvas homepage
  With irrelevant questions crossed out

## Slide 4: Today’s Goals
Introduce assembly and the x86-64 Instruction Set Architecture
  Discuss background of the factors that affected its evolution
Understand registers: the analogy to variables in assembly
Explore our first assembly instruction: mov

## Slide 5: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes

## Slide 6: Assembly (Also known as: Assembly Language, ASM)
Purpose of a CPU: execute instructions
High-level programs (like in C) are split into many small instructions
Assembly is a low-level programming language where the program instructions match a particular architecture’s operations
  Assembly is a human-readable text representation of machine code
  Each assembly instruction is one machine instruction (usually)

## Slide 7: Programs can be written in assembly or machine instructions
C Program (source code)
a = (b+c)–(d+e);
    Assembly Program
      addq %rdi, %rsi
      addq %rdx, %rcx
      subq %rcx, %rsi
      movq %rsi, %rax
Machine Instructions
0x4889D3
0x488903
0x53 0x5B

## Slide 8: There are many assembly languages
Instruction Set Architecture: All programmer-visible components of a processor needed to write software for it
  Operations the processor can execute
  The system’s state (registers, memory, program counter)
  The effect operations have on system state
Each assembly language has instructions that match a particular processor’s Instruction Set Architecture (ISA)
Assembly is not portable to other architectures (like C is)

## Slide 9: Which instructions should an assembly include?
Each assembly language has its own operations
There are some obviously useful instructions:
Add, subtract, and bit shift
Read and write memory
But what about:
Only run the next instruction if these two values are equal
Perform four pairwise multiplications simultaneously
Add two ascii numbers together (‘2’ + ‘3’ = 5)
Notes: Add two ascii numbers is a real x86 instruction. No joke

## Slide 10: Instruction Set Philosophies
Early trend: add more instructions to do elaborate operations Complex Instruction Set Computing (CISC)
  Handle many different types of operations
  More options for the compiler
  Complicated hardware runs more slowly
Opposite philosophy later began to dominate: Reduced Instruction Set Computing (RISC)
  Simpler (and smaller) instruction set makes it easier to build fast hardware
  Let software do the complicated operations by composing simpler ones
Modern reality is somewhere between these two

## Slide 11: Mainstream Instruction Set Architectures
PCs & Servers
(Intel & AMD processors)
x86 Instruction Set
Open-source, designed for cloud computing, embedded systems, academic use RISCV Instruction Set
Smartphones (iPhone, Android), Apple Hardware, Raspberry Pi, Embedded systems
ARM Instruction Set

## Slide 12: Instruction Set Architecture sits at software/hardware interface
C Language
x86-64
Intel Pentium 4
Intel Core i7
AMD Ryzen 7600
GCC
AArch64/A64 (ARMv8-v9 )
ARM Cortex-A53
Apple M4
Clang
Program B
Program A
Compiler
Source code
Architecture
Different applications
or algorithms
Perform optimizations,
generate instructions
Different implementations
Hardware
Instruction set

## Slide 13: Intel x86 Processors
Dominate desktop and server market, and Windows laptops
  No longer completely dominant in laptops though (MacOS moved to ARM)
Complex instruction set computer (CISC)
  Many different instructions with many different formats
  But only small subset encountered by normal programs
Design evolved over time
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
  Historical legacy has large impact on architecture

## Slide 14: Moore’s Law – CPU transistors counts
“Number of transistors in a chip doubles every 18 months”
Transistors are getting exponentially smaller!
How small? Today: 3nm!
< ½ the size of most viruses!
Notes: Gordon Moore – first version of the law – ’65: double every year; restated in ‘75: double every two years
Was simplified to “every 18 months”

## Slide 15: Evolution of x86 ISA
Name | Date | Transistors | Comments
8086 | 1978 | 29k | 16b processor, basis for IBM PC & DOS; 1MB address space
80286 | 1982 | 134K | Elaborate (!useful) addressing; basis for IBM PC and Windows
386 | 1985 | 275K | Extended to 32b, added “flat addressing” that Linux/gcc uses
486 | 1989 | 1.9M | Improved performance; integrated FP unit into chip
Pentium | 1993 | 3.1M | Improved performance
PentiumPro | 1995 | 6.5M | Conditional move instructions; big change in microarch. (P6)
Pentium II | 1997 | 7M | Merged Pentium/MMZ + PentiumPro, MMX instructions within P6
Pentium III | 1999 | 8.2M | Integer and floating point vector instructions (SSE); Level2 cache
Pentium 4 | 2001 | 42M | 8B ints and floating point formats to vector instructions
Pentium 4E | 2004 | 125M | Hyperthreading (able to run 2 programs simultaneously), 64b
Core 2 | 2006 | 291M | P6-like, multicore, no hyperthreading
Core i7 (Nehalem) | 2008 | 781M | Hyperthreading + multicore, TurboBoost (run fewer cores faster)
Core i3 (Nehalem) | 2010 | 383M+177M | GPU on second silicon die within package (at 2010 version)
Core i3, i5, i7 (Sandy Bridge) | 2011 | 997M (i7 – 4 cores) | Cores and GPU within the same processor die
Core i3, i5, i7 (Ivy Bridge) | 2012 | 1400M (i7 – 4 cores) | Tri-gate transistors, much lower power consumption
Xeon E7 8800 V4 (Broadwell-EX) | 2016 | >5690M (22 cores) | 14nm technology
Notes: The x86 processor line has a long evolutionary development; started with a 16b microprocessor …
This is a list of some notable models, dates and a few key features
386 – first 32b, added flat addressing for Linux
Pentium 4E – hyperthreading and 64b
Core 2 – first multicore from Intel
Each successive processor has been designed to be backward compatible – able to run code from previous version; many strange artifacts result from this

## Slide 16: Backwards Compatibility The cause of, and solution to, all of life’s problems.
Programs that worked on one x86 processor should keep working on the next one
  Old programs work on new processors, which makes upgrading possible
  Even today’s x86-64 processors boot thinking they are 8086s!
Adding powerful new features while keeping backwards compatibility is a careful balancing act
  Backwards compatibility introduces a lot of constraints
  May rule out “cleaner” designs that would break existing programs
  The cause of some “surprising” aspects of the design of x86-64
  “The x86 really isn't all that complex—it just doesn't make a lot of sense.” — Mike Johnson (AMD's x86 architect), 1994
Not just a hardware thing!

## Slide 17: In this class
x86-64: the current standard (also known as x64)
  Some asides on IA32: The traditional x86
Presentation
  Book covers x86-64; web aside on IA32
  Labs will be based on x86-64

## Slide 18: Break + Question
What instruction set does your laptop, tablet, or smartphone use?
Steps (google each of these):
  Determine what processor it has
  Determine what ISA (instruction set architecture) that processor uses
Macbook: M-series -> ARM
  Older Intel hardware (2020 and prior) -> x86-64
Windows laptop: almost definitely x86-64
iOS or Android tablets/phones: almost definitely ARM
Bonus: Playstation/Xbox -> x86-64, Nintendo -> ARM

## Slide 19: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes

## Slide 20: Hardware uses registers for variables
Unlike C, assembly doesn’t have variables as you know them
  Instead, assembly uses registers to store values
Registers are:
  Small memory chunks of a fixed size
  Can be read or written
  Limited in number
  Very fast and low power to access
Registers are different from variables or RAM:
  They don’t have an address
    We can only access them in assembly
  They don’t have types (just bits)
    The operation performed determines how contents are treated

## Slide 21: How many registers?
Tradeoff between speed and availability
  More registers can hold more variables
  Simultaneously; all registers are slower
  Also registers take physical space within the chip
x86-64 has 16 registers (for integer operations)
  Historically only 8 registers 😱
  Added 8 more with 64-bit extensions

## Slide 22: How big should each register be?
Registers are usually the size of a word
  The natural unit of data for a processor
  Width of the data type that a CPU can process in one instruction
    Likely the size of its registers
  Imprecise term that will inevitably slip into explanations
x86 processors started with 16-bit words
IA32 upgraded to 32-bit “double word” registers
x86-64 upgraded again 64-bit “quad word” registers

## Slide 23: Why did we change the register size??
Registers need to be able to hold memory addresses
So, the size of a register limits the total size of memory!!
  Each address is a single byte of memory
Memory limitations based on register size
  16-bit registers: 216 addresses = 216 bytes = 64 KB of RAM
  32-bit registers: 232 addresses = 232 bytes = 4 GB of RAM
  64-bit registers: 264 addresses = 264 bytes = 16 EB of RAM
    Kilobyte, Megabyte, Gigabyte, Terabyte, Petabyte, Exabyte
We moved to 32-bit in the early 90s and 64-bit in the late-00s
  No computer has 128-bit words, although many have special-purpose registers that big

## Slide 24: x86-64 64-bit Integer Registers
%r8
%r9
%r10
%r11
%r12
%r13
%r14
%r15
%rsp
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
original x86 registers
additional x86-64 registers

## Slide 25: Historical Register Purposes
Accumulate
Base
Counter
Data
Source Index
Destination Index
Stack Pointer (still important)
Base Pointer
%rsp
%rax
%rbx
%rcx
%rdx
%rsi
%rdi
%rbp
Name Origin (mostly obsolete)

## Slide 26: x86-64 Register Access Options
Registers can be accessed by any of these names to work with 8-byte, 4-byte, 2-byte, or 1-byte data

## Slide 27: x86-64 Register Access Options
The same data can be accessed under different names and widths
Example: store 64-bit value 0x0000000000010A0B in %rax
  %rax: 0x0000000000010A0B (64-bit)
  %eax: 0x00010A0B (32-bit)
  %ax: 0x0A0B (16-bit)
  %al: 0x0B (8-bit)

## Slide 28: x86-64 full register naming
%rax
%eax
%ax
%ah
%al
%rbx
%ebx
%bx
%bh
%bl
%rcx
%ecx
%cx
%ch
%cl
%rdx
%edx
%dx
%dh
%dl
%rsi
%esi
%si
%rdi
%edi
%di
%rbp
%ebp
%bp
%rsp
%esp
%sp
%r8
%r8d
%r8w
32-bit registers
16-bit registers
8-bit
…
%r15
%r15d
%r15w
…
…
%sil
%dil
%bpl
%spl
%r8b
%r15b
64-bit registers
8-bit

## Slide 29: Registers versus Memory
What if there are more variables than registers?
  Keep most frequently used in registers and move the rest to memory (called spilling to memory)
Why not put all variables in memory?
  Smaller is faster: registers 100-500 times faster
  Memory Hierarchy
    Registers: 16 registers * 64 bits = 128 Bytes
    RAM: 4-32 GB (4-32 billion bytes)
    SSD: 100-1000 GB (0.1-1 trillion bytes)

## Slide 30: Memory Hierarchy
Memory
Registers

## Slide 31: Special-purpose register: Instruction Pointer
Instruction Pointer: %rip (not listed in prior tables)
  Contains the address of the currently executing instruction
  Special-purpose: only used for this one thing
Processor hardware uses %rip when loading instructions
  Load instruction from memory pointed to by %rip
  Advance %rip to the next instruction
  Repeat
  Note: hardware does this automatically, you don’t (usually) interact with this at all

## Slide 32: Assembly Programmer’s View of System State
CPU
Programmer-visible state
  Named registers
    Together in “register file”
    Heavily used program data
  The Instruction Pointer (%rip in x86-64)
    Address of next instruction
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Code
Data
Stack
Addresses
Data
Instructions
Condition
Codes
  Memory
    Byte-addressable array
    Code and user data
    Includes the Stack (for supporting procedures and variables)
Notes: Preview for the coming lectures

## Slide 33: Break + Question
Which of these is FALSE?
  [A] Registers are faster to access than memory
  [B] Registers do not have a type
  [C] Registers can have special purposes
  [D] Registers are dynamically created as needed

## Slide 34: Break + Question
Which of these is FALSE?
  [A] Registers are faster to access than memory
  [B] Registers do not have a type
  [C] Registers can have special purposes
  [D] Registers are dynamically created as needed
  There are a fixed number of registers for a given architecture

## Slide 35: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes

## Slide 36: Writing Assembly Code? In 2026???
Chances are, you’ll never write a program in assembly, but understanding assembly is the key to the machine-level execution model:
  Behavior of programs in the presence of bugs
    When high-level language model breaks down
  Tuning program performance
    Understanding compiler optimizations and sources of program inefficiency
  Implementing systems software
    What are the “states” of processes that the OS must manage
    Using special units (timers, I/O co-processors, etc.) inside processor!
  Fighting malicious software
    Distributed software is in binary form
Notes: Compilers are much better and more patient than you are
I hope that you are never writing a program in assembly
  Not even to eke the very last bit of performance out
  Because compilers are much better at it
Understanding assembly will help you
  Like how C will help you better appreciate the magic that Java does for you
  Similarly, understanding assembly will help you understand what the machine is doing for you
  Sometimes you actually do have to poke around with GDB in the assembly (this is what gets shipped to you!)

## Slide 37: Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret

## Slide 38: Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret
Various assembly instructions

## Slide 39: Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret
Comments use the # symbol

## Slide 40: Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret
Labels are arbitrary names that mark a section of code
We’ll get back to these later

## Slide 41: Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret
Assembler directives
(mostly ignore these)
Can be used to specify data versus code regions, make functions linkable with other code, and many other tasks.

## Slide 42: x86-64 Instructions
General Instruction Syntax:
op src, dst
  1 operator, 2 operands
    op = operation name (“operator”)
    src1 = source location (“source”)
    dst = destination location (“destination”)
Keep hardware simple via regularity

## Slide 43: Careful! Two Syntaxes for Assembly
Intel/Microsoft mnemonics vs. ATT
  Operands listed in opposite order: mov Dest, Src vs. movl Src, Dest
  Constants not preceded by ‘$’, Denote hex with ‘h’ at end: 100h vs. $0x100
  Operand size indicated by operands rather than operator suffix: sub vs. subq
  Addressing format shows effective address computation: [eax*4+100h] vs. $0x100(,%rax,4)
gcc (gas), gdb, objdump work on the ATT format
  We will always use the ATT format as well
lea eax,[ecx+ecx*2]
sub esp,8
cmp dword ptr [ebp-8],0
mov eax,dword ptr [eax*4+100h]
leal (%ecx,%ecx,2),%eax
subl $8,%esp
cmpl $0,-8(%ebp)
movl $0x100(,%eax,4),%eax
Intel/Microsoft Format
ATT Format
Notes: ATT named after AT&T who used to operate Bell Labs many years ago; ATT is what gcc, objdump, etc consider

## Slide 44: Short Break + Example x86-64 Assembly
.text
.globl multstore
.type multstore, @function
# multiply and store to memory
multstore:
  pushq %rbx # save to stack
  movq %rdx, %rbx
  call mult2
  movq %rax, (%rbx)
  popq # restore from stack
  ret
What might this instruction do?
(op src, dst)

## Slide 45: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes

## Slide 46: Three Basic Kinds of Instructions
Transfer data between memory and register
  Load data from memory into register
    %reg = Mem[address]
  Store register data into memory
    Mem[address] = %reg
Perform arithmetic operation on register or memory data
  c = a + b; z = x << y; i = h & g;
Control flow: what instruction to execute next
  Unconditional jumps to/from procedures
  Conditional branches
    Remember: Memory is indexed just like an array of bytes!

## Slide 47: Copying Data with the “move” instruction
General form: mov_ source, destination
  Very common instruction in typical code. Copies value into destination location
  Missing letter _ specifies size of operands
  Reminder: backwards compatibility means “word” = 16 bits
movb src, dst
  Move 1-byte “byte”
movw src, dst
  Move 2-byte “word”
movl src, dst
  Move 4-byte “long word”
movq src, dst
  Move 8-byte “quad word”
  Native size for x86-64
Note: Instructions must be used with properly-sized register names And they’re also a helpful hint about the sizes being used

## Slide 48: Operand Types (src and dst)
Immediate: Constant integer data
  Examples: $0x400, $-533
  Like C literal, but prefixed with ‘$’
  Encoded with 1, 2, 4, or 8 bytes depending on the instruction
Register: 1 of 16 integer registers
  Examples: %rax, %r13
  But %rsp reserved for special use
Memory: Consecutive bytes of memory at a computed address
  Simplest example: (%rax) treats value of %rax as an address → access memory
  Various other “address modes” we’ll talk about later
%rax
%rcx
%rdx
%rbx
%rsi
%rdi
%rsp
%rbp
%rN (r8-r15)

## Slide 49: MOV Operand Combinations
 | Source | Dest | Src, Dest | C Analog
movq | Imm | Reg |  | 
 |  | Mem |  | 
 | Reg | Reg |  | 
 |  | Mem |  | 
 | Mem | Reg |  | 
var_a = 0x4;
*p_a = -147;
var_d = var_a;
*p_d = var_a;
var_d = *p_a;
Cannot do memory-memory transfer with a single instruction
  How would you do it?
movq $0x4, %rax
movq $-147, (%rax)
movq %rax, %rdx
movq %rax, (%rdx)
movq (%rax), %rdx
Notes: Mem -> Reg
Reg -> Mem
movq (%rax), %rdx
movq %rdx, (%rbx)

## Slide 50: MOV Operand Combinations
 | Source | Dest | Src, Dest | C Analog
movq | Imm | Reg | movq $0x4, %rax | 
 |  | Mem | movq $-147, (%rax) | 
 | Reg | Reg | movq %rax, %rdx | 
 |  | Mem | movq %rax, (%rdx) | 
 | Mem | Reg | movq (%rax), %rdx | 
var_a = 0x4;
*p_a = -147;
var_d = var_a;
*p_d = var_a;
var_d = *p_a;
Cannot do memory-memory transfer with a single instruction
  How would you do it? 1) Mem->Reg, 2) Reg->Mem
Notes: Mem -> Reg
Reg -> Mem
movq (%rax), %rdx
movq %rdx, (%rbx)

## Slide 51: Example of Move Instructions: swap()
%rdi
%rsi
%rax
%rdx
Registers
Memory
Register Variable
%rdi ⇔ xp
%rsi ⇔ yp
%rax ⇔ t0
%rdx ⇔ t1
void swap(long* xp, long* yp)
{
long t0 = *xp;
long t1 = *yp;
*xp = t1;
*yp = t0;
}
swap:
movq (%rdi), %rax
movq (%rsi), %rdx
movq %rdx, (%rdi)
movq %rax, (%rsi)
ret
Initial state:

## Slide 52: Example of Move Instructions: swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Notes: But actually, pointers are just addresses!
Showing here 8-byte words of memory, addresses jump by 8

## Slide 53: Example of Move Instructions: swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 54: Example of Move Instructions: swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
123
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 55: Example of Move Instructions: swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
456
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret

## Slide 56: Example of Move Instructions: swap()
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x120
0x100
123
456
Registers
Memory
123
123
456
swap:
movq (%rdi), %rax # t0 = *xp
movq (%rsi), %rdx # t1 = *yp
movq %rdx, (%rdi) # *xp = t1
movq %rax, (%rsi) # *yp = t0
ret
Note: these did not change

## Slide 57: Break + Open Question
How does the number of available registers affect a system?
  What if x86-64 only had two registers?
  What if x86-64 instead had 512 registers?

## Slide 58: Break + Open Question
How does the number of available registers affect a system?
  What if x86-64 only had two registers?
    “Register Pressure” becomes a problem
    Accessing 3+ things at once requires memory
    Way more memory reads/writes
  What if x86-64 instead had 512 registers?
    Most of the registers would never be used
      For any realistic program
    Could have spent that silicon on something more important

## Slide 59: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes

## Slide 60: Memory Addressing Modes: Basic
Common need: interact with memory
  Exact address might be made of multiple parts
Indirect: (R) Mem[Reg[R]]
  Data in register R specifies the memory address
  Like pointer dereference in C
  Example: movq (%rcx), %rax
Displacement: D(R) Mem[Reg[R]+D]
  Data in register R specifies the start of some memory region
  Constant displacement D specifies the offset from that address
  Example: movq 8(%rbp), %rdx

## Slide 61: Complete Memory Addressing Modes
General:
  D(Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S+D]
    Rb: Base register (any register)
    Ri: Index register (any register except %rsp)
    S: Scale factor (1, 2, 4, 8) – why these numbers?
    D: Constant displacement value
Special cases (see textbook Figure 3.3 or next slide)
  D(Rb,Ri) Mem[Reg[Rb]+Reg[Ri]+D] (S=1)
  (Rb,Ri,S) Mem[Reg[Rb]+Reg[Ri]*S] (D=0)
  (Rb,Ri) Mem[Reg[Rb]+Reg[Ri]] (S=1,D=0)
  (,Ri,S) Mem[Reg[Ri]*S] (Rb=0,D=0)
Sizes of common C types!
Notes: Syntax for memory operands can be more complex
Designed to do things that are common with pointers
D: displacement, add a constant
Rb: base pointer
Ri: index into array
S: scale the index (pointer arithmetic needs to scale by the size of the pointer target)
  compiler keeps track of what the pointer points to and scales accordingly
  int x[] x[i]
  ith element of an array of ints: Ri=i, S=4 (bytes)
See figure 3.3 in 3e textbook

## Slide 62: Full list of addressing mode forms

## Slide 63: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) |  | 
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 64: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) | %rdx + 0x8 | 0xf008
(%rdx,%rcx) |  | 
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 65: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) | %rdx + 0x8 | 0xf008
(%rdx,%rcx) | %rdx + %rcx*1 | 0xf100
(%rdx,%rcx,4) |  | 
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 66: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) | %rdx + 0x8 | 0xf008
(%rdx,%rcx) | %rdx + %rcx*1 | 0xf100
(%rdx,%rcx,4) | %rdx + %rcx*4 | 0xf400
0x80(,%rdx,2) |  | 
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 67: Address Computation Examples
%rdx
%rcx
0xf000
0x0100
Expression | Address Computation | Address
0x8(%rdx) | %rdx + 0x8 | 0xf008
(%rdx,%rcx) | %rdx + %rcx*1 | 0xf100
(%rdx,%rcx,4) | %rdx + %rcx*4 | 0xf400
0x80(,%rdx,2) | %rdx*2 + 0x80 | 0x1e080
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 68: Practice: what is the final value in %rdx?
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x100
2
37
15
Registers
Memory
123
224
123
456
378
568
swap:
movq (%rdi,%rsi,8), %rax
movq %rax, %rdx
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]

## Slide 69: Practice: what is the final value in %rdx?
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x100
2
568
15
Registers
Memory
123
224
123
456
378
568
swap:
movq (%rdi,%rsi,8), %rax
movq %rax, %rdx
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]
Address: 0x100 + 2*8 = 0x110
Memory at address: 568
Sets %rax to 568

## Slide 70: Practice: what is the final value in %rdx?
0x120
0x118
0x110
0x108
0x100
Word
Address
%rdi
%rsi
%rax
%rdx
0x100
2
568
568
Registers
Memory
123
224
123
456
378
568
swap:
movq (%rdi,%rsi,8), %rax
movq %rax, %rdx
D(Rb,Ri,S)
Mem[Reg[Rb]+Reg[Ri]*S+D]
Copies value from %rax to %rdx
Sets %rdx to 568
Final value in %rdx: 568

## Slide 71: Outline
Assembly Languages
Registers
x86-64 Assembly
  Introduction
  Move Instruction
  Memory Addressing Modes