## Slide 1: Lecture 14: Device Input and Output
CS343 – Operating Systems
Branden Ghena – Fall 2020
Some slides borrowed from: Stephen Tarzia (Northwestern), Shivaram Venkataraman (Wisconsin), Jaswinder Pal Singh (Princeton), and UC Berkeley CS61C and CS162

## Slide 2: Today’s Goals
Discuss I/O devices and how a computer connects to them.
Understand two different methods of reading/writing device data.
Explore patterns for device interaction:
  Synchronous versus Asynchronous
  Programmed I/O versus Direct Memory Access

## Slide 3: Outline
Overview of Device I/O
Connecting to devices
  Buses on a computer
Talking to devices
  Port-Mapped I/O and Memory-Mapped I/O
Device interactions
  Synchronous versus Asynchronous Events
  Programmed I/O versus Direct Memory Access

## Slide 4: Devices are the point of modern computers
Computation was sufficient for batch systems
  Even then, tape was the input and output mechanism
But interactive systems need to receive input from users and output responses
  Keyboard/mouse
  Disk
  Network
  Graphics
  Audio
  Various USB devices
Processor
Computer
Control
Datapath
Memory
Devices
Input
Output

## Slide 5: Devices are core to useful general-purpose computing
Computer
Mouse
Keyboard
Ethernet
Bluetooth
Monitor
Headphones
Ethernet
Bluetooth
Input
Output

## Slide 6: Devices are essential to cyber-physical systems too
Computer
Lidar
Inertial Measurement Unit
Camera
CAN
Throttle Control
Brake Control
Wheel Rotation
CAN
Input
Output

## Slide 7: Device access rates vary by many orders of magnitude
Rates in bit/sec
System must be able to handle each of these
  Sometimes needs low overhead
  Sometimes needs to not wait around
Device | Behavior | Partner | Data Rate (Kb/s)
Keyboard | Input | Human | 0.2
Mouse | Input | Human | 0.4
Microphone | Output | Human | 700.0
Bluetooth | Input or Output | Machine | 20,000.0
Hard disk drive | Storage | Machine | 100,000.0
Wireless network | Input or Output | Machine | 300,000.0
Solid state drive | Storage | Machine | 500,000.0
Wired LAN network | Input or Output | Machine | 1,000,000.0
Graphics display | Output | Human | 3,000,000.0

## Slide 8: Handling devices appropriately
OS concerns
  Communicating with devices needs to be fast and efficient
  Devices are shared resources that need to be access controlled and shared
  Devices are wildly variable and need some common interfaces for application software
General theme
  Access I/O devices similarly to memory
  Read device state and write commands to it
    With interrupts to inform kernel of events

## Slide 9: Outline
Overview of Device I/O
Connecting to devices
  Buses on a computer
Talking to devices
  Port-Mapped I/O and Memory-Mapped I/O
Device interactions
  Synchronous versus Asynchronous Events
  Programmed I/O versus Direct Memory Access

## Slide 10: Devices connect to buses on the computer
I/O Hierarchy
  Close to the CPU are very fast connections
  Farther from CPU are slower but more flexible protocols

## Slide 11: What is a bus anyways?
Common set of wires for communication between two or more components
  Lets one set of wires connect to N devices
Standardized buses have a specific set of wires and protocol for communicating over them (DMI, PCI, SATA, USB)
  Example wires: 64 address wires, 64 data wires, ~10 control wires
Concerns
  How many wires in the bus?
  Single controller or multiple with arbitration?
  Half-duplex (one direction of communication at a time) or full-duplex?

## Slide 12: Computer networks also run over buses
Ethernet is a bus too!
Network protocols specify how two computers communicate, very similarly to these buses
Internal computer buses differences from general networks
  Higher speed
  Very high reliability
  Accessed cooperatively (often with only one controller: CPU)

## Slide 13: Old version of I/O hierarchy
Hub architecture
Northbridge
  High speed memory control
  RAM + Graphics
Southbridge
  Low speed peripherals
  Disk, Network, USB

## Slide 14: Check your understanding – physical layout
Which is going to be physically closer to the CPU?
  Northbridge or Southbridge
Why?

## Slide 15: Check your understanding – physical layout
Which is going to be physically closer to the CPU?
  Northbridge or Southbridge
Why?
  Need accesses to be fast
  Electrical signals are limited by speed of light
    1 nanosecond ~= 1 foot

## Slide 16
Physical layout of an old motherboard
Note physical distance from CPU

## Slide 17: Platform Controller Hub (PCH) architecture
Enables faster communication high-throughput peripherals
  Memory and Graphics

## Slide 18: Intel NUC 8
Small form factor desktop
CPU includes PCH and GPU in single package
CPU implements many connections directly
  USB
  SATA
  Some have hardware controllers
    Ethernet (RJ45)
    Thunderbolt (Rear USB-C)
    3.5mm Audio (Front stereo headset…)

## Slide 19: Some important buses
Legacy
  Parallel Port
  Serial Port
USB
SATA
PCIe
Device driver sometimes talks to bus controller
  Which sends appropriate signals to device

## Slide 20: Parallel Port – “Printer Port” or Centronics Port
“That big long one you might have seen once”
8 data bits plus control signals
  Up to 2.5 Mbps!!
Very simple to implement
  Write 8 bits of data
  Set STROBE low
    BUSY goes low in response
  When BUSY goes high
    Set STROBE high
  Repeat

## Slide 21: Serial Port – RS-232
“That one we used to use before USB”
RS-232 serial protocol
  One wire for Transmit, one wire for receive
  Bits go one after another at a certain speed (“baudrate”)
    Up to 256 Kbps
Used to connect modems
  Still occasionally used for old devices (via a USB to RS-232 converter)

## Slide 22: USB – Universal Serial Bus
“That one you are familiar with already”
Comes in multiple form-factors and versions
  USB 3.x and type C connectors are the fast ones
Speed has increased greatly
  1.5 Mbps
  12 Mbps
  480 Mbps
  5 Gbps
  10 Gbps
  40 Gbps

## Slide 23: SATA – Serial ATA – AT Attachment – “Advanced Technology”
“That cable you plug a drive in with”
Long evolution as you might have guessed from the name
6 Gbps
  One transmit and one receive single
    Two wires for each in twisted pair
  Short connection length for high speed
SATA
Power

## Slide 24: PCIe – Peripheral Component Interconnect Express
“That slot you put a graphics card into”
  Or WiFi card, or some SSDs
Collection of point-to-point connections
  Motherboard and CPU support N “lanes” in various configurations
Different sizes for different number of bits in parallel
  Order 10s Gbps

## Slide 25: Outline
Overview of Device I/O
Connecting to devices
  Buses on a computer
Talking to devices
  Port-Mapped I/O and Memory-Mapped I/O
Device interactions
  Synchronous versus Asynchronous Events
  Programmed I/O versus Direct Memory Access

## Slide 26: How does an OS talk with I/O devices?
A device is really a miniature computer-within-the-computer
  Has its own processing, memory, software
We can mostly ignore that and deal with its interface
  Called registers (actually are from EE perspective, but you can’t use them)
  Read/Write like they’re data
How do we read/write them?
  Special assembly instructions
  Treat like normal memory

## Slide 27: Port-Mapped I/O (PMIO): special assembly instructions
x86 IN and OUT instructions
  Privileged instructions (kernel mode only)
  Two arguments: destination and data register
Each device is mapped to some port address
  IN and OUT instructions interact with interface
Example: read current value from real-time clock
  mov $0, %al out %al, $0x70 /* Select output of seconds */ in $0x71, %al /* AL register contains 0-59 */

## Slide 28
Example I/O port map
This isn’t standardized, but these are some typical values.
https://wiki.osdev.org/Can_I_have_a_list_of_IO_Ports

## Slide 29: Check your understanding – PMIO in C
How would you access PMIO with C instructions?

## Slide 30: Check your understanding – PMIO in C
How would you access PMIO with C instructions?
  Can’t! Need to use assembly (hopefully with C function wrapper)

## Slide 31: Annoying parts of Port-Mapped I/O
Special assembly instructions are hard to write in C
  Need some wrapper function that actually calls them
Feels sort of like memory read/write, but isn’t
  Why not?
  Can we just put the “port address space” somewhere in memory?
    Used to be a problem for 16-bit computers
    But today we have tons of extra physical address space laying around

## Slide 32: Memory-mapped I/O (MMIO): treat devices like normal memory
Certain physical addresses do not actually go to RAM
Instead they correspond to I/O devices
  And any instruction that accesses memory can access them too!
x86 being the historical amalgamation that it is, uses either PMIO or MMIO depending on the device
control reg.
data reg.
0x00000000
0xFFFFFFFF
0xFFFF0000
Address

## Slide 33: LED blinking code in C using MMIO (on 32-bit nRF52832)
void main(void) { const uint32_t LED_NUM = 1; // set LED pin to be an output *((volatile uint32_t*)0x50000700 + 4*LED_NUM) = 0x00000003;
while (true) { volatile int i;
// LED on
*((volatile uint32_t*)0x50000504) |= (1 << LED_NUM); for (i=0; i<400000; i++); // wait a second
// LED off *((volatile uint32_t*)0x50000504) &= ~(1 << LED_NUM); for (i=0; i<400000; i++); // wait a second
}
}

## Slide 34: Example memory map (from an old 32-bit computer)
PCI devices are mapped here

## Slide 35: Example devices on my windows computer
SATA controller is mapped into memory at two places
USB controller is mapped into a much higher memory region
Regions are large because they contain multiple control/data “registers”

## Slide 36: Other details about MMIO
Devices are mapped into physical memory
  Usually only accessible by the kernel
  But could be directly placed in virtual memory for a process in very special cases
Devices are NOT memory though
  Need to be careful not to cache them
  Cannot let compiler mess with our reads/writes either
    volatile keyword in C
Conceptually not really very different from PMIO
  Both just read/write to specific addresses the device is mapped to

## Slide 37: Outline
Overview of Device I/O
Connecting to devices
  Buses on a computer
Talking to devices
  Port-Mapped I/O and Memory-Mapped I/O
Device interactions
  Synchronous versus Asynchronous Events
  Programmed I/O versus Direct Memory Access

## Slide 38: What do interactions with devices look like?
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data

## Slide 39: Waiting can be a waste of CPU time
    while STATUS==BUSY; Wait
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
Imagine a keyboard device
  CPU could be waiting for minutes before data arrives
  Need a way to notify CPU when an event occurs
    Interrupts!

## Slide 40: Hardware devices can generate interrupts
Each device maps to some number of hardware interrupts
Done at system boot time
  Discover devices
  Map devices into address space
  Map interrupts for devices

## Slide 41: Interrupts allow waiting to happen asynchronously
Prior code example was synchronous
  Nothing else continued on the processor until access was complete
  Good for very fast devices (GPU)
  We call this “Polling”
With interrupts, device handling is now asynchronous
  Access occurs in the background and processor can do something else
  Good for very slow devices (Disk)
  Comes with all the downsides of concurrency though…

## Slide 42: Programmed I/O (PIO)
    while STATUS==BUSY; Wait (possibly on interrupt)
      (Need to make sure device is ready for a command)
    Write value(s) to DATA
    Write command(s) to COMMAND
    while STATUS==BUSY; Wait
      (Need to make sure device has completed the request)
    Read value(s) from Data
How do we read and write those values? (could be a lot)
  With normal CPU memory accesses: Programmed I/O
  Literally: you write a program to do the input and output

## Slide 43: Check your understanding – writing to disk
Let’s say that disk has MMIO registers for an entire 4 KB page
  Takes 100 ns to write each word (8 bytes) of memory
Assuming that we’re just writing all zeros (ignore reading from memory), how long does it take to write a page to MMIO?

## Slide 44: Check your understanding – writing to disk
Let’s say that disk has MMIO registers for an entire 4 KB page
  Takes 100 ns to write each word (8 bytes) of memory
Assuming that we’re just writing all zeros (ignore reading from memory), how long does it take to write a page to MMIO?
  4 KB / 8 B = 500 writes * 100 ns / write = 50 µs
    (For a 3 GHz processor, that’s 150,000 cycles)

## Slide 45: Direct Memory Access (DMA)
Alternative method that uses hardware to do memory transfers
  OS writes address of the data and the size
  Device reads data directly from memory
  CPU can go do other things while read/write is occurring
Notes
  Need to be careful about letting devices access arbitrary memory
    Are devices part of the trusted compute base?
  Often a hardware “DMA controller” does the transfer for the device
    IOMMU can even set up virtual memory spaces for devices

## Slide 46: Programmed I/O versus Direct Memory Access
SATA Controller
SATA Controller
Disk
Disk

## Slide 47: Disk access with DMA

## Slide 48: Interaction pattern with Interrupts and DMA
Interrupt from disk: IDLE (!BUSY)
  Set up DMA controller
    Device is disk
    Select Read or Write
    Specify memory address and size
  Start DMA transfer
  Continue until interrupt again
OS ends up keeping a queue of transfers to be sent to disk that needs to be accessed asynchronously from several places
  Producer/Consumer Problem!

## Slide 49: Outline
Overview of Device I/O
Connecting to devices
  Buses on a computer
Talking to devices
  Port-Mapped I/O and Memory-Mapped I/O
Device interactions
  Synchronous versus Asynchronous Events
  Programmed I/O versus Direct Memory Access