## Slide 1: Lecture 19: Virtualization
CS343 – Operating Systems
Branden Ghena – Fall 2020
Some slides borrowed from: Jaswinder Pal Singh (Princeton), Harsha V. Madhyastha (Michigan), and UC Berkeley CS162

## Slide 2: Today’s Goals
Explore notion of a “virtual machine” and how to virtualize computers.
Understand challenges and tradeoffs for several approaches
  Emulation
  Hypervisors
  Containers

## Slide 3: Outline
Virtualization
Approaches
  Emulation
  Hypervisors
  Containers

## Slide 4: Virtualization
Virtual versions of real resources are used for protection and limitation
  Memory – virtual memory
  CPU – processes and scheduler
  Disk – files
OS provides these abstractions to simplify applications
  And provide security

## Slide 5: Virtual Machines
What about virtualizing the whole computer?
  Provide interfaces that look like a normal computer
  But actually interact with software that manages and multiplexes access
Run an entire OS within an OS

## Slide 6: Original motivation: support more applications
1960s IBM mainframes had many different OSes
  But likely only a few or just one mainframe
  Some applications only written for certain OSes though
Virtualization allowed multiple OSes to run on a single mainframe
  Which let one powerful computer serve varied needs of many people
Still applies today to some degree
  I have a single desktop machine
  Run Windows and an Ubuntu VM
    Want PowerPoint and also terminal environment (vim/make/gcc)
  Not really a general need for non-developers though

## Slide 7: Modern motivation: package and isolate applications
High-performance applications aren’t really stand-alone
  Assumptions about OS
  Assumptions about libraries and services
  Multiple processes working together
A virtual machine is a method to encapsulate “entire stack”
  Even down to expectations of hardware
Cloud computing platforms run many applications together
  Need isolation from each other in a strongly controllable way
    Exactly 2 GB of RAM go to this
    Exactly two processor cores go to that

## Slide 8: Virtualization approaches
Simulate everything in the computer completely
  Emulation
Simulate parts of the computer, but not all of it (really use CPU)
  Hypervisor
Simulate the operating system (software environment)
  Containers

## Slide 9: Outline
Virtualization
Approaches
  Emulation
  Hypervisors
  Containers

## Slide 10: Software emulation
User software emulates the behavior of every single instruction
  Data structures for Processor, Memory, I/O, etc.
  Code for Instruction Cycle:
    Fetch next instruction
    Decode
    Perform operation
    Update state

## Slide 11: Real emulation: QEMU
We have been using QEMU for lab to simulate an x86-64 computer
  2 CPU cores
  2 GB of RAM
  Virtio GPU
  PS/2 mouse and keyboard
  2 PCI IDE interfaces with hard disk and CD-ROM support
    nautilus.iso connected to CD-ROM
  Floppy disk
  PCI and ISA network adapters
  Serial and parallel ports
    stdio connected to serial port
    file parport.out connected to parallel port
  Intel HD Audio Controller and HDA codec
  PCI UHCI, OHCI, EHCI or XHCI USB controller and a virtual USB-1.1 hub

## Slide 12: Emulation tradeoffs
Upsides
  Any hardware you want
  Entirely in userspace
Downside
  Slower than real hardware by definition

## Slide 13: Simple emulators: interpreted languages
Create a simple environment for code to execute within
Interpret code instructions (bytecode or lines of code) and perform actions
  Example: fakes a machine that executes Java bytecode
Still ties in to many parts of the real machine
  Filesystem
  Devices

## Slide 14: Not-quite-emulation: binary translation
ARM on Mac
  Switching to ARM processor with ARM instruction set
  Old programs were compiled for x86-64 instruction set
Solution: translate assembly instructions
  Can be translated in advance
  Or just-in-time (JIT)
  Works fine for applications that are I/O bound
Simulates a different CPU, but leaves the remainder of the computer the same

## Slide 15: Outline
Virtualization
Approaches
  Emulation
  Hypervisors
  Containers

## Slide 16: How do we speed up virtual machines?
“Efficiency … demands that a statistically dominant subset of the virtual processor’s instructions be executed directly by the real processor, with no software intervention…”
—Popek and Goldberg, 1974
Need to use some parts of the computer for real while simulating other parts

## Slide 17: Virtual Machine Monitor (VMM)
Also known as hypervisors
  OS kernel is the system “supervisor” and manages the computer
  Hypervisor manages supervisors
Creates the illusion that the OS has full control over the hardware
  And even gives real (limited) access to hardware whenever possible
  But may actually be sharing full computer resources among several OSes
Probably what you had in mind as virtual machines
  VirtualBox, VMWare, Parallels

## Slide 18: Hypervisor layering
“Bare Metal” Hypervisor
Hosted Hypervisor
Hypervisor manages hardware directly
All operating systems run on top of it
  “Guest OS” as in it isn’t actually in charge of the computer

## Slide 19: Hypervisor layering
“Bare Metal” Hypervisor
Hosted Hypervisor
Normal operating system runs on hardware
  Known as “Host OS”
Hypervisor runs on top of host and coordinates with it to enable interactions with hardware
  Some coordination may be within the kernel itself

## Slide 20: Hypervisor layering
“Bare Metal” Hypervisor
Hosted Hypervisor

## Slide 21: Abstraction choices for hypervisor
Fully virtualizing hypervisor
  Virtual machine looks exactly like a physical machine
    Though not necessarily the same machine it’s running on
  Guest OS does not need to be modified in any way
  Guest May not even be aware it’s running virtually
Para-virtualizing hypervisor
  Guest OS has extensions to cooperate with hypervisor
  Sacrifice transparency for better performance
    Same abstraction-breaking ideal from previous lectures
  Might include an API to interact with hypervisor

## Slide 22: Arbitrary combinations of these are possible
 | VMWare ESXi, Microsoft Hyper-V | VMware Workstation, VMware Fusion, Parallels, VirtualBox | 
 | Xen | User Mode Linux | 
Bare Metal Hypervisor
Hosted Hypervisor
Fully Virtualized
Para Virtualized

## Slide 23: Hypervisor example: system call
Process
1. System call: trap to OS
5. Resume execution
Guest OS
3. OS trap handler: Decode trap and execute syscall. When done issue return-from-trap
Hypervisor
2. Receive trap. Call guest OS trap handler
4. OS tried to return from trap. Do real return-from-trap

## Slide 24: Hypervisor challenges: privileged instructions
The guest OS is going to run privileged instructions
  Scheduling threads, editing page tables, modifying interrupt state
Cannot let it have full control over the hardware
  Otherwise it really isn’t a “guest” and host might never regain control
Solution: trap into hypervisor
  Bare metal: Illegal instruction fault goes directly to hypervisor
  Hosted: Illegal instruction fault in host OS passed to hypervisor
    Which can actually do something to handle it!!

## Slide 25: Problem: x86 doesn’t virtualize very well
CPU architecture is virtualizable only if sensitive instructions always trap if run in user mode
Historically, x86 does not guarantee this
  Some instructions behave differently in user mode
  For example: some instructions have no effect when run in user mode
One solution: binary translation
  Find all unacceptable instructions in the OS binary (possibly at runtime)
  Replace with different instructions that trap to hypervisor
    Which will perform the originally desired operations

## Slide 26: Virtualization extensions to x86
Intel VT and AMD-V
  Extensions to instruction set architecture to enable virtualization
  Fix virtualization problems
  Also speed up virtualization performance by requiring less trapping
VM Entry/Exit
  Swap out Virtual Machine Control Structure (VMCS) that specifies OS state
    Registers, Address Space, Executing Threads
  Example optimization: Virtual Processor ID in TLB entries
    Allows Guest OS and Host OS to share a TLB

## Slide 27: Hypervisor challenges: Memory virtualization
Guest OS maintains its own page tables, mapping virtual to physical memory
  But the guest itself is running in virtual memory
Hypervisor maintains “shadow page tables” that map Guest memory pages to actual memory pages
  Guest modifications to page tables trap to hypervisor that modifies its own tables accordingly
Virtual extensions can do this double-translation in hardware

## Slide 28: Hypervisor challenge: I/O devices
Difficult to replicate all the different drivers that can exist in a kernel in the hypervisor
One solution: leverage host OS drivers
  Present virtual I/O devices to guest OS
  Guest interacts with virtual I/O through its own device driver
  Calls get sent to hypervisor, which makes appropriate calls to host drivers

## Slide 29: Check your understanding – VirtualBox on ARM Mac
Will VirtualBox work on the new ARM Macs?
  Will the program run as-is?
  What architecture will the guest OS need to be?
  Could students run CS213 labs in it?

## Slide 30: Check your understanding – VirtualBox on ARM Mac
Will VirtualBox work on the new ARM Macs?
  Will the program run as-is?
    No. Currently compiled for x86-64. Needs to be recompiled. But it probably has a bunch of hardware-specific code that needs to be rewritten too… (VirtualBox says they won’t be supporting ARM)
  What architecture will the guest OS need to be?
    ARM. VirtualBox is a hypervisor that runs code on the actual processor.
    Windows and Linux do have some ARM support…
  Could students run CS213 labs in it?
    Not really… Any x86-64 specific stuff won’t work.

## Slide 31: Sidebar: virtualization extensions often disabled by default
Most users will never have a need for them
  And developers can probably figure out BIOS settings

## Slide 32: Outline
Virtualization
Approaches
  Emulation
  Hypervisors
  Containers

## Slide 33: Cloud platform requirements
May want to provide multiple OSes, but can do so with multiple physical machines
Really want encapsulation and isolation
  Encapsulation
    Include particular shared libraries that application needs
    Without interfering with other applications on system
  Isolation
    Guarantee certain processing and memory allocations to each application
    Limit visibility into the filesystem (without overhead of partition per app)

## Slide 34: Containers
Provide each guest with illusion of its own dedicated OS
  Isolated resources: processor and memory
  Isolated namespace: PIDs, network, filesystem
  Including only the binaries and libraries it needs

## Slide 35: Linux cgroups (control groups)
Collection of processes treated as a group for resource allocation
Provider greater performance isolation between cgroups than between processes
Hardware
System Software
User Software
syscall tbl
intr tbl
Drivers
Page Tables
intrpt handlers
syscall handlers
scheduler
subsystems
Processor
Memory
Net BW
Files
“production”
“testing”
“dev”
Example:

## Slide 36: Cgroups can be used to build containers
Devices can be connected or denied to a cgroup
  Cgroup processes will not be able to detect device at all
Accounting can be done on cgroup usage
  Memory, CPU, disk I/O

## Slide 37: Docker
Container packaging, distribution, and execution
  Also created open standard for container runtimes
Images
  Describes starting state of a Docker container
  Like a snapshot of the system
Union file system
  Image describes file system as a sequence of layers
    Each layer includes some files
  Overall file system is the union of all the layers
  Layers can be reused in different images

## Slide 38: Docker use cases
Environments are hard to set up
  Often the hardest part of starting software development
  Containerized applications encapsulate requirements
  Can be run on any system that has the same kernel it was built for
Packages an application and its requirements into a container
  Can be used by an individual to more easily run an application
  Can be deployed to a cloud server to run

## Slide 39: Outline
Virtualization
Approaches
  Emulation
  Hypervisors
  Containers