## Slide 1: Lecture 11: Swapping + RAID
CS343 – Operating Systems
Branden Ghena – Fall 2025
Some slides borrowed from: Stephen Tarzia (Northwestern), Shivaram Venkataraman (Wisconsin), and UC Berkeley CS162

## Slide 2: Administrivia
Paging Lab
  5/6 PMs agree that this is the hardest lab
  Get working on it ASAP!

## Slide 3: Today’s Goals
Introduce swapping as a mechanism for enabling more virtual memory than physical memory.
Understand several page replacement policies that control swapping.
Explore topic of RAID – redundancy in disks.

## Slide 4
CPU
Process A
Process B
VPN | PPN | Valid?
0 | 2 | 1
1 | X | 0
2 | X | 0
3 | 6 | 1
4 | X | 0
5 | X | 0
6 | X | 0
7 | 4 | 1
8 | X | 0
Process B Page Table
Virtual Memory
(Process B Only!)
0
1
2
3
4
5
6
7
8
Process B
Process B
Process B
Process A
Process B
Process A
Process A
Process B
Process B
Process A
0
1
2
3
4
5
6
Physical Memory (RAM)
Shared

## Slide 5
CPU
Process A
Process B
Virtual Memory
(Process B Only!)
0
1
2
3
4
5
6
7
8
Process B
Process B
Process B
Process B
Process B
Process B
Process B
Process B
Process B
Process B
0
1
2
3
4
5
6
Physical Memory (RAM)
Shared
Process B
Process B
Process B
Process B
DISK

## Slide 6: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID

## Slide 7: Motivation for swapping
Processes should be independent of the amount of physical memory
  Should be correct, even if not performant
OS goal: support processes when not enough physical memory
  Multiple processes combining to more than physical memory
  Single process with very large address space
    Video games: Death Stranding 2 – 92 GB
    Large-scale data processing: Compiling Android – 64 GB
      Google uses 72-core machines with 64 GB of RAM for a 40-minute build
OS provides illusion of more physical memory by using disk

## Slide 8: Locality of reference
If disk is involved with memory, won’t this be ridiculously slow?
Leverage locality of reference within process
  Spatial: memory addresses near referenced address likely to be next
  Temporal: referenced addresses likely to be referenced again
  Processes spend majority of time in a small portion of code
    Estimate: 90% of time spent in 10% of code (loops)
Implication
  Process only uses small amount of address space at any moment
  Only small amount of address space needs to be in physical memory
  RAM acts as a sort of cache for program memory

## Slide 9: How swapping works
OS moves some pages from RAM to disk
Processes can still run when not all pages are in physical memory
OS and hardware cooperate to make memory available when needed
  Same behavior as if all of address space always was in memory
  Except in terms of time, but processes don’t know about time…
Requirements
  OS needs mechanism to identify location of address space pages on disk and move them into RAM when necessary
  OS needs policy to determine which pages go in RAM or disk

## Slide 10: Combination of swapping and paging
Processes have memory pages, which are distributed among RAM and Disk
Example:
  Processes 0, 1, and 2 are partially in RAM
  Process 3 is entirely in “swap space” on disk

## Slide 11: Paging on Windows
Windows lets you see and even set the size of swap space on disk
  This is only space for temporary storage of physical memory pages (from RAM)
  After it runs out, other processes can’t be loaded!
  This is separate from leaving some parts of a process on disk on unloaded

## Slide 12: Mechanisms to support swapping
Each page in virtual address space lives in a location
  Physical memory
  Disk
  Nowhere (doesn’t exist)
Use one of the bits in each page table entry to track this – Present bit
  Page table entry contains: Physical Page Number, Permissions, Present, Metadata
    Page in memory: Present
    Page on disk: Not Present
      Trap to OS on attempted access
      Page Table Entry points to block on disk instead!
      Maybe never loaded before, or maybe moved to swap space (works the same either way)
    Invalid page: Not Present (and invalid block number)
      Trap to OS on attempted access
      Fault process

## Slide 13: Types of page faults
Minor/soft: Page is loaded in memory, but PTE is not configured:
  Memory could be a shared library already in memory from another process.
  OS could be tracking accesses to this page. (hardware without a dirty bit)
  Response: update the PTE.
Major/hard: A disk access will be needed:
  Anonymous page (process data) may have been swapped out.
  Lazy-loading program executable. (this is the more common reason)
  Response: load the page from disk
Invalid: User program misbehaved:
  Dereference null or invalid pointer.
  Write to page that is read-only.
  Execute code on a page that is not executable (for security).
  Response: terminate the process.

## Slide 14: Short Break + Question
Which types of pages do we need to save on disk if they can’t fit in RAM?
  File-backed (loaded from a file initially) or Anonymous (all zeros initially)
  File-backed, unmodified?
  File-backed, modified?
  Anonymous, unmodified?
  Anonymous, modified?

## Slide 15: Short Break + Question
Which types of pages do we need to save on disk if they can’t fit in RAM?
  File-backed (loaded from a file initially) or Anonymous (all zeros initially)
  File-backed, unmodified?
    No need to save, can just read again from file on disk
  File-backed, modified?
    Must save
  Anonymous, unmodified?
    No need to save, all zeros anyways
  Anonymous, modified?
    Must save
Modified pages always need to be saved!

## Slide 16: Other bits in a page table entry
Page Base Address can be reused to hold disk block
Dirty bit
  Whether page has been modified
  If page needs to be swapped out, only preserve if modified
64-bit version is mostly a bigger Page Base Address
  Plus some reserved bits
  And most-significant bit is “Execute Disable”

## Slide 17: Steps to a memory access with swapping
Hardware checks TLB for virtual address
  If Hit, address translation complete AND page in physical memory
Hardware (or OS) walks page tables
  If valid and present, then page in physical memory
Trap into OS (a.k.a. Page Fault!)
  If invalid or bad permissions, fault process (segmentation fault)
  If valid but not present
    If memory is full, select a victim page in memory to replace
      If modified (dirty), write to disk
      Invalidate TLB entry for that page
    OS reads referenced page from disk into memory
    Page table is updated, present bit is set
    Resume process execution
New!

## Slide 18: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID

## Slide 19: Policies to determine swapping evictions
Goal: minimize the number of hard page faults
  Hard page faults need to read/write from disk and are very slow
  So the OS can take plenty of time to make a good decision
OS has two decisions
  Page Selection
    When should a page be brought into memory?
  Page Replacement
    When should a page be swapped into disk?
    Which page should be swapped out of physical memory?

## Slide 20: When do we load in pages? (page selection)
Demand paging: Load page only when page fault occurs (lazy)
  Intuition: Wait until page must absolutely be in memory
  When process starts: No pages are loaded in memory
  Problems: Pay cost of page fault for every newly accessed page
Pre-paging (prefetching): Load page before referenced (eager)
  OS predicts future accesses and brings pages into memory early
  Works well for some access patterns (e.g., sequential)
Hints: Combine above with user-supplied hints about page references
  User specifies: “may need page in future”, “don’t need this page for a while”, or “sequential access pattern”, ...
  Example: madvise() in POSIX – gives the OS advice about use of memory

## Slide 21: madvise() hints
https://man7.org/linux/man-pages/man2/madvise.2.html

## Slide 22: When do we swap out pages? (page replacement)
Demand swapping: whenever the page fault actually occurs
  Simplest method
  Swap actually occurs asynchronously
    Start the disk I/O and block the process that faulted
Background swapping: preemptively when RAM is getting full
  Background service in kernel periodically runs (Linux - kswapd)
  If number of free physical pages < “low water mark”, evict a bunch
    Writing many pages to disk in one operation is way more efficient

## Slide 23: Thrashing
Thrashing: when swapping happens frequently
  Policy could be bad (working set keeps getting swapped to disk)
  More likely RAM is too small
Frequent swapping slows down the whole computer to a crawl
  Constantly waiting on disk I/O!
Solution for thrashing
  Kill processes until it stops (relieves memory pressure)
  Install more RAM in the computer

## Slide 24: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID

## Slide 25: Which page should be evicted?
Page replacement policy determines which page to evict
Very similar process as cache eviction or TLB eviction
  Misses are expensive, so make sure you evict the right page
  Difference: hard page faults are extremely long and handled in software
    So a sophisticated policy is possible

## Slide 26: Optimal page replacement policy
Optimal page replacement
  Evict page that will be accessed furthest in the future
Advantages
  Guaranteed to minimize the number of page faults
Disadvantages
  Requires the OS to predict the future 🧙
  Doesn’t actually exist
This is a performance “upper bound”
  This is the best anything can do, so it is useful to compare against
  Easy enough to calculate after memory accesses have finished
  Still has misses due to cold-start and capacity

## Slide 27: First-In-First-Out replacement policy
FIFO replacement
  Evict page that has been in memory the longest
Advantages
    Fair as all pages have equal residency
    Easy to implement
Disadvantages
    Some pages of memory are always needed (stack)
      Memory doesn’t really need “fairness” like processes did

## Slide 28: Least Recently Used replacement policy
LRU replacement
  Replace page not accessed for longest time
  Using the past to predict the future (temporal locality)
Advantages
  With locality, LRU approximates Optimal
Disadvantages
  Harder to implement as we need to track when pages are accessed
  Cyclical patterns can make LRU fail (bigger concern for cache than RAM)

## Slide 29: Practice – simple replacement policies
D |  |  |  | 
D |  |  |  | 
B |  |  |  | 
B |  |  |  | 
A |  |  |  | 
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D |  |  |  | 
D |  |  |  | 
B |  |  |  | 
B |  |  |  | 
A |  |  |  | 
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D |  |  |  | 
D |  |  |  | 
B |  |  |  | 
B |  |  |  | 
A |  |  |  | 
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
time
Optimal
FIFO
LRU
Page Requested

## Slide 30: Practice – simple replacement policies
D |  |  |  | 
D |  |  |  | 
B |  |  |  | 
B |  |  |  | 
A |  |  |  | 
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D |  |  |  | 
D |  |  |  | 
B |  |  |  | 
B |  |  |  | 
A |  |  |  | 
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
time
Optimal
FIFO
LRU
Page Requested
D
D
Miss
D
D
Hit
B
D
B
Miss
B
D
B
Hit
A
D
B
A
Miss
C
B
D
B
D

## Slide 31: Practice – simple replacement policies
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
time
Optimal
FIFO
LRU
Page Requested
These are only replacement policies. So they don’t matter until RAM is full!

## Slide 32: Practice – simple replacement policies
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
time
Optimal
FIFO
LRU
Page Requested
D
D
Miss
D
D
Hit
B
D
B
Miss
B
D
B
Hit
A
D
B
A
Miss
C
D
B
C
Miss
B
D
B
C
Hit
D
D
B
C
Hit
B
D
B
C
Hit
D
D
B
C
Hit
For Optimal, which page do we replace?

## Slide 33: Practice – simple replacement policies
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | D | B | C | Miss
B | D | B | C | Hit
D | D | B | C | Hit
B | D | B | C | Hit
D | D | B | C | Hit
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | 
B |  |  |  | 
D |  |  |  | 
B |  |  |  | 
D |  |  |  | 
time
Optimal
FIFO
LRU
Page Requested
D
D
Miss
D
D
Hit
B
D
B
Miss
B
D
B
Hit
A
D
B
A
Miss
C
C
B
A
Miss
B
C
B
A
Hit
D
C
D
A
Miss
B
C
D
B
Miss
D
C
D
B
Hit
For FIFO, which pages do we replace?

## Slide 34: Practice – simple replacement policies
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | D | B | C | Miss
B | D | B | C | Hit
D | D | B | C | Hit
B | D | B | C | Hit
D | D | B | C | Hit
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | C | B | A | Miss
B | C | B | A | Hit
D | C | D | A | Miss
B | C | D | B | Miss
D | C | D | B | Hit
time
Optimal
FIFO
LRU
Page Requested
D
D
Miss
D
D
Hit
B
D
B
Miss
B
D
B
Hit
A
D
B
A
Miss
C
C
B
A
Miss
B
C
B
A
Hit
D
C
B
D
Miss
B
C
B
D
Hit
D
C
B
D
Hit
For LRU, which pages do we replace?

## Slide 35: Practice – simple replacement policies
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | D | B | C | Miss
B | D | B | C | Hit
D | D | B | C | Hit
B | D | B | C | Hit
D | D | B | C | Hit
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | C | B | A | Miss
B | C | B | A | Hit
D | C | D | A | Miss
B | C | D | B | Miss
D | C | D | B | Hit
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
B | D | B |  | Hit
A | D | B | A | Miss
C | C | B | A | Miss
B | C | B | A | Hit
D | C | B | D | Miss
B | C | B | D | Hit
D | C | B | D | Hit
time
Optimal
FIFO
LRU
Page Requested
Miss rate = 40%
Miss rate = 60%
Miss rate = 50%
For each, what are the final miss rates?

## Slide 36: Break + Open Question
Come up with a scenario where LRU does worse than FIFO
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
D | D | B |  | Hit
A | D | B | A | Miss
? |  |  |  | 
? |  |  |  | 
? |  |  |  | 
? |  |  |  | 

## Slide 37: Break + Open Question
Come up with a scenario where LRU does worse than FIFO
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
D | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | Miss
? |  |  |  | 
? |  |  |  | 
? |  |  |  | 
Needs to start with a miss to evict something

## Slide 38: Break + Open Question
Come up with a scenario where LRU does worse than FIFO
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
D | D | B |  | Hit
A | D | B | A | Miss
C |  |  |  | Miss
B |  |  |  | 
D |  |  |  | 
A |  |  |  | 
Repeat prior access pattern
LRU assumes you won’t use the least recent data. So patterns that always use the least recent data are BAD!

## Slide 39: Break + Open Question
Come up with a scenario where LRU does worse than FIFO
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
D | D | B |  | Hit
A | D | B | A | Miss
C | D | C | A | Miss
B | B | C | A | Miss
D | B | C | D | Miss
A | B | A | D | Miss
D | D |  |  | Miss
D | D |  |  | Hit
B | D | B |  | Miss
D | D | B |  | Hit
A | D | B | A | Miss
C | C | B | A | Miss
B | C | B | A | Hit
D | C | D | A | Miss
A | C | D | A | Hit
FIFO
LRU

## Slide 40: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID

## Slide 41: Implementing LRU
Implementing perfect LRU is difficult in practice
Software perfect LRU
  OS maintains an ordered list of physical pages by reference time
    When page is referenced: move to end of list
    When swap is needed: evict front of list
  Tradeoff: slow on memory reference, fast on replacement (unacceptable)
Hardware perfect LRU
  Associate a timestamp with each physical page
    When page is referenced: hardware updates timestamp for page
    When swap is needed: OS searches through all pages for oldest
  Tradeoff: fast on memory reference, extremely slow on replacement and needs special hardware

## Slide 42: Clock algorithm
LRU approximates Optimal anyways, so approximate a little more
  Goal: find an old page, not necessarily the oldest page
  Real memory has many pages, so there are likely many similarly old pages
Clock algorithm
  One “accessed” bit added to each page
    When page is referenced: accessed bit is set to one (hardware)
    When swap is needed:
      Cycle through pages looking for one with accessed bit zero
      Update accessed bit to zero after checking a page
      Continue from where you left off when next swap is needed
  Essentially looks for page that hasn’t been referenced this “cycle”

## Slide 43: Accessed bit on x86
Accessed bit
  Set to 1 automatically by the hardware
  Must be cleared manually by software
Enables Clock algorithm

## Slide 44: Clock algorithm example
A, 0
B, 0
C, 0
D, 0
E, 0
F, 0
Initial setup
  6 pages total fit in memory
  Accessed starts as zero
  “clock hand” points at first page
(Page Name, Accessed Bit)

## Slide 45: Clock algorithm example
A, 1
B, 1
C, 0
D, 0
E, 1
F, 0
After running a little while
  Pages A, B, E are accessed
(Page Name, Accessed Bit)

## Slide 46: Clock algorithm example
A, 1
B, 1
C, 0
D, 0
E, 1
F, 0
OS needs to swap pages
  Algorithm starts
A is recently accessed
(Page Name, Accessed Bit)

## Slide 47: Clock algorithm example
A, 0
B, 1
C, 0
D, 0
E, 1
F, 0
OS needs to swap pages
  Algorithm starts
A is recently accessed
B is recently accessed
(Page Name, Accessed Bit)

## Slide 48: Clock algorithm example
A, 0
B, 0
C, 0
D, 0
E, 1
F, 0
OS needs to swap pages
  Algorithm starts
A is recently accessed
B is recently accessed
C has not been recently accessed
(Page Name, Accessed Bit)

## Slide 49: Clock algorithm example
A, 0
B, 0
G, 0
D, 0
E, 1
F, 0
OS needs to swap pages
  Algorithm starts
A is recently accessed
B is recently accessed
C has not been recently accessed
  So swap it
  And advance hand once more
(Page Name, Accessed Bit)

## Slide 50: Clock algorithm example
A, 0
B, 0
G, 1
D, 1
E, 1
F, 1
Programs continue running for a while
  Pages G, D, F are accessed
(Page Name, Accessed Bit)

## Slide 51: Clock algorithm example
A, 0
B, 0
G, 1
D, 1
E, 1
F, 1
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
(Page Name, Accessed Bit)

## Slide 52: Clock algorithm example
A, 0
B, 0
G, 1
D, 0
E, 1
F, 1
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
D recently accessed
(Page Name, Accessed Bit)

## Slide 53: Clock algorithm example
A, 0
B, 0
G, 1
D, 0
E, 0
F, 1
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
D recently accessed
E recently accessed
(Page Name, Accessed Bit)

## Slide 54: Clock algorithm example
A, 0
B, 0
G, 1
D, 0
E, 0
F, 0
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
D recently accessed
E recently accessed
F recently accessed
(Page Name, Accessed Bit)

## Slide 55: Clock algorithm example
A, 0
B, 0
G, 1
D, 0
E, 0
F, 0
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
D recently accessed
E recently accessed
F recently accessed
A gets swapped!
(Page Name, Accessed Bit)

## Slide 56: Clock algorithm example
A, 0
B, 0
G, 1
D, 0
E, 0
F, 0
OS needs to swap again
  Algorithm begins again
  But with hand starting somewhere new
D recently accessed
E recently accessed
F recently accessed
A gets swapped
  Was A or B the actual LRU?
  Probably doesn’t matter
(Page Name, Accessed Bit)

## Slide 57: Clock algorithm is actually used in real computers
Modern OSes often use some variation on Clock Algorithm
x86 hardware supports an accessed bit in page table entries
Clock algorithm could be built without hardware support too
  Mark all pages as valid but not present initially (soft page fault)
  On OS fault, update accessed bit for page, mark as present
    Only fault on first access per clock-hand-cycle
  Reset page to not present whenever accessed is reset to zero
  ARM implementations do this
https://www.kernel.org/doc/gorman/html/understand/understand013.html
https://stackoverflow.com/questions/32943129/how-does-arm-linux-emulate-the-dirty-accessed-and-file-bits-of-a-pte

## Slide 58: Improving clock algorithm access notion
Add multiple “accessed” bits to create accessed counter
  Increment or decrement bits on use or clock-hand-pass respectively
  Only remove pages with 0 accessed (or less than some minimum)
Combine with timestamp notion to ensure page is “old” (WSClock)
  Keep a timestamp in addition to accessed bit
  Only remove pages with 0 accessed and older than some amount
    Still not necessarily oldest, but definitely old

## Slide 59: Improving clock algorithm evictions
Keep track of number of times a page re-enters memory (Clock-PRO)
  Give eviction preference to pages that haven’t been brought back a bunch
  Bringing it back implies it was important, even if it was old
Keep track of which pages are dirty
  Give eviction preference to clean pages (also to read-only pages)
  Means no write to disk is necessary!
Evict several pages at once each time it is required
  Find first N with accessed bit of zero
  Takes advantage of disk I/O properties

## Slide 60: Break + Nerdy Computer Science Sayings
Source: these are things my advisor (Prabal Dutta) likes to say
“I’m going to have to page that back in.”
  Translation: It’s been a while since I used that information and it’s going to take me a bit to remember it.
“I’m thrashing right now.”
  Translation: I’m working on many tasks and switching between them frequently causing me to be inefficient.
“What’s the most-significant bit of this idea?”
  Translation: What’s the part of this idea that has the most impact

## Slide 61: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID

## Slide 62: Traditional hard disk drives (HDDs) use magnetic regions

## Slide 63: Solid state drives (SSDs) use flash memory
Still non-volatile
Significantly faster
  0.1 ms to access (10 ms for disk)
More limited lifetime than disk
  Limited writes
NMOS transistor with an additional conductor between gate and source/drain which “traps” electrons. The presence/absence is a 1 or 0

## Slide 64: Failure rates for disks are a serious problem
Problem: disks fail
  HDDs have physical actuators that wear out
  SSDs have limited numbers of writes
Big problem: servers have many disks
  Assume rate of failure per year of disk is 1%
    And failures aren’t correlated
  And a server has 264 disks
  What are the odds that a disk will fail this year?
  1 – (1 – 0.01)264 = 93% odds that at least one disk will fail

## Slide 65: Database server at Northwestern
264 fast (10k RPM) magnetic disks (for production)
56 slow (7200 RPM) magnetic disks (for backup)
~150 TB storage capacity
Comprised of 6 physical chassis (boxes) in one big cabinet, about the size of a coat closet.

## Slide 66: Redundant Array of Independent Disks (RAID)
Observation in 1988 (Patterson, Gibson, Katz)
  Servers could use a high-quality mainframe disk drive
  OR for the same cost
  Servers could use several redundant low-quality consumer disk drives
Using an array of cheap disks actually improves multiple things
  Reduce impact of a failure by storing data redundantly on multiple disks.
  Increase capacity by making multiple disks available to store data.
  Increase throughput by accessing data in parallel on multiple disks.

## Slide 67: Basic idea of RAID
Combine many disks to create one superior virtual disk.
The RAID array provides the same interface as a single disk.
Computer thinks it’s dealing with this:
Sector r/w requests
But it’s just an illusion. The reality is:
Sector r/w requests
RAID controller
RAID virtual disk

## Slide 68: How does RAID fit into the OS?
RAID can be implemented in software or hardware
Software RAID means that the OS is responsible for assembling multiple disks into a RAID.
  Implements a generic block device.
Hardware RAID requires a specialized controller card that coordinates the multiple disks, presenting interface of one disk.
  OS just needs a driver for the RAID controller, like any other disk controller.

## Slide 69: RAID levels
RAID 0 – Striping:
  Distribute data across 2 disks for twice the peak throughput.
RAID 1 – Mirroring:
  Copy data onto 2 disks to tolerate failure of one.
RAID 4/5/6 – Parity:
  Keep parity bits around for each block to check for errors and rebuild.
  Typically involves 3+ disks.

## Slide 70: RAID 0 – Striping (for throughput and capacity)
Divide the logical disk into chunks
  (A1, A2, A3 …) 1 or more blocks in size
Distribute the chunks regularly over two or more (N) physical disks.
(+) Throughput for both random and sequential access scales with N.
    TRAID0 = N * Tdisk
(+) Capacity also scales by N.
(+) Cost per byte is identical
(–) But Mean Time To Failure is worse because failure of a single disk is catastrophic:
    MTTFRAID0 = MTTFdisk/N

## Slide 71: RAID 1 – Mirroring (for fault tolerance)
Duplicate each chunk on each of N physical disks.
(+) It is impossible to lose data unless all disks fail simultaneously.
  i.e., failure window is reduced to the time it takes to replace a broken disk.
(–) Write throughput is not improved
(–) Capacity is the same as a single disk
(–) Cost per byte is greater
  $RAID1 = N * $disk

## Slide 72: Check your understanding – RAID 1
(–) Write throughput is not improved
Is write throughput reduced in RAID 1? Or is it the same as a single disk?
What about read throughput?

## Slide 73: Check your understanding – RAID 1
(–) Write throughput is not improved
Is write throughput reduced in RAID 1? Or is it the same as a single disk?
  Same as a single disk
  Write can go to both disks in parallel
What about read throughput?
  Better than a single disk
  Can read two different blocks at once!

## Slide 74: RAID 4 – Parity (for fault tolerance, capacity & throughput)
Redundant data
Distribute the chunks across the first (N-1) disks.
On the Nth disk, store a corresponding parity chunk.
  Parity block is redundant data about a set of chunk (a stripe)
Can tolerate loss of any one disk
Parity disk becomes bottleneck for writes limiting throughput

## Slide 75: How does parity work?
Even parity – add a 0 or 1 such that the total number of 1’s is even.
  There also exists odd parity which makes the total number of 1’s odd
Examples (Even Parity):
  0b0000_0000 – zero ones -> parity bit = 0
  0b1111_1111 – eight ones -> parity bit = 0
  0b0110_1101 – five ones -> parity bit = 1
If a single bit is lost, the parity bit allows us to infer the value of the lost bit

## Slide 76: Check your understanding – Parity Recovery
What are the values of the missing bits?
  Even Parity: make the total number of 1s even
[0, 0, 1, 0, ?, 0, 1, 1] – Even Parity with value: 1
[0, ?, 1, 1, 1, 0, 0, 0] – Even Parity with value: 0

## Slide 77: Check your understanding – Parity Recovery
What are the values of the missing bits?
  Even Parity: make the total number of 1s even
[0, 0, 1, 0, ?, 0, 1, 1] – Even Parity with value: 1
  Value must be a 0
  Because parity plus ones is already even
[0, ?, 1, 1, 1, 0, 0, 0] – Even Parity with value: 0
  Value must be a 1
  Because parity plus ones is not currently even

## Slide 78: Parity can only fix a single error
What if two bits are missing?
[?, 0, 1, 0, ?, 0, 1, 1] – Even Parity: 1
  Could both be zeros
  Could both be ones
  Impossible to tell which
More advanced “error correcting codes” are possible to detect/fix two or more errors
  Hamming Code (single error correcting, double error detecting)

## Slide 79: Parity chunk in RAID
Parity is computed bit-wise across corresponding chunks.
Chunks are one or more blocks (multiple of 4 kB) in size
Writing a small file will involve one disk plus the parity disk.
  (parity disk can become a bottleneck)
Writing a large file will involve all the disks.
Disk 0 | Disk 1 | Disk 2 | Disk 3 (parity)
0001 0010 1100 1100 | 0000 1111 0000 1111 | 1101 1111 0011 0001 | 1100 0010 1111 0010
1111 1111 1111 1111 | 0001 0001 0001 0001 | 1101 1001 0110 0110 | 0011 0111 1000 1000
0000 0000 0000 0000 | 1101 1011 0011 0011 | 1111 0011 0011 1000 | 0010 1000 0000 1011
Useful storage capacity
Redundancy overhead

## Slide 80: Rebuilding an array after failure
If a disk fails, then we remove it and replace it with a working disk.
Then scan through the entire array to compute and write missing data.
  This is called “rebuilding” the array
  We cannot tolerate another disk failure until rebuild completes.
  Reads/writes can continue while array is rebuilding!
Disk 0 | Disk 1 | Disk 2 | Disk 3 (parity)
0001 0010 1100 1100 |  | 1101 1111 0011 0001 | 1100 0010 1111 0010
1111 1111 1111 1111 |  | 1101 1001 0110 0110 | 0011 0111 1000 1000
0000 0000 0000 0000 |  | 1111 0011 0011 1000 | 0010 1000 0000 1011
Disk failed!

## Slide 81: RAID 5 – Distributed Parity (the winner in practice)
Distribute parity chunks across the disks, to avoid a small-write bottleneck
(+) Failure of one disk is OK
(+) Throughput is good
  TRAID5 = (N-1) * Tdisk
  (+) Cost per byte is good
  $RAID1 = N/(N-1) * $disk
(–) High overhead for small N
(–) Failure risk is high for large N
N is typically 3 to 8

## Slide 82: RAID 6 – Double Parity (for large arrays)
Add another disk and keep two parity chunks per stripe
  2nd parity is computed differently
(+) Failure of two disks is OK
(~) Throughput is less:
  TRAID5 = (N-2) * Tdisk
  (~) Cost per byte is higher:
  $RAID1 = N/(N-2) * $disk
Makes sense for larger N (>8)

## Slide 83: Outline
Swapping
  Overview
  When To Swap
  Page Replacement Policies
  Implementing LRU
RAID