## Slide 1: Lecture 18: Embedded OS
CS343 – Operating Systems
Branden Ghena – Spring 2024

## Slide 2: Today’s Goals
Introduce embedded OS concerns and how they are different from general-purpose computing.
Provide insight into an alternative OS approach from Unix.
  Tock embedded operating system
Explore what OS research looks like.
Sidebar: I promise not to test you on specific Tock details
  Although I might ask you about embedded OS in general

## Slide 3: General Tock resources
https://github.com/tock/tock
https://www.tockos.org/
“Multiprogramming a 64 kB Computer Safely and Efficiently” Levy et al. 2017. Symposium on Operating Systems Principles. https://brandenghena.com/projects/tock/levy17multiprogramming.pdf

## Slide 4: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications

## Slide 5: What are embedded systems?
An “embedded computer”, as in a computer within something else
  Interacted with as a device, not as a computer
  Smart lightbulbs, autonomous vehicles, wearable devices
  Internet of Things, Robotics, Industry 4.0, Smart Home
Common desire of interaction with the real world
  Variety of possible concerns
    Cost
    Power
    Real-time
    Fault-tolerance

## Slide 6: Resource-constrained embedded systems
Class of embedded systems with onerous constraints
  Limited memory, compute, and power
  Often used in battery-operated or energy-harvesting scenarios
This is the domain of ubiquitous computing
  Cheap systems that can be deployed anywhere
  Wireless sensor networks
We’ll be exploring this area in this lecture
  This is where my research has been focused
  Takes problems that normal computing can mostly ignore
    And amplifies them to an extreme point

## Slide 7: Microcontrollers drive embedded systems
Microcontroller is ~95% of a computer within a single chip
  CPU
  RAM
  Flash storage
  Hardware controllers for various signals and buses
    Digital I/O, Analog I/O, PWM
    UART, I2C, SPI, sometimes CAN or even Ethernet
  Radio for wireless communication
    Bluetooth Low Energy, 802.15.4 (Zigbee), WiFi
What’s missing?
  Power, Sensors, Connectors, Antennas
7 mm x 7 mm

## Slide 8: Microcontrollers are comparatively very constrained
CPU
  Single core, very simple pipeline
  32-bit or 16-bit (although 8-bit systems still exist)
  100 MHz or less (e.g. 32 kHz)
RAM
  1-256 KB
  Systems often disable some RAM to save power…
Flash storage
  32-2048 KB
  Mapped directly into memory
  Code usually executes from flash!

## Slide 9: Drivers are incredibly important
Vast variety of sensors that might be used
  Temperature, Humidity, Light Intensity, Light Color, Air Pressure, Air Quality, Acceleration, Rotation, Magnetic Field, Buttons
Variety of other systems to communicate with
  SD cards, radios, GPS, other microcontrollers
Devices are the core purpose of embedded systems
  Which makes correct drivers more important
  But variety means you’re constantly writing new drivers

## Slide 10: Energy is often the dominant concern
Normal computer power (varies a lot)
  ~10-500 W total
  CPU uses ~60 Watts
  Powered by plug into mains
Embedded systems often run on batteries
  Four AA batteries: 15 Watt-hours
    Average power to get 1 year of life: 1.7 mW
  Coin cell battery: 0.36 Watt-hours
    Average power to get 1 year of life: 41 μW
Embedded system power (also varies a lot)
  ~50 mW when active
  ~10 μW when in sleep mode
    Goal of an embedded system: get back to sleep mode

## Slide 11: Note: this is only one class of embedded
Robotics: ROS (Robot OS) on top of normal Linux
Industrial and smart home IoT
  QNX (Unix-like RTOS)
  Azure IoT (platform for secure, updatable devices)
    Hardware/Software design with multiple microcontrollers
    One just for security and managing resources
    One just for managing over-the-air updates

## Slide 12: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications

## Slide 13: Embedded needs its own operating systems
Can’t use normal Linux!
  Too little memory and processing in embedded hardware
  Too much concern about power in embedded applications
  Microcontrollers don’t have the necessary hardware features (virtual memory)
Important: Linux is never going to be the solution
  Capabilities of general computers are orders of magnitude better
  Embedded systems are gaining more capabilities
  But new lower-power, lower-cost systems keep emerging too

## Slide 14: Typical embedded OS design
Assumption: embedded device has one single purpose
One application and one kernel combined into a single program
  Application might be multiple cooperative tasks
  Kernel is mostly drivers, with maybe a scheduler
  No protection, and usually minimal resource management
Contiki-NG

## Slide 15: Two needs not met by traditional embedded OSes
Security
  Protect the core platform from applications
Multiprogramming
  Run multiple, unrelated applications (securely)

## Slide 16: Challenge for secure embedded: no virtual memory
No hardware support for virtual memory
  So all addresses on the system are real physical addresses
Nothing prevents applications from
  Manipulating kernel data structures
  Directly accessing hardware
All applications on the system must be trusted
  Devices do have one single purpose
  But any weak link leaves the whole system broken

## Slide 17: Embedded devices are a weak link
Custom, application-specific code written in C
  Limited code-reuse
  Low testing coverage
All code on the system is trusted
  No isolation: any code can directly access hardware registers
  Little distinction between “kernel” and “application”

## Slide 18: Reminder: Mirai botnet (2016)
Takes control of up to 600,000 insecure connected devices
  IP-attached cameras, DVRs, routers, printers

## Slide 19: Weak devices provide network entry points
IoT devices can be used as a network entry point
  Step one: hack the device
  Step two: use the device to access information on the private network
Example: casino high-rollers database obtained through an IoT fish tank thermostat
  https://interestingengineering.com/a-casinos-database-was-hacked-through-a-smart-fish-tank-thermometer

## Slide 20: Modern systems increasingly need support for multiprogramming
Example: USB authentication key
  Universal Second Factor (U2F)
  HMAC One-time Password (HOTP)
  GPG Key (GNU Privacy Guard)

## Slide 21: Security layering is desirable
Different domains with different expectations
  Applications, services, and platform

## Slide 22: Platform layer
Core kernel plus microcontroller-specific code
  ~10 developers
  Trusted compute base
Goal: possible to correctly extend TCB

## Slide 23: Services layer
Device drivers, networking, libraries
  ~100 developers
  Auditable, but possibly still buggy
Goal: protect kernel from safety violations

## Slide 24: Applications layer
End-user functionality
  ~1000 developers
  Third-party applications, potentially malicious
Goal: end-users can install 3rd-party apps

## Slide 25: Break + Question
What are challenges for updating IoT device firmware?

## Slide 26: Break + Question
What are challenges for updating IoT device firmware?
  Manufacturer needs to create update (still exist AND care)
    Software is usually closed source, so others can’t update it
  Update needs to get to the device
    Either the device needs an internet connection to check
    Or consumer needs to be aware of update and have a mechanism to upload it

## Slide 27: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications

## Slide 28: Tock
Embedded OS designed for secure multiprogramming
  Kernel written in Rust programming language
  Applications written in any language
  Runs on multiple hardware platforms
Open-source research project
  2015 collaboration between Stanford, UC Berkeley, and Michigan
    Since expanded to 6-7 universities (Princeton, UCSD, Northwestern)
    Plus several companies (Google, Western Digital)
https://github.com/tock/tock
https://tockos.org/

## Slide 29: Tock software organization
Hardware
CPU
I2C
SPI
RNG
UART
Timer
AES
ADC
DAC
GPIO
USB
Core Kernel
Scheduler, Process management, etc.
Standardized Hardware Interface Layer (HIL)
Microcontroller-specific Peripheral Drivers
SPI
I2C
RNG
Timer
ADC
GPIO
UART
AES
DAC
USB
Kernel (Rust)
Thread
Virt. Timer
BLE
Temp. Sensor
System Calls
6LoWPAN
SI7021
SD Card
Console
Untrusted
(unsafe forbidden)
Trusted
(unsafe allowed for MMIO, PIC, etc.)
Untrusted
(isolated by the MPU and preemptively scheduled)
App written in Rust
C App Ported to Tock
[Service] BLE Environmental Sensing Profile
while(1)
😈
Capsules
libtock
libtock-rs
libtock
libnrf
Syscall Interface

## Slide 30: Tock’s isolation mechanisms
Processes
Standalone executable in any language
  C, C++, Rust, Lua
Isolation enforced at runtime
Higher overhead
Applications
Capsules
Rust code linked into kernel
Isolation enforced at compile-time
Lower overhead
Used for device drivers, protocols, timers...
Trusted for liveness, not safety
Totally untrusted

## Slide 31: How do applications access devices?
System calls are used to access devices
Three generic syscalls
  Command – takes a 32-bit numerical argument
  Allow – takes a pointer to a buffer to read/write
  Subscribe – takes a pointer to a function to callback
First two arguments to all syscalls
  Driver number (the driver it wants to interact with)
  Minor number (driver-specific identifier)

## Slide 32: Example: console capsule (driver number: 1)
Command syscall values
  Transmit from buffer, argument is length
  Receive into buffer, argument is length
  Cancel request
Allow syscall values
  Pointer to buffer for sending
  Pointer to buffer for receiving
Subscribe syscall values
  Send complete handler
  Receive complete handler
Writing bytes to console:
uint8_t buffer[20] = {…data…}
Allow(1, 1, buffer)
Command(1, 1, 20)

## Slide 33: Event-driven programming
Tock adopts an event-driven model to avoid concurrency issues
  Single core system, so the source of concurrency is interrupts
  Exposed to applications through “subscribe” callbacks
Callbacks never occur during normal operation
  Even if application is descheduled due to timeslice
Additional syscall: yield – no arguments
  Application pauses until a callback is ready for it
  Once one or more events are ready
    Call the callback handlers, one at a time
    Return from yield statement

## Slide 34: Yield example
void sensor_callback (int value) { printf("Got sensor reading %i\n", value); }
int main () { sensor_register(sensor_callback); // calls allow sensor_sample(); // calls command yield(); }

## Slide 35: Synchronous interactions with event model
bool sensor_flag = false;
void sensor_callback (int value) {
printf("Got sensor reading %i\n", value);
sensor_flag = true;
}
void sample_sensor_blocking () {
sensor_flag = false;
sensor_register(sensor_callback); // calls allow
sensor_sample(); // calls command while (!flag) {
yield();
} }

## Slide 36: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications

## Slide 37: Tock threat models
Threat model – the universe of concerns for a system design
  Systems can’t defend against every possible attack
  So what attacks is the OS actually concerned about?
Tock splits threat model into application and kernel parts

## Slide 38: Kernel threat model
What does security mean for the kernel?
Confidentiality
  Secrets may not be accessed by applications or capsules.
Integrity
  Applications and capsules may not modify kernel data except through exposed APIs.
Availability
  Applications cannot starve the kernel of resources or deny service.
  Capsules may deny service but should be designed to prevent starvation.

## Slide 39: Guarantees of safety from parts of the kernel
How do we guarantee these without virtual memory?
  Secrets may not be accessed by applications or capsules.
  Applications and capsules may not modify kernel data except through exposed APIs.
In normal operating systems, drivers are run in kernel mode
  Full access to memory and hardware on the system
Otherwise, they would be in userspace with limited access
  Likely resulting in slower operation

## Slide 40: Tock solution: use language features
Tock uses the Rust programming language for the kernel
Systems language
  Represents how hardware actually interacts
  Strong type system and memory safety
  Runtime behavior similar to C
Result: capsules cannot access memory they do not own
  Cannot access application secrets
  Cannot modify other kernel structures (even by accident)

## Slide 41: What problems is Rust trying to solve?
Memory lifetime
  Use-after-free
  Common example: pass a reference into a function, then free it
Data races
  Multiple access to data and at least one modifies it
  Problems we were solving with locks
Generally: have the compiler handle for you whatever it can

## Slide 42: Rust has a strong notion of “ownership”
Ownership is a notion of managing memory and sharing.
Rust ownership rules
  Each value has a variable that’s called its owner.
  There can only be one owner at a time.
  When the owner goes out of scope, the value is dropped.
Last one is straightforward:
  Values on the stack go away at the end of the function (or any block { })
  This lifetime works just like C or C++

## Slide 43: Example: ownership with strings
Rust ownership rules
  Each value has a variable that’s called its owner.
  There can only be one owner at a time.
let s1 = String::from("hello");
let s1 = String::from("hello"); let s2 = s1;

## Slide 44: Ownership is transferred through function calls
fn main() { let s = String::from("hello"); // s comes into scope takes_ownership(s); // s's value moves into the function... // s is no longer valid here } // Here, s goes out of scope. But because s's value // was moved, nothing special happens. fn takes_ownership(some_string: String) { // some_string comes into scope println!("{}", some_string); } // Here, some_string goes out of scope and `drop` is called. // The backing memory is freed.

## Slide 45: Ownership model prevents data races
References allow multiple read-only access to a value
  For example: passing a value into a function by reference
  Any number of references may exist to a value
Requesting a writable (mutable) reference requires sole ownership
  No other references may exist
  Original owner cannot access value
This is enforced by the compiler!!!
  So there is no runtime cost
  And programmers cannot do bad things by accident

## Slide 46: Tock downside: all drivers must be written in Rust
Why hasn’t every OS taken the “language support” path?
  Primarily, it wasn’t really available. C or C++ were the only real options.
Also, the vast majority of developers know C but not Rust
  And the vast majority of existing code is in C and not Rust
One of Tock’s major challenges is that things like networking stacks need to be re-written in Rust
  BLE, 802.15.4, WiFi

## Slide 47: My feelings about writing code in Rust
Three steps of Rust acceptance
You are confused about little weird syntax things.
You are frustrated by so many compilation errors.
You realize your code mostly works if it compiles.

## Slide 48: Sidebar: the future of Rust
Rust is still growing in popularity but still young
  Many people are excited to have a safe alternative to C
  But there is a steep learning curve to using Rust
  And a vast body of existing code already in C
How dominant would it have to be to switch our curriculum?
  Unclear. We’ve taught C for decades.
  Certainly considering it for CS211, but no immediate plan to change
    Still can’t stop teaching C (too useful)
    Rust in 5 weeks at the end of CS211 would be much harder than C++

## Slide 49: Learning Rust
No class at Northwestern uses it right now 😢
So you’ll definitely need to learn it on your own
  https://www.rust-lang.org/learn
  https://serokell.io/blog/learn-rust

## Slide 50: Break + Programming languages personified
https://leftoversalad.com/c/015_programmingpeople/

## Slide 51: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications

## Slide 52: Tock OS research question
How do you design a secure operating system that runs on constrained embedded systems hardware?
  What are the primary challenges of doing so?
  What are the solutions to those challenges?

## Slide 53: Application threat model
How does Tock define security for applications?
Confidentiality
  Secrets may not be accessed by other applications or capsules.
Integrity
  Data may not be modified by other applications or capsules except when the applications allows access.
Availability
  Applications may not deny service to one another, except that finite resources may be granted in a first-come, first-served order.

## Slide 54: Problems to deal with in applications
How do we prevent malicious accesses without virtual memory?
  Secrets may not be accessed by other applications
  Data may not be modified by other applications

## Slide 55: Memory access protection with hardware
Modern microcontrollers have a memory safety feature
  Memory Protection Unit (MPU)
Base-and-bounds model of security
  Bounds checking, but no translation
mode == user?
Physical Address
Physical Address
Yes
No
Memory Protection Unit
< lower bound?
No
Yes
Fault
No
> upper bound?

## Slide 56: Problems to deal with in applications
How do we prevent malicious accesses without virtual memory?
  With Memory Protection Unit hardware
How do we load multiple applications without virtual memory?
  We do not want to compile programs for specific physical addresses

## Slide 57: Application addresses managed by Position-Independent Code
Position Independent Code (PIC)
  Compile program using only relative assembly instructions
  Plus a register (base pointer) that is set to point to data section
  Feature available in modern GCC for ARM
All accesses in program become relative
  Stack accesses relative to stack pointer
  Data accesses relative to base pointer
  Heap accesses relative to base pointer (plus size of data)
  Code accesses relative to current instruction pointer
OS kernel sets up stack, base, and instruction pointers for where program was really placed in memory

## Slide 58: Problems to deal with in applications
How do we prevent malicious accesses without virtual memory?
  With Memory Protection Unit hardware
How do we load multiple applications without virtual memory?
  With Position Independent Code
How do we manage having so little memory?
  Applications may not deny service to one another

## Slide 59: Example of denial of service with timers
Multiple applications like want their own individual timers
Timer Driver

## Slide 60: Example of denial of service with timers
Static allocation of timers results in needs of some applications denying service to others
Timer Driver

## Slide 61: Example of denial of service with timers
Dynamic allocation leads to needs of unrelated drivers denying service to applications
Timer Driver

## Slide 62: Example of denial of service with timers
Dynamic allocation leads to needs of unrelated drivers denying service to applications
Timer Driver

## Slide 63: Example of denial of service with timers
Dynamic allocation leads to needs of unrelated drivers denying service to applications
Timer Driver

## Slide 64: Example of denial of service with timers
Dynamic allocation leads to needs of unrelated drivers denying service to applications
Timer Driver

## Slide 65: Example of denial of service with timers
Dynamic allocation leads to needs of unrelated drivers denying service to applications
Timer Driver
AES Driver
Bluetooth Driver

## Slide 66: How does memory allocation work lead to limitations?
Data
Stack
Code
Process
RAM
Allocation
Flash
Process
Accessible
Memory
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap

## Slide 67: Per-process heaps limit failures to that one process
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 68: Per-process heaps limit failures to that one process
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 69: Per-process heaps limit failures to that one process
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 70: Traditional kernel heap allocation results in shared fate across all processes
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
Data
Stack
Code
Heap

## Slide 71: Traditional kernel heap allocation results in shared fate across all processes
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 allocation
Data
Stack
Code
Heap

## Slide 72: Traditional kernel heap allocation results in shared fate across all processes
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 allocation
P2 allocation
Data
Stack
Code
Heap

## Slide 73: Traditional kernel heap allocation results in shared fate across all processes
Data
Stack
Code
Heap
Data
Stack
Code
Kernel
RAM
Allocation
Flash
Heap
P1 allocation
P2 allocation
P2 allocation
P2 allocation
P2 allocation
P2 allocation
Data
Stack
Code
Heap

## Slide 74: Solution: per-process kernel heaps
Grant section is only accessible to the kernel
  Used to store application-specific kernel structures

## Slide 75: Grants balance reliability and flexibility
Using too much memory only affects processes that do so
No application can deny kernel services to another application
Timer Driver

## Slide 76: Problems to deal with in applications
How do we prevent malicious accesses without virtual memory?
  With Memory Protection Unit hardware
How do we load multiple applications without virtual memory?
  With Position Independent Code
How do we manage having so little memory?
  With Grant regions

## Slide 77: Tock research contributions
Design of an OS kernel using language safety features
  What parts of this were particularly challenging?
Design of a multiprogramming OS under severe memory restrictions
  No virtual memory
  ~64 KB of RAM for the entire system (kernel and applications)
    Grants as a solution for reliable flexibility
“Multiprogramming a 64 kB Computer Safely and Efficiently” Levy et al. 2017. Symposium on Operating Systems Principles. https://brandenghena.com/projects/tock/levy17multiprogramming.pdf

## Slide 78: Outline
Embedded Systems
Embedded Operating Systems
Tock
  Overview
  Designing a secure kernel
  Designing secure applications