## Slide 1: Lecture 15 LPWANs Challenges
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2022
Materials in collaboration with Pat Pannuto (UCSD)
With images from Swarun Kumar (CMU)

## Slide 2: Today’s Goals
Consider LPWAN use cases, looking at a particular automotive study
Explore academic research improving LoRaWAN capabilities
Deep-dive into challenges LPWANs face

## Slide 3: Outline
LPWAN Use Cases
Improving LoRaWAN
LPWAN Challenges

## Slide 4: Project Background
Research project with automotive company (circa 2019)
LPWAN protocols are potentially interesting for automotive uses
New design points allow trading bandwidth, range, power, and cost.
Could these enable new valuable applications?

## Slide 5: Problem Statement
Is there an opportunity to complement existing high-bandwidth low-latency networks, with emerging low-cost long-range networks for certain automotive use cases?
What new uses cases can be realized by the addition of these new communications capabilities?
How would future vehicle architectures change to support these networks?

## Slide 6: Low-Power Applications
Now
Asset Tracking
Report location of vehicle prior to sale even when off
Parked Status
Monitor and report several sensors when vehicle is parked and off
Near
Vehicle Security
Detect suspicious behavior near the vehicle and report to user
Far
Distributed Data Collection
Collect sensor data from vehicles throughout a city

## Slide 7: Asset Tracking Application
Track the vehicle’s location in real time from factory to point-of-sale.
Envision a web application that can label each vehicle on a dealer’s lot.
Could be useful to owner as well for theft-tracking purposes.
Would utilize:
  GPS
  Accelerometers (detect if vehicle is in motion)

## Slide 8: Parked Status Application
Alert the user of flat tires, dead batteries, or other issues that can occur while the vehicle is parked and off.
Envision a smartphone app that could send owners a notification if something goes wrong.
Would utilize:
  Tire pressure sensors
  Battery status sensors
  Door, trunk, window, and roof opened/closed sensors
  Fuel level sensor
  Accelerometers (collision detection)

## Slide 9: Vehicle Security Application
Detect suspicious activity around the vehicle and send notifications to the owner.
Envision a smartphone app that notifies the owner with a picture of the nearby activity.
Would be enabled by sensors already in place for vehicle autonomy purposes.
Would utilize:
  Cameras
  Motion sensors
  Door, trunk, window, and roof opened/closed sensors
  Accelerometers

## Slide 10: Distributed Data Collection Application
Collect and collate various sensor data from cars parked throughout a region.
Parked vehicles can be used as a city-scale sensor network to determine various phenomena.
  Track weather down to local levels.
  Measure air quality throughout a city.
  Sense and report nearby traffic congestion.
This is a little further-term than other applications, but cities and researchers could benefit greatly from available data.

## Slide 11: Project Takeaways
Unlicensed LPWANs seem limited in applicability to vehicles
Coverage areas and bandwidth capabilities are too limited
Cellular LPWANs can enable inactive vehicle applications
Applications have long lifetimes, even using a backup battery
Architecture changes to support low-power communications appear feasible
Low-power, inactive-vehicle applications are worth further investigation
Asset tracking and parked vehicle status are realizable in near-term
What would the costs of realizing these applications be?
How much value would they add for customers and company

## Slide 12: Break + Brainstorm
Other applications for automotive use?

## Slide 13: Outline
LPWAN Use Cases
Improving LoRaWAN
LPWAN Challenges

## Slide 14: Resources
Swarun Kumar (CMU) - https://swarunkumar.com/lpwan.html
Choir
  https://swarunkumar.com/papers/choir-sigcomm2017.pdf
  https://swarunkumar.com/slides/choir-sigcomm2017.pdf
Charm
  https://swarunkumar.com/papers/charm-ipsn2018.pdf
Opportunistic Packet Recovery
  https://swarunkumar.com/papers/opr-mobisys2020.pdf

## Slide 15: Choir concept
Can we distinguish data from LoRa chirps that have collided?
  Yes! By applying signal processing to the problem
Data in time domain
Data in frequency domain

## Slide 16: What happens when LoRa chirps collide?

## Slide 17: What happens when LoRa chirps collide?

## Slide 18: Imperfections in hardware create offsets

## Slide 19: Decoding colliding packets

## Slide 20: Choir results
Recovering collided packets resolves losses due to Aloha transmission!
Increases maximum throughput on the network considerably!
Does require modifications to hardware on gateways though

## Slide 21: Charm
Take advantage of multiple gateways in range of a device
Combine signals received at each gateway to recover packets that weren’t received cleanly
Particularly useful at decoding weak signals

## Slide 22: Coherent combining
Signal received at each receiver is a combination of
  Signal
  Wireless channel
  Random noise
Signal and wireless channel are similar at all receivers
Noise is different though! Independent
When combined, signals are coherent (build in strength) whereas noise is incoherent (spreads out)

## Slide 23: Charm uses coherent combining across gateways
Gateways send signal data to the cloud
The cloud can perform combining on the data and recover signals
Challenges
  Only send the data when it’s needed
  Tight time synchronization on the data
  Gateway hardware changes

## Slide 24: Opportunistic Packet Recovery (OPR)
Can we recover packets that have bad CRCs?
  What if we have some information about where the interference might have occurred during the signal transmission?
  OPR demonstrates that we can recover packets!
Process
  Receive bits even for bad packets
  Measure RSSI for each bit along the way
  Look for changes in RSSI that signals interference
  Try different values for the effected bits until the CRC succeeds!

## Slide 25: Detecting error bits in transmitted packets
Correctly identifies 83% of the corrupted bits with 17% false positives

## Slide 26: Multiple gateways do even better
If multiple gateways receive the packet, they can compare their received data
Common bits are likely correct, while differences are likely interference

## Slide 27: OPR total design
Bad packets are sent to the OPR Server for handling along with RSSI data
OPR server attempts to reconstruct the packet
In practice, system can correct up to 72% of CRC errors!
  Also completes correction in time for the ACK response (within 1 second)

## Slide 28: Break + Open Question
What are the challenges in translating this research into real-world use?

## Slide 29: Break + Open Question
What are the challenges in translating this research into real-world use?
  Improve gateway hardware: how do people buy/make it?
    Needs a manufacturer to be interested
  Multiple gateways are necessary
    Not applicable to very small deployments
    Network operators (TTN or Helium) would be good targets
    They also have backend stuff running anyways, so adding OPR should be possible!

## Slide 30: Outline
LPWAN Use Cases
Improving LoRaWAN
LPWAN Challenges

## Slide 31: Do novel networks meet application needs?
How do we compare varied requirements and capabilities?
  Networks have throughput per gateway and range of gateway.
  Applications have throughput per device and deployment area.
Each gateway must support throughput for all devices in its coverage area.
  Deployment areas are often wider than a single gateway’s range.
Solution: compare the density of communication.
  Data communication rate per unit area.

## Slide 32: New metric for wide-area communication.
Our proposed metric: bit flux
Units: bit per hour / m2
First suggested by Mark Weiser
Branden Ghena, et al. "Challenge: Unlicensed LPWANs Are Not Yet the Path to Ubiquitous Connectivity." MobiCom’19
Notes: bit flux is our metric for data density
throughput divided by coverage area
As with many ideas, this was first suggested by Mark Weiser

## Slide 33: Bit flux can measure application needs.
For an application:
Assumes a relatively homogeneous distribution.
Notes: For applications, bit flux sums the data needs for each device in the deployment
And divides by the total deployment area
To determine the application uplink density

## Slide 34: Bit flux can measure network capabilities.
For a network:
Assumes a non-overlapping deployment of gateways.
Note that bit flux alone ignores the total number of gateways required.
Notes: For networks, we divide the goodput of a network
By the coverage area of a single gateway
This gives us a number that represents the data density that a network can support, at any width of deployment

## Slide 35: Bit flux accounts for spatial reuse.
Reducing coverage area and deploying additional gateways improves capacity.
Notes: Bit flux also accounts for spatial reuse in networks
Reducing range (and deploying more gateways), reduces the coverage area for each gateway, increasing the network bit flux

## Slide 36: Bit flux measurement for LoRaWAN.
ALOHA access control
Hata model
Notes: Here is the bit flux measurement for a LoRaWAN network
In the US, LoRaWAN has 64 channels for uplink
But it relies on an ALOHA access control mechanism, so packet collisions reduce throughput significantly

## Slide 37: Networks differ in capability by orders of magnitude.
Notes: We can calculate bit flux for each of the networks we’re interested in
We note that there are several orders of magnitude difference in the throughput capability of each network
Particularly between cellular communication and unlicensed LPWANs

## Slide 38: Range reduction results in a bit flux curve for each network.
Notes: These points are at the maximum range for each network, but they have the ability to perform power control and reduce range
This creates a curve for each network, where we can reduce range (and install more gateways) in order to increase network capability

## Slide 39: Let’s compare network capabilities to a real-world application.
Smart household electric meters.
~250 bytes of data every 4 hours
~370000 electric customers in San Francisco
Notes: Now that we can measure the capability of each network, lets compare that to the needs of an application
The example I’ll be talking through is Electricity Metering, there are about a dozen others in the paper
PG&E smart meters send about 250 bytes every 4 hours
This isn’t a lot of data, but smart meters are densely deployed, with three hundred thousand across San Francisco

## Slide 40: All networks are capable of meeting the data needs of electricity metering.
Electricity Metering Application
Notes: We can plot the need of the Electricity Metering application as a line on our bit flux figure
Any network above this line is capable of serving the application’s needs
Sigfox needs range reduction, but all networks are capable of serving this application’s needs
So, great! Networks can serve ubiquitous applications. Problem solved, right?

## Slide 41: Unlicensed LPWANs lag behind Cellular IoT in ability to support applications.
2G < 0.03% utilized
Notes: Let’s visualize this instead as the number of gateways deployed and the proportion of network utilized.
  Again, because of power control, there is a tradeoff here. We could deploy a single gateway for everything, or many gateways with reduced range to increase capacity.
Cellular networks have no problem with this application
  With a single gateway, LTE-M could spend 1% of its capacity to service this app.
Unlicensed LPWANs, however, have choices to make on how many gateways they deploy and how much capacity they are willing to spend on this one application

## Slide 42: Sigfox requires range reduction to meet application needs.
Capacity Problem
Throughput capability of Sigfox is insufficient to support application needs
It can only support the application with reduced range and additional gateways
Notes: There are two particular problems we can see with the unlicensed LPWANs
The first is a capacity issue:
  Sigfox can’t satisfy the application at all without power control.
  Range is sufficient for a single gateway to cover the city, but it wouldn’t be able to keep up with the data.

## Slide 43: Capacity solutions are relatively straightforward.
Better access control mechanisms. Explore CSMA?
Recover simultaneous transmissions (Choir and Charm).
Increase bandwidth (TV white spaces).
All likely come at the cost of increased energy usage…
  Results in a protocol that looks pretty similar to cellular…
Adwait Dongare, et al. "Charm: exploiting geographical diversity through coherent combining in low-power wide-area networks.“ IPSN’18
Rashad Eletreby, et al. "Empowering low-power wide area networks in urban settings." SIGCOMM’17
Abusayeed Saifullah, et al. "SNOW: Sensor network over white spaces." SenSys’16
Notes: Solving these capacity problems is relatively straightforward
And a lot of research from our community has begun that path
One solution would be better access control mechanisms than the ALOHA
We could also significantly increase the available bandwidth through the use of TV white spaces

## Slide 44: LoRaWAN devotes most of its network capacity to a single application.
Coexistence Problem
LoRaWAN can meet application needs
But only by using 50% of the 915 MHz unlicensed-band spectrum
Notes: But there is a second problem, that of coexistence
  LoRaWAN could handle the application with only 2 or 3 gateways
  Remember, that we are calculating bit flux for LoRaWAN using all available channels
  As long as you are willing to commit 50% of the 915 MHz spectrum to electricity metering

## Slide 45: Coexistence is inevitable in urban areas.
Urban environments and long range lead to many overlapping deployed networks.
Capacity problems worsen coexistence by devoting more bandwidth to one application.
It’s not just electricity metering…
Notes: You might try to say it’s fine to dedicate so much of a network to a single application. I dedicate 50% of my home WiFi to Netflix all the time…
But coexistence cannot be ignored in urban areas
There won’t just be one network, but two, or three, or more
And they all have to share the same bandwidth for all deployed applications

## Slide 46: Coexistence in unlicensed bands is a more difficult problem.
No methods for inter-network negotiation so far.
Without buy-in from most deployments, all access control becomes uncoordinated.
Cellular IoT does not have this problem
Notes: Solving these coexistence problems are more difficult
We need methods for coordination and negotiation between deployed networks
And without buy-in from all networks, collisions are inevitable
It doesn’t matter that you are using a wonderful scheduling TDMA algorithm to send data without collisions if your neighbor is transmitting whenever they want
And a really important point is that cellular IoT doesn’t face this problem

## Slide 47: Cellular may dominate future deployments.
LTE-M and NB-IoT are now deployed in the US (and worldwide).
Licensed bandwidth avoids the coexistence problem.
Cellular may solve many applications but is not a perfect solution.
  Still has higher energy and monetary costs for use.
  Also limited to where service is already available.
Notes: Occupying licensed bands means LTE-M and NB-IoT don’t have multiple overlapping networks to coordinate with
So coexistence isn’t a concern
And they already have more capacity than the unlicensed protocols
Without solutions for unlicensed LPWANs, deployments will move to cellular networks
And when the applications leave, research will leave as well
Without real solutions to the problems they face, we’re in danger of losing an exciting research domain
We pose this as a challenge to the community to develop coexistence and capacity solutions for unlicensed LPWANs

## Slide 48: Unlicensed LPWANs are still useful for some scenarios.
Controlled or unoccupied regions have reduced coexistence concerns.
  Industrial factories, farms, parks and forests.
Unlicensed networks are very exciting for research.
  Anyone can deploy a network wherever they want.
  Much easier to explore protocol modifications and new technologies.
Research suffers without real-world applications.
  Problem areas are strong recommendations for new research.
  New research is only useful if they will have real-world impacts.

## Slide 49: Implications – Low-Power Wide-Area Networks.
Existing unlicensed LPWANs face significant challenges in supporting urban applications.
  Best suited for industrial or agricultural uses in controlled environments.
Research directions for unlicensed LPWANs:
  improve network capacity,
  and enable coexistence.
Cellular IoT networks (LTE-M and NB-IoT) are positioned to solve the needs of city-scale sensing.
  If the money and energy costs are there.

## Slide 50: Outline
LPWAN Use Cases
Improving LoRaWAN
LPWAN Challenges