## Slide 1: Lecture 02 Network Fundamentals
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2024
Some slides borrowed from: Peter Steenkiste (CMU), Christian Poellabauer (Notre Dame)
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Let me know if you don’t have access to something
Wireless lab comes out either late tonight or early tomorrow
  Individual: using wireshark and sniffing packets
Group survey is out (posted on Piazza)
  Everyone will be working in groups of three
  If you’re missing a group member, I can pair you
  If you have a full group, still fill it out so I know

## Slide 3: Forgotten last lecture: late policy and slip days
Late policy
  You can submit assignments late
  20% reduction in maximum points per day late
Slip days
  Automatically extend deadlines without penalty (automatic, don’t ask)
  Three total to use throughout the quarter
  Example
    Submit an assignment three days late with no penalty
    Submit an assignment four days late with a one-day penalty
    Submit three assignments each one day late with no penalty
  Warning: all group members are charged a slip day
    So it’s possible one person gets a penalty when the others don’t

## Slide 4: Today’s Goals
Introduce OSI layer model of communication
Provide background on Internet layering
Overview of concerns for the Physical layer
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols

## Slide 5: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 6: Communication layers
Application
Presentation
Session
Transport
Network
Data Link
Physical
What goes on at each of these?

## Slide 7: OSI model of communication layers
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
Open Systems Interconnection (OSI)

## Slide 8: Where does this class focus?
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
CS domain
CS340, CS440
EE domain EE307, EE378, EE380
This course!

## Slide 9: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
    i.e., bytes are added to the start/end of it
  Packet is wrapped with header for the link to make a frame
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 10: Analogy: Sending a letter
Application: Purpose/type of letter
Transport: Carrier service
Named recipient
Network: Street Address
Courier
Mailing/shipping infrastructure
Link: Transfer to post office
Physical: Moving tangible object

## Slide 11: Example of layering for Ethernet and IP
Headers for each layer of communication wrap data
  Data is wrapped with header for network to make a packet
  Packet is wrapped with a header for the link to make a frame

## Slide 12: Packet encapsulation
Upper-layer packet is the payload for the lower-layer packet

## Slide 13: Transmitting data between networks
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
(2)
internet packet
(7)
data
PH
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header
LAN1 frame

## Slide 14: Model does not equal reality
Wireless protocols don’t always split between layers cleanly
  Usually explain parts of physical, data link, and possibly upper layers
Model still helps conceptualize stack-up though
  Layering of some type still occurs

## Slide 15: Layering for IoT (joke) (kind of)
MQTT
MQTT is a publish/subscribe message broker

## Slide 16: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 17: The global Internet
Most famous example of an internet (uppercase to distinguish)
Based on the TCP/IP protocol family
  IP (Internet Protocol)
    Provides a naming scheme and unreliable delivery of packets from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable data delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable data delivery from process-to-process
Accessed via a mix of Unix file I/O and the sockets interface

## Slide 18: Hardware and software organization of an Internet application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 19: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.7.30
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.7.30 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 20: 1. IP addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian)
    Remember: most computers use little-endian😭
  True in general for any integer transferred in a packet header from one machine to another
    E.g., the port number used to identify an Internet connection
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8169071E = 129.105.7.30
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 21: 2. Internet domain names
.net
.edu
.gov
.com
northwestern
berkeley
mit
eecs
mccormick
moore
129.105.7.30
wot
unnamed root
www
129.105.1.129
hanlon
129.105.7.27
amazon
www
54.230.48.28
Top-level domain names
Second-level domain names
Third-level domain names
and onwards…
Note: Northwestern owns 129.105.x.x

## Slide 22: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries
  Each host entry defines the mapping between a set of domain names and IP addresses
A special name: localhost
  Refers back to the computer being used (IP address 127.0.0.1)

## Slide 23: 3. Internet connections
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
    IP address identifies the computer
    Port identifies the process on the computer
Clients and servers communicate by sending streams of bytes over connections. Most connections are:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  [TCP adds] Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.

## Slide 24: Ports are used to identify services to the kernel
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 25: How does the Internet handle routing packets?
IP layer
  Describes application connection
    Packets from my computer <---> Google
Link layer (Ethernet)
  Describes individual links
    Packets from my computer <---> my router
Routing
  Using link-layer building blocks to get packets from one IP to another

## Slide 26: Addressing
How to solve the routing problem?
  I need to know how to get data from me to you
How does the post office work?
  I know where you live (your address)
    Zip Code
    City
    Street
    House Number
    Name

## Slide 27: A problem with addressing
Your computer moves all the time
  Home, school, Starbucks...

## Slide 28: Assigning and finding IP address ranges
In general, network operators don’t change that often
Solution:
  Tie IP addresses to network operators
  Assign computers IPs as they join networks
Key Point:
  Networks ”own” a block of IP address space
  ”The Internet” is a network of networks

## Slide 29: Routing
1.0.0.0/8
5.0.0.0/8
2.0.0.0/8
10.0.0.0/8
4.0.0.0/8

## Slide 30: Routing
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 31: Routing Adaptation
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 32: Identifying your computer?
Every network card has its own MAC address
  IPs are (somewhat) dynamic, ”owned” by local networks
  MACs are hardware and static, ”owned” by specific computers
    Manufacturers own blocks of MACs, ”spend” them each time they make a device
”Connecting” to a network
  Your computer leases an IP from the local network
  Only the local router knows your MAC, everyone else sees your IP
    Note: this overview ignores NATs, which are commonplace today

## Slide 33: So how does the Internet of Things fit into the Internet?
“IP is the Narrow Waist of the Internet”
  IP is Dead, Long Live IP for Wireless Sensor Networks
A recurring theme in this class:
  How does this actually attach to the Internet
    Physically, direct IP connection [hello Hue Hub, Wyze Hub, August Hub, …]
    Logically, through another device [are BLE devices really part of the IoT?]

## Slide 34: Break + Thinking
What are the steps for viewing a website?

## Slide 35: Break + Thinking
What are the steps for viewing a website?
You enter a domain name for the website
Computer looks up domain name to get IP Address
Computer sends request to IP_address:80
Computer gets back data, which it renders into a website

## Slide 36: ALL the layers
A ‘famous’ interview question
  “What happens when you type google.com into your browser’s address bar and press enter?”
  https://github.com/alex/what-happens-when (11 pages!)
    Keyboard events
    Parsing URL
    DNS lookup
    Opening socket
    HTTP protocol
    HTML parsing
    GPU rendering

## Slide 37: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 38: Physical Layer
How bits are transmitted
  Wireless makes this entirely different from wired cases
Important considerations
  Signal strength
  Modulation
  Frequency

## Slide 39: Why use wireless?
There are no wires!
No need to install and maintain wires
  Reduces cost
  Simplifies deployment – place devices wherever makes sense
Supports mobile users
  Move around office, campus, city
  Move devices around home

## Slide 40: What is hard about wireless?
There are no wires!
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all

## Slide 41: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 42: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links just increases interference
  Need to expand to different frequencies

## Slide 43: Model of RF communication
Energy that radiates spherically from an antenna
Attenuation with distance
  Density of energy reduces over time, distance
  Signal strength is reduced, errors go up
Two key features
  Error rates depend on distance
  Spatial reuse of frequencies

## Slide 44: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 45: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 46: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 47: Signal strength is measured in decibels
Power is measured in Watts or dBw or dBm
dBm is most relevant to the IoT domain
  0 dBm equals 1 mW transmit power
  Example
    Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
    Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
Rule of thumb: +3 dB is double the power

## Slide 48: Signal strength varies significantly across technologies
Bluetooth Low Energy (local area)
  nRF52840 transmit power: 8 dBm (6.31 mW)
  nRF52840 receive sensitivity: -95 dBm (316.2 fW)
LoRa (wide area)
  SX127X LoRa transmit power: 20 dBm (100 mW)
  SX127X LoRa receive sensitivity: -148 dBm (1.6 attoWatt)

## Slide 49: Propagation degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out  Free Space Path Loss (FSPL)

## Slide 50: Some intuitions for signal propagation, power, gain, etc
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 51: Wait, is not an antenna
Indeed, this little strip of metal is the actual antenna
  Receiver only recovers the part of the signal that hits its antenna (“aperture”)

## Slide 52: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 53: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
.25 m

## Slide 54: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
1 m

## Slide 55: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m

## Slide 56: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 57: Okay.. So what’s the limit?
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
8 dBm – -95 dBm = 103 dB link margin
For FSPL alone for a 2.4 GHz signal, 103 dB is 1,400 m!
Bluetooth does not go 1.4 km…

## Slide 58: Free-Space Path Loss Model
https://semfionetworks.com/blog/free-space-path-loss-diagrams/

## Slide 59: Propagation is one thing that degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out -> free space path loss
Important: distance is NOT the only signal strength loss
  Free space path loss calculation will not give you accurate range for a signal
Obstacles can weaken signal through absorption or reflection
  Precise quantitative details are in the EE domain
  We’ll use examples to develop qualitative instincts in this class

## Slide 60: Many factors affect the ability to actually receive data
Here’s some examples, from DW1000 [ultra wideband transceiver]

## Slide 61: ITU model for Indoor Attenuation
Models like this are more trustworthy less bad than Free-Space Path Loss
  https://en.wikipedia.org/wiki/ITU_model_for_indoor_attenuation

## Slide 62: Lower received energy increases error rates
More Errors
Less Errors
More Energy Received
Less Energy Received
BER: Bit Error Rate
Odds that a transmitted bit will be received incorrectly

## Slide 63: Big Idea: many RF factors are interconnected
Energy, Distance, Throughput, and Reliability are all interconnected in communication
Protocols make choices of some and get the results on the others
To get more distance, choose one or more:
  Increase energy
  Communicate slower
  Accept a higher error rate

## Slide 64: Break + Say hi to your neighbors
Things to share
  Name
  Major
  One of the following
    Favorite Candy
    Favorite Pokemon
    Favorite Emoji

## Slide 65: Break + Say hi to your neighbors
Things to share
  Name -Branden
  Major -EE, CE, and CS
  One of the following
    Favorite Candy - Twix
    Favorite Pokemon - Eevee
    Favorite Emoji - 🍢

## Slide 66: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 67: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 68: Sum of sinusoids can be reversed
RF signals are fundamentally sinusoids of electromagnetic energy
Sinusoids at different frequencies can be combined and pulled apart again later
  Particularly, it’s relatively easy for hardware to determine if there’s energy present on a given frequency
  Although very close frequencies might be difficult to disentangle

## Slide 69: Complex waveforms have a center frequency and a width
A pure sinusoid is energy at exactly one frequency
A messy sinusoid with data layered on top of it has nearby energy
  There’s a center of the signal energy
  Plus some amount of width, which depends on how complicated the data layered on top is

## Slide 70: How do radio stations work?
FM radio in cars is a good example of frequencies
  All of FM radio has an allocation of 87.5 to 108.0 MHz
  Each station takes has up to ~200 kHz of bandwidth
First station is 87.7 MHz +/- 100 kHz
  Ranges from 87.6 to 87.8
Second station is 87.9 MHz +/- 100 kHz
  Ranges from 87.8 to 88.0
What if they overlapped? They interfere with each other
  You’d possibly hear both. Or get junk data that’s neither.

## Slide 71: RF communication frequencies
IoT focus

## Slide 72: Wireless spectrum is allocated to specific uses

## Slide 73: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi

## Slide 74: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?

## Slide 75: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why? No interference from other users

## Slide 76: Different technologies use spectrum in different ways
How spectrum is used affects: cost ($), robustness, throughput…
  We will talk about how each technology uses spectrum, and implications
This graphic shows how BLE and WiFi interoperate; more on this next week

## Slide 77: Frequency Hopping Spread Spectrum
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 78: Sidebar: inventor of FHSS – Hedy Lamarr
Actress, inventor, and all-around badass
  Designed FHSS with George Antheil during WWII based on music ideas
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventing_career

## Slide 79: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 80: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 81: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 82: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 83: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Usually differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 84: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 85: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation