## Slide 1: Lecture 03 Data Link Layer + BLE Introduction
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2024
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Hw: Background
  Goal: brush up on some embedded systems and networks background
  Due tonight
  Submit on Gradescope
Lab: Wireless
  Goal: familiarize yourself with Wireshark
    Install it, do some basic scanning, explore a little
  Submission:
    Due Tuesday by end-of-day
    Submit on Gradescope
    Reminder: not a formal writeup or anything. Just the answers

## Slide 3: Partnership survey
Labs (after this first one) will be in groups of exactly three
I’m trying to
  Figure out what the groups are
  Match up students who need groups
Please fill out the survey posted on Piazza
I’ll go through this weekend and match up groups

## Slide 4: OSI model of communication layers
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
Open Systems Interconnection (OSI)

## Slide 5: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.7.30
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.7.30 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 6: How does the Internet handle routing packets?
IP layer
  Describes application connection
    Packets from my computer <---> Google
Link layer (Ethernet)
  Describes individual links
    Packets from my computer <---> my router
Routing
  Using link-layer building blocks to get packets from one IP to another

## Slide 7: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 8: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 9: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 10: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Usually differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 11: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 12: Today’s Goals
Overview of concerns for the Data link layer
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols
Describe Medium Access Control mechanisms
Introduction to Bluetooth Low Energy
  What are the goals of the protocol?
  What do the lower layers look like?

## Slide 13: Bluetooth Low Energy Resources
Good walkthrough of BLE:
  https://www.silabs.com/documents/public/user-guides/ug103-14-fundamentals-ble.pdf
[5.2 specification] [4.2 specification] (link to PDF download)
  Also: [Supplement v9]
I used a mix of 5.2 and 4.2 for this
  Will talk about BLE 5 differences as part of next lecture

## Slide 14: Outline
Data Link Layer
BLE Background
BLE Layers
  Physical Layer
  Link Layer

## Slide 15: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 16: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Possible wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 17: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 18: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 19: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Task: in one minute you will have to start counting from zero
  One person per number
  Count quickly
  You all fail if two people speak at the same time
  We’ll take it in groups
  After a whole group speaks, they’ll explain what strategy they used
  Each group must have a unique strategy
    So be creative! Or have a backup strategy

## Slide 20: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)
Everyone speak in different languages -> code division multiple access (sort of, but not really)
Others?

## Slide 21: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 22: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 23: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 24: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad
My transmission
My transmission
Other transmission
Other transmission

## Slide 25: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
My transmission
Other transmission
Other transmission
My transmission
time

## Slide 26: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 27: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 28: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 29: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 30: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Very challenging for wireless systems
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm
  Area of active research!

## Slide 31: Hidden terminal problem
Device A
Device B
Device C

## Slide 32: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low
    Not always worth it

## Slide 33: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 34: Contention-free access control protocols
Goal: split up communication such that devices will not conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 35: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
  Usually in conjunction with another scheme (but not always)
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 36: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 37: Break + Question
What is an advantage of Aloha over TDMA?

## Slide 38: Break + Question
What is an advantage of Aloha over TDMA?
  Simplicity! It’s really easy to implement Aloha
  No required centralization
    TDMA time schedule needs to be decided by something
    That thing is “in charge”
    Aloha can be entirely distributed

## Slide 39: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 40: Outline
Data Link Layer
BLE Background
BLE Layers
  Physical Layer
  Link Layer

## Slide 41: Basics of Bluetooth Low Energy (BLE)
Direct device-to-device communication
  Usually: Computer to Thing
  Smartphone to device, Laptop to device, etc.
Focus on making the “Thing” really low energy
  Push energy-intensive requirements onto “Computer”
Devices (Computer or Thing) are servers with accessible fields
  Not the traditional send-explicit-packets interface you might be expecting
  Lower layers are still exchanging packets to make it work

## Slide 42: A note on outdated notation
Master/Slave paradigm
  Master is the “Computer” and is in charge of interaction
  Slave is the “Device” and has little control over interaction parameters
  Really common notation in EE side of the world.
    Not intended to be harmful, but also literally inconsiderate.
Field is changing for the better. It’s going to take some time.
  Central/Peripheral
  Device/Peripheral
  Controller/Peripheral
  Master/Minion
  Primary/Secondary

## Slide 43: BLE development
Protocol development
  Research product
  Specification
  Hardware support
  Usefulness and iteration
Bluetooth Low Energy
  Research in early 2000s: Bluetooth Low End Extension and Wibree
  Specification in 2009: Bluetooth version 4.0
  Hardware support in 2011/12: iPhone 4s, nRF51 series
  4.1 and 4.2 (2014), 5.0 (2016, first in phones 2017, really 2019 though)

## Slide 44: Bluetooth has a long history — the IoT is near-exclusively BLE (Bluetooth 4.0+) as opposed to Bluetooth Classic (<4.0)

## Slide 45: Bluetooth Specification
Problem: a bit overwhelming…
  5.2 spec: 3256 pages
  We only care about Vol 6: Low Energy Controller
    Part A: Physical Layer Specification
    Part B: Link Layer Specification
    CSS: Part A: Data Types Specification
    So ~250 pages
Tip: be willing to just ignore things when skimming specs
  5.2 spec covers BLE and Bluetooth Classic and a bunch of upper layer stuff that we never have to care about

## Slide 46: BLE Layers
Host – Configuration and Server
  GAP – Generic Access Profile
    Configure advertising
  GATT – Generic ATTribute profile
    Configure connections
HCI - Host Controller Interface (sigh)
Controller - Communication
  Link Layer – send packets
  RF and PHY – send bits
GAP
Host
Controller

## Slide 47: BLE mechanisms
Advertising
  Discovery
  Advertisements – broadcast messages indicating device details
  Ephemeral, uni-directional communication from Advertiser to Scanner(s)
  ALOHA access control
Connections
  Interaction
  Bi-directional communication between Peripheral and Central
  Maintained for some duration
  TDMA access control

## Slide 48: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 49: Multiple roles at the same time
Topology picture is a simplification of roles
A single device can have multiple roles simultaneously
  Scanning and Advertising simultaneously
  Peripheral and Scanner and Advertiser simultaneously
  Peripheral and Scanner and Central and Advertiser simultaneously
    Getting a bit out of hand though
One Peripheral can even be connected to multiple Centrals
  Not in the original design though: you’ll find old docs saying you can’t
  And it’s not a normal use-case for BLE

## Slide 50: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
  Laptop
  Smartphone

## Slide 51: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
    Advertiser and Peripheral
  Laptop
    Scanner and Central
  Smartphone
    Advertiser, Peripheral, Scanner, and Central

## Slide 52: Outline
Data Link Layer
BLE Background
BLE Layers
  Physical Layer
  Link Layer

## Slide 53: BLE frequency
2.4 GHz carrier, Forty 2-MHz channels, 1 Mbps data rate
  37, 38, 39 for advertising
  0-36 for connection (FHSS)
Why doesn’t BLE avoid WiFi altogether?

## Slide 54: BLE frequency
2.4 GHz carrier, Forty 2-MHz channels, 1 Mbps data rate
  37, 38, 39 for advertising
  0-36 for connection (FHSS)
Why doesn’t BLE avoid WiFi altogether?
Can’t on 2.4 GHz
Wants 2.4 GHz for technology improvements

## Slide 55: BLE modulation
Gaussian Frequency-Shift Keying (GFSK)
  Improvement on base Frequency-shift Keying
  Smoother transitions between bits -> reduces nearby interference

## Slide 56: Why use GFSK?
Gaussian FSK lessens spectral leakage at the expense of some loss in intersymbol discriminability
Translation: GFSK reduces bandwidth at the cost of bit errors
Notes: Images from http://j3.rf-explorer.com/40-rfe/article/53-tutorial-how-to-use-rf-explorer-to-monitor-a-rfbee?start=4

## Slide 57: An example from `good case` BLE hardware
Notes: Fig 8 in https://download.ni.com/evaluation/rf/intro_to_bluetooth_test.pdf

## Slide 58: BLE signal strength
Remember nRF52840 capabilities
  Transmit: up to 8 dBm
  Receive sensitivity: -95 dBm

## Slide 59: Outline
Data Link Layer
BLE Background
BLE Layers
  Physical Layer
  Link Layer

## Slide 60: Packet structure
Same packet structure for both advertisements and connections
  Fields are filled in little endian (the opposite of network byte order 😡)
Access address unique for each connection (randomly chosen)
  In Advertising always set to 0x8E89BED6
Data

## Slide 61: Device addresses
Public and private address forms
Public
  48 bits: 24-bits of company ID, 24-bits of company assigned number
  Literally the same MAC address scheme as Ethernet and WiFi
Private
  Top two MSbs specify type
    46 bits of random
    46 bits of hash of an identity key
Why have the two types?

## Slide 62: Device addresses
Public and private address forms
Public
  48 bits: 24-bits of company ID, 24-bits of company assigned number
  Literally the same MAC address scheme as Ethernet and WiFi
Private
  Top two MSbs specify type
    46 bits of random
    46 bits of hash of an identity key
Why have the two types? Privacy

## Slide 63: Data whitening
Avoid long series of repetitive bits (all zeros or all ones)
  Would cause RF noise to be more focused in one direction
  Radio hardware desires output to have zero DC-bias (or close to that)
  Great example of the PHY and MAC being interwoven in wireless
I always forget this exists, since hardware usually handles it automatically

## Slide 64: Bit processing pipeline

## Slide 65: Break + Question
With enough scanners, could you track BLE devices as they move?

## Slide 66: Break + Question
With enough scanners, could you track BLE devices as they move?
  Link Layer
    Depends on how long they use a device address for
    You can do a scan of BLE transmissions to find device addresses
    Scans at multiple locations can detect when a device moves throughout an area
    But if the device re-randomizes between two scanners, you can’t follow it anymore
      Re-randomizing at a scanner could be detectable…
      Or if the user has more than one device with unsynchronized rotation schedules

## Slide 67: Break + Question
With enough scanners, could you track BLE devices as they move?
  Physical Layer
    Fingerprint unique physical-layer imperfections in signals
    Looking at things like amplitude and timing
    2022 paper out of UCSD explores this

## Slide 68: Outline
Data Link Layer
BLE Background
BLE Layers
  Physical Layer
  Link Layer