## Slide 1: Lecture 09 IoT Network Routing
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Spring 2024
With slides from Federico Ferrari (ETH Zurich) and assistance from Andreas Biri (ETH Zurich)
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Today’s Goals
Overview of routing for mesh networks
  Walkthrough of one protocol (AODV: what ZigBee uses)
Describe research in improving data dissemination

## Slide 3: Outline
Simple Routing
Mesh Routing
Better Flooding
Low-power Access Control

## Slide 4: Routing goals
Have a packet, have a destination, how do we connect them?
We’ll think about a couple of approaches here
  Simple techniques
    Broadcast, tree structures
  Mesh techniques
    Understand the available routes and select a “good” one

## Slide 5: Simple routing solutions
Broadcast
  The link-layer solution for everything
Star topology
  Only one location to send to: parent
  Single parent needs to store information about all children
    Addresses, schedules, etc.
Tree topology
  “Star of stars”
  Two choices: send to descendent or send to parent
  Each parent needs to store information about all children beneath it
  Original ZigBee approach (knowledge built into addressing scheme)

## Slide 6: Many-to-one routing (Collection Tree Protocol, CTP)
Tree optimization for sensor networks
  Keep all devices except the “gateway” as simple as possible
Each device only needs to remember hop to gateway
  If gateway wants to send message back, it must include a full hop path

## Slide 7: Outline
Simple Routing
Mesh Routing
Better Flooding
Low-power Access Control

## Slide 8: Mesh Routing
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 9: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?

## Slide 10: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?
  Maximum retransmissions counter on each packet
    Decrement at each hop. Drop packet when it hits zero
    Need some guess for how many hops to destination
  Or keep some history of recently flooded packets
    Don’t retransmit a recently sent packet

## Slide 11: Reactive routing
Build up a map of the routes through a network
  Hopefully the “optimal” routes
Map routes in reaction to a packet arrival
  Sensor devices are slow and limited
  Most likely to resend to same prior address
  Discover a route when it is needed, then cache for next time

## Slide 12: Ad-hoc On-demand Distance Vector Routing (AODV)
On-demand: Construct routes only when needed
Modern ZigBee routing approach (for Mesh topology)
Routing table
  Destination node -> Next hop (for all cached destinations)
  Store only next hop instead of full route
    All routers along the path must also have Destination->Next mappings
  Also keep hops-to-destination and last-seen-destination-sequence-number
Route discovery
  Upon demand: check table
  If not cached send Route Request (RREQ) via Flooding
    Route is unknown, so flooding is needed
AODV documentation: https://www.ietf.org/rfc/rfc3561.txt

## Slide 13: AODV Route Requests (RREQs)
Request ID identifies this RREQ
  Used to discard duplicates during flooding
  Unless less hops and equally recent, OR more recent
Sequence Numbers are per-device, monotonically increasing
  Used as a notion of “how recently” device has been seen
  Source SeqNo is the source’s most recent sequence number
  Destination SeqNo is the most recently seen from the destination by the source. (Defaults to zero)
Hop Count is the number of hops this request has taken
  Starts at 1 and incremented by each transmitter along the path
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count

## Slide 14: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
A wants to find a route to F, so it sends out an RREQ

## Slide 15: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 1
B and D also opportunistically add a routing table entry for A

## Slide 16: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
B goes first via some access control protocol (D also in contention)
A and D ignore duplicate Request ID C opportunistically adds a routing table entry to A

## Slide 17: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
D goes next by some access control protocol (C also in contention)
A, B, and C ignore duplicate Request ID E and F opportunistically add routing table entries to A

## Slide 18: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 3
C and E repeat this process with Hop Count 3 (but everyone ignores them)
They go one-at-a-time, but I’m getting tired of drawing these
Actually, they’re in contention with the response from F

## Slide 19: AODV Route Response (RREP)
Reply is sent unicast back to the source via newly constructed route
  Each node along the way already knows the route back
Includes most recent own sequence number as a sense of recency
  “Destination” from the perspective of the original RREQ
  No need for source sequence number anymore
Source Address | Destination Address | Destination SeqNo | Hop Count

## Slide 20: Example AODV RREP (F to A)
A
B
C
D
E
F
Source Address | Destination Address | Destination SeqNo | Hop Count
F | A | 7 | 2
F sends response back to A via D
D opportunistically adds a routing table entry for F

## Slide 21: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
A
B
C
D
E
F

## Slide 22: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
    RREQs:
      C -> (B,D,F)
      (B or D) -> A
      (D or F) -> E
    RREPs:
      E -> (D or F) -> C
  Network could have multiple configurations
A
B
C
D
E
F

## Slide 23: RREP optimization
An intermediate node responds with RREP if it already has a path to destination with a more recent Destination sequence number
Source may get multiple RREP responses with different recency and hop counts
  So, some intermediate node could respond “here’s the route I knew of when sequence number was 5”
  Then, destination node could respond “here’s the route right now, I’m actually on sequence number 12”
  Likely want the most recent
    If equally recent, use the least hops

## Slide 24: When to update your route
Routing table entries are updated on RREP if:
  Sequence number in routing table is marked as invalid
  Destination sequence number in the RREP is greater the listed one
  Sequence numbers are the same, but the route was marked as inactive
  Sequence numbers are the same, but the hop count is smaller

## Slide 25: Route maintenance in AODV
If a link in the routing table breaks, all active neighbors are informed with Route Error (RERR) messages
  After some number of retransmissions and timeouts
  RERR contains destination address that broke
Nodes receiving RERR can start RERQ for destination address
  Which lets them find a new path through the network
  And updates everyone’s cached next-hops

## Slide 26: Similar alternative: Dynamic Source Routing (DSR)
Another reactive routing technique
  Similar design as AODV
In DSR, routing tables have full route to destination
  Each packet transmission includes a list of hops to destination
  So the route to an important destination only has to be stored on the source device that cares about it
  Intermediate nodes do not need any route storage for that destination
    Cost is extra bytes used in each packet for route
During discovery, all paths are returned by destination
  So source gets a full list of possible route choices

## Slide 27: Tradeoffs for reactive routing
Upside: no transmissions unless there is demand
  Routes might appear, disappear, reappear, but no need to update if no one actually wants to transmit anything
Downside: large, variable delay when actually sending a packet
  Full RREQ/RREP protocol before data can actually be sent
  Route might have broken at some point
    So data will be sent based on cached information
    RERR will occur
    RREQ/RREP will occur
    Then data will be sent again

## Slide 28: Proactive routing
Alternative to reactive is to know the routes ahead of time
Periodically query for the possible routes in the network
  Save all routes that are important (maybe just all routes?)
  Also redetermine routes whenever topology changes (nodes join/leave)
Upside: when a packet arrives, route to destination is already known
Downside: requires more memory and effort on part of routers
  Wastes some network bandwidth on checking for route changes

## Slide 29: Distance-Vector
Keep routes as “next hops” rather than full routes
  AODV uses this method (DV for Distance Vector)
Can be combined with proactive techniques too
  Each router periodically informs neighbors of its shortest paths to each destination (in terms of hop count)
    Essentially just broadcast your routing table
  Routers choose the best route available
    Either old next-hop it was already aware of
    Or new next-hop through neighbor (with cost of their hops + 1)
  Need to be careful to avoid loops!

## Slide 30: Thread routing
Uses a proactive, distance-vector protocol for unicast routing
If node is a child, send packet to parent router
If node is a router,
  Consult table for address within mesh
    (RLOC helps here!)
  Send to border router for address outside of mesh
Multicast uses a data dissemination protocol (Trickle)
  Or falls back to flooding

## Slide 31: Break + Discussion
Hop count is one possible metric for determining routes
What else might be considered?

## Slide 32: Reliability as a cost metric
Link quality can very from node to node
  Fewest hops might not be the “fastest” or “most reliable” path
ETX: minimize “expected transmissions”
  Measure link quality over time to determine each link’s reliability
A
B
C
D
E
F

## Slide 33: Alternative cost metrics
Spatial reuse
  Prefer transmission on links that do not interfere with each other
  Improves ability to pipeline data through network
  Example: A<->B and E<->F
Energy availability
  Prefer routing through nodes with more remaining available energy
  Prefer wall-powered nodes over battery-powered
Arbitrarily complex combinations possible

## Slide 34: Outline
Simple Routing
Mesh Routing
Better Flooding
Low-power Access Control

## Slide 35: Flooding is a recreation of broadcasts
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Really, the desire for data dissemination is just to broadcast to all nodes
  But broadcast transmissions don’t reach far enough to cover entire mesh

## Slide 36: Glossy: what if we expand broadcast range by having multiple nodes participate?

## Slide 37: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 38: Sidebar: broadcast transmission acknowledgements
A-MAC: https://web.eecs.umich.edu/~prabal/pubs/papers/dutta12amac.pdf
P = Probe (data request) A = Acknowledgement
D = Data transmission L = Listening period
P-CW = Probe with Contention Window for response

## Slide 39: How do we avoid interference?
Fundamental insight:
  “say exactly the same thing at exactly (enough) the same time” leads to coherence instead of interference
In 802.15.4, an ACK is sent exactly 192 µs after receiving
  The ACK packet contains only the sequence number being ACK’d
  Does not contain source address of the ACK-er
  Which is why this works:

## Slide 40: Glossy key techniques
Temporally decouple network flooding from application tasks
Exploit synchronous transmissions for fast network flooding

## Slide 41: Fast packet propagation in Glossy

## Slide 42: Fast packet propagation in Glossy

## Slide 43: Fast packet propagation in Glossy

## Slide 44: Fast packet propagation in Glossy

## Slide 45: Glossy details
When Glossy starts
  All nodes turn on radios to receive

## Slide 46: Glossy details
Initiator
  Set relay counter in packet, C = 0
  Broadcast packet

## Slide 47: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 48: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 49: Glossy details
Stop rebroadcasting and turn off radio when
  Already transmitted N times
  Networks pick N for reliability/energy tradeoff

## Slide 50: Glossy details
Tslot is constant by design
  Needs to be short to make constructive interference work
Beginning of slot (tref) provides synchronization point
  As a bonus, all nodes are synchronized after flooding event

## Slide 51: Glossy implementation
Device must be able to have tight time bounds on rx/tx
  500 ns wiggle room maximum
  Includes receive, processing, transmission
    Implies a maximum physical distance for a network
Need to pick an N for reliability

## Slide 52: Application of Glossy: avoid routing altogether
Low-Power Wireless Bus (LWB)
  Federico Ferrari, Zimmerling, Mottola, Thiele. SenSys’12
Use Glossy for all device communication
  Make one broadcast domain (a bus) where all nodes communicate
  Avoids all issues of routing, everything is a broadcast
    Works for unicast, multicast, anycast, and broadcast transmissions
General idea: TDMA Glossy floods
  Synchronization is already given to nodes by Glossy
  One coordinator makes the TDMA schedule

## Slide 53: Outline
Simple Routing
Mesh Routing
Better Flooding
Low-power Access Control

## Slide 54: Always-on Radios Simplify Protocols
Many protocols assume a more-powerful device with lots of energy
  BLE: Central
  Thread: Router/Leader
  Zigbee: Router/Coordinator
  WiFi: Router
  LoRa: Gateway
This assumption simplifies the “when to listen” problem
  Powerful device: always listen
  Low-power device: listen-after-talk or synchronized schedule

## Slide 56
Early 2000s

## Slide 57: Early days of low power sensor nodes
WINSng [Pottie00]
Mica [Hill01]
Rene [Hill99]
Mica2 [Xbow03]
MicaZ [Xbow05]
PC/104 [Cerpa01]
PASTA [Bajura05]
mPlatform[Lymberopoulos07]
WeC [Hill98]
WINS [Rockwell]
Stargate [Intel]
Telos/Tmote
[Polastre05]
Iris [Xbow07]
Tmote Mini
[Sentilla07]
MicaZ Stamp
[Xbow06]
Iris OEM
[Xbow07]

## Slide 58: Low power goal: multi-year operation using batteries
Powernode = PCPU + PTX + PRX + PSLEEP
EnergyBATT = Pnode * lifetime
For Lifetime to increase, Pnode must decrease
  PCPU ≫ PSLEEP
  PTX ≫ PSLEEP
  PRX ≫ PSLEEP
  Solution: Minimize Compute, TX, and RX
    Maximize Sleep

## Slide 59: Low power MAC principles
Communication is possible if one device is receiving while other is transmitting
Devices can only coordinate using the data communication channel (i.e. no out-of-band communication)
  No global synchronization mechanism
Goal: scheme to schedule TX and RX to permit communication while minimizing energy
Energy is paramount, but additional metrics:
  Latency
  Throughput
  Reliability
  Network scale
A
B
Both devices want to minimize the time they are receiving or transmitting (i.e. their radio is on) to reduce power draw

## Slide 60: Low Power Listening (LPL) - B-MAC (2004)
Method:
  Receiver periodically samples the channel
  Transmitter sends a preamble long enough to ensure receiver will detect it
  Upon detection, receiver stays awake to receive transmitted packet
  Receiver ACKs if packet received correctly
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004
CCA
TX ACK
RX ACK

## Slide 61: LPL performance
CCA check interval
  Too small: energy wasted on idle listening
  Too large: energy wasted on transmissions (long preambles)
In general, it’s better to have larger preambles than to check more often!
Sensor sample period controls the packet rate
Time between listening
(checking if the channel is idle)
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 62: LPL Drawback
CCA
Receiver
Transmitter
Sleep
Sleep
CCA
Sleep
RX
Sleep
Preamble
TX
Sleep
CCA
Sleep
Sleep
CCA
TX ACK
RX ACK
Spend time listening to packets for someone else!
A
B
C
CCA
Receiver
Sleep
Sleep
CCA
Sleep
RX
Sleep
CCA
Sleep
CCA
DROP
A
B
C
Versatile Low Power Media Access for Wireless Sensor Networks. Joseph Polastre, Jason Hill and David Culler. SenSys 2004

## Slide 63: X-MAC: Shorter preambles and destination information
Method
  Transmitter sends a short “I have a packet for this address” packet
  Nodes periodically listen, and ACK if the packet is for them
  Upon receiving the ACK, the transmitter sends full packet
  Receiver successfully receives the full packet.
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
TX (DST ID)
TX (DST ID)
TX (DST ID)

## Slide 64: X-MAC: Overhearing node drops out early
RX
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX (DST ID)
TX
Sleep
RX
Sleep
Sleep
RX
TX ACK
RX ACK
A
B
TX ACK
RX ACK
RX
Overhearer
Sleep
Sleep
RX
Sleep
C
TX (DST ID)
TX (DST ID)
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 65: X-MAC: lower power draw than LPL with multiple nearby transmitters
X-MAC: A Short Preamble MAC Protocol for Duty-Cycled Wireless Sensor Networks. Michael Buettner, Gary V. Yee, Eric Anderson, Richard Han. SenSys 2006.

## Slide 66: LPL (B-MAC) and X-MAC are transmitter-initiated MAC protocols
Receiving nodes continuously periodically sample the wireless channel
  When they detect a transmission they listen to receive packets
Transmitting nodes are only active when they want to transmit
Receiving nodes prone to unnecessary wakeups
  Have to receive all nearby transmissions to see if the packet happens to be for them
  Unnecessary wakeups lead to increasing receive energy  shorter lifetime
  In general, difficult for receiver to know if it should stay awake or go back to sleep

## Slide 67: Low Power Probing (LPP) is receiver initiated
Method
  Receiver periodically transmits a probe, listens afterward
  Transmitter listens for probe packet from intended recipient
  Transmitter sends packet after receiving the correct probe packet
  Works a lot like BLE advertisements!!
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX ACK
A
B
RX ACK
TX Probe
TX Probe
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.
RX
RX

## Slide 68: LPP introduces a new challenge for multiple nodes. What happens with multiple transmitters?
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
Sleep
RX
TX Probe
TX Probe
If multiple transmitters receive a probe, they both transmit, leading to a collision and a lost packet
Receiver is unsure if there even was a packet at all, or just noise/interference on the channel
Transmitter
Sleep
TX
Sleep
RX
Collision!!
Koala: Ultra-Low Power Data Retrieval in Wireless Sensor Networks. Razvan Musaloiu-E., Chieh-Jan Mike Liang, Andreas Terzis. IPSN 2008.
RI-MAC: A Receiver-Initiated Asynchronous Duty Cycle MAC Protocol for Dynamic Traffic Loads in Wireless Sensor Networks. Yanjun Sun, Omer Gurewitz, David B. Johnson. SenSys 2008.

## Slide 69: A-MAC resolves this with backcast constructive interference
TX Probe
Receiver
Transmitter
Sleep
Sleep
RX
Sleep
TX
Sleep
Sleep
RX
TX ACK
TX Probe
RX ACK
Method
  Transmitters send an ACK in response to a probe packet
  With multiple transmitters, the ACKs collide, but interfere non-destructively, so the receiver still receives an ACK
  The receiver stays awake to receive a packet, but the packet collides
  The receiver sends a new probe, informing transmitters there was a collision
  Transmitters use CSMA/CA to send packets
Transmitter
Sleep
TX
Sleep
RX
TX ACK
Collision!!
Design and Evaluation of a Versatile and Efficient Receiver-Initiated Link Layer for Low-Power Wireless. Prabal Dutta, Stephen Dawson-Haggerty, Yin Chen, Chieh-Jan Mike Liang, and Andreas Terzis. SenSys 2010.
TX Probe
CCA
TX
CCA
Listen
TX ACK
CCA
TX ACK
TX
RX ACK
RX ACK
Sleep
RX
RX
Listen
RX
RX
Listen

## Slide 70: Summary: asynchronous low power MAC protocols
Transmitter initiated protocols
  Receivers periodically sample the channel
  Transmitters transmit sufficiently to ensure recipients heard
  Examples: LPL, X-MAC
  Pros:
    Simple, intuitive
    Can balance TX and RX energy with sample interval
  Cons:
    Receivers prone to false wake-ups
    High idle listening energy costs
Receiver initiated protocols
  Receivers periodically transmit probes
  Transmitters listen for a probe before sending a packet
  Examples: RI-MAC, Koala, A-MAC
  Pros:
    Fixed, small listening energy cost for receivers
  Cons:
    Multiple transmitters leads to collisions

## Slide 71: Outline
Simple Routing
Mesh Routing
Better Flooding
Low-power Access Control