## Slide 1: Lecture 13 Cellular IoT & LPWAN Design
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2025
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Hw: Cellular
  Be sure to claim your countries soon
  Only two students per country
Final Design Project
  Writeup, due early exam week
  A few big parts
    A: Explain some application
    A: Consider the constraints on the application
    A: Choose wireless technologies that seem to best work for it
    B: Model and compare energy/battery life
    C: Compare other aspects of performance
    C: Choose a best option for your system

## Slide 3: Today’s Goals
Understand how modern “Cellular for IoT” fit into the existing cellular infrastructure, and what they do at a technical level to suit IoT needs
Discuss real-world concerns with cellular device deployments
Apply knowledge from the course to understand LPWAN design

## Slide 4: Outline
Cellular IoT
IoT on Global Cellular
LPWAN Design

## Slide 5: Reminder: the cell in cellular technologies
Place towers at corners of cells
  Directional antennas send three different frequency bands, one per cell
  Each cell gets three tower and three bands
Density of cells varies based on expected number of users
  Change cell size using Power Control

## Slide 6: 3GPP (aka: the actual answer for what stuff is really doing)
3rd Generation Partnership Project (3GPP)
Industry alliance for development of telecoms standards
  Established around 1998
  Makes “Releases” which are roughly analogous to IEEE standards/versions
    Release 8 (2008) LTE ~4G
    Release 15 (2018) NR (New Radio) ~5G
Focused on the practical
  ITU post-hoc defined “4G”, 3GPP defined LTE

## Slide 7: Mapping ”4G”, “LTE”, “LTE Advanced”, etc onto actual technologies
This Qualcomm presentation is great: https://www.qualcomm.com/media/documents/files/demystifying-3gpp-and-the-essential-role-of-qualcomm-in-leading-the-expansion-of-the-mobile-ecosystem.pdf

## Slide 8: LTE Categories
Different equipment supports different “categories” of LTE
  Maximum MCS index supported
Examples
  iPhone 6 (2015): Cat 4
  Pixel 3 (2018): Cat 16
Notes: MCS = Modulation Coding Scheme
https://mcsindex.com/ looks like all the tables for WiFi; not clear whether this is the same for cell

## Slide 9: Additional low-end categories for IoT
LTE Cat 0
  Traditional LTE, but focused on the really low end
  1 Mbps for uplink and downlink
LTE-M (LTE Cat M1)
  375 kbps uplink, 300 kbps downlink (for the commonly implemented mode)
  Reduced power and maximum bandwidth
  Increased range
NB-IoT (LTE Cat NB1)
  65 kbps uplink, 26 kbps downlink
  Reduced power and greatly reduced bandwidth
  Greatly increased range

## Slide 10: LTE-M and NB-IoT were developed in parallel

## Slide 11: Why do we need “special categories” for IoT on cell?
We can treat IoT devices differently than human-centric devices
Pragmatic for the end device
  Lower power
  Allow for long-off periods
Pragmatic for network operators
  Allows for scale– network no longer needs to assume that devices could always be on in each cell or that they all possibly need a lot of throughput

## Slide 12: LTE-M and NB-IoT downlink and uplink
OFDMA downlink
  Put the more complicated hardware in the cell tower [simple FFT demodulator]
SC-FDMA (single carrier FDMA) uplink
  Blocks of subchannels combined into one signal
  Essentially just send a single signal, with increased bandwidth.
    Simpler for end devices to implement

## Slide 13: LTE resource allocation
Cellular uses OFDMA to schedule
  Time + Frequency -> “2D Scheduling”
Cellular uses single channels up to 20 MHz
  Further divides these into 100 Resource Blocks
Resource Block
  12 subcarriers for OFDM in frequency (15 kHz each)
  7 symbols in time (0.5 ms)
Devices are allocated frequency and time based on what they are sending
  Allocated in units of Resource Blocks
One “Resource Block”

## Slide 14: Resources used by LTE-M and NB-IoT
LTE-M uses up to 6 resource blocks
  1.4 MHz of bandwidth (1.080 MHz)
  Can co-exist with other normal LTE traffic, scheduled by cell tower
  Limited to only some capability of LTE (much less throughput)

## Slide 15: Resources used by LTE-M and NB-IoT
NB-IoT uses up to 1 resource block
  200 kHz of bandwidth (180 kHz)
  Multiple deployment options
    In-band or Guard-band very common in practice

## Slide 16: Reducing energy use for IoT devices
Reduce max Tx power to 20 dBm
  Increased receive sensitivity at tower will cover it
Extended Discontinuous Reception (eDRX)
  Allow devices to reduce paging period and still stay on network
  Cell tower will hold messages
What does this get to?
  “For a LTE-M1 device that transmits data once per day, and wakes up every 60 hyper frames to check for commands (this would be about every 10 minutes), a life of 4.7 years is achievable on 2 AA batteries.”
Graphics, quote from https://www.link-labs.com/blog/lte-e-drx-psm-explained-for-lte-m1

## Slide 17: Further power reduction for simple devices
Power Saving Mode (PSM)
  For very simple, uplink-focused devices, allow them to turn off entirely but stay connected
  Minutes to days in duration
  Notify tower before sleeping, listen for packets after each transmission
Graphics from https://www.link-labs.com/blog/lte-e-drx-psm-explained-for-lte-m1

## Slide 18: Some numbers from an actual telecom: Aeris [n.b. Aeris has been a leader in cellular M2M since the 90’s]
PSM has two timers, devices request values, tower chooses actual:
  Extended Timer (“sleep” timer)
    3GPP max is 35,712,00s [413.33 days]
    Aeris timer range: Min 240m [4h]; Max 413 days
    “Aeris Fusion” timer range: Max: 12.9 days
  Active Timer (how long will the device stay in idle after communication?)
    Seconds or minutes
Numbers from https://aeriscom.zendesk.com/hc/en-us/articles/360049848254-Understanding-LTE-M-Power-Management-Modes
Notes: Really hard to tell difference between Aeris and Aeris Fusion. I think Aeris Fusion is a new product that allows devices (same SIM?) to dynamically switch between an IoT profile and a full-fledge voice / high-bw data profile. My guess then is that Aeris network is all their own owned infra, and Fusion is them acting as an MVNO [thus limited to others for wakeup range]

## Slide 19: Variety of features supported in real-world
Probably out-of-date details for NB-IoT networks
  PSM 0 seconds – 3 hours (or 4-50 seconds?)
  eDRX 20 seconds – 3 hours (or not supported at all?)
  Packet buffering none to 10 packets (or dynamic???)
https://docs.iotcreators.com/docs/nb-iot-network-information

## Slide 20: Improved range for LTE-M and NB-IoT
LTE defines a Maximum Coupling Loss (MCL) a.k.a Link Budget
  Traditional cellular: 144 dB (~2.5 km)
  LTE-M: 160 dB (~5 km)
  NB-IoT: 164 dB (~10 km)
  Sigfox: ~155 dB
  LoRaWAN: ~143 dB
Note that many cellular bands are often on higher frequencies
  Example: 1900 GHz
  Coarsely, lower frequency is longer range, but it’s complicated

## Slide 21: Cellular deployments
Originally unclear which would be dominant
  Verizon and AT&T focused on LTE-M
  T-Mobile focused on NB-IoT
  All rolled out services nationwide in the 2018-2019 timeframe
Networks expanded provide both capabilities
  LTE-M: AT&T, T-Mobile, Verizon, US Cellular
  NB-IoT: AT&T, T-Mobile, Verizon
Pricing models still very uncertain
  NB-IoT example: $5 per device per year up to 12 MB, 10 packets per hour
  Future adoption will greatly depend on these

## Slide 23: Microcontroller support
Devices need to be certified
  Hardware and software
  Tend to be modules or dual-core systems
Add a SIM card to connect to network

## Slide 24: Break + Open Question
Cellular hardware almost always requires certified radio modules where you can’t change the code at all. Why?

## Slide 25: Break + Open Question
Cellular hardware almost always requires certified radio modules where you can’t change the code at all. Why?
  Otherwise you could cheat at the protocols!!
  Or just generally not follow them fairly.
  Avoids “tragedy of the commons” by allowing specific trusted devices only

## Slide 26: What about 5G?
NB-IoT and LTE-M are the low-power, wide-area 5G solutions
  Intent is to coexist with 5G solutions for human-centric devices
Even if 4G sunset occurs, LTE-M and NB-IoT will still be around
https://www.ericsson.com/en/reports-and-papers/nb-iot-and-lte-m-in-the-context-of-5g-industry-white-paper

## Slide 27: Support for IoT - Non-IP Data Delivery (NIDD)
Reduce the amount of data necessary to transmit
  Registers device with a single “destination IP”
  Device just transmits data payload, network handles sending it to server
https://nickvsnetworking.com/nb-iot-nidd-basics/
TCP Data Transmission
UDP Data Transmission
NIDD Data Transmission

## Slide 28: Outline
Cellular IoT
IoT on Global Cellular
  Story by Pat Pannuto & nLine
LPWAN Design

## Slide 29: Sizing networks is hard
Sometimes you just lose performance…

## Slide 30: Traffic fluctuates in all networks, for cellular it becomes a function of both when and where you are
Understanding Mobile Traffic Patterns of Large Scale Cellular Towers in Urban Environment; Xu, Li, Wang, Zhang, Jin; IEEE ToN

## Slide 31: What is an MVNO “Mobile Virtual Network Operator”
Decoupling the builders of infrastructure from the sellers
Not a new concept, but seeing aggressive growth
  MetroPCS; Cricket; Boost Mobile; etc
  GoogleFi; Xfinity Cellular

## Slide 32: Why does this matter for IoT Deployments?
Say you’re building a power grid sensor you want to deploy globally…

## Slide 33: So how does Particle, a small IoT platform startup, provide global cellular coverage?
We deployed some Electrons in Accra, Ghana sending a message once per minute 24/7 for a few weeks
  PRR [POST Reception Rate] changes over time
  Almost zero PRR from ~7-9am and ~4-7pm daily
Introducing traffic priority
  Call Particle: “What gives?”
    Particle buys from T-Mobile
    T-Mobile buys from Deutsche-Telekom [didn’t own them yet]
    DT buys from Vodafone
    Vodafone buys from MTN
    MTN has 5 tiers of traffic priority on their network [guess which tier we were in?]

## Slide 34: So how do you get higher on the priority list?
You buy from MTN
… also not easy
  Limit of 3 SIMs / person due to fraud
    Particularly important due to prevalence of SIM-based mobile money

## Slide 35: So how do you deploy in Tanzania?
Not limited in SIMs, but limited in payment plans
Post-paid plans not an option
  Need to purchase ‘airtime recharges’
  Which you use by texting from that phone to an SMS shortcode
    So now you must have in-country staff!

## Slide 36: So how do you actually realize this claim?
Good. Question.

## Slide 37: Outline
Cellular IoT
IoT on Global Cellular
LPWAN Design

## Slide 38: LTE-M and NB-IoT design constrained by fitting within existing cellular ecosystem
What might a fresh design look like?
Caveat: In ISM bands!
  So it’s an unlicensed, shared communication band

## Slide 39: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?

## Slide 40: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?
  Modulation
  Tx Power
  Carrier Frequency Band
  Data Throughput
  Channel Bandwidth

## Slide 41: Design a wide-area network (ignore low-power for now)
What PHY choices would you make?
  Modulation
    Unclear. Can’t be too crazy for cheap devices but there’s a bit of leeway there.
  Tx Power
    High (much higher than 0 dBm)
  Carrier Frequency Band
    Low (something lower than 2.4 GHz, 915 MHz or lower?)
  Data Throughput
    Low (much lower than 1 Mbps. Reduce )
  Channel Bandwidth
    Unclear. Likely less bandwidth available on lower frequency carrier.
    Higher bandwidth gives longer range (by increasing reliability)
    Lower bandwidth gives more simultaneous devices (for a fixed allocation)

## Slide 42: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Device Roles
  When do devices listen?
  Access Control Mechanism

## Slide 43: Design a low-power wide-area network
Any particular MAC choices for lower power?
  Device Roles
    Diversity of devices in network
    High power gateway, low power devices in star topology
  When do devices listen?
    Devices should be off whenever possible
    Listen-after send for downlink
  Access Control Mechanism
    No TDMA access control if it can be avoided
      Removes requirement for synchronization
    CSMA is problematic due to hidden terminal problem
    What’s left: Aloha, FDMA, CDMA, ???

## Slide 44: Long-range CSMA is problematic
Long-range makes everything more challenging
  Kilometers of range mean kilometers between devices
Detection of channel use is less reliable
  Active research in clear channel assessment for LPWANs
Hidden terminal problem has a wider range
  Distance between two sensors >1x range <2x range
    For WiFi, this is ~100 m. For LPWANs this could be ~1 km
  Might make RTS/CTS more important
Result: CSMA doesn’t dominate LPWANs like it does WLANs

## Slide 45: LPWANs overview (common qualities)
Unlicensed 915 MHz band (902-928 MHz)
Higher power transmissions: ~20 dBm (100 mW)
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 46: Outline
Cellular IoT
IoT on Global Cellular
LPWAN Design