## Slide 1: Lecture 02 Network Fundamentals
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Some slides borrowed from: Peter Steenkiste (CMU), Christian Poellabauer (Notre Dame)
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Let me know if you don’t have access to something
Hw: Background out now
  Due Thursday
First lab this Friday: Wireshark
  Individual lab just playing around with Wireshark
  Location: Frances Searle 3220 at 11:00 AM
Temporary office hours
  1:00-3:50 PM on Wednesday (04/08)
  Tech L368 (my office)
  I hope to have a full schedule next week

## Slide 3: Today’s Goals
Introduce OSI layer model of communication
Provide background on Internet layering
Overview of concerns for the Physical layer
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols

## Slide 4: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 5: OSI model of communication layers
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
Open Systems Interconnection (OSI)

## Slide 6: Where does this class focus?
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
CS domain
CS340, CS440
EE domain EE307, EE378, EE380
This course!

## Slide 7: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
    i.e., bytes are added to the start/end of it
  Packet is wrapped with header for the link to make a frame
Upper-layer packet is the payload for the lower-layer packet

## Slide 8: Analogy: Sending a letter
Application: Purpose/type of letter
Transport: Carrier service
Named recipient
Network: Street Address
Courier
Mailing/shipping infrastructure
Link: Transfer to post office
Physical: Moving tangible object

## Slide 9: Example of layering for Ethernet and IP
Headers for each layer of communication wrap data
  Data is wrapped with header for network to make a packet
  Packet is wrapped with a header for the link to make a frame

## Slide 10: Transmitting data between networks
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
(2)
internet packet
(7)
data
PH
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header
LAN1 frame

## Slide 11: Model does not equal reality
Wireless protocols don’t always split between layers cleanly
  Usually explain parts of physical, data link, and possibly upper layers
Model still helps conceptualize stack-up though
  Layering of some type still occurs

## Slide 12: Layering for IoT (joke) (kind of)
MQTT
MQTT is a publish/subscribe message broker

## Slide 13: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 14: The global Internet
Most famous example of an internet (uppercase to distinguish)
Based on the TCP/IP protocol family
  IP (Internet Protocol)
    Provides a naming scheme and unreliable delivery of packets from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable data delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable data delivery from process-to-process
Accessed via a mix of Unix file I/O and the sockets interface

## Slide 15: Hardware and software organization of an Internet application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 16: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.5.212
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.5.212 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 17: 1. IP addresses
32-bit identifier for a computer on the Internet
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x816905D4 = 129.105.7.212
Each computer you want to access needs a unique IP address
  Blocks of IP addresses are owned by various network operators and distributed to computers on their networks
    For servers, these need to be long-term consistent
    For clients, they can be short-term leases

## Slide 18: Northwestern IPv4 ranges
Format: ip.addr/NUM
NUM is the number of meaningful bits, from the most-significant bit
  129.105.0.0/16 means the most-significant 16 bits are meaningful i.e., 129.105.x.x
  Remaining bits can be used for unique addresses
    2(32-NUM) machines

## Slide 19: 2. Internet domain names
.net
.edu
.gov
.com
northwestern
berkeley
mit
eecs
mccormick
moore
129.105.5.212
wot
unnamed root
www
165.124.149.20
hanlon
129.105.5.211
amazon
www
54.230.48.28
Top-level domain names
Second-level domain names
Third-level domain names
and onwards…
Note: Northwestern owns 129.105.0.0/16 and 165.124.0.0/16

## Slide 20: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries
  Each host entry defines the mapping between a set of domain names and IP addresses
A special name: localhost
  Refers back to the computer being used (IP address 127.0.0.1)

## Slide 21: 3. Internet connections
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
    IP address identifies the computer
    Port identifies the process on the computer
Clients and servers communicate by sending streams of bytes over connections. Most connections are:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  [TCP adds] Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.

## Slide 22: Ports are used to identify services to the kernel
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 23: How does the Internet handle routing packets?
Network layer (IP)
  Describes computer-to-computer connection
    Packets from my computer <---> Google server
Link layer (Ethernet)
  Describes individual links
    Packets from my computer <---> my router
Routing
  Using link-layer building blocks to get packets from one IP to another

## Slide 24: Addressing
How to solve the routing problem?
  I need to know how to get data from me to you
How does the post office work?
  I know where you live (your address)
    Zip Code
    City
    Street
    House Number
    Name

## Slide 25: A problem with addressing
Your computer moves all the time
  Home, school, Starbucks...

## Slide 26: Assigning and finding IP address ranges
In general, network operators don’t change that often
Solution:
  Tie IP addresses to network operators
  Assign computers IPs as they join networks
Key Point:
  Networks ”own” a block of IP address space
  ”The Internet” is a network of networks

## Slide 27: Routing
1.0.0.0/8
5.0.0.0/8
2.0.0.0/8
10.0.0.0/8
4.0.0.0/8

## Slide 28: Routing
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 29: Routing Adaptation
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 30: Identifying your computer?
Every network card has its own MAC address
  IPs are (somewhat) dynamic, ”owned” by local networks
  MACs are hardware and static, ”owned” by specific computers
    Manufacturers own blocks of MACs, ”spend” them each time they make a device
”Connecting” to a network
  Your computer leases an IP from the local network
  Only the local router knows your MAC, everyone else sees your IP
  Actually, with NAT, you probably have a private IP address
    This is how we make 32-bit addresses sufficient for the whole Internet

## Slide 31: Network Address Translation (NAT)
https://en.wikipedia.org/wiki/Network_address_translation

## Slide 32: So how does the Internet of Things fit into the Internet?
“IP is the Narrow Waist of the Internet”
  IP is Dead, Long Live IP for Wireless Sensor Networks
A recurring theme in this class:
  How does this actually attach to the Internet
    Physically, direct IP connection [hello Hue Hub, Wyze Hub, August Hub, …]
    Logically, through another device [are BLE devices really part of the IoT?]

## Slide 33: Break + Thinking
What are the steps for viewing a website?

## Slide 34: Break + Thinking
What are the steps for viewing a website?
You enter a domain name for the website
Computer looks up domain name to get IP Address
Computer sends request to IP_address:80
Computer gets back data, which it renders into a website

## Slide 35: ALL the layers
A ‘famous’ interview question
  “What happens when you type google.com into your browser’s address bar and press enter?”
  https://github.com/alex/what-happens-when
    12 pages worth of material
      Keyboard events
      Parsing URL
      DNS lookup
      Opening socket
      HTTP protocol
      HTML parsing
      GPU rendering

## Slide 36: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 37: Physical Layer
How bits are transmitted
  Wireless makes this entirely different from wired cases
Important considerations
  Signal strength
  Modulation
  Frequency

## Slide 38: Why use wireless?
There are no wires!
No need to install and maintain wires
  Reduces cost
  Simplifies deployment – place devices wherever makes sense
Supports mobile users
  Move around office, campus, city
  Move devices around home

## Slide 39: What is hard about wireless?
There are no wires!
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all

## Slide 40: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 41: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links just increases interference
  Need to expand to different frequencies

## Slide 42: Model of RF communication
Energy that radiates spherically from an antenna
Attenuation with distance
  Density of energy reduces over time, distance
  Signal strength is reduced, errors go up
Two key features
  Error rates depend on distance
  Spatial reuse of frequencies

## Slide 43: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 44: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 45: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 46: Signal strength is measured in decibels
Power is measured in Watts or dBw or dBm
dBm is most relevant to the IoT domain
  0 dBm equals 1 mW transmit power
  Example
    Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
    Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
Rule of thumb: +3 dB is double the power

## Slide 47: Signal strength varies significantly across technologies
Bluetooth Low Energy (local area)
  nRF52840 transmit power: 8 dBm (6.31 mW)
  nRF52840 receive sensitivity: -95 dBm (316.2 fW)
LoRa (wide area)
  SX127X LoRa transmit power: 20 dBm (100 mW)
  SX127X LoRa receive sensitivity: -148 dBm (1.6 attoWatt)

## Slide 48: Propagation degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out  Free Space Path Loss (FSPL)

## Slide 49: Some intuitions for signal propagation, power, gain, etc
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 50: Wait, where is the antenna??
This little strip of metal is the actual antenna
  Receiver only recovers the part of the signal that hits its antenna (“aperture”)

## Slide 51: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 52: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
.25 m

## Slide 53: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
1 m

## Slide 54: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m

## Slide 55: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 56: Free-Space Path Loss Model
https://semfionetworks.com/blog/free-space-path-loss-diagrams/

## Slide 57: Okay.. So what’s the limit?
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
8 dBm - -95 dBm = 103 dB link margin
With Free Space Path Loss model:
  103 dB corresponds to 1400 meter range!
  Can anyone get 1.4 km on their Bluetooth headphones?

## Slide 58: Propagation is one thing that degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out -> free space path loss
Important: distance is NOT the only signal strength loss
  Free space path loss calculation will not give you accurate range for a signal
Obstacles can weaken signal through absorption or reflection
  Precise quantitative details are in the EE domain
  We’ll use examples to develop qualitative instincts in this class

## Slide 59: ITU model for Indoor Attenuation
Models like this are more trustworthy less bad than Free-Space Path Loss
  https://en.wikipedia.org/wiki/ITU_model_for_indoor_attenuation

## Slide 60: Many factors affect the ability to actually receive data
Here’s some examples, from DW1000 [ultra wideband transceiver]

## Slide 61: Lower received energy increases error rates
More Errors
Less Errors
More Energy Received
Less Energy Received
BER: Bit Error Rate
Odds that a transmitted bit will be received incorrectly

## Slide 62: Big Idea: many RF factors are interconnected
Energy, Distance, Throughput, and Reliability are all interconnected in communication
Protocols make choices of some and get the results on the others
To get more distance, choose one or more:
  Increase energy
  Communicate slower
  Accept a higher error rate

## Slide 63: Break + Say hi to your neighbors
Things to share
  Name
  Major
  One of the following
    Favorite Candy
    Favorite Pokemon
    Favorite Emoji

## Slide 64: Break + Say hi to your neighbors
Things to share
  Name -Branden
  Major -EE, CE, and CS
  One of the following
    Favorite Candy - Twix
    Favorite Pokemon - Eevee
    Favorite Emoji - 🍢

## Slide 65: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 66: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 67: Sum of sinusoids can be reversed
RF signals are fundamentally sinusoids of electromagnetic energy
Sinusoids at different frequencies can be combined and pulled apart again later
  Particularly, it’s relatively easy for hardware to determine if there’s energy present on a given frequency
  Although very close frequencies might be difficult to disentangle

## Slide 68: Complex waveforms have a center frequency and a width
A pure sinusoid is energy at exactly one frequency
A messy sinusoid with data layered on top of it has nearby energy
  There’s a center of the signal energy
  Plus some amount of width, which depends on how complicated the data layered on top is

## Slide 69: How do radio stations work?
FM radio in cars is a good example of frequencies
  All of FM radio has an allocation of 87.5 to 108.0 MHz
  Each station takes has up to ~200 kHz of bandwidth
First station is 87.7 MHz +/- 100 kHz
  Ranges from 87.6 to 87.8
Second station is 87.9 MHz +/- 100 kHz
  Ranges from 87.8 to 88.0
What if they overlapped? They interfere with each other
  You’d possibly hear both. Or get junk data that’s neither.

## Slide 70: RF communication frequencies
IoT focus

## Slide 71: Wireless spectrum is allocated to specific uses

## Slide 72: 433 MHz Band
Amateur radio (ham radio) was provided with specific frequencies to use
  There are quite a few: https://en.wikipedia.org/wiki/Amateur_radio_frequency_allocations
433 MHz is within one of these bands in the US but globally is set aside as its own thing
  Designated for low-power devices
  Unlicensed use
  Vehicle key-less entry devices, garage door openers, weather stations
    Some IoT protocols use it as well! LoRa for example

## Slide 73: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi

## Slide 74: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?

## Slide 75: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why? No interference from other users

## Slide 76: Wireless spectrum is limited...and valuable
FCC auctions blocks in US
August 2020
  70 MHz in 3.5 GHz spectrum
  $4.6 billion
February 2021
  300 MHz in 3.7-9 GHz spectrum
  $81 billion
https://www.fiercewireless.com/wireless/t-mobile-pays-304m-fill-holes-its-25-ghz-spectrum

## Slide 77: Different technologies use spectrum in different ways
How spectrum is used affects: cost ($), robustness, throughput…
  We will talk about how each technology uses spectrum, and implications
This graphic shows how BLE and WiFi interoperate; more on this next week

## Slide 78: Frequency Hopping Spread Spectrum
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 79: Sidebar: inventor of FHSS – Hedy Lamarr
Actress, inventor, and all-around badass
  Designed FHSS with George Antheil during WWII based on music ideas
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventing_career

## Slide 80: Frequency and Data Rate
Which can send data faster (more bits/second)?
  Signal at 2 GHz frequency with 1 MHz of bandwidth
  Signal at 20 GHz frequency with 1 MHz of bandwidth

## Slide 81: Frequency and Data Rate
Which can send data faster (more bits/second)?
  Signal at 2 GHz frequency with 1 MHz of bandwidth
  Signal at 20 GHz frequency with 1 MHz of bandwidth
  They are identical!
Data rate is a function of bandwidth and power (not frequency)
  Shannon-Hartley Theorem:
    C – channel capacity in bits per second
    B – bandwidth
    S/N – signal to noise ratio (measure of signal power)

## Slide 82: Frequency and Range
Oof. This gets a little tricky
Does frequency affect range: yes and no
  Identical energy would mean identical range regardless of frequency
  BUT
  Lower frequencies use larger antennas
  Larger antennas collect more energy
  More energy allows for farther range
Also, RF waves may or may not be affected by obstacles
  Depends on wavelength (frequency) with obstacles much smaller than the wavelength having a minimal effect
    Low frequencies can diffract around obstacles
  Also depends on the materials of the obstacle

## Slide 83: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation

## Slide 84: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 85: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 86: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 87: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Usually differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 88: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 89: Break + Video
Excellent explanation of modulation techniques: https://youtu.be/0faCad2kKeg?si=kK6l0g63XGVPdut9&t=240
  Listen for 3.5 minutes until 7:30 in the video
  “How Cell Service Actually Works” by Wendover Productions

## Slide 90: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation