## Slide 1: Lecture 03 Data Link Layer
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Hw: Background
  Goal: brush up on some embedded systems and networks background
  Due tonight. Don’t waste a slip day on this
  Submit on Gradescope
Lab: Wireshark
  Goal: familiarize yourself with Wireshark
    Install it, do some basic scanning, explore a little
  See you all in lab tomorrow!
    Friday 11:00-12:30 pm in Frances Searle 3320

## Slide 3: Partnership survey
Labs (after this first one) will be in groups of three
I posted a form for recording groups on Ed Discussion
  You can also submit without a full group, and I’ll help match!
Tomorrow in labs, you can all do a little networking to find people you might want to work with

## Slide 4: Today’s Goals
Finish Physical Layer topics
Overview of concerns for the Data link layer
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols
Describe Medium Access Control mechanisms
If we have time: BLE Intro and Background

## Slide 5: Review: OSI model of communication layers
Transport
  Sending data between applications
  TCP and UDP
Network
  Sending data between networked computers
  IP
Data Link
  Sending collections of bits
  Ethernet, WiFi
Physical
  Sending individual bits
  Ethernet, WiFi
Open Systems Interconnection (OSI)

## Slide 6: Review: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.7.30
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.7.30 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 7: Review: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 8: Review: Signal strength
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 9: Big Idea: many RF factors are interconnected
Energy, Distance, Throughput, and Reliability are all interconnected in communication
Protocols make choices of some and get the results on the others
To get more distance, choose one or more:
  Increase energy
  Communicate slower
  Accept a higher error rate

## Slide 10: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 11: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 12: Sum of sinusoids can be reversed
RF signals are fundamentally sinusoids of electromagnetic energy
Sinusoids at different frequencies can be combined and pulled apart again later
  Particularly, it’s relatively easy for hardware to determine if there’s energy present on a given frequency
  Although very close frequencies might be difficult to disentangle

## Slide 13: Complex waveforms have a center frequency and a width
A pure sinusoid is energy at exactly one frequency
  But no data
A messy sinusoid with data layered on top of it has nearby energy
  There’s a center of the signal energy
  Plus some amount of width, which depends on how complicated the data layered on top is and what the data rate is
  Adding data on top of a signal inherently sums sinusoids, using bandwidth

## Slide 14: Wireless spectrum is allocated to specific uses

## Slide 15: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi

## Slide 16: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?

## Slide 17: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why? No interference from other users

## Slide 18: Wireless spectrum is limited...and valuable
FCC auctions blocks in US
August 2020
  70 MHz in 3.5 GHz spectrum
  $4.6 billion
February 2021
  300 MHz in 3.7-9 GHz spectrum
  $81 billion
https://www.fiercewireless.com/wireless/t-mobile-pays-304m-fill-holes-its-25-ghz-spectrum

## Slide 19: Frequency Hopping Spread Spectrum
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 20: Sidebar: inventor of FHSS – Hedy Lamarr
Actress, inventor, and all-around badass
  Designed FHSS with George Antheil during WWII based on music ideas
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventing_career
More modern comparison: imagine Scarlett Johansson invented a new wireless technology

## Slide 21: Frequency and Data Rate
Which can send data faster (more bits/second)?
  Signal at 2 GHz frequency with 1 MHz of bandwidth
  Signal at 20 GHz frequency with 1 MHz of bandwidth

## Slide 22: Frequency and Data Rate
Which can send data faster (more bits/second)?
  Signal at 2 GHz frequency with 1 MHz of bandwidth
  Signal at 20 GHz frequency with 1 MHz of bandwidth
  They are identical!
Data rate is a function of bandwidth and power (not frequency)
  Shannon-Hartley Theorem:
    C – channel capacity in bits per second
    B – bandwidth
    S/N – signal to noise ratio (measure of signal power)

## Slide 23: Frequency and Range
Oof. This gets a little tricky
Does frequency affect range: yes and no
  Identical energy would mean identical range regardless of frequency
  BUT
  Lower frequencies use larger antennas
  Larger antennas collect more energy
  More energy allows for farther range
Also, RF waves may or may not be affected by obstacles
  Depends on wavelength (frequency) with obstacles much smaller than the wavelength having a minimal effect
    Low frequencies can diffract around obstacles
  Also depends on the materials of the obstacle

## Slide 24: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 25: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 26: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 27: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 28: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Often differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 29: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but this modulation is still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 30: Break + Video
Excellent explanation of modulation techniques: https://youtu.be/0faCad2kKeg?si=kK6l0g63XGVPdut9&t=240
  Listen for 3.5 minutes until 7:30 in the video
  “How Cell Service Actually Works” by Wendover Productions

## Slide 31: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 32: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 33: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Possible wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 34: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 35: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 36: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Task: Break into groups of 5 students each
  In two minutes I’m going to ask each group a question
  Everyone in the group needs to answer as quickly as possible
  Rules:
    If two people talk at the same time the group loses
    Every group must use a unique method
      I’ll have each group explain what their method was after they use it
      So be creative and have multiple options ready to go

## Slide 37: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)
Everyone speak in different languages -> code division multiple access (sort of, but not really)
Others?

## Slide 38: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 39: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 40: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 41: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad
My transmission
My transmission
Other transmission
Other transmission

## Slide 42: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
My transmission
Other transmission
Other transmission
My transmission
time

## Slide 43: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 44: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 45: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
ALOHA
CSMA
FDMA
TDMA
CDMA

## Slide 46: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 47: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Very challenging for wireless systems
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm
  Area of active research!

## Slide 48: Hidden terminal problem
Device A
Device B
Device C

## Slide 49: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low
    Not always worth it

## Slide 50: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
CDMA
ALOHA
CSMA

## Slide 51: Contention-free access control protocols
Goal: split up communication such that devices will never conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 52: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
  Usually in conjunction with another scheme (but not always)
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 53: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 54: CDMA – Code Division Multiple Access
Split transmissions in ‘codes’
  Not new; original applications in radar and early satellite communications
Analogy: Multiple speakers in the same room all in different languages
  [The human brain is crazy good at ignoring what it doesn’t understand ]
Requires signal power coordination
  [everyone needs to speak ~the same volume]
  Can be hard in uncontrolled / dynamic environments
Also can be more performant with highly synchronized clocks
  i.e. if the code clock is known to both devices

## Slide 55: Break + Question
What is an advantage of Aloha over TDMA?

## Slide 56: Break + Question
What is an advantage of Aloha over TDMA?
  Simplicity! It’s really easy to implement Aloha
  No required centralization
    TDMA time schedule needs to be decided by something
    That thing is “in charge”
    Aloha can be entirely distributed

## Slide 57: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 58: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background

## Slide 59: Bluetooth Low Energy Resources
Good walkthrough of BLE:
  https://www.silabs.com/documents/public/user-guides/ug103-14-fundamentals-ble.pdf
[5.2 specification] [4.2 specification] (link to PDF download)
  Also: [Supplement v9]
I used a mix of 5.2 and 4.2 for this
  Will talk about BLE 5 and BLE 6 differences as part of next lecture

## Slide 60: Basics of Bluetooth Low Energy (BLE)
Direct device-to-device communication
  Usually: Computer to Thing
  Smartphone to device, Laptop to device, etc.
Focus on making the “Thing” really low energy
  Push energy-intensive requirements onto “Computer”
Devices (Computer or Thing) are servers with accessible fields
  Not the traditional send-explicit-packets interface you might be expecting
  Lower layers are still exchanging packets to make it work

## Slide 61: A note on outdated notation
Master/Slave paradigm
  Master is the “Computer” and is in charge of interaction
  Slave is the “Device” and has little control over interaction parameters
  Really common notation in EE side of the world.
    Not intended to be harmful, but also literally inconsiderate.
Field is changing for the better. It’s going to take some time.
  Central/Peripheral
  Device/Peripheral
  Controller/Peripheral
  Master/Minion
  Primary/Secondary

## Slide 62: BLE development
Protocol development
  Research product
  Specification
  Hardware support
  Usefulness and iteration
Bluetooth Low Energy
  Research in early 2000s: Bluetooth Low End Extension and Wibree
  Specification in 2009: Bluetooth version 4.0
  Hardware support in 2011/12: iPhone 4s, nRF51 series microcontrollers
  4.1 and 4.2 (2014), 5.0 (2016, first in phones 2017, really 2019 though)

## Slide 63: Bluetooth has a long history — the IoT is near-exclusively BLE (Bluetooth 4.0+) as opposed to Bluetooth Classic (<4.0)

## Slide 64: Bluetooth Specification
Problem: a bit overwhelming…
  5.2 spec: 3256 pages
  We only care about Vol 6: Low Energy Controller
    Part A: Physical Layer Specification
    Part B: Link Layer Specification
    CSS: Part A: Data Types Specification
    So ~250 pages
Tip: be willing to just ignore things when skimming specs
  5.2 spec covers BLE and Bluetooth Classic and a bunch of upper layer stuff that we never have to care about

## Slide 65: BLE mechanisms
Advertising
  Discovery
  Advertisements – broadcast messages indicating device details
  Ephemeral, uni-directional communication from Advertiser to Scanner(s)
  ALOHA access control
Connections
  Interaction
  Bi-directional communication between Peripheral and Central
  Maintained for some duration
  TDMA access control

## Slide 66: BLE network topology
Advertiser
Peripheral
Advertiser
Advertiser
Peripheral
Central & Scanner
Scanner
Connection
Connection
Advertisement
Advertisement
Advertisement
Advertisement

## Slide 67: Multiple roles at the same time
Topology picture is a simplification of roles
A single device can have multiple roles simultaneously
  Scanning and Advertising simultaneously
  Peripheral and Scanner and Advertiser simultaneously
  Peripheral and Scanner and Central and Advertiser simultaneously
    Getting a bit out of hand though
One Peripheral can even be connected to multiple Centrals
  Not in the original design though: you’ll find old docs saying you can’t
  And it’s not a normal use-case for BLE

## Slide 68: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
  Laptop
  Smartphone

## Slide 69: Break + Check your understanding
Which roles is each device likely to have?
  Keyboard
    Advertiser and Peripheral
  Laptop
    Scanner and Central
  Smartphone
    Advertiser, Peripheral, Scanner, and Central

## Slide 70: BLE Layers
Host – Configuration and Server
  GAP – Generic Access Profile
    Configure advertising
  GATT – Generic ATTribute profile
    Configure connections
HCI - Host Controller Interface (sigh)
Controller - Communication
  Link Layer – send packets
  RF and PHY – send bits
GAP
Host
Controller

## Slide 71: Outline
Physical Layer
  Overview
  Signal Strength
  Signal Frequency and Bandwidth
  Signal Modulation
Data Link Layer
BLE Background