## Slide 1: Lecture 05 BLE Connections
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Lab: Wireshark
  Submit to Gradescope by the end of today
Lab: BLE
  On Friday!
  Group work. I emailed everyone about groups
  I’ll pass out hardware boards for people to borrow
    Bring a USB-C to USB-A adapter if you need one
Quiz1 next week Tuesday
  Covers material in lectures 1-5 (includes today)
  15 minutes, on paper
  No notes or calculator all you need is a pencil (and class knowledge)

## Slide 3: Today’s Goals
Explore how connections work
  What does the link layer look like?
  How do higher layers interact to share data?
Investigate network questions about connections
Overview of additions in BLE 5.0

## Slide 4: Useful documentation
[5.2 specification] [4.2 specification] (link to PDF download)
https://www.novelbits.io/deep-dive-ble-packets-events/
Thinking about BLE connection data transfer rates
  https://punchthrough.com/maximizing-ble-throughput-on-ios-and-android/
  https://punchthrough.com/maximizing-ble-throughput-part-2-use-larger-att-mtu-2/
  https://punchthrough.com/maximizing-ble-throughput-part-3-data-length-extension-dle-2/

## Slide 5: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 6: Recall: BLE advertisements lead to connections
Central
Advertisement:
“I’m the Living Room Light”
Peripheral
Connection Request
Connected (stops advertising)
“Set light brightness to 50%”
(note: this is highly simplified)
We’ll explore what happens here!
Notes: Advertiser
Scanner
Central
Peripheral
https://community.nxp.com/t5/Wireless-Connectivity/A-view-on-Bluetooth-Low-Energy-stack-roles/m-p/380310

## Slide 7: Overview of connections
Connections are for bi-directional communication with higher throughput than advertisements
  Half-duplex: only one direction at a time
Simple view
  A peripheral is either advertising or in a connection
  A central is scanning and in one or more connections
  Not quite accurate: devices can have several roles simultaneously
While in a connection both devices act like servers
  Either device can read/write fields available on the other device

## Slide 8: Once a connection is established, BLE has more PHY options
LE 1M (default)
  1 Msym/s
  BLE encodes 1 bit / symbol, so this is also 1 Mbit/s
LE 2M (added in BLE 5.0)
  2 Msym/s
LE Coded (added in BLE 5.0)
  1 Msym/s + Forward Error Correction
    S = 2
      ~2x range, ½ effective data rate – 500 Kbit/s goodput
    S = 8
      ~4x range, 125 Kbits/s goodput
FSK Example
0
0
1
1
1
Each of these are symbols

## Slide 9: Connection Timeline
Peripheral advertises
Central sends a connection request packet on advertising channel just after receiving advertisement
Peripheral stops advertising
Central and peripheral switch to a data channel
Central
Peripheral
Notes: - Animate
- Change text to annotations

## Slide 10: BLE uses 2.4 GHz ISM Band with Data and Advertisement Channels
Recall: Each BLE channel is 2 MHz wide, 40 channels (0-39)
  3 channels for advertising (37, 38, 39)
  37 channels for connections (0 - 36)
Notes: Source: https://i0.wp.com/embeddedcentric.com/wp-content/uploads/2019/03/bluetooth_ble_spectrum.png?ssl=1

## Slide 11: Choosing a data channel for communication
Why do you switch from advertising channel to data channel?
  For better reliability and to improve quality of service
How to pick a channel out of the 37 data channels?
  Randomize for reduced chance of collision
What if two connections pick same channel?
  Higher chance of collision occurring
  Some way to not be tied to the same data channel is needed

## Slide 12: Frequency Hopping Spread Spectrum (FHSS)
Recall: Each BLE channel is 2 MHz wide, 40 channels,
  3 are used for advertising, remaining 37 are for connections
  Frequency hopping: fn+1 = (fn + hop) mod 37
Which exact channels are used and in what order might vary
  “Adaptive Frequency Hopping” avoids bad channels

## Slide 13: How do the Central and Peripheral agree on things?
For a packet to be received:
  Central and peripheral should be listening and sending on same data channel
For the hopping to be successful, both must:
  Follow same hop sequence
    Which channels to use and the order to follow
  Hop at a given time schedule
  Agree on when to schedule their first communication
Some synchronization is needed!

## Slide 14: Connection request packet
Scanner waits until it sees an advertisement from a device it wants to connect to
  Requesting a connection (in higher layers) just starts this search process
Sends connection request payload in response to advertisement

## Slide 15: Connection request parameters examined
Specifies parameters of the connection
  Peripheral must either agree or totally reject the connection
  Peripheral can later propose a change to the connection parameters
Interval is how frequently connection events occur (7.5ms – 4000ms)
  BLE 6.2 updates this: 0.375ms – 4000 ms
Notes: Figure from video would be good

## Slide 16: Steady-state connection timing
Some data can be exchanged at each interval
  Might just be acknowledgements
  Additional packets can be sent if there is a lot to transmit
  Each interval is on the next channel in the hopping sequence
Peripheral can skip a number of intervals to save energy
  Defined by the Latency connection request parameter
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Central to Peripheral
Peripheral to Central
Connection Interval
Hop to next data channel
Hop to next data channel
Optional packets

## Slide 17: How do you schedule the very first connection event?
WinSize and WinOffset specify start of the first connection event
  First connection event: first exchange after CONNECT_REQ packet)
  Starts the TDMA communication schedule
    Allows Central to avoid prior, existing connections in time
    Repeats based on the interval after the first event
WinOffset: Time from now until first event
  Analogy: “Let’s meet 2 hours from now”
WinSize: Flexible window of time to expect first transmission
  Analogy: “I might be up to 15 minutes late”
Notes: Figure from video would be good

## Slide 18: How do you agree on hopping pattern?
Channel Map (ChM) and Hop define the FHSS pattern
Channel Map (ChM): Map of which channels to use
Hop: next hop increment
  Next hop channel cn+1 = (cn + hop) mod 37
Notes: Figure from video would be good

## Slide 19: Connection packet layering
Optional authentication
LLID – link layer ID
Empty data / Fragment
Data
Control
MD – more data (continues connection event)
[Next Expected] Sequence Number – acknowledgements

## Slide 20: Acknowledgement protocol
See §4.2.3 of Reliability Doc for more

## Slide 21: Now that a connection exists, packets can be exchanged over it
Next step: actually communicate between devices
  Either sending data, or sending “control” messages
“Control” and “Data” separation: very common networking theme
LLID – link layer ID
  Empty data / Fragment
  Data
  Control
MIC: Message Integrity Code for encryption validation

## Slide 22: Link Layer header length
Question: What is the maximum possible payload size?
Notes: Expectation: They look at “length” and say 2^8 = 255 (or maybe 256; why is that wrong?)

## Slide 23: Link Layer header length
Question: What is the maximum possible payload size?
251 Bytes
= 257 - header - MIC
Notes: Expectation: They look at “length” and say 2^8 = 255 (or maybe 256; why is that wrong?)

## Slide 24: Control payloads
Examples:
Request update to connection parameters like interval (by peripheral)
Begin encrypting communication
Terminate a connection
Note: Control payloads can all be handled by the link layer – not passed up to applications!

## Slide 25: Data payloads
Length (16 bits) | Channel ID (16 bits) | L2CAP SDU Length* (16 bits) | Information Payload (0 to 249 octets)
SDU – Service Data Unit
Logical packet that may be split into several physical packets
Channel ID
Destination for data
Usually Attributes (GATT part of lecture)

## Slide 26: Summarizing what’s sent in a BLE connection
Control packets
  Version
    Bluetooth version, Company ID of Software Stack
  Features
    Various connection features supported by the device
    Encryption, Ping, Channel selection algorithms, Various 5.0 features
  Etc.
    Extended packet length, Various 5.0 features (change PHY)
    Various “procedures” for setting up changes in the connection
Data packets
  Attribute discovery
  Attribute reading

## Slide 27: Very briefly: security in connections
Excellent TI resource here for more details: https://dev.ti.com/tirex/explore/node?node=AOPOY.GDApakIOYjiwoY6A__pTTHBmu__LATEST
Either side can request secure connection [central -> Pairing; peripheral -> Security Req]
“Bonding” saves pairing info between connections

## Slide 28: Very briefly: security in addresses
All devices have a unique, hardware “Identity Address”, but may not share it
  Public Address - Use the Identity Address. (The BDA never changes.)
  Random Static Address - Generate a random address per power cycle. The address cannot be regenerated at any other time. Can be used as an Identity Address.
  Resolvable Private Address (RPA) - Generate a random address with a given time interval. Generated using Identity Resolving Key (IRK) which can also be used by trusted peers (bonded devices) to resolve the Random Address to the Identity Address.
  Non-resolvable Private Address - Generate a random address with a given time interval. Generated randomly. Cannot be resolved to an Identity Address.

## Slide 29: Ending connections
Termination control packet exists
Also a Timeout parameter from connection parameters
  Human-based devices may just wander away from each other
  Or be shut off, or reprogrammed, etc.

## Slide 30: Break + Check your understanding
What makes connections more reliable than advertisements?
How does a Peripheral send data to a Central in a connection?
Why is a “termination” control packet useful?

## Slide 31: Break + Check your understanding
What makes connections more reliable than advertisements?
  Each packet sent is acknowledged or resent
  TDMA schedule and FHSS means less likely to collide
How does a Peripheral send data to a Central in a connection?
  Wait until next connection interval
  Respond to packet from Central with a data payload
Why is a “termination” control packet useful?
  Timeout could delay for a while
  Enables re-connection if desired

## Slide 32: Summary: Connection timeline
Initiating a connection
  Peripheral is sending broadcast advertisements
  Central is scanning and receives an advertisement
  Central sends connection request
During a connection
  Central sends a packet each “connection interval”
  Peripheral immediately responds with a packet
  Multiple packets may be exchanged this way until done
  Repeat at next connection interval
Ending a connection
  Either device sends termination packet
  Timeout occurs on either device

## Slide 33: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 34: Let’s analyze this type of network
Things we care about:
  Robustness
  Performance
  Scalability
Consideration: what are the figures of merit?
  What variables do we want to maximize/minimize?

## Slide 35: Questions about how a connection “network” works
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
  Figure of merit: Number of devices
How much throughput can a device have?
  Figure of merit: Data rate (bits/second)

## Slide 36: Questions about how a connection “network” works
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
  Figure of merit: Number of devices
How much throughput can a device have?
  Figure of merit: Data rate (bits/second)

## Slide 37: How is the TDMA schedule created/managed?
Only the central needs to know the schedule
  It controls interactions with the peripheral(s) it is connected to
Anchor point and connection interval determines the schedule for a specific device
Central to Peripheral
Central to Peripheral
Peripheral to Central

## Slide 38: How is synchronization managed?
Central sends first packet at each connection interval
  So peripheral must be synchronized to central
  Resynchronization can occur on each received packet
Specification describes how a peripheral must widen its listening window based on “Source Clock Accuracy”

## Slide 39: Clock drift is an energy burden due to large guard bands and energy cost of precise timekeeping
Wall time
Device time
CC2520 Radio + AM18xx RTC:
300s * 2ppm * 2 = 1.2 ms guard
1.2 ms * 60 mW = 36 μJ (RF loss)
300s * 150nW = 45 μJ (RTC loss)
≈ 100 μJ loss / packet @ 300 s
300 s
Guard
1200 μs
@ 2ppm
Static Power:
100 nW+
(CC2520 is a 15.4 radio, but same idea applies) Max connection interval in BLE is 4 seconds

## Slide 40: Questions about how a connection “network” works
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
  Figure of merit: Number of devices
How much throughput can a device have?
  Figure of merit: Data rate (bits/second)

## Slide 41: How many devices can be connected?
We can schedule with granularity of at least 1.25 ms (offset steps)
  That’s at least 800 devices per second
Intervals go up to 4 seconds, so multiply by four
  That’s 3200 devices per max interval
Plus central can skip intervals on occasion without dropping the connection
  And really the offset defines a window. More granularity is available
Answer: thousands of devices
  Although each is sending minimum-sized packets each interval

## Slide 42: How many devices can be connected in the real world?
The limit is much much lower on real devices
  Example: Android sets a limit at around 4-15
  nRF52 s140 softdevice allows up to 20
  Nintendo Switch & Switch 2: 8 controllers (which counts controller halves)
Connection management is often done in firmware
  Softdevice for nRF, firmware on the radio chip in smartphones
Limited by memory and complexity

## Slide 43: Questions about how a connection “network” works
How does TDMA MAC for connections work?
  Implies a schedule
  Implies synchronization
How many devices can be in a network?
  Figure of merit: Number of devices
How much throughput can a device have?
  Figure of merit: Data rate (bits/second)

## Slide 44: How much throughput can a device have?
1 Mbps? That’s the PHY data rate

## Slide 45: How much throughput can a device have?
1 Mbps? That’s the PHY data rate
  Not even close. Packet overhead plus timing delays
Step 1: decrease connection interval as much as possible
  More connection events per second mean more data
  Range: 7.5 ms to 4.0 s
  Somewhat device-specific configuration
    Android allows 7.5 ms
    iOS allows 15 ms

## Slide 46: How much throughput can a device have?
Step 2, increase packet size
Using maximum-sized payloads has less overhead
Notes: https://punchthrough.com/maximizing-ble-throughput-part-3-data-length-extension-dle-2/
Connection event length = time duration where tx happens (different from connection interval)

## Slide 47: How much throughput goodput can a device have?
488 bytes of useful data per connection event
  Maximum sized packets, discounting headers and timing delays
Connection event every 7.5 ms
Result: 520 kbps (65 kilobytes per second)
  iOS result 260 kbps
  Original BLE 4.1 result on Android: 128 kbps
  A little lower in practice due to lost packets
  Modern results will be better, due to size increases and IFS reductions
This is roughly half of the PHY rate!

## Slide 48: Break + Question
This powerpoint presentation is roughly 4 MB
At 520 kbps (65 kB per second) of goodput, how long would it take to send over a BLE connection?

## Slide 49: Break + Question
This powerpoint presentation is roughly 4 MB
At 520 kbps (65 kB per second) of goodput, how long would it take to send over a BLE connection?
  4 MB / 65 kB per second = 62.5 seconds…

## Slide 50: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 51: How is data actually exchanged between central and peripheral?
Attribute Protocol (ATT) and Generic Attribute Profile (GATT) used for this!
ATT is the underlying framework for GATT
  Two roles: Client and Server
Data that the server exposes is structured as attributes
ATT Client
ATT Server
Attribute Protocol
Central
Peripheral

## Slide 52: Attribute server keywords
Characteristic
  A field with a value and size/type
  Descriptor: metadata about the characteristic (readable, writeable, notifications when it updates)
Service
  Collection of characteristics
Profile
  Collection of services

## Slide 53: Overview of Generic Attribute Profile (GATT)
Attribute Type is specified as a UUID

## Slide 54: UUIDs and handles
Universally Unique Identifiers
  128-bit, mostly random with a few bits for versioning
  Example: 00000000-0000-1000-8000-00805F9B34FB
    This is the default BLE UUID for known services
    You can generate your own UUID for custom services
Handles
  Too long to pass around all the time, so pick 16 bits that mean that UUID
    Must be unique among services/characteristics on that device
  Taken from UUID: 0000xxxx-0000-1000-8000-00805F9B34FB
  Handle often sequentially incremented for each new characteristic within a service
Resource: Useful stackoverflow post on identifying handles in the wild

## Slide 55: Example: Time Profile

## Slide 56: Current time characteristic
The Bluetooth SIG are pedantic people
But details matter for interoperability!

## Slide 57: Interacting with characteristics
Depends on their permissions
  Readable, Writable, Notify-able, etc.
Notify
  Automatically get a message sent whenever the characteristic value updates
  Note: have to enable this on both sides, it’s not the default behavior
Long characteristics are automatically fragmented across multiple packets and/or connection events
  Lower layers are in charge of this without the application having to consider it

## Slide 58: Discovery
When a connection first occurs, each device can query the other for a list of services
  And can further query for a list of characteristics in that service
  Gets a list of handles/UUIDs
Standardized UUIDs can be interpreted immediately
  Custom services/characteristics need documentation from the manufacturer

## Slide 59: Documentation of GATT standards
https://www.bluetooth.com/specifications/gatt/
  Various profiles and services that have been standardized
GATT Specification Supplement
  Various characteristic definitions that have been standardized
Both incredibly specific and woefully inexhaustive

## Slide 60: Break + Example Services
https://btprodspecificationrefs.blob.core.windows.net/assigned-values/16-bit%20UUID%20Numbers%20Document.pdf

## Slide 61: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5

## Slide 62: Changes in BLE 5 and BLE 6
Major changes
  Multiple physical layers
    BLE 5: Faster and slower options
  Advertising extensions
    BLE 5: Much longer advertisements
  Connection updates
    BLE 6: negotiate inter-frame spacing, better timing sensitive data, shorter connection intervals
  Localization extensions
    BLE 5 and 6 add stuff here
    We’ll discuss in a later lecture on localization
Minor changes
  Various quality of life improvements
  Examples:
    Advertise on channels in any order
    Better data channel hopping algorithm
Most recent update: BLE 6.2 in November 2025

## Slide 63: Revised physical layers
2 Mbps PHY
  Transmit data faster
  Transmit more data in the same time
Coded PHY
  Forward Error Correction in the data stream
    1 bit -> 2 symbols or 8 symbols
  Makes bits more reliable -> longer distance
  500 kbps and 125 kbps modes
Connections can switch to these PHYs after creation
Advertisements can use these, but only in a special “extended” mode

## Slide 64: Coded PHY mixes physical and link layers
Different PHY settings at different times
  Make beginning headers extra-reliable
  Data might be slightly less reliable as a trade for faster speed
Packet sent with coded PHY

## Slide 65: Revised processing path

## Slide 66: Extended advertising
Allow bigger payloads and/or different PHYs
  Uses Data Channels not Advertising Channels. Why?
  Regular advertisements point to extended advertisements

## Slide 67: Extended advertising
Allow bigger payloads and/or different PHYs
  Uses Data Channels not Advertising Channels. Why? Packet collisions!
  Regular advertisements point to extended advertisements

## Slide 68: Procedure for scanning extended advertisements
Scan on 3 primary channels for advertising packets.
If ADV_EXT_IND is scanned, record the secondary channel information (which channel and when etc.)
Scan the specific secondary channel at the given time.

## Slide 69: Extended advertisement train on data channels
Use case: long advertisements that need to be fragmented
Up to 1650 bytes total

## Slide 70: Bi-directional “Periodic Advertisement with Responses”
BLE 5.4 addition allowing bidirectional communication during advertisements
Advertiser can provide multiple listening windows after advertisement
Other device picks one of the windows and sends a response message
  Which window and what data is application-specific

## Slide 71: BLE “Auracast” (Audio Sharing)

## Slide 72: Periodic advertising on data channels
Use case: publicly-available localized audio sources
TV in a bar
Commentary in a museum
Broadcast analogy of a connection
Probably only able to follow one of these at a time

## Slide 73: Outline
Connection PHY and Link Layer
Connection Investigations
GATT
BLE 5