## Slide 1: Lecture 11 WiFi MAC
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Hw: Matter due today
One more week on Lab: Thread
Lab: WiFi starts on Friday
  I’ll bring new hardware to class for you all

## Slide 3: Today’s Goals
Introduce MAC layer concepts in 802.11
Understand what exists, what is actually used, and why
Explore two additional areas in 802.11
  Microcontroller use of WiFi
  Future of WiFi

## Slide 4: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 5: Basic WiFi network
Star topology network
Basic Service Set (BSS)
  Access point(s)
  Multiple connected clients
Service Set ID (SSID)
  Identifies network
  Broadcast by access point in beacons

## Slide 6: WiFi superframe structure
Beacon followed by contention-free period followed by contention
  Repeats periodically (default ~100 ms)
  802.15.4 adopted a similar superframe
This is more hypothetical than real

## Slide 7: Contention-free access
Known as Point Coordination Function (PCF)
  Allocates a contention-free period for specific devices
  Access Point decides when to grant based on requests
Drawbacks
  Latency depends on beacon intervals
  Mechanism for explicit Quality of Service is unclear
PCF is not used in practice
  802.11e adds a revised Quality of Service mechanism
  Especially with the adoption of MU-MIMO and OFDMA techniques, it’s just not necessary

## Slide 8: WiFi superframe in practice
Continuous contention access period
  Any device may send at any time
  PCF is unused in practice
Periodic beacons
  Which also use CSMA and therefore may be delayed
Time
Delayed Beacon
Beacon
Contention
Based Access

## Slide 9: 802.11 beacons
Transmitted periodically (~100 ms by default)
  Enable discovery of network
    Contain capabilities and SSID for the network (802.11b/g/n/ac/ax…)
  Assign contention-free slots if used
  Notify devices of waiting packets
    Traffic Indication Map (TIM) has a bitmap specifying which devices data is for
    Enables devices to sleep, skipping a number of beacons
  Handles broadcast/multicast messages
    Every N beacons includes a notation of available broadcast messages
    Messages are transmitted during next contention access period using normal CSMA
    Defines maximum sleep period for devices (must listen to these beacons)

## Slide 10: Contention-based access
Known as Distributed Coordination Function (DCF)
  Base communication method for WiFi (essentially always)
  All packets are immediately ACK’d by receiving device
  Uses CSMA/CA to determine when it can send
    With random backoff
  Problem: packets can be very long (up to 20 milliseconds)
  Solution: Network Allocation Vector (NAV)
    Packets include a notation of their duration
    Sensing the beginning of a packet allows backoff to skip the whole packet duration before continuing

## Slide 11: Reminder: hidden terminal problem
Two devices communicating with Access Point may not be able to hear each other
  CSMA fails and Access Point losses both messages
A solution: RTS/CTS (Request/Clear To Send)

## Slide 12: Drawbacks of RTS/CTS
Four packets per data (RTS, CTS, Data, Ack)
  Could have just sent data instead of RTS
Significant portion of traffic are application-layer Acks
  Probably better to just have it fail and try again later
RTS/CTS only used for very large packets in practice
  *It’s mentioned still in 802.11n and 802.11ac, so not entirely unused

## Slide 13: Backoff in WiFi
Listen for activity
  If free
    Wait for Inter Frame Spacing (IFS)
    If still free, transmit
  If busy
    Randomly select a number of backoff Slots
    Count down slots whenever medium is not busy
    If busy when backoff completes:
      Increase maximum backoff Slots
      Repeat
Slot time: basic time unit for protocol
  Total time of: switch from Rx to Tx, plus processing time, plus propagation delay

## Slide 14: Prioritizing packets with varying IFS
Tiered Contention Multiple Access (TCMA)
  Idea: assign different inter-frame spacing based on traffic class
  Inherently prioritizes communication
Acknowledgements sent with Short IFS (SIFS)
  Will always transmit before new data clears CSMA check
New data sent with longer DCF IFS (DIFS)

## Slide 15: Putting backoff together
Two variables
  Contention Window (CW) – maximum backoff amount
  Backoff Count (BO) – current remaining backoff
When attempting to send, if busy Backoff selected in [0, CW]
  Countdown Backoff slots whenever medium is not busy
  At 0, attempt to transmit if not busy
  If busy, double Window and select Backoff again
802.11g values:
  Slot time= 20 us, CWmin= 15 slots (300 us), CWmax= 1023 slots (20 ms)
  SIFS= 10 us, DIFS= 50 us

## Slide 16: 802.11 backoff example
A and B want to send, but they see that the medium is busy
  Followed by an Acknowledgement after SIFS
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B

## Slide 17: 802.11 backoff example
Each chooses a random backoff [0, CW] (we’ll say CW is 32)
  Start counting down backoff slots
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8

## Slide 18: 802.11 backoff example
C wants to send, waits DIFS, and can send immediately
  No other traffic is going on
  A and B pause backoff for packet duration
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic

## Slide 19: 802.11 backoff example
A and B used NAV to pause backoff for entire traffic plus ACK
  After DIFS, resume backoff count from its previous value
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
SIFS
ACK
DIFS

## Slide 20: 802.11 backoff example
B reaches zero backoff, finds channel empty, transmits
  A pauses its backoff again for duration plus ACK
Arrival A
A
B
C
Other Traffic
ACK
SIFS
DIFS
Arrival B
Backoff = 10
Backoff = 8
Arrival C
DIFS
C Traffic
Backoff = 6
Backoff = 4
B Traffic
SIFS
ACK
DIFS

## Slide 21: Break + Hacking
If you wanted maximum data throughput on a WiFi radio, and you were willing to be non-standards-compliant, what would you do?

## Slide 22: Break + Hacking
If you wanted maximum data throughput on a WiFi radio, and you were willing to be non-standards-compliant, what would you do?
  Never backoff at all. Just try during the next open period
    Always be “device C” in our previous example
  Use a shorter SIFS than other devices
    If you start transmitting sooner, you get to keep transmitting!
    Other devices will backoff on your transmission
  Tragedy of the Commons: this utterly fails if many radios follow it

## Slide 23: WiFi 6 Adds OFDMA Access Control
OFDMA: allocate subcarriers to a device for an amount of time
  Turns OFDM into an access control mechanism (frequency + time)
  Complicated question: which device gets which subcarriers at which time?
Only useful if multiple devices can do OFDMA

## Slide 24: CSMA + OFDMA
For WiFi 6 to be backwards compatible, the OFDMA stuff has to obey the normal CSMA/CA rules as well
Downlink from AP
  The AP wins contention and then transmits various data at various frequencies
Uplink to AP
  The AP wins contention, sends a “OFDMA uplink trigger frame”, then devices send their responses
https://ieeexplore.ieee.org/document/8422767

## Slide 25: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 26: 802.11 frame
Frame control (various bits)
  Type of packet (Control, Management, Data)
  Subtype (Association, RTS, CTS, Ack, etc.)
  Indication of to/from “distribution system” (Internet rather than intranet)
Duration
  Specifies on-air time of full packet in microseconds
  Note: no actual length field 😱
Surprising, but smart!
Recall MCS vary — but everyone needs to be able to parse header (for duration, for NAV)
Length can be very large (e.g. in ac: 5.5 ms max duration is 4.5 MB length!); sent at full data rate

## Slide 27: 802.11 frame
Sequence control
  4-bit fragment number
  12-bit sequence number
Quality of Service control
  Identifies traffic category
High Throughput Control
  Configurations for selecting best data rate
Frame body
  Max size depends on PHY
    ~2000 for lower rates
    ~8000 for 802.11n
    ~11000 for 802.11ac
Frame check sequence
  32-bit CRC

## Slide 28: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
1
Devices filter on Address 1

## Slide 29: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
2
2
Devices filter on Address 1

## Slide 30: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
3
3
Devices filter on Address 1

## Slide 31: Address field use cases
 | To DS | From DS | Address 1 | Address 2 | Address3 | Address4 | Use Case
1 | 0 | 0 | Destination Addr | Source Addr | BSS ID | - | Direct communication
2 | 0 | 1 | Destination Addr | BSS ID | Source Addr | - | Traffic from Internet
3 | 1 | 0 | BSS ID | Source Addr | Destination Addr | - | Traffic to Internet
4 | 1 | 1 | Receiver Addr | Transmitter Addr | Destination Addr | Source Addr | Repeater
AP
Source
Destination
Repeater
4
4
Devices filter on Address 1

## Slide 32: Sending frames in WiFi
Frame bursting (handles one really big packet)
  Transmit multiple frames in a row
Frame fragmentation
  Split service data over multiple frames
Frame aggregation (handles many very small packets)
  Multiple service data in a single frame
  Allows multiple packets to reach Access Point in a single transmission

## Slide 33: Calculating packet durations
Example duration for a 1500 byte 802.11g packet
  6 Mbps for header
  24 Mbps for payload
  566 μs for total packet
    Plus 10 μs for SIFS
    Plus 34 μs for ACK
https://sarwiki.informatik.hu-berlin.de/Packet_transmission_time_in_802.11

## Slide 34: Implementation Drives Specification Sometimes
SIFS nominally defined by processing time
  Aside: Big challenge for SDRs
Convolutional decoders need(ed) 16 µs to finish processing
  For highest-rate MCS (ERP-OFDM)
  SIFS is 10 μs, so extension needed
Processing must finish before next packet starts
  To be able to decode NAV in header
Notes: https://www.electronics-notes.com/articles/connectivity/wifi-ieee-802-11/802-11g.php

## Slide 35: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 36: 802.11e improves MAC layer
Hybrid Coordination Function (HCF)
  Modifies contention-free access (still no one uses it)
  Modifies contention-based access: Enhanced Distributed Channel Access (EDCA)
Adapts Quality of Service based on application
  Example of breaking layering for an optimization
  Categories (lowest to highest priority):
    Background
    Best Effort
    Video
    Voice

## Slide 37: Different priority for different application category
Expand to more IFS lengths for different traffic categories
  Smallest AIFS (equal to DIFS) goes to Voice, Largest to Background
  Contention Window min and max also change for each category
    Selects a probability that most important category goes first

## Slide 38: Multiple queues within a single device

## Slide 39: Brief 802.11ax (WiFi 6) aside
WiFi 6 and beyond use EDCA for their OFDMA scheduling. Steps:
  Access point decides to start an OFDMA communication window
    Mechanism called “Buffer Status Report Poll” asks how much data each device has queued to send
  Access Point wins contention in the normal CSMA method
  Access Point sends a TXOP (Transmit Opportunity) message with schedule
    Some back-and-forth handshakes here
  Devices respond back with uplink messages
    Uses a fast IFS to maintain contention

## Slide 40: 802.11e also adds maximum durations
802.11e also defines duration a device can transmit for
  Based on PHY in use and Application category
  Background/Best Effort: one frame per contention win
  Example, up to 11 ms for Voice on 802.11ac
    Could be one really big frame at a low data rate
    Could be multiple frames in a row separated by SIFS

## Slide 41: Break + xkcd
https://xkcd.com/2199/

## Slide 42: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 43: How do WiFi devices decide to change networks?
WiFi “handoffs” are always initiated by the Client
  It decides to change to a different network
802.11k
  Access Points track information about neighbors
  Clients can request a list of nearby Access Points
802.11v
  Access Points can send messages to Clients with recommendations of which network to connect to
    Which devices may choose to ignore

## Slide 44: Apple roaming decision details
Devices look at RSSI of packets from the Access Point
  -70 to -75 dBm triggers roaming
  Looks for Access Points that are 8-12 dBm stronger
Given multiple choices, prefers in this order
  Better version (WiFi 6 > WiFi 5)
  Larger bandwidth (80 MHz > 40 MHz)
Result ends up preferring faster communication
  When likely more reliable due to better signal strength
https://support.apple.com/guide/deployment/wi-fi-roaming-support-dep98f116c0f/web
Android has a more complicated “scoring” mechanism

## Slide 45: Handling roaming
For a basic WiFi connection, several packets must be sent
  Probe response from all Access Points with details
  Authentication does basic connection to network
  Association shares encryption options and 802.11 capabilities

## Slide 46: Security has complicated this process
Additional packets need to be sent to verify the device’s identity and exchange keys
  EAPOL packets (Extensible Authentication Protocol over LAN)
802.1x (not 11) is a standard for an authentication server
  Enterprise networks often use this

## Slide 47: 802.11r shares information for faster connections
FT: Fast Transition

## Slide 48: Modern WiFi mesh systems
Internet
Modem
AP
Device
Device
Device
Device
Device
AP
AP
All APs present as the same network
  With fast handoff between them
APs use a mesh to transmit data back to modem
  Various connection implementations

## Slide 49: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 50: Why / why not, talk WiFi in a wireless for IoT class
Pros
  Ubiquitous
  High-performance
Cons
  Complex configuration
  And security requirements
    Device-Northwestern anyone?
  Expensive in energy and money

## Slide 51: ESP8266
Espressif is a chip company in China
  Makes chip designs, including radios and microprocessors
2014: ESP8266 microcontroller + WiFi radio
  ESP-01 module uses it, about $5 to purchase
  Became very popular for hardware/software projects
Essentially microcontrollers had become capable enough to run a WiFi radio, and Espressif was the first to capitalize on it in a cheap product

## Slide 52: WiFi capability in microcontrollers
ESP32 (since 2016)
  Microcontroller plus WiFi radio in single chip
  Same idea as nRF52840 but with a WiFi focus
Basic Capabilities
  802.11b/g/n 2.4 GHz only
  20 MHz or 40 MHz channels
  Single antenna only
  MCS0-7
    7 Mbps – 150 Mbps
  Tx power up to 20.5 dBm
Newest models are even better
  ESP32-C6 does 802.11ax, MIMO, MCS0-9
    Still only 20 or 40 MHz though

## Slide 53: Low power WiFi
Question: should a microcontroller stay connected or reconnect?
  Light sleep: stay connected always, only listening to beacons
  Deep sleep: reconnect to network each time data is ready
Answer for ESP32 depends on security and data interval
  Resecuring during connection takes lots of energy
    Crossover point is about 60 seconds
  Insecure transmissions have a crossover of 5-15 seconds
https://blog.voneicken.com/2018/lp-wifi-esp-comparison/#conclusions

## Slide 54: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT

## Slide 55: MQTT – an answer to the “where do you send data” question

## Slide 56: MQTT Roles
MQTT: Message Queueing Telemetry Transport
Broker
  Server that distributes information
Client
  Any device connected to the Broker

## Slide 57: Pub/Sub Architecture
Topic
  String that names the data being sent
Publish
  Sends data with an associated Topic to Broker
Subscribe
  Inform Broker of which Topics you want data from
  ALL subscribed Clients get copies of the data

## Slide 58: MQTT Access Control
Nothing is required by default
  Which is its own concern
Can require a password to communicate with Broker
Can make access control lists on a per-topic basis
  Each user with a given password can only access certain topics

## Slide 59: Value of MQTT
And that’s pretty much everything there is to MQTT
  MQTT is very simple, and that’s a benefit
  Packets are sent over TCP, so the reliability is already handled sufficiently
    Variants can function over UDP instead
How is data formatted?
  However you want. It’s just bytes attached to a Topic string
  Could be an array of data bytes, JSON blob, image data, whatever
    Up to MB of data in a single payload
  Application-level probably knows how to decode

## Slide 60: Outline
802.11 Access Control
802.11 Frame format
802.11e Improvements to MAC
Roaming
Microcontrollers and WiFi
MQTT