## Slide 1: Lecture 12 Evolution of Cellular
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Lab: Thread due Thursday
Lab: WiFi due next week Thursday
Lab office hours on Friday
  Come finish WiFi lab and be free next week
Quiz today at 1:30
  Tell your friends

## Slide 3: Today’s Goals
Introduction to the Wide-area communication space
Understand fundamentals of cellular technology
Learn how “older” cellular technology works
  And why it is relevant to the IoT today
Good video overview of cellular: https://www.youtube.com/watch?v=0faCad2kKeg
  (we watched a few minutes of this on modulation earlier in class)

## Slide 4: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond

## Slide 5: Wide area networks
Communication at the region/city scale rather than the building/residence scale
  Throughout cities
  Agricultural deployments
  Industrial facilities
City-scale sensing is one very popular domain
  What might we want to sense throughout a city?

## Slide 6: Air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2018.
[1]
[1]
[2]
[2]

## Slide 7: Audio detection, classification, and localization
[1] Girod et al. The Design and Implementation of a Self-Calibrating Distributed Acoustic Sensing Platform. 2006. [2] Lédeczi et al. Multiple Simultaneous Acoustic Source Localization in Urban Terrain. 2005. [3] Sounds of New York City. 2016.
[1]
[1]
[2]
[3]

## Slide 8: Traffic queue sensing and congestion control
[1] Sen et al. Kyun Queue: A Sensor Network System To Monitor Road Traffic Queues, 2012
[1]
[1]
[1]

## Slide 9: Array of Things project - Chicago

## Slide 11: Considering wide-area networks
Data
Throughput
Range
WiFi

## Slide 12: Considering wide-area networks
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range

## Slide 13: Considering wide-area networks
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 14: Considering wide-area networks
Bluetooth
WiFi
2G
3G
4G
BLE
Zigbee
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 15: Takeaway: Cellular provides the IoT the only reliable global coverage available today
If the goal is deploy-today + work-anywhere, cell is the only option
  (Or increasingly satellite, we’ll cover that later in class)
That’s not to say cell actually works everywhere!
  Just the best-available

## Slide 16: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond

## Slide 17: Poll: What decade was the first commercial mobile phone?
1910-1920
1920-1930
1930-1940
1940-1950
1950-1960
1960-1970
1970-1980
1980-1990
1990-2000
2000-2010

## Slide 18: The first commercial mobile phone was in 1946!
By 1948, 5000 users placing around 30,000 calls weekly
https://www.smithsonianmag.com/innovation/first-mobile-phone-call-was-made-75-years-ago-180978003/
  “The equipment, of course employing vacuum tubes, weighed eighty pounds, filled much of a vehicle’s trunk and drew so much power that it would cause the headlights to dim. Service cost $15 per month, plus thirty to forty cents per local call, equivalent to $175 2012 dollars, plus $3.50 to $4.65 per call. “
https://ethw.org/The_Foundations_of_Mobile_and_Cellular_Telephony

## Slide 19: The first `mobile` network architecture
Single transmitter tower, multiple receiver towers
  Why?
Notes: A single transmitter on a central tower provided a handful of channels for an entire metropolitan area. Between one and eight receiver towers handled the call return signals. At most, three subscribers could make calls at one time in any city using the single transmitter and the tiny amount of spectrum allocated by the Federal Communications Commission to this service. It was in effect a massive party line, where a tightly controlled number of subscribers had to listen first for someone else on the line, and, if finding the line free, signal an operator, who would place the call. During the call, the user depressed a button on the handset to talk and released it to listen.

## Slide 20: The first `mobile` network architecture
Single transmitter tower, multiple receiver towers
  Why? Transmission energy of phone!
Medium Access Control?
  Push-to-talk [half-duplex]
  City-wide “party line”
  Maximum of three concurrent callers
Notes: A single transmitter on a central tower provided a handful of channels for an entire metropolitan area. Between one and eight receiver towers handled the call return signals. At most, three subscribers could make calls at one time in any city using the single transmitter and the tiny amount of spectrum allocated by the Federal Communications Commission to this service. It was in effect a massive party line, where a tightly controlled number of subscribers had to listen first for someone else on the line, and, if finding the line free, signal an operator, who would place the call. During the call, the user depressed a button on the handset to talk and released it to listen.

## Slide 21: 1965: The Improved Mobile Telephone Service
“More spectrum”
  Bell: VHF Low (35-44 MHz, 9 channels), VHF High (152-158 MHz, 11 channels), UHF (454-460 MHz, 12 channels)
  7 channels at VHF, and 12 channels at UHF for "RCCs" (Radio Common Carriers)
    These will end up becoming pagers, mostly
“Full Duplex”
  Implemented as channel pairs (two half-duplex)
Increased spectrum is still not enough
  Limited to 40,000 total subscribers
  E.g. NYC had 2,000 people on 12 channels with a typical wait of 30 minutes to place a call
Phones fit in a briefcase now
Notes: Also now full duplex, and no more operators

## Slide 22: Quick review: How can we share spectrum?
Frequency division
  Already doing that
Time division
  Already doing that
Code division
  Won’t come to mobile networks until the 80’s
Spatial division!!

## Slide 23: What’s wrong inefficient with this picture?
Early mobile networks handled the mobility challenge with wide-area coverage
The active user could be anywhere in the 40~60 mile range of the transmit tower
  So they had exclusive access to that whole area!
12 frequency channels  12 users

## Slide 24: The “cell” in cellular networks
Cells use spatial division
  Reduce transmit power, smaller area
Now…
  12 / 3 = 4 channels per cell
  * 6 cells in area
  = 24 users of same spectrum!
And we can choose the cell size based on our expected needs

## Slide 25: Spatial division tradeoffs
Need more infrastructure (more towers)
Need logic to support handoff
  Cellular concept in Bell labs at 1947 [one year after first mobile], but no handoff solution yet
?

## Slide 26: How often does handoff need to happen anyway?
Really a question of “how big are cells”
A back-of-envelope answer for “Handoffs per 3-minute call”:
 | Speed (mph) | Speed (kph) | Cell Radius (km) | Handoffs
Freeway, rural | 65 | 104 | 16 | 0.33
Freeway, urban | 65 | 104 | 1.6 | 3.25
Surface streets, urban | 30 | 48 | 1 | 2.4
Pedestrian, urban | 1.5 | 2.4 | 1 | 0.12
Pedestrian, microcell | 1.5 | 2.4 | 0.1 | 1.2
Table data from Arthur H. M. Ross, PhD: http://www.cdg.org/technology/cdma_technology/a_ross/handoff.asp

## Slide 27: Sidebar: bullet trains and airplanes
Commercially operating high-speed rail (~200-400 km/h)
  Fastest: 431 km/h (268 mph) – Shanghai Maglev
Commercial airlines (~800-1200 km/h)
  Standard: 988 km/h (614 mph) – Boeing 747
  Fastest: 2180 km/h (1354 mph) – Concorde (no longer operational)
5G specs seem to support up to 500 km/h
  Per prior chart: ~1.5 handoffs per 3 minute call
  Less impactful for non-real-time internet browsing

## Slide 28: Introducing 1G! (First Generation)
AMPS — Advanced Mobile Phone Service (circa 1983)
  Other 1G’s:
    Nordic Mobile Telephone (NMT) — Nordics, Eastern Europe, Russia
    Total Access Communications System (TACS) — UK, West Germany, Portugal South Africa
    Radiocom 2000 — France
1G is defined by:
  Analog voice channels
  Established by digital control channel  handoffs

## Slide 29: Break + Discussion: How to implement handoff?
<brainstorm>

## Slide 30: How does AMPS implement handoff?
Base station detects weak signal
Base station tells mobile about new, better tower
Base station sends cutover trigger
Lots bad about this:
  No `make before break` — many drops!
  Mobile has better estimates than base station

## Slide 31: Spatial division in practice
Directional antennas at tessellation corners provide redundant coverage [robustness!]

## Slide 32: Spatial division in practice
Directional isolation is imperfect, requires many bands in practice
  ~5-7 cells are within conflict range, so we need to divide channels by ~7

## Slide 33: Over time, AMPS did also get more frequencies
AMPS in the US:
  850 MHz band
  Divided into “A” block and “B” block
    Granted to local phone company and “wireless company” respectively
  Each block had 21 control, 395 voice channels
    Divide by 7 to get voice channels per cell: ~56
    So ~56 users per cell, rather than 12 for the entire city
Several expansions of this frequency block
  Most interesting: in 1989 UHF TV channels 70-83 added 666 more channels

## Slide 34: The first “sunset”
Single-user analog channels is not very efficient
Wireless carriers want to replace 1G
  Key Takeaway: Spectrum allocation is the most scarce resource, therefore want to maximize efficiency of its use [efficiency: number of paying customers / spectrum?]
But many things in the built environment rely on AMPS
  Because when they were built, AMPS was the most reliable
    OnStar
    ADT home alarms [got sued!]
  Some systems made adapters, others just stopped working
FCC required network support until early 2008 (dropped soon after)
Notes: Options: SOL mostly. People sold adapter kits to replace transmit modules where possible [see 2G OnStar example for this happening now later in slides]. ADT got sued class-action for selling products that were ‘destined to fail’ (suit failed).

## Slide 35: Aside: Super cool hackaday projects
Building your own 1G network!
  https://hackaday.com/tag/amps/
  https://github.com/unsynchronized/gr-amps
  ⚠ ⚠ ⚠ This uses spectrum you do not own ⚠ ⚠ ⚠
    “The FCC can levy fines of up to $11,000, per transmitter, per day, with up to six months in federal prison, for violations of the Code of Federal Regulations.”
    Could deploy with wired connections though…

## Slide 36: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond

## Slide 37: IS-54 aka 2G aka TDMA aka D-AMPS (Digital AMPS)
Deployed ~1993
Used TDMA to share AMPS channels
  Each AMPS analog channel-pair was 30 kHz
  Digital compression allowed for 3 time slots per channel — tripled capacity!
    Later iterations would compress further, 6 time slots per channel
    Without additional bandwidth: 6*56 = 336 simultaneous devices per cell
Beat out competing FDMA analog solution from Motorola
  Narrowband AMPS, “N-AMPS”, compressed calls to fit in 10 kHz channels
Also encrypted [poorly: CMEA broken publicly in 1997]

## Slide 38: GSM aka 2G
Wait, didn’t the last slide say 2G was something else?
What is “2G” then?
  Exactly.
  “2G” isn’t one technology, it’s a collection of “second generation” protocols
  This is true for later generations too
And if you think this is confusing, it only gets worse
  Anecdote: Pat as a Qualcomm intern in 2010 asked everyone I met there “what actually is 4G,” and every engineer just laughed at me

## Slide 39: Cellular generations
Multiple competing technologies
Edges of these get quite a bit “fuzzy”

## Slide 40: CDMA in 2G
One family of 2G protocols used CDMA access control
Deployed mostly in North America, Japan, and South Korea
Eventually lost out to GSM family, which evolved into today’s LTE and 5G systems

## Slide 41: CDMA Principle
High level concept
  Expand binary data into larger bit patterns, like DSSS does
  Each phone gets a unique bit pattern
  Use those bit patterns to distinguish data
    Which works even when packets collide
Hard parts
  Bit patterns must be “orthogonal” and unique to each phone sharing a cell
    Orthogonal: dot product is zero. Means they don’t affect each other
  Packets must either be sent synchronously (downlink from station)
    Or asynchronously (uplink to station) but with a probability of loss

## Slide 42: CDMA math example for two transmitters
Transmitting: data bit 1: +code, data bit 0: -code
Receiving: dot product of signal and code: >0 = 1, <0 = 0
Device A: Code (1, -1)
  Data bits: {1, 0} -> {+code, -code} -> {(1, -1), (-1, 1)}
Device B: Code (1, 1),
  Data bits: {0, 0} -> {(-1, -1), (-1, -1)}
Signal: {(1, -1), (-1, 1)} + {(-1, -1), (-1, -1)} = {(0, -2), (-2, 0)}
Decoding
  Data for Device A: (1, -1) ⋅ {(0, -2), (-2, 0)} = {2, -2} -> {1, 0}
  Data for Device B: (1, 1) ⋅ {(0, -2), (-2, 0)} = {-2, -2} -> {0, 0}

## Slide 43: GSM
D-AMPS was sunset when AMPS was sunset in 2008
So “modern” 2G is entirely built upon GSM
“Global System for Mobile Communications”
  It is a standard [the dominant 2G]
  GSM meant “phone” for a while in parts of Europe
    (and apparently still in Belgium?)
  GSMA is the GSM Association; which a lot of people just call GSM
    Because GSM made [a] 3G and LTE [which is a 4g?] and 5g [ish! more next time]
  Yay.

## Slide 44: Origins of GSM
An incredible sweet spot of timing, technology need, and politics?
1987: 13 European countries sign accord to use one wireless standard
  10 months later: GSM standard ratified
  Insight: Not a ton new in GSM by ‘87, just a lot of arbitrary design decisions
    Combined with broad agreement
Not a very `mobile` mobile network…
Notes: Lot of patting-on-back for co-operation history, but it seems somewhat genuine; plus 4 dudes who just plowed through their standard
— Insight: GSM

## Slide 45: The real innovation of GSM was the indirection and interoperability it enabled
Europe hit this problem before the US because the US is large
  (and US telecoms owned/operated subsidiaries in Canada)
Coincided with major growth in global mobility
  Mobile devices needed to be able to use other carriers infrastructure
Early GSM isn’t anything fancy in modulation, data, etc
  It’s all about the control channels

## Slide 46: GSM evolved over time to add data
GSM was voice-only at first
Then overlaid data on the voice channel
  Circuit Switched Data (CSD)
    9.6 — 14.4 kb/s
    Previous hacks were literally cell phone calling a modem (~3.5 kb/s); same concept
Then added actual packetized data [“2.5G”]
  General Packet Radio Service (GPRS)
    Throughput 9.2 – 21.55 kbit/s/timeslot [goodput 8-20 kbit/s/timeslot]
  Enhanced Data Rates for GSM Evolution (EDGE)

## Slide 47
https://en.wikipedia.org/wiki/File:Gsm_structures.svg

## Slide 48: Circuit switching

## Slide 49: Comparing circuits vs packets
Circuit switching
  Virtual electrical connections between two devices
  Full capacity is dedicated to only those two devices
Packet switching
  Chunks of data get routed between devices
  Overhead to figure out where they go

## Slide 50: So why does the IoT care about 2G?
It’s easy to implement
  2G == GMSK
    3G = QPSK [requires better hardware]
    4G and up is more complex
It’s cheap
  Relative to other cellular plans, anyways. This may be changing finally
It’s low power*
  *For select IoT workloads
  Energy-per-bit of continuous stream improves each generation
  Energy-per-event of infrequent event is more tricky though

## Slide 51: Corollary to improved throughput is improved energy performance
Same philosophy as high-performance architecture, etc
  There is always baseline load, which going faster amortizes
Notes: Pic as citation pretty lazy Pat… :D

## Slide 52: But energy per transaction is complex
Radios, cellular protocols, and cellular providers have state machines
  Hard to predict a priori and globally 
Characterizing radio resource allocation for 3G networks; Feng Qian, Zhaoguang Wang, Alexandre Gerber, Zhuoqing Morley Mao, Subhabrata Sen, Oliver Spatscheck; SIGCOMM’10

## Slide 53: Why might 2G continue to survive [globally]?
More coverage for lower costs
  2G has longer range than 3G
It fills the legacy niche
  High performance HW includes fallbacks
    2G/3G radios, then 2G/3G/4G radios, now 2G/3G/4G/5G radios
    Consider the iPhone 16 Pro (2024):
  Brick phones still popular!

## Slide 54: 2G in the US… [Plans]
AT&T stopped servicing 2G networks in 2016
Verizon Wireless also phased out its 2G CDMA network at the end of 2020
Sprint had plans to shut down 2G in April 2022
  Purchased by T-Mobile anyways
T-Mobile plans on
  2023 April 2024 February 2025 Still running…
  2026: they’ve apparently been slowly phasing out regions

## Slide 55: Does GM ever learn? [Could they have?]
What would you put in cars if you were the PM of OnStar today?
  Moved to 4G…

## Slide 56: Break + xkcd
https://xkcd.com/925/

## Slide 57: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond

## Slide 58: Starting with the end: the 3G sunset
Announced retirements:
  Verizon: Dec 2022
  AT&T: Feb 2022
  T-Mobile: Finally got there in July 2022 (after months of delays)
2G reminder
  Verizon and AT&T actually did sunset 2G
  T-Mobile plans on ???
AT&T: 2.7% of customers will be affected by 3G shutdown

## Slide 59: Why does 2G have staying power that 3G doesn’t?
T-Mobile’s letter to Congress on 2g/3g sunset
  n.b. Senator Schatz seems to get this stuff
Notes: Pat’s personal guess: There are critical infrastructure bits that are/will-be effectively 2G only that will take a long time to replace. One band of 2G will live on for years. These are less frequent M2M, so one band is plenty and hit the pragmatic long-tail of legacy devices; also fixes 3g sunset. Reading between the lines, T-Mobile [which is really Deutsche-Telekom, which is really a global conglomerate, which can’t sunset 2g globally for a long time and so will have internal infra anyway] will provide 2g services for everything left; can do MVNO-like takeover of devices that need to run on sunset networks [assuming they can roam to the one band that’s left]

## Slide 60: So what did [*]G provide over 2G anyway?
Biggest thing is throughput
  Not really relevant for IoT stuff
And a spectrum land-grab
  Wireless providers advocated for global availability of channels
    With some success
Terahertz Band: The Last Piece of RF Spectrum Puzzle for Communication Systems (preprint; Elayan et al.)

## Slide 61: Aside: Eventually, the naming thing got annoying, so an international standards body fixed* it *Yeah, you know how this story will end
The International Telecommunications Union (ITU) is a UN branch
  ITU-R set standards for what can be considered “a 4G technology”
”Generations” are now defined by speed
  E.g. to qualify as “a 4G technology”: 100 Mb/s+ (mobile), 1 Gb/s+ (stationary)
  Fun game: How fast is LTE?
    LTE spec maxes out at 300 MB/s down and 75 MB/s up
    It seems LTE has been retroactively classified as 3.95G
      [By everyone except the wireless carriers?]

## Slide 62: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond

## Slide 63: Outline
Wide-Area Network Background
Cellular Network Technologies
  1G
  2G
  3G/4G and beyond
Bonus: IoT on Global Cellular
  Story by Pat Pannuto & nLine

## Slide 64: Sizing networks is hard
Sometimes you just lose performance…

## Slide 65: Traffic fluctuates in all networks, for cellular it becomes a function of both when and where you are
Understanding Mobile Traffic Patterns of Large Scale Cellular Towers in Urban Environment; Xu, Li, Wang, Zhang, Jin; IEEE ToN

## Slide 66: Why does this matter for IoT Deployments?
Say you’re building a power grid sensor you want to deploy globally…

## Slide 67: What is a MVNO “Mobile Virtual Network Operator”
Decoupling the builders of infrastructure from the sellers
Not a new concept, but seeing aggressive growth
  MetroPCS; Cricket; Boost Mobile; etc
  GoogleFi; Xfinity Cellular

## Slide 68: So how does Particle, a small IoT platform startup, provide global cellular coverage?
We deployed some Electrons in Accra, Ghana sending a message once per minute 24/7 for a few weeks
  PRR [POST Reception Rate] changes over time
  Almost zero PRR from ~7-9am and ~4-7pm daily
Introducing traffic priority
  Call Particle: “What gives?”
    Particle buys from T-Mobile
    T-Mobile buys from Deutsche-Telekom [didn’t own them yet]
    DT buys from Vodafone
    Vodafone buys from MTN
    MTN has 5 tiers of traffic priority on their network [guess which tier we were in?]

## Slide 69: So how do you get higher on the priority list?
You buy from MTN
… also not easy
  Limit of 3 SIMs / person due to fraud
    Particularly important due to prevalence of SIM-based mobile money

## Slide 70: So how do you deploy in Tanzania?
Not limited in SIMs, but limited in payment plans
Post-paid plans not an option
  Need to purchase ‘airtime recharges’
  Which you use by texting from that phone to an SMS shortcode
    So now you must have in-country staff!

## Slide 71: So how do you actually realize this claim?
Good. Question.