## Slide 1: Lecture 18 Backscatter & RFID
CS433 – Wireless Protocols for IoT
Branden Ghena – Spring 2026
Some slides borrowed from Ambuj Varshney (NUS)
Materials in collaboration with Pat Pannuto (UCSD) and Brad Campbell (UVA)

## Slide 2: Administrivia
Lab: LoRa
  Get checkoffs at office hours this week
  Evan’s office hours will still be held this Friday if late checkoffs are needed
Final Design Project
  Formal design review of an application
    Consider energy, costs, etc.
  Writeup due Tuesday of exam week
    No late days on this one. Submit it on time.
  Working on Cellular homework grading
    Common lost points: no inline citations

## Slide 3: Quiz today
FYI

## Slide 4: Today’s Goals
Describe backscatter communications
Understand one use of backscatter: RFID
Explore how backscatter techniques can be used for applications
    Sensor networks
    Localization

## Slide 5: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 6: What does an antenna do?
Animation by Chetvorno - Own work, CC0, https://commons.wikimedia.org/w/index.php?curid=40789783
Loosely: Converts between radio waves and electric signals

## Slide 7: What generates electric waves?
RF front end
  can be done with high-speed digital components (e.g. fast DACs)

## Slide 8: What receives electric waves?
Again, lots of stuff nowadays…
  Could be a high-speed ADC, more often with analog pieces in front:
Graphics from Analog Devices whitepaper: https://www.analog.com/media/en/technical-documentation/tech-articles/480501640radio101.pdf — significantly more detail here

## Slide 9: Making ultra-low power radios
How do we make a radio that’s lower power?
What is the most costly part of the radio?
  Carrier-frequency generation is expensive
  Modulating bits is comparatively lower energy
Solution: do not generate carrier
  Instead, use existing RF signal transmitted nearby
  Common case: sent from nearby higher capability device
  Dream case: use ambient RF signals to communicate
  Bonus: could harvest energy from the signal being received
Two versions in practice: backscatter and inductive coupling

## Slide 10: What happens if nothing ‘receives’ the wave?
From: https://www.flippingphysics.com/standing-waves.html

## Slide 11: ”Fixed end” and “Free end” in electronic transmission
~
~
Short Circuit = “Free End”
- Reflects wave
Open Circuit = “Fixed End”
- Inverts wave
~
Matched Load
- Absorbs wave (no reflection)

## Slide 12: Backscatter theory of operation
Vary between absorbing or reflecting signal to modulate data
  Wireless transmissions at microwatts of power draw (10000x savings)
  Frequency bands: 400 MHz, 900 MHz, 2.4 GHz
  These are the really really cheap tags (~$0.15 each)
RF Switch
Modulating Signal (Digital)
Antenna
Backscatter tag
Ambient RF signal
Reflected (backscatter) signal
Reader/ Receiver

## Slide 13: Backscatter radio designs
Simple versions just ‘reflect or don’t reflect’
Modern designs can do more advanced modulation as well
https://ieeexplore.ieee.org/stamp/stamp.jsp?arnumber=8368232

## Slide 14: Break + Spycraft
How could a spy use backscatter for malicious, covert purposes?

## Slide 15: Break + Spycraft
How could a spy use backscatter for malicious, covert purposes?
  Use microphone to change if antenna is grounded or not
  Transmit power at the backscatter tag and collect microphone data from the response

## Slide 16: Backscatter is an old idea — history in spycraft!
1945: Leon Theremin* creates “The Thing” (aka Great Seal Bug)
  *Yes, same guy who invented the instrument
  Discovered when a British embassy radio operator heard recorded conversations (after hanging for 7 years in the ambassador’s office)

## Slide 17: Lots of very active research in backscatter
Two broad paths…
  Passive sensing
    ”Detune” antennas predictably based on physical phenomenon
  Cross-technology communication
    Figure out how to speak “standard” WiFi, BLE, 15.4, etc. with backscattered signals

## Slide 18: e.g., How much force is applied to a tag?
ForceSticker: Wireless, Batteryless, Thin & Flexible Force Sensors

## Slide 19: Simple sensors can trigger backscatter
Backscatter fed directly from a sensor
  SATURN is an energy-free microphone made of treated paper
  Use it to trigger transistor for backscattering
  Nivedita Arora (Northwestern ECE faculty)

## Slide 20: Complete transmission path for SATURN audio

## Slide 21: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 22: RFID is everywhere nowadays
Fundamental design principle is asymmetry
  Extremely simple, cheap tags
  Complex readers

## Slide 23: Radio Frequency ID
Cheap, low-power ubiquitous communication
  RFID tags on (or in) products
  NFC communication to/from smartphone
Requirements
  Need to transmit small amount of data (ID)
  Need to operate with little or no energy
    Most do not have batteries
  Short interaction time (fast enough bit rate)
  Range can be extremely limited
    Meters to centimeters (or millimeters)

## Slide 24: A brief digression to be precise in terminology
RFID = Radio Frequency Identification = a communication standard
  A ton of standards through the ~early 90’s
  Most now EPC (Electronic Product Code) Gen2
There are actually three types of “RFID” device
  Passive Tags - harvest power from reader & reflect
  Semi-Passive Tags - on-board power, but reflect data
  Active Tags - on-board power that transmit data
Notes: The point: Papers misuse “RFID” to mean backscatter, and misuse “passive tag” to mean anything that doesn’t actively emit RF.
Most things that do backscatter don’t do the energy harvesting bit
Many papers that do backscatter describe themselves as RFID, but don’t follow any RFID communication standard

## Slide 25: Car RFID systems
Usually two mounted antennas
  One broadcasts energy, activating the RFID device
  The other receives the reflected data
Devices are often battery powered for longer-range operation
  Semi-passive
  Don’t have to energize themselves with signal
  Batteries last a decade

## Slide 26: E-ZPass System
RFID for toll road payments
  Originally a battery-powered active system
  Recently switched to passive backscatter tags

## Slide 27: Let’s look at RFID standards to get a sense of the numbers
Low Frequency (~300 kHz) — mostly legacy
  ~10cm read range (inductive coupling)
High Frequency (3~30 MHz; often 13.56 MHz)
  Passive: 4~7 m max (usually inductive coupling, I think)
  Semi-Passive: 10~30 m max
  Active: 30+ m
Ultra-High Frequency (300 MHz ~ 3 GHz)
  Passive: Up to 12 m (backscatter)
  Active: Up to 100 m

## Slide 28: Ranges and typical frequency ranges of RFID systems

## Slide 29: Inductive coupling versus RF communication
Magnetic field induces a current in the tag
Change in current can be used to communicate
Very short range (<1 meter)
Electromagnetic waves propagate between two antennas
Includes backscatter techniques
Range depends on energy
Reader
Tag
Reader
Tag
Inductive Coupling
Inductive Coupling

## Slide 30: RFID Cards
Northwestern Wildcards are RFID cards with a chip inside
  Likely 13.56 MHz inductive coupling (not backscatter)

## Slide 31: RFID challenges
Essentially free communication!
  Minimal cost (besides having a higher-capability device)
Difficult to reflect energy when it is already so low
  Essentially double the path loss (there and back)
Range is very limited (or transmit power needs to be high)
  Meters of range, maximum
  Centimeters for inductive coupling
  Alternatively, could decouple signal generation from reception

## Slide 32: MAC layer for RFID tags
Cards are limited in capability so we can’t do anything fancy
  But tags are frequently co-located, so some solution is necessary
Option 1: Aloha with pseudo-random timing
  Reader sends out initialization, tags randomly respond back
Option 2: Adaptive binary tree
  Reader sends out initialization, along with first bit of ID
  All cards matching that ID respond
  Reader sends out a second bit of ID
  Repeat until CRC is valid, then go back and choose other branches

## Slide 33: Electronic Product Code (EPC)
Format created by GS1
  Not-for-profit org that created and standardized barcodes
12-byte identifier for products for RFID use
Header | EPC Manager | Object Class | Serial Number
8 bits | 28 bits | 24 bits | 36 bits
(version number) | (Company ID) | (Product type SKU) | (Unique per instance of product)

## Slide 34: Break + Security Consideration
What data should an ID card send?
  Is just sending ID bits sufficient? What problem could occur?

## Slide 35: Break + Security Consideration
What data should an ID card send?
  Is just sending ID bits sufficient? What problem could occur?
  Simple identification, maybe. (e.g. products in a store)
  For authentication, no. Need to avoid replay attacks.
Include some kind of challenge and response
  Probably also encrypted
May also read/write from an arbitrary memory in the card
  Up to several hundred bits of storage

## Slide 36: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 37: How does RFID, Backscatter, etc map back to the IoT?
Well, as always, “Power and Communication are the hard part”
  RFID works, but only in the presence of an RFID reader
  Recent research looks at eliminating that latter clause
Power: RF Harvesting for general purpose computation
  WISP
  Moo
Communication: Repurposing extant RF signals for other uses
  Ambient Backscatter
  Inter-Technology Backscatter

## Slide 38: “Embedded” sensors
How do you change batteries in a device that’s inside a wall or inside someone’s body?

## Slide 39: RF energy harvesting alone is useful
Wiliot IoT Pixels harvest RF energy for power
  Microcontroller, BLE radio, maybe even a sensor
  $0.10 each at high volume
Idea: powered transmitter sends energy into area activating tags. Standard BLE receiver captures data.
  (not a backscatter system)
Walmart partnership for pallet-level tracking
https://www.mobileworldlive.com/industry/walmart-wiliot-go-large-on-ambient-iot/

## Slide 40: Backscatter for sensor networks
Backscatter allows transmissions at up to 10000x lower power than conventional radios
  Makes it very attractive for low-energy sensing devices
Backscatter
Transmissions
Conventional
Radio
Backscatter Tag

## Slide 41: RFID sensors
First iterations were literally RFID sensors
  Limited by cost and range of RFID readers (only a few meters)
WISP 5.0
University of Washington
Moo 1.0
University of Massachusetts

## Slide 42: Backscatter + LPWAN = usable?
Idea:
  Backscatter is about low energy operation
  LPWANs are about long-range operation
  Can we combine them for low energy and medium-long range?
LoRea: long-range transmissions at μW
  (Next few slides stolen from Ambuj’s talks)
Varshney et al. ”LoRea: A Backscatter architecture that achieves a long communication range” SenSys 2017

## Slide 43: Design element #1: LoRea decouples the carrier signal generation and reception
Bi-static setup spatially separates carrier generation from the receiver
Use devices that surround us for providing the necessary carrier signal
Self-interference reduced due to path loss suffered by carrier signal
Bi-static configuration
Monostatic configuration
Notes: + If we look into a RFID reader's configuration, there is a single device that both receives the backscatter transmissions and generates the necessary carrier signal. This is called a monostatic configuration.
+ In LoRea, we decouple the task of carrier signal generation and the reception of the backscatter transmissions. We adopt a bistatic configuration as we show in the slide. We have a dedicated device for carrier signal generation and reception.
+The advantage of the bistatic configuration is two-fold: First, we can attenuate the carrier signal arriving at the receiver due to the path loss suffered due to the propagation of the wireless signal. This helps us reduce interference from stronger carrier signal to much weaker backscatter transmission. Second, it also enables us to use the devices that surround us, such as smartphones or wifi router, as sources for providing the necessary carrier signal to support backscatter transmissions. In fact, in lorea, we demonstrate the use of these devices to provide the carrier signal.’

## Slide 44: Design element #2: LoRea backscatters at a frequency offset from the carrier signal
Backscatter is a mixing process
Transceivers attenuate interference at adjacent frequency channels
Frequency separation reduces interference from carrier to backscatter signal
No complex self-interference mechanisms required at reader
Notes: + The second design element that we incorporate in the design of LoRea is that we create separation in frequency between the carrier signal and the reflected transmissions. We transmit the backscattered signal at a particular offset from the carrier signal. This is unlike systems such as RFIDs that transmit at the same frequency as the carrier signal, requiring complex and expensive self-interference cancellation mechanisms.
+ To backscatter at an offset from the carrier signal, we take advantage of the property that the backscatter is a mixing process. If a carrier signal is incident on the backscatter tag, and if we toggle the antenna, i.e., change the antenna's state between absorption and reflection state at a frequency delta f, we can now create backscatter transmissions at a frequency offset of Fc+delta F due to the mixing property.
+ Most modern radio transceivers have bandpass filters present in adjacent frequency bands. They support these to enable co-existence on the shared wireless spectrum to suppress interference from adjacent traffic. We use these filters to our advantage; we place the carrier signal in the bandpass filter and significantly attenuate the carrier signal.
+ By incorporating the decoupling in space and frequency, we can reduce the interference to the weak backscatter transmissions from stronger carrier signal by up to 50-70 dB. We do not need to employ any complex self-interference cancellation mechanisms that are used on existing RFID readers. We use off-the-shelf commodity transceivers that just cost a few usd to carrier generation and the reception, thus significantly lowering the infrastructure's cost and complexity to support backscatter transmissions.

## Slide 45: Ran out of space while performing experiments…
State-of-art few meters. System achieved kilometers, was difficult to anticipate
Initial experiments conducted near the university and a river in Uppsala
Experiment Setup
Receiving transmissions 1km away from the setup

## Slide 46: LoRea outperforms state-of-the-art systems
System name | Communication range
LoRea – 868 MHz (SENSYS 2017) | 3400 m
LoRea – 2.4 GHz (SENSYS 2017) | 225 m
RFID | < 18 m
BackFi (SIGCOMM 2015) | 5 m
Passive WiFi (NSDI 2016) | 30 m
HitchHike (SENSYS 2016) | 54 m
Interscatter (SIGCOMM 2016) | 30 m
LoRa Backscatter (UBICOMP 2017) | 2800 m
Range reported are line of sight, with backscatter tag co-located with carrier source

## Slide 47: Future research directions for backscatter sensor communication
Improve capabilities for “ambient” backscatter
  Reuse existing RF signals rather than relying on carrier generation
MAC layers for backscatter
  Need ability to communicate with very low power
  How do you manage access to the medium?
Real-world usable backscatter stacks and hardware
  Needs to be deployable and usable by non-experts

## Slide 48: Backscatter as a sensor: soil moisture
Idea: bury backscatter tags in soil
  Measure round-trip-time for signal to reflect
  Ts (time signal travels through ground) changes based on the moisture in the soil
Josephson, Colleen, et al. "Low-cost In-ground Soil Moisture Sensing with Radar Backscatter Tags.“ COMPASS 2021

## Slide 49: Break + Open Question
What would you use a backscatter sensor for?
  Requirement: sensing has to be extremely low power too

## Slide 50: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 51: Slocalization: Ultra wideband backscatter localization
Notes: Image (free use): https://www.google.com/imgres?imgurl=http%3A%2F%2Fwww.crismatec.com%2Fpython%2Fmo%2Finteriors-photography-modern-office-workspace-for-metaphore-design_office-decoration.jpg&imgrefurl=http%3A%2F%2Fwww.crismatec.com%2F1489389139%2Fmnc%2Fb3b60136b4fec2dd%2F&docid=rzPzabXuQo6qOM&tbnid=Ag7dvYLgrHLwIM%3A&vet=1&w=1800&h=1200&hl=en&safe=images&bih=803&biw=1440&ved=2ahUKEwiZ45vr19fdAhUBiIMKHfF8Dv0QxiAoBnoECAEQGg&iact=c&ictx=1

## Slide 52: Why RF, why ultra wideband, why backscatter for ubiquitous localization?
Mautz, Rainer. "Indoor positioning technologies." (2012).

## Slide 53: Why RF, why ultra wideband, why backscatter for ubiquitous localization?
Narrowband
Ultra-Wideband
5.31 GHz
5.33 GHz
5 GHz
6 GHz
Time Domain
Frequency Domain

## Slide 54: Reflections make time-of-flight estimation difficult and inaccurate

## Slide 55: Ultra wideband can better disambiguate multipath and identify signal arrival time

## Slide 56: Design: localizing a UWB reflector tag
Sender
(mW - W)
Receiver
(mW - W)
Reflector
(nW)

## Slide 57: There is a new tradeoff to introduce to enable wide-area ultra-low power, high-quality localization
Covers areas 30m+
  “through walls”
Decimeter accurate
<1 µW tag
  (COTS, can do order of magnitude or more better with VLSI)
(Nearly) unlimited number of concurrent tags
Cost: 1-15+ minutes per location fix
  A latency/energy tradeoff for localization
Slocalization: Sub-μW Ultra Wideband Backscatter Localization Pat Pannuto, Kempke, Benjamin, and Prabal Dutta Proceedings of the 17th ACM/IEEE International Conference on Information Processing in Sensor Networks (IPSN’18). Best Paper Finalist.

## Slide 58: UWB Backscatter is passive reflection of a lot less energy than traditional communications
5m
5m
-41.3 dBm
-100 dBm
-101 dBm
-159 dBm
36 dBm
-56 dBm
-9.5 dBm
-10.5 dBm
900 MHz ISM
Sender
Reflector
Receiver
Notes: NB: 900 Mhz -> wavelength = 299792458 / 900e6 = 0.33
20 * log10(.33 / (4 * pi * 5)) = -45.6
Over 100 dB (or over 1 billion times more power)

## Slide 59: UWB Backscatter is passive reflection of a lot less energy
5m
5m
-41.3 dB
-100 dB
-101 dB
-159 dBm
36 dB
-56 dBm
-9.5 dB
-10.5 dB
900 MHz ISM
Typical receiver sensitivity
ranges from -94 to -106
Notes: NB: 900 Mhz -> wavelength = 299792458 / 900e6 = 0.33
20 * log10(.33 / (4 * pi * 5)) = -45.6
Just 60 dB, only a million times off!

## Slide 60: How do we recover a signal that is way below the noise floor?
Exploit tag stationarity and environmental stability
A
A
Notes: Environment does not change

## Slide 61: How do we recover a signal that is way below the noise floor?
Exploit tag stationarity and environmental stability
A
A

## Slide 62: Ideally, the only change in the channel impulse response is the tag reflection
Subtracting the environment finds the tag

## Slide 63: The goal is to estimate the time difference of arrival (TDoA) and trilaterate
First peak is anchor—anchor path, then anchor—tag—anchor
TDoA

## Slide 64: Extracting the tag signal in the real world has a few additional challenges
The environment is not actually static
  But noise is largely white & Gaussian
  And we can filter out the rest (sets floor for tag frequency, active power)
Finding tag phase offset currently requires brute force search

## Slide 65: Does it really work?
15 minutes can cover 30 meters
30 cm average error (3D Euclidean distance)
15m
15m
65
After a few seconds
After a few minutes

## Slide 66: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 67: Near Field Communication (NFC)
One type of RFID communication
  Inductive Coupling concept (13.56 MHz)
    Not actually backscatter at all
  But attached to a powered and capable device (smartphone)
  10-20 cm range max (usually <10)
Can act as a tag or as a reader
  Allows smartphone to power a tag if needed
  Alternatively, smartphone could act like a card and respond to a reader
  Two smartphones can communicate without power transfer
Data rate 100-400 kbps!
  nRF52840 capable of 100 kbps communication with attached antenna

## Slide 68: Inductive coupling theory of operation
A shared magnetic field is created between the two devices
  Change in current through one device induces current change through the other
  Device can vary load to transmit data
Very low frequency bands (135 KHz, 13.56 MHz)
  Transmit through materials including skin
  Sensitive to metal

## Slide 69: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
2G
NFC

## Slide 70: NFC Active and Passive Devices
Active NFC device is usually microcontroller-based like an NFC enabled smartphone. Can exchange information with other NFC devices. It powers itself.
A passive device, such as an NFC tag, contains information that other devices can read but does not read any information itself. NFC tag does not have its own power source.

## Slide 71: NFC Tags – Encoding data
NDEF (NFC Data Exchange Format) Structure
  Binary format for data
  Messages contains records
  Each record has header
NFC read returns the NDEF message

## Slide 72: NFC Forum NDEF record types
Record Type Definitions
  RTD Technical - Specifies the format and rules for building standard record types used by NFC Forum application definitions and third parties that are based on the NDEF data format.
  Text - Provides an efficient way to store text strings in multiple languages by using the RTD mechanism and NDEF format. An example of using this specification is included in the Smart Poster RTD.
  URI - Provides an efficient way to store Uniform Resource Identifiers (URI) by using the RTD mechanism and NDEF format. An example of using this specification is included in the Smart Poster RTD.
  Smart Poster - Defines an NFC Forum Well Known Type to put URLs, SMSs or phone numbers on an NFC tag, or to transport them between devices. The Smart Poster RTD builds on the RTD mechanism and NDEF format and uses the URI RTD and Text RTD as building blocks.
  Generic Control - withdrawn
  Signature - Specifies the format used when signing single or multiple NDEF records. Defines the required and optional signature RTD fields, and also provides a list of suitable signature algorithms and certificate types that can be used to create the signature. Does not define or mandate a specific PKI or certification system, or define a new algorithm for use with the Signature RTD.
  PHDC - Addresses a need for an openly-defined standard for the exchange of personal health data between devices using Near Field Communication technology.
Derived types
  Android Application NDEF Record
  Application NDEF Record
  Contact NDEF Record
  Email NDEF Record
  File NDEF Record
  Geolocation NDEF Record
  Phone NDEF Record
  SMS NDEF Record
  Website NDEF Record
  WiFi NDEF Record

## Slide 73: NDEF Format

## Slide 74: Investigating NFC on your own
NFC tools app allows you to inspect NFC tags

## Slide 75: Outline
Backscatter
Backscatter Uses
  RFID
  Sensors (Backscatter LoRa)
  Localization
NFC

## Slide 76: Class Summary
Network Fundamentals
Bluetooth Low Energy
  Advertisements, Connections
802.15.4
  Thread, Zigbee, Mesh Routing
WiFi
Cellular
LPWANs
  LoRaWAN, Sigfox, Research and Challenges
Other
  Localization, Satellite Communication, Backscatter

## Slide 77: Outline
Bonus: Wakeup Radios

## Slide 78: Wakeup radios are another form of “RF-lite”
How do you make a radio really low power?
  Turn it off
Problem: how do you know when to turn the radio on?
Idea: can we design a simpler radio where the only purpose is determining whether a signal exists or not?

## Slide 79: Concept: Can we design something (much?) lower power that can’t do general purpose data, but can signal wakeup?
Energy detectors
  Simple, but prone to false wakeups
Extremely simple signaling?
  Very often some form of on-off-keying (OOK)
  Seeing new life
    In mainstream networks, e.g. 802.11ba
    In sensor network research, e.g. Zippy
    Tuned energy harvesting frontends
    Manipulated standards for lower-BW signals

## Slide 80: (Re)-emerging new ideas in wakeup design
Decoupling synchronization from communication
External synchronization sources?
  Ambient 60 Hz wave
  Sudden change in room lighting, or a noise
Synchronization and time-keeping burden is shifted to infrastructure