## Slide 1: Lecture 02 Physical and Link Layers
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021
Some slides borrowed from: Peter Steenkiste (CMU), Christian Poellabauer (Notre Dame)

## Slide 2: Today’s Goals
Introduce OSI layer model of communication
Overview of concerns for the Physical and Data link layers
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols
Describe Medium Access Control mechanisms

## Slide 3: Outline
OSI Layers
Physical Layer
Data Link Layer

## Slide 4: Communication layers
Application
Presentation
Session
Transport
Network
Data Link
Physical
What goes on at each of these?

## Slide 5: OSI model of communication layers
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
  CS domain: CS340
Data Link
  How to send frames of data
  Ethernet, WiFi
  Our focus
Physical
  How to send individual bits
  Ethernet, WiFi
  EE domain: EE307, EE380, EE395

## Slide 6: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
  Packet is wrapped with header for the link to make a frame
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 7: Transmitting data between networks
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
(2)
internet packet
(7)
data
PH
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header
LAN1 frame

## Slide 8: Model != reality
Wireless protocols don’t always split between layers cleanly
  Usually explain parts of physical, data link, and possibly upper layers
Model still helps conceptualize stack-up though
  Layering of some type still occurs

## Slide 9: Layering for IoT (joke) (kind of)
MQTT
MQTT is a publish/subscribe message broker

## Slide 10: Outline
OSI Layers
Physical Layer
Data Link Layer

## Slide 11: Physical Layer
How bits are transmitted
  Wireless makes this entirely different from wired cases
Important considerations
  Signal strength
  Modulation
  Frequency

## Slide 12: Why use wireless?
There are no wires!
No need to install and maintain wires
  Reduces cost
  Simplifies deployment – place devices wherever makes sense
Supports mobile users
  Move around office, campus, city
  Move devices around home

## Slide 13: What is hard about wireless?
There are no wires!
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all

## Slide 14: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 15: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links just increases interference
  Need to expand to different frequencies

## Slide 16: Model of RF communication
Energy that radiates spherically from an antenna
Attenuation with distance
  Density of energy reduces over time, distance
  Signal strength is reduced, errors go up
Two key features
  Error rates depend on distance
  Spatial reuse of frequencies

## Slide 17: Signal strength is measured in decibels
Power is measured in Watts or dBw or dBm
dBm is most relevant to the IoT domain
  0 dBm equals 1 mW transmit power
  Example
    Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
    Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
Rule of thumb: +3 dB is double the power

## Slide 18: Propagation degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out -> free space path loss
Obstacles can weaken signal through absorption or reflection
Important: distance is NOT the only signal strength loss
  Free space path loss calculation will not give you accurate range for a signal

## Slide 19: ITU model for Indoor Attenuation
Models like this are more trustworthy than FSPL
  https://en.wikipedia.org/wiki/ITU_model_for_indoor_attenuation

## Slide 20: Modulation
Encoding digital data in an analog “carrier” signal
Basic forms:
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal
Phase-shift Keying (PSK)
  Modify phase of carrier signal

## Slide 21: RF communication frequencies
IoT focus

## Slide 22: Wireless spectrum is allocated to specific uses

## Slide 23: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?

## Slide 24: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why? No interference from other users

## Slide 25: Frequency Hopping Spread Spectrum
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 26: Sidebar: inventor of FHSS – Hedy Lamarr
Actress and Inventor
  Designed FHSS with George Antheil during WWII
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventor

## Slide 27: Outline
OSI Layers
Physical Layer
Data Link Layer

## Slide 28: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 29: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 30: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 31: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 32: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”

## Slide 33: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)
Others?

## Slide 34: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 35: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 36: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad

## Slide 37: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
time

## Slide 38: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 39: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 40: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 41: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Somewhere between challenging and impossible for wireless
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm

## Slide 42: Hidden terminal problem
Device A
Device B
Device C

## Slide 43: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 44: Contention-free access control protocols
Goal: split up communication such that devices will not conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 45: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 46: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 47: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 48: Outline
OSI Layers
Physical Layer
Data Link Layer