## Slide 1: Lecture 14 Deep-Dive into LPWANs
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2021

## Slide 2: Today’s Goals
Overview of other unlicensed LPWAN approaches
  Sigfox
  802.11ah
  TV Whitespaces
Discuss Cellular IoT protocols
Deep-dive into challenges LPWANs face

## Slide 3: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges

## Slide 4: Sigfox
Very low-rate (600 bps), very long-range (10+ km) communication
Star-topology networks, with always-listening gateways
  Any number of low-power end devices
Uplink-focused communication
Applications: very low-rate metering

## Slide 5: Sigfox PHY
Unlicensed-band communication
  Europe 868 MHz. US 902-928 MHz (915 MHz band)
Ultra-narrowband 600 Hz (100 Hz Europe) channel bandwidth
  Detection only needs to occur at very specific frequency
  Helps improve signal-to-noise ratio

## Slide 6: Sigfox unbalanced uplink and downlink
Uplink
  600 Hz bandwidth, 600 bps, DBPSK
Downlink
  1.5 kHz bandwidth, 600 bps, GFSK
Particularly optimized for Europe
  Uplink on 1% duty cycle channel, up to 14 dBm
  Downlink on 10% duty cycle channel, up to 27 dBm
Works fine in US too
  Gets more power (24 dBm up is typical, up to 32 dBm down) and more range

## Slide 7: Sigfox link budget
Why transmit at 100-600 bps?
  For greatly increased link budget
Link budget: 150-160 dBm
  Assuming Tx at ~20 dBm
  Means Rx Sensitivity of -130 dBm (10 dBm better than LoRaWAN)
Resulting range: 10-15 km in urban environments
  Except that buildings lead to dead spots in range

## Slide 8: Sigfox MAC
Aloha-style access control (send whenever)
  No acknowledgements!
Send message three times for increased reliability
  Then listen for downlink at a set period later on a known frequency

## Slide 9: Sigfox uplink packet
Up to 29 bytes total per packet
  Payload: up to 12 bytes 😱
Other fields
  Preamble + Frame Sync are really a 6 byte field for radio sync
  Authentication: 2-5 bytes
  Frame Check Sequence: 16-bit CRC

## Slide 10: Aside: why faster bitrate in the US?
Packet size up to 29 bytes (232 bits)
  At 100 bps: 2.32 seconds on air
  At 600 bps: 0.387 seconds on air
Maximum dwell time for 915 MHz band: 400 ms

## Slide 11: Sigfox downlink packet
Similar structure, 28 bytes total
  Payload: up to 8 bytes
Larger preamble + frame sync of 13 bytes
Error Correcting Code for increased reliability

## Slide 12: Sigfox deployments
Proprietary network with managed deployment
  Like cellular networks
  Sigfox deploys networks and transports data
  140 uplink messages plus 4 downlink message per day
Connectionless communication
  Devices are registered with the networks
  Keys are provided in the software image
  Any deployed Sigfox gateway can collect transmitted data
    Enables mobile applications

## Slide 13: Sigfox coverage (Winter 2021)

## Slide 14: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges

## Slide 15: IEEE standard for LPWANs
802.11ah (HaLow) standard in 2016
  First real hardware in 2020
  Still not in real-world use yet
Focus on the indoor-to-outdoor scenario
  Medium range (maximum 1 km)
915 MHz communication
  NOT interoperable with other 802.11 access points and devices
Theoretically up to 356 Mbps
  Practically, most devices are expected to implement 150 kbps to 8 Mbps

## Slide 16: 802.11ah allows multiple bandwidth allocations

## Slide 17: 802.11ah architecture
Star topology
  Up to 8191 devices per access point
Devices are assigned to a group
  Groups are scheduled slots with TDMA
  Within a slot CSMA/CA is used for contention among devices
  Devices not in the group can sleep until their slot
Traditional IP communication on top of that
  And traditional 802.11 security mechanisms (WPA2/TLS)

## Slide 18: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges

## Slide 19: TV whitespaces
Unused TV channels between 54 MHz and 698 MHz
  VHF (54-216 MHz)
  UHF (470-698 MHz)
  6 MHz channel width
Allocated but unused
  FCC allows unlicensed use
  IF you do not interfere with primary users

## Slide 20: Sensing channel use
Variation in use
  Spatial: Cannot assume same channel will be free everywhere
  Temporal: Cannot assume channel will be free at all times
Cognitive radio approach
  Dynamically identify unused portions of spectrum
Database approach
  Let someone else do the scanning. Consult database based on location and time

## Slide 21: Sensor Networks Over tv Whitespaces (SNOW)
A design for sensor networks over whitespaces
  Base Station manages channel for deployment
  Frequency division for devices. Each uplinks on separate subcarrier
  Downlink is one OFDM transmission. Each device hears its frequency

## Slide 22: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges

## Slide 23: 3GPP
3rd Generation Partnership Project (3GPP)
  Developed 3G, 4G, 5G
Industry alliance for development of telecoms standards
  Established around 1998
  Makes “Releases” which are roughly analogous to IEEE standards/versions
    Release 8 (2008) LTE ~4G
    Release 15 (2018) NR (New Radio) ~5G
Focused on the practical
  Different group actually defined 4G (ITU). 3GPP made LTE

## Slide 24: Cells in a cellular network
Split a physical area into a number of non-overlapping cells
  Each cell gets a cell tower and a frequency band assigned to it
  Apply frequency bands so nearby cells use different frequencies

## Slide 25: More complicated real-world cells
Place towers at corners of cells
  Directional antennas send three different frequency bands, one per cell
  Each cell gets three tower and three bands
Density of cells varies based on expected number of users
  Change cell size using Power Control

## Slide 26: LTE Categories
Different equipment supports different “categories” of LTE
  Maximum MCS index supported
Examples
  iPhone 6 (2015): Cat 4
  Pixel 3 (2018): Cat 16

## Slide 27: Additional low-end categories for IoT
LTE Cat 0
  Traditional LTE, but focused on the really low end
LTE-M (LTE Cat M1)
  375 kbps uplink, 300 kbps downlink (for the actually implemented mode)
  Reduced power and maximum bandwidth
  Increased range
NB-IoT (LTE Cat NB1)
  65 kbps uplink, 26 kbps downlink
  Reduced power and greatly reduced bandwidth
  Greatly increased range

## Slide 28: LTE-M and NB-IoT were developed in parallel

## Slide 29: LTE-M and NB-IoT downlink and uplink
OFDMA downlink
  Put the more complicated hardware in the cell tower
SC-FDMA (single carrier FDMA) uplink
  Blocks of subchannels combined into one signal
  Similar concept, but simpler for end devices to implement

## Slide 30: LTE resource allocation
Cellular uses OFDMA to schedule
  Time + Frequency -> “2D Scheduling”
Cellular uses single channels up to 20 MHz
  Further divides these into 100 Resource Blocks
Resource Block
  12 subcarriers for OFDM in frequency (15 kHz each)
  7 symbols in time (0.5 ms)
    Remember, better modulation can pack many bits into a symbol
Devices are allocated frequency and time based on what they are sending
  Allocated in units of Resource Blocks

## Slide 31: Resources used by LTE-M and NB-IoT
LTE-M uses up to 6 resource blocks
  1.4 MHz of bandwidth (1.080 MHz)
  Can co-exist with other normal LTE traffic, scheduled by cell tower
  Limited to only some capability of LTE
NB-IoT uses up to 1 resource block
  200 kHz of bandwidth (180 kHz)
  Multiple deployment options
    Guard-band in practice

## Slide 32: Reducing power for IoT devices
Reduce maximum Tx power to 20 dBm
  Increased receive sensitivity will cover it
Extended Discontinuous Reception
  Allow devices to reduce paging period and still stay on network
  Cell tower will hold messages

## Slide 33: Further power reduction for simple devices
Power Saving Mode
  For very simple, uplink-focused devices allow them to turn off entirely but stay connected
  Minutes to days in duration
  Notify tower before sleeping, listen for packets after each transmission

## Slide 34: Improved range for LTE-M and NB-IoT
LTE defines a Maximum Coupling Loss (MCL) a.k.a Link Budget
  Traditional cellular: 144 dB (~2.5 km)
  LTE-M: 160 dB (~5 km)
  NB-IoT: 164 dB (~10 km)
  Sigfox: ~155 dB
  LoRaWAN: ~143 dB
Note that cellular networks are on higher frequencies
  Example: 1900 GHz

## Slide 35: Cellular deployments
Originally unclear which would be dominant
  Verizon and AT&T focused on LTE-M
  T-Mobile focused on NB-IoT
  All rolled out services nationwide in the 2018-2019 timeframe
Networks are expanding to provide both capabilities
  LTE-M: AT&T, T-Mobile, US Cellular, Verizon
  NB-IoT: AT&T, T-Mobile
Pricing models still very uncertain
  NB-IoT example: $5 per device per year up to 12 MB, 10 packets per hour
  Future adoption will greatly depend on these

## Slide 36: Microcontroller support
Devices need to be certified
  Hardware and software
  Tend to be modules or dual-core systems
Add a SIM card to connect to network

## Slide 37: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges

## Slide 38: Do novel networks meet application needs?
How do we compare varied requirements and capabilities?
  Networks have throughput per gateway and range of gateway.
  Applications have throughput per device and deployment area.
Each gateway must support throughput for all devices in its coverage area.
  Deployment areas are often wider than a single gateway’s range.
Solution: compare the density of communication.
  Data communication rate per unit area.

## Slide 39: New metric for wide-area communication.
Our proposed metric: bit flux
Units: bit per hour / m2
First suggested by Mark Weiser
Branden Ghena, et al. "Challenge: Unlicensed LPWANs Are Not Yet the Path to Ubiquitous Connectivity." MobiCom’19
Notes: bit flux is our metric for data density
throughput divided by coverage area
As with many ideas, this was first suggested by Mark Weiser

## Slide 40: Bit flux can measure application needs.
For an application:
Assumes a relatively homogeneous distribution.
Notes: For applications, bit flux sums the data needs for each device in the deployment
And divides by the total deployment area
To determine the application uplink density

## Slide 41: Bit flux can measure network capabilities.
For a network:
Assumes a non-overlapping deployment of gateways.
Note that bit flux alone ignores the total number of gateways required.
Notes: For networks, we divide the goodput of a network
By the coverage area of a single gateway
This gives us a number that represents the data density that a network can support, at any width of deployment

## Slide 42: Bit flux accounts for spatial reuse.
Reducing coverage area and deploying additional gateways improves capacity.
Notes: Bit flux also accounts for spatial reuse in networks
Reducing range (and deploying more gateways), reduces the coverage area for each gateway, increasing the network bit flux

## Slide 43: Bit flux measurement for LoRaWAN.
ALOHA access control
Hata model
Notes: Here is the bit flux measurement for a LoRaWAN network
In the US, LoRaWAN has 64 channels for uplink
But it relies on an ALOHA access control mechanism, so packet collisions reduce throughput significantly

## Slide 44: Networks differ in capability by orders of magnitude.
Notes: We can calculate bit flux for each of the networks we’re interested in
We note that there are several orders of magnitude difference in the throughput capability of each network
Particularly between cellular communication and unlicensed LPWANs

## Slide 45: Range reduction results in a bit flux curve for each network.
Notes: These points are at the maximum range for each network, but they have the ability to perform power control and reduce range
This creates a curve for each network, where we can reduce range (and install more gateways) in order to increase network capability

## Slide 46: Let’s compare network capabilities to a real-world application.
Smart household electric meters.
~250 bytes of data every 4 hours
~370000 electric customers in San Francisco
Notes: Now that we can measure the capability of each network, lets compare that to the needs of an application
The example I’ll be talking through is Electricity Metering, there are about a dozen others in the paper
PG&E smart meters send about 250 bytes every 4 hours
This isn’t a lot of data, but smart meters are densely deployed, with three hundred thousand across San Francisco

## Slide 47: All networks are capable of meeting the data needs of electricity metering.
Electricity Metering Application
Notes: We can plot the need of the Electricity Metering application as a line on our bit flux figure
Any network above this line is capable of serving the application’s needs
Sigfox needs range reduction, but all networks are capable of serving this application’s needs
So, great! Networks can serve ubiquitous applications. Problem solved, right?

## Slide 48: Unlicensed LPWANs lag behind Cellular IoT in ability to support applications.
2G < 0.03% utilized
Notes: Let’s visualize this instead as the number of gateways deployed and the proportion of network utilized.
  Again, because of power control, there is a tradeoff here. We could deploy a single gateway for everything, or many gateways with reduced range to increase capacity.
Cellular networks have no problem with this application
  With a single gateway, LTE-M could spend 1% of its capacity to service this app.
Unlicensed LPWANs, however, have choices to make on how many gateways they deploy and how much capacity they are willing to spend on this one application

## Slide 49: Sigfox requires range reduction to meet application needs.
Capacity Problem
Throughput capability of Sigfox is insufficient to support application needs
It can only support the application with reduced range and additional gateways
Notes: There are two particular problems we can see with the unlicensed LPWANs
The first is a capacity issue:
  Sigfox can’t satisfy the application at all without power control.
  Range is sufficient for a single gateway to cover the city, but it wouldn’t be able to keep up with the data.

## Slide 50: Capacity solutions are relatively straightforward.
Better access control mechanisms.
Recover simultaneous transmissions (Choir and Charm).
Increase bandwidth (TV white spaces).
All likely come at the cost of increased energy usage…
  Results in a protocol that looks pretty similar to cellular…
Adwait Dongare, et al. "Charm: exploiting geographical diversity through coherent combining in low-power wide-area networks.“ IPSN’18
Rashad Eletreby, et al. "Empowering low-power wide area networks in urban settings." SIGCOMM’17
Abusayeed Saifullah, et al. "SNOW: Sensor network over white spaces." SenSys’16
Notes: Solving these capacity problems is relatively straightforward
And a lot of research from our community has begun that path
One solution would be better access control mechanisms than the ALOHA
We could also significantly increase the available bandwidth through the use of TV white spaces

## Slide 51: LoRaWAN devotes most of its network capacity to a single application.
Coexistence Problem
LoRaWAN can meet application needs
But only by using 50% of the 915 MHz unlicensed-band spectrum
Notes: But there is a second problem, that of coexistence
  LoRaWAN could handle the application with only 2 or 3 gateways
  Remember, that we are calculating bit flux for LoRaWAN using all available channels
  As long as you are willing to commit 50% of the 915 MHz spectrum to electricity metering

## Slide 52: Coexistence is inevitable in urban areas.
Urban environments and long range lead to many overlapping deployed networks.
Capacity problems worsen coexistence by devoting more bandwidth to one application.
It’s not just electricity metering…
Notes: You might try to say it’s fine to dedicate so much of a network to a single application. I dedicate 50% of my home WiFi to Netflix all the time…
But coexistence cannot be ignored in urban areas
There won’t just be one network, but two, or three, or more
And they all have to share the same bandwidth for all deployed applications

## Slide 53: Coexistence in unlicensed bands is a more difficult problem.
No methods for inter-network negotiation so far.
Without buy-in from most deployments, all access control becomes uncoordinated.
Cellular IoT does not have this problem
Notes: Solving these coexistence problems are more difficult
We need methods for coordination and negotiation between deployed networks
And without buy-in from all networks, collisions are inevitable
It doesn’t matter that you are using a wonderful scheduling TDMA algorithm to send data without collisions if your neighbor is transmitting whenever they want
And a really important point is that cellular IoT doesn’t face this problem

## Slide 54: Cellular may dominate future deployments.
LTE-M and NB-IoT are now deployed in the US (and worldwide).
Licensed bandwidth avoids the coexistence problem.
Cellular may solve many applications but is not a perfect solution.
  Still has higher energy and monetary costs for use.
  Also limited to where service is already available.
Notes: Occupying licensed bands means LTE-M and NB-IoT don’t have multiple overlapping networks to coordinate with
So coexistence isn’t a concern
And they already have more capacity than the unlicensed protocols
Without solutions for unlicensed LPWANs, deployments will move to cellular networks
And when the applications leave, research will leave as well
Without real solutions to the problems they face, we’re in danger of losing an exciting research domain
We pose this as a challenge to the community to develop coexistence and capacity solutions for unlicensed LPWANs

## Slide 55: Unlicensed LPWANs are still useful for some scenarios.
Controlled or unoccupied regions have reduced coexistence concerns.
  Industrial factories, farms, parks and forests.
Unlicensed networks are very exciting for research.
  Anyone can deploy a network wherever they want.
  Much easier to explore protocol modifications and new technologies.
Research suffers without real-world applications.
  Problem areas are strong recommendations for new research.
  New research is only useful if they will have real-world impacts.

## Slide 56: Implications – Low-Power Wide-Area Networks.
Existing unlicensed LPWANs face significant challenges in supporting urban applications.
  Best suited for industrial or agricultural uses in controlled environments.
Research directions for unlicensed LPWANs:
  improve network capacity,
  and enable coexistence.
Cellular IoT networks (LTE-M and NB-IoT) are positioned to solve the needs of city-scale sensing.
  If the money and energy costs are there.

## Slide 57: Outline
Unlicensed LPWANs
  Sigfox
  802.11ah
  TV Whitespaces
Cellular IoT
LPWAN Challenges