## Slide 1: Lecture 02 Network Fundamentals
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2023
Some slides borrowed from: Peter Steenkiste (CMU), Christian Poellabauer (Notre Dame)
Materials in collaboration with Pat Pannuto (UCSD)

## Slide 2: Administrivia
Piazza
  Everyone should have access to it
  If you don’t, try going to the Piazza tab on the sidebar in Canvas
  If that still doesn’t work, this is the exception when you should email me
Canvas
  Most important information is on the Canvas homepage
  I’m posting slides there too

## Slide 3: Today’s Goals
Introduce OSI layer model of communication
Provide background on Internet layering
Overview of concerns for the Physical and Data link layers
  Speak the “lingo” of wireless communication
  Present technology aspects that we will return to in specific protocols
Describe Medium Access Control mechanisms

## Slide 4: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
Data Link Layer

## Slide 5: Communication layers
Application
Presentation
Session
Transport
Network
Data Link
Physical
What goes on at each of these?

## Slide 6: OSI model of communication layers
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
Data Link
  How to send frames of data
  Ethernet, WiFi
Physical
  How to send individual bits
  Ethernet, WiFi

## Slide 7: OSI model of communication layers
Transport
  How to form connections between computers
  TCP and UDP
Network
  How to send packets between networks
  IP
Data Link
  How to send frames of data
  Ethernet, WiFi
Physical
  How to send individual bits
  Ethernet, WiFi
CS domain
CS340, CS440
EE domain EE307, EE378, EE380
This course!

## Slide 8: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for the network to make a packet
    i.e., bytes are added to the start/end of it
  Packet is wrapped with header for the link to make a frame
Data
Packet Header
Frame Header
Internet Packet
Ethernet Frame

## Slide 9: Protocols are “layered”
Headers for each layer of communication wrap data
  Data is wrapped with header for network to make a packet
  Packet is wrapped with a header for the link to make a frame

## Slide 10: Packet encapsulation
Upper-layer packet is the payload for the lower-layer packet

## Slide 11: Transmitting data between networks
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
(2)
internet packet
(7)
data
PH
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header
LAN1 frame

## Slide 12: Model does not equal reality
Wireless protocols don’t always split between layers cleanly
  Usually explain parts of physical, data link, and possibly upper layers
Model still helps conceptualize stack-up though
  Layering of some type still occurs

## Slide 13: Layering for IoT (joke) (kind of)
MQTT
MQTT is a publish/subscribe message broker

## Slide 14: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
Data Link Layer

## Slide 15: The global Internet
Most famous example of an internet (uppercase to distinguish)
Based on the TCP/IP protocol family
  IP (Internet Protocol)
    Provides a naming scheme and unreliable delivery of packets from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable data delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable data delivery from process-to-process
Accessed via a mix of Unix file I/O and the sockets interface

## Slide 16: Hardware and software organization of an Internet application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 17: A programmer’s view of the internet
1. Hosts are mapped to a set of 32-bit IP addresses
  129.105.7.30
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  129.105.7.30 is mapped to moore.wot.eecs.northwestern.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 18: 1. IP addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian)
    Remember: most computers use little-endian😭
  True in general for any integer transferred in a packet header from one machine to another
    E.g., the port number used to identify an Internet connection
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8169071E = 129.105.7.30
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 19: 2. Internet domain names
.net
.edu
.gov
.com
northwestern
berkeley
mit
eecs
mccormick
moore
129.105.7.30
wot
unnamed root
www
129.105.1.129
hanlon
129.105.7.27
amazon
www
54.230.48.28
Top-level domain names
Second-level domain names
Third-level domain names
and onwards…
Note: Northwestern owns 129.105.x.x

## Slide 20: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries
  Each host entry defines the mapping between a set of domain names and IP addresses
A special name: localhost
  Refers back to the computer being used (IP address 127.0.0.1)

## Slide 21: 3. Internet connections
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
    IP address identifies the computer
    Port identifies the process on the computer
Clients and servers communicate by sending streams of bytes over connections. Most connections are:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  [TCP adds] Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.

## Slide 22: Ports are used to identify services to the kernel
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 23: How does the Internet handle routing packets?
IP layer
  Describes the overall goal
    Packets from my computer <---> Google
Link layer (Ethernet)
  Describes individual links
    Packets from my computer <---> my router
Routing
  Using link-layer building blocks to get packets from one IP to another

## Slide 24: Addressing
How to solve the routing problem?
  I need to know how to get data from me to you
How does the post office work?
  I know where you live (your address)
    Zip Code
    City
    Street
    House Number
    Name

## Slide 25: The problem with addressing
Your computer moves all the time
  Home, school, Starbucks...

## Slide 26: Assigning and finding IP address ranges
In general, network operators don’t change that often
Solution:
  Tie IP addresses to network operators
  Assign computers IPs as they join networks
Key Point:
  Networks ”own” a block of IP address space
  ”The Internet” is a network of networks

## Slide 27: Routing
1.0.0.0/8
5.0.0.0/8
2.0.0.0/8
10.0.0.0/8
4.0.0.0/8

## Slide 28: Routing
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 29: Routing – ”Adaptive”
1.0.0.0/8
  2.0.0.0/8
    10.0.0.0/8
  4.0.0.0/8
    5.0.0.0/8
      10.0.0.0/8
5.0.0.0/8
  10.0.0.0/8
2.0.0.0/8
  10.0.0.0/8
10.0.0.0/8
4.0.0.0/8
  5.0.0.0/8
    10.0.0.0/8

## Slide 30: Identifying your computer?
Every network card has its own MAC address
  IPs are (somewhat) dynamic, ”owned” by local networks
  MACs are hardware and static, ”owned” by specific computers
    Manufacturers own blocks of MACs, ”spend” them each time they make a device
”Connecting” to a network
  Your computer leases an IP from the local network
  Only the local router knows your MAC, everyone else sees your IP
    Note: this overview ignores NATs, which are commonplace today

## Slide 31: So how does the Internet of Things fit into the Internet?
“IP is the Narrow Waist of the Internet”
  IP is Dead, Long Live IP for Wireless Sensor Networks
A recurring theme in this class:
  How does this actually attach to the Internet
    Physically [hello Hue Hub, Wyze Hub, August Hub, …]
    Logically [are BLE devices really part of the IoT?]

## Slide 32: Break + Thinking
What are the steps for viewing a website?

## Slide 33: Break + Thinking
What are the steps for viewing a website?
You enter a domain name for the website
Computer looks up domain name to get IP Address
Computer sends request to IP_address:80
Computer gets back data, which it renders into a website

## Slide 34: ALL the layers
A ‘famous’ interview question
  “What happens when you type google.com into your browser’s address bar and press enter?”
  https://github.com/alex/what-happens-when (11 pages!)
    Keyboard events
    Parsing URL
    DNS lookup
    Opening socket
    HTTP protocol
    HTML parsing
    GPU rendering

## Slide 35: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
Data Link Layer

## Slide 36: Physical Layer
How bits are transmitted
  Wireless makes this entirely different from wired cases
Important considerations
  Signal strength
  Modulation
  Frequency

## Slide 37: Why use wireless?
There are no wires!
No need to install and maintain wires
  Reduces cost
  Simplifies deployment – place devices wherever makes sense
Supports mobile users
  Move around office, campus, city
  Move devices around home

## Slide 38: What is hard about wireless?
There are no wires!
Wired networks are constant, reliable, and physically isolated
  Ethernet has the same throughput minute-to-minute
  Bits sent through Ethernet or USB are (usually) received
Wireless networks are variable, error-prone, and shared
  WiFi throughput changes based on location and walls
  Signals from nearby devices interfere with your signals
  Individual bits might flip or never be heard at all

## Slide 39: Wireless is a shared medium
Wired communication has signals confined to a conductor
  Copper or fiber
  Guides energy to destination
  Protects signal from interference
Wireless communication is inherently broadcast
  Energy is distributed in space
  Signals must compete with other signals in same frequency band

## Slide 40: Increasing network capacity is challenging
Wired networks just add more wires
  Buses are many signals in parallel to send more data
Wireless networks are harder
  Adding more links just increases interference
  Need to expand to different frequencies

## Slide 41: Model of RF communication
Energy that radiates spherically from an antenna
Attenuation with distance
  Density of energy reduces over time, distance
  Signal strength is reduced, errors go up
Two key features
  Error rates depend on distance
  Spatial reuse of frequencies

## Slide 42: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 43: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 44: Signal strength is measured in decibels
Power is measured in Watts or dBw or dBm
dBm is most relevant to the IoT domain
  0 dBm equals 1 mW transmit power
  Example
    Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
    Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
Rule of thumb: +3 dB is double the power

## Slide 45: Signal strength varies significantly across technologies
Bluetooth Low Energy (local area)
  nRF52840 transmit power: 8 dBm (6.31 mW)
  nRF52840 receive sensitivity: -95 dBm (316.2 fW)
LoRa (wide area)
  SX127X LoRa transmit power: 20 dBm (100 mW)
  SX127X LoRa receive sensitivity: -148 dBm (1.6 attoWatt)

## Slide 46: Propagation degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out  Free Space Path Loss (FSPL)

## Slide 47: Some intuitions for signal propagation, power, gain, etc
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 48: Wait, is not an antenna
Indeed, this little strip of metal is the actual antenna
  Receiver only recovers the part of the signal that hits its antenna (“aperture”)

## Slide 49: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
6.31 mW

## Slide 50: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
.25 m

## Slide 51: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
1 m

## Slide 52: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m

## Slide 53: Some Intuitions for Signal Propagation, Power, Gain, etc.
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
2 m
0.00016 mW
46 dB path loss!

## Slide 54: Okay.. So what’s the limit?
We will use the nrf52840 in lab:
  Max BLE transmit power for nRF52840: 8 dBm (6.31 mW)
  Min BLE receive sensitivity for nRF52840: -95 dBm (316.2 fW)
8 dBm – -95 dBm = 103 dB link margin
For FSPL alone for a 2.4 GHz signal, 103 dB is 1,400 m!
Bluetooth does not go 1.4 km…

## Slide 55: Propagation is one thing that degrades RF signals
Attenuation in free space
  Signals get weaker as they travel over long distances
  Signal spreads out -> free space path loss
Important: distance is NOT the only signal strength loss
  Free space path loss calculation will not give you accurate range for a signal
Obstacles can weaken signal through absorption or reflection
  Precise quantitative details are in the EE domain
  We’ll use examples to develop qualitative instincts in this class

## Slide 56: Many factors affect the ability to actually receive data
Here’s some examples, from DW1000 [ultra wideband transceiver]

## Slide 57: ITU model for Indoor Attenuation
Models like this are less bad than Free-Space Path Loss
  https://en.wikipedia.org/wiki/ITU_model_for_indoor_attenuation

## Slide 58: Lower received energy increases error rates
More Errors
Less Errors
More Energy Received
Less Energy Received
BER: Bit Error Rate
Odds that a transmitted bit will be received incorrectly

## Slide 59: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 60: RF communication frequencies
IoT focus

## Slide 61: Wireless spectrum is allocated to specific uses

## Slide 62: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why?

## Slide 63: Unlicensed bands are where IoT thrives
902 MHz – 928 MHz
  LPWANs
2.4 GHz to 2.5 GHz
  WiFi, BLE, Thread
5 GHz
  Faster WiFi
Cellular uses licensed bands at great cost
  Why? No interference from other users

## Slide 64: Different technologies use spectrum in different ways
How spectrum is used affects: cost ($), robustness, throughput…
  We will talk about how each technology uses spectrum, and implications
This graphic shows how BLE and WiFi interoperate; more on this next week

## Slide 65: Frequency Hopping Spread Spectrum
Transmitter hops through a sequence of transmit channels
  Spend some “dwell time” on each channel before hopping again
  Receiver must know the hopping pattern
Avoid causing or receiving prolonged interference

## Slide 66: Sidebar: inventor of FHSS – Hedy Lamarr
Actress and Inventor
  Designed FHSS with George Antheil during WWII
  Idea: torpedo control can’t be easily jammed if it jumps around
https://en.wikipedia.org/wiki/Hedy_Lamarr#Inventor

## Slide 67: Signal qualities
Signal strength
  The amount of energy transmitted/received
Signal frequency and bandwidth
  Which “channel” the signal is sent on
Signal modulation
  How data is encoded in the signal

## Slide 68: Modulation
Encoding signal data in an analog “carrier” signal
  Carrier signal defines the frequency
  Modulation scheme + data define bandwidth required

## Slide 69: Modulation types
Encoding binary data on a signal
Amplitude-shift Keying (ASK)
  Modify amplitude of carrier signal
  On-Off Keying (OOK) is an extreme example
Frequency-shift Keying (FSK)
  Modify frequency of carrier signal

## Slide 70: Modulation types
Phase-shift keying (PSK)
  Modify phase of carrier signal
  Usually differential: the change signifies data
More complicated possibilities exist
  QAM (Quadrature Amplitude Modulation) combines amplitude and phase shift keying
    Allows for more than one bit per “symbol”

## Slide 71: Modulation tradeoffs
Various tradeoffs between different modulation schemes
  Bandwidth requirements, transceiver hardware, immunity to noise, etc.
ASK (amplitude) is simple but susceptible to noise
  Noise exists in the real world
FSK (frequency) is relatively simple and robust to noise, but uses more bandwidth
  Bandwidth is limited, but still commonly used
PSK (phase) energy efficient and robust, but more complex hardware
  More expensive hardware, but very commonly used

## Slide 72: Break + Say hi to your neighbors
Things to share
  Name
  Major
  One of the following
    Favorite Candy
    Favorite Pokemon
    Favorite Emoji

## Slide 73: Break + Say hi to your neighbors
Things to share
  Name -Branden
  Major -EE, CE, and CS
  One of the following
    Favorite Candy - Twix
    Favorite Pokemon - Eevee
    Favorite Emoji - 🍢

## Slide 74: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
Data Link Layer

## Slide 75: Data Link Layer
Framing
  Combine arbitrary bits into a “packet” of data
Logical link control
  Manage transfer between transmitter and receiver
  Error detection and correction
Media access
  Controlling which device gets to transmit next
Inherently coupled to PHY and its decisions

## Slide 76: Framing
Typical packet structure
  Preamble - Existence of packet and synchronization of clocks
  Header - Addresses, Type, Length
  Data - Payload plus higher layer headers (e.g. IP packet)
  Trailer - Padding, CRC
Wireless considerations
  Control information for Physical Layer
  Ensure robustness for header
  Explicit multi-hop routing
  Possibly different data rates for different parts of packet
Preamble | Destination Address | Source Address | Type and Length | Data | CRC

## Slide 77: Error control: detection and recovery
Detection: only detect errors
  Make sure corrupted packets get discarded
  Cyclical Redundancy Checks
    Detect single bit errors
    Detect “burst” errors of several contiguous bits
Recovery: also try to recover from small bit errors
  Forward error correction
  Retransmissions
  Far more important for wireless because the cost of transmission is higher

## Slide 78: Medium Access Control
How does a network determine which transmitter gets to transmit?
Remember: the wireless medium is inherently broadcast
  Two simultaneous transmitters may lose both packets

## Slide 79: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Task: in one minute you will have to recite the alphabet
  We’ll jump by tables, one person per letter
  You all fail if two people speak at the same time
  I will ban any strategy that two tables use

## Slide 80: Analogy: wireless medium as acoustic
How do we determine who gets to speak?
  Two simultaneous speakers also lose both “transmissions”
Eye contact (or raise hand) -> out-of-band communication
Wait until it’s quiet for some time -> carrier sense multiple access
Strict turn order -> time division multiple access
Just speak and hope it works -> ALOHA
Everybody sing at different tones -> frequency division multiple access (stretching the metaphor)
Everyone speak in different languages -> code division multiple access
Others?

## Slide 81: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 82: ALOHA
ALOHAnet (1971)
  University of Hawaii – Norman Abramson
  First demonstration of wireless packet network
Rules
  If you have data to send, send it
Two (or more) simultaneous transmissions will collide and be lost
  Wait a duration of time for an acknowledgement
  If transmission was lost, try sending again “later”
    Want some kind of exponential backoff scheme here

## Slide 83: Packet collisions
Each packet transmission has a window of vulnerability
  Twice the on-air duration of a packet
  Transmissions during the packet are bad
  Transmissions before packet can also be bad
My transmission
My transmission
Other transmission
Other transmission

## Slide 84: Slotted ALOHA
Split time into synchronized “slots”
Any device can transmit whenever it has data
  But it must transmit at the start of a slot
  And its transmission cannot be longer than a slot
  Removes half of the possibilities for collisions!
    At the cost of some synchronization method
My transmission
Other transmission
Other transmission
My transmission
time

## Slide 85: ALOHA throughput
It can be shown that traffic maxes out at
  ALOHA: 18.4%
  Slotted ALOHA: 36.8%
Assuming Poisson distribution of transmission attempts
Slotted throughput is double because the “before” collisions can no longer occur

## Slide 86: Capture effect
Actually, two packets at once isn’t always a total loss
  The louder packet can still sometimes be heard if loud enough
How much louder?
  Ballpark 12-14 dB
When does this work?
  Depends on the radio hardware
  Louder packet first almost always works
  Louder packet second sometimes works

## Slide 87: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 88: CSMA/CA – Carrier Sense Multiple Access with Collision Avoidance
First listen for a duration and determine if anyone is transmitting
  If idle, you can transmit
  If busy, wait and try again later
“listen before send”
Can be combined with notion of slotting
  If current slot is idle, transmit in next slot
  If current slot is busy, follow some algorithm to try again later

## Slide 89: CSMA/CD – CSMA with Collision Detection
Detect collisions during your own transmission
  Works great on wired mediums (Ethernet, I2C)
Very challenging for wireless systems
  Transmit and receive are usually the same antenna
  Receiving while transmitting would be drowned out by transmission
    Remember: TX at 8 dBm and RX at -95 dBm
  Area of active research!

## Slide 90: Hidden terminal problem
Device A
Device B
Device C

## Slide 91: CSMA with RTS/CTS
Hidden terminal problem means that two transmitters might never be able to detect each other’s transmissions
A partial solution
  When channel is idle, transmitter sends a short Request To Send (RTS)
  Receiver will send a Clear To Send (CTS) to only one node at a time
  RTS collisions are faster and less wasteful than hidden terminal collisions
  Downside: overhead is high for waiting for CTS when contention is low

## Slide 92: MAC protocol categorization
Medium Access Control Protocols
Contention-Based Protocols
Contention-Free Protocols
FDMA
TDMA
Also, CDMA
ALOHA
CSMA

## Slide 93: Contention-free access control protocols
Goal: split up communication such that devices will not conflict
Can be predetermined or reservation-based
  Devices might request to join the schedule and be given a slot
    Devices lose their slot if it goes unused for some amount of time
    Reservations often occur during a dedicated CSMA contention slot
  Assignment of schedules can be complicated
Really efficient at creating a high-throughput network
  Assuming they are all following the same protocol
  Otherwise, interference can be very problematic

## Slide 94: FDMA – Frequency Division Multiple Access
Split transmissions in frequency
  Different carrier frequencies are independent
  Fundamentally how RF spectrum is split
Technically, each device uses a separate, fixed frequency
  Walkie-talkies
Conceptually, how RF channels work
  WiFi networks pick different bands
  802.15.4 picks a channel to communicate on

## Slide 95: TDMA – Time Division Multiple Access
Split transmissions in time
  Devices share the same channel
Splits time into fixed-length windows
  Each device is assigned one or more windows
  Can build a priority system here with uneven split among devices
Requires synchronization between devices
  Often devices must listen periodically to resynchronize
  Less efficient use of slots reduce synchronization
    Large guard windows. E.g. 1.5 second slot for a 1 second transmission

## Slide 96: Real-world protocol access control
ALOHA
  BLE advertisements
  Unlicensed LPWANs: Sigfox, LoRaWAN
CSMA
  WiFi (slotted, CSMA/CA)
TDMA
  BLE connections
  Cellular LPWANs: LTE-M and NB-IoT

## Slide 97: Outline
OSI Layers
Internet Architecture (Upper Layers)
Physical Layer
Data Link Layer