## Slide 1: Lecture 09 IoT Network Routing
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2023
With slides from Federico Ferrari (ETH Zurich) and assistance from Andreas Biri (ETH Zurich)
Materials in collaboration with Pat Pannuto (UCSD)

## Slide 2: Today’s Goals
Overview of routing for mesh networks
  Walkthrough of one protocol (AODV: what ZigBee uses)
Describe research in improving data dissemination

## Slide 3: Outline
Simple Routing
Mesh Routing
Better Flooding

## Slide 4: Routing goals
Have a packet, have a destination, how do we connect them?
We’ll think about a couple of approaches here
  Simple techniques
    Broadcast, tree structures
  Mesh techniques
    Understand the available routes and select a “good” one

## Slide 5: Simple routing solutions
Broadcast
  The link-layer solution for everything
Star topology
  Only one location to send to: parent
  Single parent needs to store information about all children
    Addresses, schedules, etc.
Tree topology
  “Star of stars”
  Two choices: send to descendent or send to parent
  Each parent needs to store information about all children beneath it
  Original ZigBee approach (knowledge built into addressing scheme)

## Slide 6: Many-to-one routing (Collection Tree Protocol, CTP)
Tree optimization for sensor networks
  Keep all devices except the “gateway” as simple as possible
Each device only needs to remember hop to gateway
  If gateway wants to send message back, it must include a full hop path

## Slide 7: Outline
Simple Routing
Mesh Routing
Better Flooding

## Slide 8: Mesh Routing
Mesh topology makes routing question more complicated
  Multiple hops in a route
  Multiple routes between source and destination
  Becomes a graph theory question based on cost metric
A
B
C
D
E
F

## Slide 9: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?

## Slide 10: Flooding
Mesh equivalent of broadcast
  Each node sends to each other node
  Eventually packets will reach the desired destination
  Not really routing at all…
Question: how do we make it stop?
  Maximum retransmissions counter on each packet
    Decrement at each hop. Drop packet when it hits zero
    Need some guess for how many hops to destination
  Or keep some history of recently flooded packets
    Don’t retransmit a recently sent packet

## Slide 11: Reactive routing
Build up a map of the routes through a network
  Hopefully the “optimal” routes
Map routes in reaction to a packet arrival
  Sensor devices are slow and limited
  Most likely to resend to same prior address
  Discover a route when it is needed, then cache for next time

## Slide 12: Ad-hoc On-demand Distance Vector Routing (AODV)
On-demand: Construct routes only when needed
Modern ZigBee routing approach (for Mesh topology)
Routing table
  Destination node -> Next hop (for all cached destinations)
  Store only next hop instead of full route
    All routers along the path must also have Destination->Next mappings
  Also keep hops-to-destination and last-seen-destination-sequence-number
Route discovery
  Upon demand: check table
  If not cached send Route Request (RREQ) via Flooding
    Route is unknown, so flooding is needed
AODV documentation: https://www.ietf.org/rfc/rfc3561.txt

## Slide 13: AODV Route Requests (RREQs)
Request ID identifies this RREQ
  Used to discard duplicates during flooding
  Unless less hops and equally recent, OR more recent
Sequence Numbers are per-device, monotonically increasing
  Used as a notion of “how recently” device has been seen
  Source SeqNo is the source’s most recent sequence number
  Destination SeqNo is the most recently seen from the destination by the source. (Defaults to zero)
Hop Count is the number of hops this request has taken
  Starts at 1 and incremented by each transmitter along the path
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count

## Slide 14: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
A wants to find a route to F, so it sends out an RREQ

## Slide 15: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 1
B and D also opportunistically add a routing table entry for A

## Slide 16: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
B goes first via some access control protocol (D also in contention)
A and D ignore duplicate Request ID C opportunistically adds a routing table entry to A

## Slide 17: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 2
D goes next by some access control protocol (C also in contention)
A, B, and C ignore duplicate Request ID E and F opportunistically add routing table entries to A

## Slide 18: Example AODV RREQ (A to F)
A
B
C
D
E
F
Request ID | Source Address | Destination Address | Source SeqNo | Destination SeqNo | Hop Count
1 | A | F | 1 | 0 | 3
C and E repeat this process with Hop Count 3 (but everyone ignores them)
They go one-at-a-time, but I’m getting tired of drawing these
Actually, they’re in contention with the response from F

## Slide 19: AODV Route Response (RREP)
Reply is sent unicast back to the source via newly constructed route
  Each node along the way already knows the route back
Includes most recent own sequence number as a sense of recency
  “Destination” from the perspective of the original RREQ
  No need for source sequence number anymore
Source Address | Destination Address | Destination SeqNo | Hop Count

## Slide 20: Example AODV RREP (F to A)
A
B
C
D
E
F
Source Address | Destination Address | Destination SeqNo | Hop Count
F | A | 7 | 2
F sends response back to A via D
D opportunistically adds a routing table entry for F

## Slide 21: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
A
B
C
D
E
F

## Slide 22: Break + Practice
C wants to send a packet to E
  What RREQ(s) are sent and what RREP(s) are sent?
    RREQs:
      C -> (B,D,F)
      (B or D) -> A
      (D or F) -> E
    RREPs:
      E -> (D or F) -> C
  Network could have multiple configurations
A
B
C
D
E
F

## Slide 23: RREP optimization
An intermediate node responds with RREP if it already has a path to destination with a more recent Destination sequence number
Source may get multiple RREP responses with different recency and hop counts
  So, some intermediate node could respond “here’s the route I knew of when sequence number was 5”
  Then, destination node could respond “here’s the route right now, I’m actually on sequence number 12”
  Likely want the most recent
    If equally recent, use the least hops

## Slide 24: When to update your route
Routing table entries are updated on RREP if:
  Sequence number in routing table is marked as invalid
  Destination sequence number in the RREP is greater the listed one
  Sequence numbers are the same, but the route was marked as inactive
  Sequence numbers are the same, but the hop count is smaller

## Slide 25: Route maintenance in AODV
If a link in the routing table breaks, all active neighbors are informed with Route Error (RERR) messages
  After some number of retransmissions and timeouts
  RERR contains destination address that broke
Nodes receiving RERR can start RERQ for destination address
  Which lets them find a new path through the network
  And updates everyone’s cached next-hops

## Slide 26: Alternative: Dynamic Source Routing (DSR)
Another reactive routing technique
  Similar design as AODV
In DSR, routing tables have full route to destination
  Each packet transmission includes a list of hops to destination
  So the route to an important destination only has to be stored on the source device that cares about it
  Intermediate nodes do not need any route storage for that destination
    Cost is extra bytes used in each packet for route
During discovery, all paths are returned by destination
  So source gets a full list of possible route choices

## Slide 27: Tradeoffs for reactive routing
Upside: no transmissions unless there is demand
  Routes might appear, disappear, reappear, but no need to update if no one actually wants to transmit anything
Downside: large, variable delay when actually sending a packet
  Full RREQ/RREP protocol before data can actually be sent
  Route might have broken at some point
    So data will be sent based on cached information
    RERR will occur
    RREQ/RREP will occur
    Then data will be sent again

## Slide 28: Proactive routing
Alternative to reactive is to know the routes ahead of time
Periodically query for the possible routes in the network
  Save all routes that are important (maybe just all routes?)
  Also redetermine routes whenever topology changes (nodes join/leave)
Upside: when a packet arrives, route to destination is already known
Downside: requires more memory and effort on part of routers
  Wastes some network bandwidth on checking for route changes

## Slide 29: Distance-Vector
Keep routes as “next hops” rather than full routes
  AODV uses this method (DV for Distance Vector)
Can be combined with proactive techniques too
  Each router periodically informs neighbors of its shortest paths to each destination (in terms of hop count)
    Essentially just broadcast your routing table
  Routers choose the best route available
    Either old next-hop it was already aware of
    Or new next-hop through neighbor (with cost of their hops + 1)
  Need to be careful to avoid loops!

## Slide 30: Thread routing
Uses a proactive, distance-vector protocol for unicast routing
If node is a child, send packet to parent router
If node is a router,
  Consult table for address within mesh
    (RLOC helps here!)
  Send to border router for address outside of mesh
Multicast uses a data dissemination protocol (Trickle)
  Or falls back to flooding

## Slide 31: Break + Discussion
Hop count is one possible metric for determining routes
What else might be considered?

## Slide 32: Reliability as a cost metric
Link quality can very from node to node
  Fewest hops might not be the “fastest” or “most reliable” path
ETX: minimize “expected transmissions”
  Measure link quality over time to determine each link’s reliability
A
B
C
D
E
F

## Slide 33: Alternative cost metrics
Spatial reuse
  Prefer transmission on links that do not interfere with each other
  Improves ability to pipeline data through network
  Example: A<->B and E<->F
Energy availability
  Prefer routing through nodes with more remaining available energy
  Prefer wall-powered nodes over battery-powered
Arbitrarily complex combinations possible

## Slide 34: Outline
Simple Routing
Mesh Routing
Better Flooding

## Slide 35: Flooding is a recreation of broadcasts
Goal: get information to all nodes
  This is the problem of “data dissemination”
Problem: difficult in Mesh topologies
  Packet loss, retransmission delays
Really, the desire for data dissemination is just to broadcast to all nodes
  But broadcast transmissions don’t reach far enough to cover entire mesh

## Slide 36: Glossy: what if we expand broadcast range by having multiple nodes participate?

## Slide 37: Synchronous transmissions
Multiple nodes transmit same packet at same time
R can receive packet with high probability if Δ is small
  May even improve probability of reception (more energy at receiver)
500 ns is 1/32 of a symbol for 802.15.4 (chip duration)

## Slide 38: Sidebar: broadcast transmission acknowledgements
A-MAC: https://web.eecs.umich.edu/~prabal/pubs/papers/dutta12amac.pdf
P = Probe (data request) A = Acknowledgement
D = Data transmission L = Listening period
P-CW = Probe with Contention Window for response

## Slide 39: How do we avoid interference?
Fundamental insight:
  “say exactly the same thing at exactly (enough) the same time” leads to coherence instead of interference
In 802.15.4, an ACK is sent exactly 192 µs after receiving
  The ACK packet contains only the sequence number being ACK’d
  Does not contain source address of the ACK-er
  Which is why this works:

## Slide 40: Glossy key techniques
Temporally decouple network flooding from application tasks
Exploit synchronous transmissions for fast network flooding

## Slide 41: Fast packet propagation in Glossy

## Slide 42: Fast packet propagation in Glossy

## Slide 43: Fast packet propagation in Glossy

## Slide 44: Fast packet propagation in Glossy

## Slide 45: Glossy details
When Glossy starts
  All nodes turn on radios to receive

## Slide 46: Glossy details
Initiator
  Set relay counter in packet, C = 0
  Broadcast packet

## Slide 47: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 48: Glossy details
At packet reception:
  Increment relay counter C
  Transmit synchronously (at a fixed period after the reception)

## Slide 49: Glossy details
Stop rebroadcasting and turn off radio when
  Already transmitted N times
  Networks pick N for reliability/energy tradeoff

## Slide 50: Glossy details
Tslot is constant by design
  Needs to be short to make constructive interference work
Beginning of slot (tref) provides synchronization point
  As a bonus, all nodes are synchronized after flooding event

## Slide 51: Glossy implementation
Device must be able to have tight time bounds on rx/tx
  500 ns wiggle room maximum
  Includes receive, processing, transmission
    Implies a maximum physical distance for a network
Need to pick an N for reliability

## Slide 52: Application of Glossy: avoid routing altogether
Low-Power Wireless Bus (LWB)
  Federico Ferrari, Zimmerling, Mottola, Thiele. SenSys’12
Use Glossy for all device communication
  Make one broadcast domain (a bus) where all nodes communicate
  Avoids all issues of routing, everything is a broadcast
    Works for unicast, multicast, anycast, and broadcast transmissions
General idea: TDMA Glossy floods
  Synchronization is already given to nodes by Glossy
  One coordinator makes the TDMA schedule

## Slide 53: Outline
Simple Routing
Mesh Routing
Better Flooding