## Slide 1: Lecture 14 Unlicensed LPWANs
CS397/497 – Wireless Protocols for IoT
Branden Ghena – Winter 2023
Materials in collaboration with Pat Pannuto (UCSD)

## Slide 2: Administrivia
Friday (Feb 24): WiFi Lab
Wednesday (Mar 01): Cellular Homework
  Last homework
  Counts as double points
This weekend: LoRa Lab

## Slide 3: Today’s Goals
Overview of unlicensed-band LPWAN approaches
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 4: Resources
LoRaWAN
  LoRaWAN Specification version 1.1
  LoRaWAN Regional Parameters version 1.0.2
Sigfox
  Sigfox Technical Overview
  IETF Descriptions
    https://www.ietf.org/proceedings/97/slides/slides-97-lpwan-25-sigfox-system-description-00.pdf
    https://tools.ietf.org/html/draft-zuniga-lpwan-sigfox-system-description-04

## Slide 5: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 6: Wide area networks
Communication at the region/city scale rather than the building/residence scale
  Throughout cities
  Agricultural deployments
  Industrial facilities
City-scale sensing is one very popular domain
  What might we want to sense throughout a city?

## Slide 7: Example application: air quality monitoring
[1] Cheng et al. AirCloud: a cloud-based air-quality monitoring system for everyone. 2014. [2] Purple Air. 2019.
[1]
[2]
[2]

## Slide 8: How do we collect data from a sensor?
Manually collect measurements
  Too much work
Connect it to WiFi (or Ethernet)
  Too many separate networks
Pay for cellular access
  Too expensive for many devices

## Slide 9: How do we collect data from MANY sensors?
Manually collect measurements
  Too much work
Connect it to WiFi (or Ethernet)
  Too many separate networks
Pay for cellular access
  Too expensive for many devices

## Slide 10: We need another network option
Requirements:
Wide area of coverage
  Deploy fewer gateways
Low power
  So we can deploy on batteries
Doesn’t need high throughput
  Sensor data is relatively small

## Slide 11: Long-range, low-data needs haven’t historically been met
Data
Throughput
Range
WiFi

## Slide 12: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range

## Slide 13: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
BLE
Zigbee
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost

## Slide 14: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
2G
3G
4G
BLE
Zigbee
2G
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
3G

## Slide 15: Long-range, low-data needs haven’t historically been met
Bluetooth
WiFi
3G
4G
BLE
Zigbee
Low-Power Wide-Area Networks
Data
Throughput
Range
Lower Power & Lower Cost
Higher Power & Higher Cost
2G

## Slide 16: LPWANs overview (common qualities)
Higher power transmissions: ~20 dBm (100 mW)
Unlicensed 915 MHz band (902-928 MHz)
Many channels to support lots of devices
Low data rate 100 kbps or less
Range on the order of multiple kilometers
Simple Aloha access control

## Slide 17: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 18: LoRaWAN
Open communication standard built with proprietary LoRa PHY
Low rate (1-20 kbps) and long range (~5 km)
  Shorter range than Sigfox but much higher bit rate
Most popular LPWAN protocol
  Target of academic research
  Industry involvement in hardware and deployments

## Slide 19: LoRa PHY uses a different modulation
Chirp Spread Spectrum (CSS)
  Modulation technique where frequency is varied linearly from lowest to highest within a channel

## Slide 20: Chirp Spread Spectrum
Data is modulated in the starting and ending points of chirp
  Frequency increases linearly, modulo bounds of the channel

## Slide 21: CSS has a Spreading Factor which determines bit rate
Spreading Factor is essentially the rate-of-change of frequency
  Slope of the line
  Lower values of spreading factor (steeper slope) are faster data rate
Important: different spreading factors are (mostly) orthogonal!
  Two can overlap in time, space, and channel without a collision

## Slide 22: LoRaWAN channels (in the US)
Sixty-four, 125 kHz uplink channels
  Frequency Hopping over the 64 uplink channels
  Plus eight, 500 kHz overlapping uplink channels (not very used in practice)
Eight, 500 kHz downlink channels

## Slide 23: LoRaWAN data rates
Data Rate Index | Spreading Factor | Bit Rate
125 kHz Uplink Rates |  | 
0 | SF10, 125 kHz | 980 bps
1 | SF9, 125 kHz | 1760 bps
2 | SF8, 125 kHz | 3125 bps
3 | SF7, 125 kHz | 5470 bps
500 kHz Uplink Rates |  | 
4 | SF8, 500 kHz | 12500 bps
500 kHz Downlink Rates |  | 
8 | SF12, 500 kHz | 980 bps
9 | SF11, 500 kHz | 1760 bps
10 | SF10, 500 kHz | 3900 bps
11 | SF9, 500 kHz | 7000 bps
12 | SF8, 500 kHz | 12500 bps
13 | SF7, 500 kHz | 21900 bps
Data rate options depend on channel in use
  Unbalanced uplink and downlink
64-channel uplink
  1-5 kbps data rate
Allowable rates based on US dwell time restriction (400 ms)
  Different in different regions

## Slide 24: LoRaWAN link budget
Typical TX power 20 dBm
  Up to 30 dBm for 64-channel hopping
  Up to 26 dBm for 8-channel hopping
Receive sensitivity -119 dBm
  Compare to -100 dBm for 802.15.4 and -95 dBm for BLE
Resulting range is about a kilometer in urban environments

## Slide 25: LoRaWAN gateways
No synchronization with end devices
Instead listen to entire bandwidth simultaneously
  Only 12 MHz total
  Recognize preambles and allocate hardware to decode packet
    Cheap gateways: 8 decoders
    Good gateways: 64 decoders

## Slide 26: LoRaWAN MAC
Uplink: Aloha - transmit whenever
  Randomly split across 64 uplink channels (reduced odds of collision)
  Devices a different spreading factors also do not collide
  Packets are very long though: up to 400 ms in duration
Downlink: listen-after-send (class A device)
  Two windows for RX on different channels

## Slide 27: Optional downlink mechanisms
Periodic listening (class B device)
  Synchronized with periodic beacons
    TX still unsynchronized Aloha
  Mostly unused
Continuous listening (class C device)
  Always-on receivers

## Slide 28: LoRaWAN packet format
Frame header includes device address
MAC Payload maximum size depends on data rate
  Again based on dwell time in the US
Data Rate Index | MAC Payload Size
0 | 19 bytes
1 | 61 bytes
2 | 133 bytes
3 | 250 bytes
4 | 250 bytes

## Slide 29: LoRaWAN network details

## Slide 30: LoRaWAN hardware
Numerous hardware modules and development kits
  Almost all use Semtech radio chips (Semtech owns LoRa PHY)
Recent addition: STM32WLE5 LoRa SoC
  Cortex-M4 + LoRa radio (analogous to nRF52840)

## Slide 31: LoRaWAN network providers
You can always manage your own network
  Buy a gateway and run whatever backend software you want
Somewhat-managed network providers
  The Things Network (predominantly in Europe)
    But available in the US too!
  Helium
    Anyone can buy and install their own gateway, which serves everyone
    Microtransactions to pay for communication

## Slide 32: TTN Scale [Jan 2022]
About 97000 devices in Feb 2023

## Slide 33: Helium Scale [Jan 2022]
May 2022: 800,000 hotspots, with +80K in last 30 days
Feb 2023: 980,000 hotspots, with +3K in last 30 days

## Slide 34: Quick reality check: Cellular?
~350,000 sites across ~150,000 towers
  In the just US

## Slide 35: LoRaWAN interested parties
MachineQ is a subsidiary of Comcast providing LoRaWAN networks
Long-term goal
  Indoor-to-outdoor LoRaWAN gateways combined with WiFi/Cellular
  Tune down power for 100-200 meter range
Current focus: IoT Platform-as-a-service
  Devices, network, analytics

## Slide 36: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink

## Slide 37: Break + Open Question
What kinds of use cases exist for LoRaWAN?
  What can you do with 1-5 kbps uplink, 1-22 kbps downlink?
  Multiplied by 64 channels uplink, 8 channels downlink
Outdoor small-sized sensing seems possibly achievable!
  With a low enough rate, it could support many devices
Code updates on devices could be tough

## Slide 38: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 39: Sigfox
Very low-rate (600 bps), very long-range (10+ km) communication
Star-topology networks, with always-listening gateways
  Any number of low-power end devices
Uplink-focused communication
Applications: very low-rate metering

## Slide 40: Sigfox PHY
Unlicensed-band communication
  Europe 868 MHz. US 902-928 MHz (915 MHz band)
Ultra-narrowband 600 Hz (100 Hz Europe) channel bandwidth
  Detection only needs to occur at very specific frequency
  Helps improve signal-to-noise ratio

## Slide 41: Sigfox unbalanced uplink and downlink
Uplink
  600 Hz bandwidth, 600 bps, DBPSK
Downlink
  1.5 kHz bandwidth, 600 bps, GFSK
Particularly designed for Europe
  Uplink on 1% duty cycle channel, up to 14 dBm
  Downlink on 10% duty cycle channel, up to 27 dBm
Works fine in US too
  Gets more power (24 dBm up is typical, up to 32 dBm down) and more range

## Slide 42: Sigfox link budget
Why transmit at 100-600 bps?
  For greatly increased link budget
Link budget: 150-160 dBm
  Assuming Tx at ~20 dBm
  Means Rx Sensitivity of -130 dBm (10 dBm better than LoRaWAN)
Resulting range: 10-15 km in urban environments
  Except that buildings lead to dead spots in range

## Slide 43: Sigfox MAC
Aloha-style access control (send whenever)
  No acknowledgements!
Send message three times for increased reliability
  Then listen for downlink at a set period later on a known frequency

## Slide 44: Sigfox uplink packet
Up to 29 bytes total per packet
  Payload: up to 12 bytes 😱
Other fields
  Preamble + Frame Sync are really a 6 byte field for radio sync
  Authentication: 2-5 bytes
  Frame Check Sequence: 16-bit CRC

## Slide 45: Aside: why faster bitrate in the US?
Packet size up to 29 bytes (232 bits)
  At 100 bps: 2.32 seconds on air
  At 600 bps: 0.387 seconds on air
Maximum dwell time for 915 MHz band: 400 ms

## Slide 46: Sigfox downlink packet
Similar structure, 28 bytes total
  Payload: up to 8 bytes
Larger preamble + frame sync of 13 bytes
Error Correcting Code for increased reliability

## Slide 47: Sigfox deployments
Proprietary network with managed deployment
  Like cellular networks
  Sigfox deploys networks and transports data
  140 uplink messages plus 4 downlink message per day
Connectionless communication
  Devices are registered with the networks
  Keys are provided in the software image
  Any deployed Sigfox gateway can collect transmitted data
    Enables mobile applications

## Slide 48: Sigfox coverage (Spring 2022)
Not focused on US coverage right now (coverage is blue)
  Much higher availability in Europe
  No longer planned rollout in US (purple)
January 2022
  Sigfox filed for bankruptcy
April 2022
  Sigfox purchased by UnaBiz

## Slide 49: Break + Open Question
What kinds of use cases exist for Sigfox?
  What can you do with 600 bps uplink, 600 bps downlink?
  Multiplied by ?hundreds? of channels (~400 in Europe)

## Slide 50: Break + Open Question
What kinds of use cases exist for Sigfox?
  What can you do with 600 bps uplink, 600 bps downlink?
  Multiplied by ?hundreds? of channels (~400 in Europe)
Many devices that aren’t doing very much
  Simple status monitoring (water, electric, etc.)
    Not metering necessarily, but activity detection
    Did a breaker trip?, is water flowing?, etc.
Definitely no code updates

## Slide 51: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 52: IEEE standard for LPWANs
802.11ah (HaLow) standard in 2016
  First real hardware in 2020
  Still not in real-world use yet
Focus on the indoor-to-outdoor scenario
  Medium range (maximum 1 km)
915 MHz communication
  NOT interoperable with other 802.11 access points and devices
Theoretically up to 356 Mbps
  Practically, most devices are expected to implement 150 kbps to 8 Mbps

## Slide 53: 802.11ah allows multiple bandwidth allocations

## Slide 54: 802.11ah architecture
Star topology
  Up to 8191 devices per access point
Devices are assigned to a group
  Groups are scheduled slots with TDMA
  Within a slot CSMA/CA is used for contention among devices
  Devices not in the group can sleep until their slot
Traditional IP communication on top of that
  And traditional 802.11 security mechanisms (WPA2/TLS)

## Slide 55: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces

## Slide 56: TV whitespaces
Unused TV channels between 54 MHz and 698 MHz
  VHF (54-216 MHz)
  UHF (470-698 MHz)
  6 MHz channel width
Allocated but unused
  FCC allows unlicensed use
  IF you do not interfere with primary users

## Slide 57: Sensing channel use
Variation in use
  Spatial: Cannot assume same channel will be free everywhere
  Temporal: Cannot assume channel will be free at all times
Cognitive radio approach
  Dynamically identify unused portions of spectrum
Database approach
  Let someone else do the scanning. Consult database based on location and time

## Slide 58: 802.11af
IEEE standard for whitespaces circa 2014
  Not much (any?) use to date
US/Canada-specific
  Limits general-purpose product appeal
Requires infrastructure about whitespace availability
  People are figuring this out, but not really available yet
  [n.b. very active area of research; including here]

## Slide 59: Sensor Networks Over tv Whitespaces (SNOW)
A design for sensor networks over whitespaces
  Base Station manages channel for deployment
  Frequency division for devices. Each uplinks on separate subcarrier
  Downlink is one OFDM transmission. Each device hears its frequency

## Slide 60: Outline
Wide-Area Network Background
Unlicensed LPWANs
  LoRaWAN
  Sigfox
  802.11ah
  TV Whitespaces